## Slide 1: CMS status report
Pierluigi Paolucci (INFN of Napoli)
on behalf of the CMS collaboration
118th meeting of LHCC Open Session – 4 June 2014 CERN

## Slide 2: Outline
LS1 activities
Sub-system status report
DAQ-Offline-Computing
Physics highlights
Conclusion

## Slide 3
LS1 activities
Sub-system status report
DAQ-Offline-Computing
Physics highlights
Conclusion

## Slide 4: Technical Coordination
Currently configuring for beam-pipe installation
new central beam-pipe installation (45mm outer
diameter) starts next week followed by pixel
Installation.
Bake-out
July-Aug
Install pixel
(barrel+forward)
BCM+PLT
Aug-Sep
Closed for
magnet test
& CRAFT
Oct-Nov
Keep contingency for re-opening
beam-pipe pump-down:
Jan 2015 then ready for physics

## Slide 5: LS1 winding down
A sample of what still needs to be deployed…
  DAQ2
  Trigger Control and Distribution System (TCDS)
  L1 trigger improvements
  Forward HCAL back-end electronics
  Lumi DAQ

## Slide 6
Global Run tentative schedule
Cooling maintenance + DAQ2 installation/commissioning
Commissioning runs
Cosmic alignment run at B=0T
Cosmic alignment run at B=3.8T

## Slide 7
LS1 activities
Sub-system status report
DAQ-Offline-Computing
Physics highlights
Conclusion

## Slide 8: Trigger Upgrade Status
  Trigger rate up to 6 times the RUN1 is expected.
  Calorimeter and Muon trigger upgrade necessary.
  CALO: Legacy trigger and new trigger for 2015 run
Calo Layer 1 (CTP7)
  2 prototypes + 6 additional pre-production boards built.
  Excellent results with processor system, power supplies,
  clock system and optical/backplane links
    Tested 4.8 & 6.4 & 9.6 Gbps synch. and 10 Gbps asynch.
Calo Layer 2 (MP7) about ready
Muon: combining 3 independent subsystem triggers
Work in progress:
Muon trigger link concentration and fan-out
Muon Track-Finder (barrel/endcap/overlap)
Muon
Calo

## Slide 9: Tracker readiness for RUN2 ready to operate at -15 oC (validated at -20 oC)
Final insulation from the bulkhead periphery all the way to the edge of the vac-tank
Pixels are pre-calibrated on surface lab
Pixel almost ready for re-installation
Finalizing the new molds for the inner nose
9

## Slide 10: ECAL + eg trigger
Upgrade to ECAL Level-1 trigger: change links between ECAL Trigger Concentrator Cards (TCC) and Regional Calorimeter Trigger (RCT) from electrical to optical
All hardware in place and optical fibers being installed and commissioned
Removal of SLBRCT cables (the white ones, underneath!)
Replacing SLBs with oSLBs
Nov. 2013: damaged connector found on ES.
Both ES removed from CMS to the surface, repaired, reinstalled and now re-commissioned.
99.95% channels operational.
Finishing the repair of ES

## Slide 11: HCAL status
Installation and commissioning of SiPM readout on HO (April) - DONE
Installation of new thin window, multi-anode PMTs DONE
  Being commissioned by July
Production of new Back-End board for HF
  Pre-production (10 boards) ok, production ordered and expected delivery at CERN in July
  Commissioning planned for late September.
HF Front End
Test of new QIE10-based readout successfully tested at FNAL test beam
Expected installation in Year-end Technical Stop 2015/16

## Slide 12: Drift Tubes towards Run2
250 chambers
172200 drift tubes
Sector Collector (Read-Out and Trigger) relocated out of UXC: installed 3500 optical links that make single outputs of all 250 chambers available in USC
Chamber HV: 312 channels recovered
Chamber Minicrates:
3200 channels recovered

## Slide 13: Review of CSC activities during LS1
Focused on 3 main areas (in order of priority):
  Present system consolidation, maintenance and repair
    Repair system faults from Run 1 –> recover highest efficiency. Improve system reliability (HV, LV, racks, detector infrastructure)
  ME1/1 chamber electronics upgrade
    72 chambers extracted, refurbished and reinstalled in CMS.
    Increase capacity for data rate and exploit full chamber segmentation in 2.1<|h|<2.4 to enhance rate capability (including @ HL-LHC) and improve muon reconstruction
  Completion of station 4 (ME4/2 ring 1.2<|h|<1.8 )
    Re-establish 4-station redundancy over all 0.9<|h|<2.4 range. Improve muon-ID efficiency and sustain high-Lumi L1 rates at a reasonably low pT threshold
    Construct and test 72 CSC at CERN, install and commission in CMS (in close coordination with RE4 project)
Chamber efficiency during Run 1

## Slide 14: CSC consolidation in pictures
ME1/1 refurbishment lab
in SX5
ME1/1
installation
ME4/2 chamber factory in B904
ME4/2
installation

## Slide 15: RPC upgrade
RPC upgrade (RE4) completed on May 5.
686 gaps produced in 22 months
72 super-modules installed ahead of schedule
Commissioning is on-going. No major problem encountered until now.
RE4 project has been completed on schedule and in the budget
Production quality
Naked Super-Module
Production quality
Maintenance and repairs
99.5% of working channels today

## Slide 16: RPC RE4 144 chambers installed

## Slide 17: Beam monitoring and luminosity
Upgrade Fast Beam Conditions monitor
  Single integrated PCB with rigid and stiff component, minimizing material budget and connections: structure done.
Si-Pixel Luminosity Telescope
  Success trial installation of new detector mock-up in pixel volume
  Hybrid board production & testing in full swing
Some members of the Design and production team at CERN
BRIL (Beam Radiation Instrum. and Luminosity) milestones achieved
PLT calib.

## Slide 18: April Global Run: some achievements
All: clock frequency scan
ECAL: test new optical links
Strips: run constantly at 15°C
HCAL: Commission new SiPMs
DT: Commission relocated electronics
Muon Endcap: First global run with 4th endcap station (RPC and CSC)
First run with Prompt Calibration Loop on cosmics
Lots of new things in the April Global Run (7-11 April)

## Slide 19
LS1 activities
Sub-system status report
DAQ-Offline-Computing
Physics highlights
Conclusion

## Slide 20: DAQ status
DAQ2: New central DAQ system for run 2
  Aim:
    Accommodate new uTCA based sub-detector back-end electronics as well as legacy ones
    Replacement of most networking and computing equipment (5-years end-of-life)
    Lumi-DAQ system to acquire data time-based (independent of level-1 triggers)
    Various improvements motivated by operational experience from run 1
  Status:
    Most components demonstrated on small scale test bed
    Custom electronics 100% produced and installed
    Most of the IT-equipment delivered and installed
  On track for changeover scheduled July-2014 (global run)
HLT farm for RUN2: plan to order CPU and storage in few months
Online cloud: Use of HLT farm for offline processing
  Was recently used for offline production (Heavy Ion reprocessing for QM2014)

## Slide 21
Planning integrated Computing, Software and Analysis Challenge 2014 (CSA14) for Summer
major milestone for analysis readiness towards data-taking
  New lepton ID, new PU rejection, new jet definition for high-PU 13TeV collisions
  Realistic beam conditions, detector alignment and calibration
  Intense work to update DQM code (online and offline) to new run conditions and new DAQ
Bunch Spacing [nsec] | Int. Lumi | Target Lumi [1033 cm-2s-1] | PU
50 | 100 pb-1 | 7.5 | 40
25 | > 1 fb-1 | 7 to 14 | 20 to 40
Run II readiness: CSA14
Considered scenarios

## Slide 22: Computing
Resources are fully utilized
  Several high-priority campaigns (detector upgrade studies, CSA14, specific physics results)
Computing improvements will be validated during CSA14:
  More flexible and efficient access to data
Chart: CMS Utilization
| 40178.0 | 40209.0 | 40237.0 | 40268.0
Tier-1 | 143.99 | 114.22 | 139.28 | 103.25
Tier-2 | 80.5 | 86.16 | 123.62 | 108.81
125% utilization at Tier1s
99.8% utilization at Tier2s
  Improved distributed analysis tools
  Prompt reconstruction distributed also to Tier1 sites

## Slide 23: Next major CMSSW version to be released in June
Major new features include:
  Geometry for 2015 CMS detector
  Integration of Geant 4.10
  Deployment of multi-threaded framework
Our change to a multi-threaded framework is needed in 2015 to:
  Process large samples in less time
  Reduce the total memory per node
Modifications to our reconstruction algorithms have been done to effectively use this framework

## Slide 24
LS1 activities
Sub-system status report
DAQ-Offline-Computing
Physics highlights
Conclusion

## Slide 25: Published papers (from CDS)
Steady rate of publication, in all groups
309 published

## Slide 26: Breakdown of CMS Publications
Table with April 2014: submitted “collision” papers
312 274
June 2014

## Slide 27
Constraints on the Higgs boson width
arXiv: 1405.3455 – submitted to PLB 14 May
A measurement of relative off-shell and on-shell production and H→ZZ decay provides direct information on ΓH
H→ZZ→4l channel: at high mass 2D fit on m4l and a matrix element likelihood discriminant Dgg
H→ZZ→2l2ν channel: fit on the transverse mass or ET
Combined with H→ZZ→4l on-shell measurement, an upper limit is set at 95% CL of ΓH < 22 MeV (corresponding to 5.4×ΓHSM)
dashed line total yield for ΓH = 10 ΓSM
4-lepton invariant mass distribution
A clear enhancement is visible using
ΓH = 25 ΓSM

## Slide 28: Top Mass from 8 TeV data
At the recent “Rencontres de Moriond” conference, the CMS collaboration presented a new improved mass measurement (80% of the data collected during Run I).
The new measurement yields a top quark mass mtop=172.04±0.19±0.75 GeV
Signature: 1 lepton + 4 jets (2 from b) + missing transverse momentum
Reconstructed invariant mass distributions for events before and after the kinematic fit to a top-quark pair event hypothesis.
Systematic: jet energy scale, pile-up effect and modeling of the jet-energy resolution

## Slide 29
Heavy Ions highlights
Nuclear modification factor in pPb normalized to p-p. It rise above 1 (anti-shadow region)
ATLAS (left) and CMS (right)
PAS-HIN-14-006
Gives info about the mechanism of particle production in proton-nuclei collision.
The azimuthal anisotropy Fourier harmonic v2, extracted with 4, 6, 8 and all (LYZ) particle correlations shows that the v2 signal in pPb collisions is of COLLECTIVE nature. This supports the interpretation that hydrodynamic expansion behavior is observed in pPb collisions as well as previously in PbPb interactions.
ATLAS confirmed the surprising Hadron RpPb result
CMS made public in November 2013.
5.02 TeV pp reference data to increase RpPb precision
The 2-4 particles correlation analysis extended to 6-8

## Slide 30: More data analysis results
Since LHCC March 5th
EXO-12-030 - Search for LQ with top+tau pairs
FSQ-13-003 - Drell-Yan pT distributions at low and high mass
HIG-14-003 - H -> gamma gamma with Dalitz decays
HIG-14-001 - tHq, H -> gamma gamma
TOP-14-006 - LHC Top charge asymmetry combination
SUS-13-018 - Search for direct Sbottom production
TOP-13-014 - Top Mass World Combination
TOP-14-001 - Top mass in lepton+jets (e,mu)
SUS -13 020 - pMSSM interpretation 8TeV
HIG-14-002 - Width measurement from off-shell production in H->ZZ S
Since Moriond
HIG-13-032 - H->hh->2gammagamma 2b
GEN-14-001 - Underlying Event Tunes and Double Parton Scattering
TOP-14-003 - Search for anomalous single top + photon production (FCNC)
TOP-14-007 - Limits on anomalous couplings and FCNC in t-channel single top
B2G-13-004 - Search for Dark Matter production in association with top quark pairs
EXO-12-047 - Monophoton search
SMP-13-013 - Measurement of Z production as function of pT, Y
QCD-11-006 - Studies of Multijet Events at 7 TeV

## Slide 31: Summary
Maintenance and repair of the present system is proceeding very well.
Set of global and cosmic runs foreseen in 2014 to prepare the community for RUN2.
Muon upgrade (CSC and RPC) have been completed in time and within budget.
Many improvements on-going in the reconstruction and online software.
DAQ upgrade (DAQ2) progressing on schedule.
Trigger for 2015 on schedule.
309 papers published.
A lot of new results in the physics analyses.
Not covered here: preparation of Technical Proposal for Phase II in full swing.

## Slide 32: 24 & 25 May - general public 4536 visitors: 300 people/h visiting

## Slide 33: New CMS building at P5: inaugurated 24 May

## Slide 34
Thanks a lot

## Slide 35: Backup

## Slide 36: HIN Analyses for Quark Matter
Analysis Entry | Description
HIN-12-007 | Psi(2s)/Psi(1s) in PbPb w/ updated 2013 pp reference
HIN-13-007 | W boson x-section and charge asymmetry in pPb
HIN-14-001 | Jet x-section and nuclear modification factor in pPb
HIN-14-002 | Long-range (ridge) correlations with K0s and Λ in high multiplicity pPb
HIN-14-003 | Z boson x-section and forward-to-backward ratio in pPb
HIN-14-004 | Exclusive B meson x-section and nuclear modification factor in pPb
HIN-14-006 | Multiparticle correlations in PbPb and high multiplicity pPb
HIN-14-007 | b-jet x-section and nuclear modification factor in pPb
HIN-14-008 | Eta dependence of long-range (ridge) correlations in pPb
HIN-14-010 | Jet-track correlations (missing pT) in PbPb
HIN-14-012 | Flow factorization breaking in pPb and PbPb
HIN-14-013 | Bose-Einsten correlations w/ identified pions and kaons
https://twiki.cern.ch/twiki/bin/view/CMSPublic/PhysicsResultsHIN

## Slide 37: Trigger Coordination Status
Many changes in the object reconstruction at HLT
  Goals: reduce CPU time, particularly in tracking
  improve resolution to allow tighter thresholds
  Improve efficiencies

## Slide 38: 2015 Intermediate Calo Trigger Upgrade
Connection of legacy trigger from Regional Calo Trigger to new uTCA Layer-2 processors for jets, EG, taus, and energy sums via ORSC optical interface
Met key milestone this month on testing the ORSC optical link interface to the MP7 layer-2 processor (10 Gbps asynchronous link)
  50 hour communication test of 2 ORSCs to one MP7 (full calorimeter input) at 10 Gbps asynch. with no errors and with data aligned