ISOLDE DECAY STATION
Guy Rosin

---
Detector Setup
The Decay station contains several detectors to measure radioactive decay, as of now ,
 the high purity Germaniums
 detectors (Clover
and Miniball),
LaRB3 Scintillators
and plastic detectors

---
Detector setup
Gr Detectors have high energy resolution, but low response time (~microseconds), Scintillators have high response time (~nanoseconds), but more noise. The HPGs are used to distinguish events from noise
and the scintillators are then
used to get a more accurate
of gamma decays.

---
Computer Drawing

---
5968,66
65,00
775,03
1682,72
10000,00
1
7
6
3
,
3
8
4
8
3
0
,
2
1
7
9
7
,
9
6
8
7
8
,
0
0
3
5
6
0
,
4
4

---
Beam Line

---
Deflector
Diagnostic box
-calorimeter
-Faraday cup
Quadrupole focusing

---
Quadrupole Focus

---
Tape Station
Tape Station is used to remove the noise from the decay products. Products of radioactive decay still emit radiation which interferes with the detectors, so the tape removes the decay products from the detector configuration.  The decay products are implemented in the Mylar tape and cycled down to the lead protected bin.

---
Stress Test
Future uses, One of the things the CAD drawing might be used for is a stress analysis. A stress analysis shows the net force on the objects in the model (usually from gravity). The equipment usually sags
 under its own weight which
 causes error in the alignment.
 Stress test can be used
to calculate in advance
corrections in the equipment

---
Liquid Drop Model of the Nucleus

---
Shell Model
The most stable nuclei have filled up a proton or neutron shell. The “magic numbers” of stability correspond to a full shell.