## Slide 1: Two Beam Module Program News
Organizational changes
Measurements on the Test Module
Status of the CLEX module
Outlook and conclusions

## Slide 2: Organizational changes
Germana left the BE-department and the rf-group as of May 1st
All activities have been integrated into BE-RF-MK (section leader: Olivier Brunner)
Nuria took on the x-band structure fabrication and development
Markus and Steffen are responsible for the two beam module program
Future industrialization studies remain with Philippe, some structure related studies are likely followed up by Nuria

## Slide 3: TBM status
infrared camera
Mechanical prototype module successfully constructed
Currently under thermal and alignment testing
Two more modules under assembly for integrated tests
One module under construction for beam testing in CTF3. Installation will start end of June
Module test program in the lab until 2015, in CLEX until 2016
Future plans: Incorporate lesson learned form the test program into the design of next generation modules and industrialization studies

## Slide 4: Thermal test data example
Water only
Unloaded
Loaded
Temperature evolution (Zero - Unloaded - Loaded conditions)
Temperature fluctuation: ± 0.2 oC
Elena Daskalaki, Alex Vamvakas,
Anastasia Xydou

## Slide 5: Results
Component | Time constant τ (min)
SAS#1 | 5.16
SAS#2 | 5.30
SAS#3 | 5.05
SAS#4 | 5.08
AS Load 1 | 1.86
AS Load 2 | 2.00
AS Load 3 | 1.90
AS Load 4 | 1.80
PETSu#1 | 16.19
PETSu#2 | 18.83
WG | 18.61
RFN Loads | 1.80
Thermal time constants
Chart: 
ΔΤ
τ
62.3% of ΔΤ
Elena Daskalaki

## Slide 6: Results and comparison with FE-simulations
Components’ temperatures in steady-state (oC)
 | DBQ only |  |  | Unloaded |  |  | Loaded |  | 
 | Experiment | Simulation | Diff. | Experiment | Simulation | Diff. | Experiment | Simulation | Diff.
SAS#1 | 23.7 | 24.5 | 0.8 | 29.5 | 31.9 | -2.4 | 29.0 | 30.7 | -1.7
SAS#2 | 24.3 | 24.5 | 0.2 | 32.2 | 29.7 | 2.5 | 31.5 | 29.3 | 2.2
SAS#3 | 24.4 | 24.5 | 0.1 | 32.2 | 31.8 | 0.4 | 31.5 | 31.2 | 0.3
SAS#4 | 24.2 | 24.4 | 0.2 | 32.2 | 29.2 | 3.0 | 31.5 | 29.0 | 2.5
PETSu#1 | 22.7 | 23.2 | 0.5 | 25.9 | 29.8 | -3.9 | 26.4 | 27.6 | -1.2
PETSu#2 | 23.2 | 23.2 | 0.0 | 29.4 | 32.4 | -3.0 | 30.1 | 29.3 | 0.8
DBQ#1 | 37.6 | 39.3 | 1.7 | 34.4 | 32.2 | 2.2 | 33.2 | 31.8 | 1.4
DBQ#2 | 36.1 | 38.4 | 2.3 | 33.6 | 33.9 | -0.3 | 31.8 | 33.6 | -1.8
Elena Daskalaki, Alex Vamvakas, Anastasia Xydou

## Slide 7: Further analysis
Twater, out
Twater, in
ΔTwater
Tamb
Qwater
Qair
Q
Elena Daskalaki, Alex Vamvakas, Anastasia Xydou

## Slide 8: Further analysis
 | Twater,in (oC) | Twater,out (oC) | ΔT (oC) | Qwater (W) | Tamb (oC) | Tcomp (oC) | Qair (W) | Qtot (W) | F (m3/h) | Fmeasured (m3/h)
SAS1 | 24.12 | 30.02 | 5.90 | 744 | 20.00 | 29.16 | 73 | 817 | 0.108 | 
SAS2 | 24.44 | 32.12 | 7.69 | 720 | 20.00 | 32.18 | 97 | 817 | 0.081 | 
SAS3 | 25.05 | 35.01 | 9.96 | 701 | 20.00 | 34.53 | 116 | 817 | 0.061 | 
SAS4 | 25.12 | 33.34 | 8.22 | 714 | 20.00 | 32.94 | 103 | 817 | 0.075 | 
SAS total |  |  |  |  |  |  |  |  | 0.324 | 
PETS | 24.63 | 29.37 | 4.74 | 267 | 20.00 | 27.79 | 153 | 420 | 0.048 | 
Total |  |  |  |  |  |  |  |  | 0.373 | 0.311
One flow meter measures the total flow
Flow at each cooling channel (4 SAS and PETS) is not known
Flow meter accuracy: ± 2% measured value
Elena Daskalaki, Alex Vamvakas, Anastasia Xydou

## Slide 9: CLEX module installation
Dmitry Gudkov

## Slide 10: CLEX module supporting system received and tested

## Slide 11
Status of main components
Pets, DB-Quad and girder available
ACC-structures: final brazing steps
Waveguide system: final brazing steps
BPM: rf test and assembly
Missing: some supports, clamps, transition beam chambers

## Slide 12
CLEX module installation
Cabling scheme preparations
Dmitry Gudkov, Stephane Curt, Wilfrid Farabolini

## Slide 13
CLEX module installation
Equipment identification and naming for control integration
Dmitry Gudkov, Stephane Curt, Wilfrid Farabolini

## Slide 14
Module electronics for CLIC
Adriaan Rijllart
Examples base on NI-hardware, a radiation environment test is planned in CTF3 acquiring rf signals from the CLEX module

## Slide 15
Alexandre Samochkine
Klystron base module design

## Slide 16
Klystron base module design

## Slide 17: Outlook and conclusions
The two beam module program will continue as advised by the module review committee
Good progress in analyzing the data taken on the Lab-module (see as well Helene’s talk), to be continued
Highest priority right now is to get the CLEX module installed and start experiments with it
Will have to review (again) the objectives and configurations of the lab-based module program evolution
Prepare transition to ‘next’ generation modules

## Slide 18: End
Alexandre Samochkine

## Slide 19: Phase 2: Duty cycles tests
STEP | # | INPUT |  |  |  |  |  |  |  |  | 
 |  | Tamb (°C) | vair (m/s) | Q (W) |  |  |  |  | Ti,water (°C) | ΔTo,water (°C) | 
 |  |  |  | SAS | AS Load | PETS | RFN Load | DBQ |  | SAS | PETS
Nominal operation mode | DBQ only | 20 | 0.7 | 0 | 0 | 0 | 0 | 150 | 25 | 0 | 0
 | Unloaded | 20 | 0.7 | 820 | 178 | 220 | 178 | 150 | 25 | 10 | 6
 | Loaded | 20 | 0.7 | 683 | 137 | 220 | 178 | 150 | 25 | 8.3 | 6
 | DBQ only | 40 | 0.7 | 0 | 0 | 0 | 0 | 150 | 25 | 0 | 0
 | Unloaded | 40 | 0.7 | 820 | 178 | 220 | 178 | 150 | 25 | 10 | 6
 | Loaded | 40 | 0.7 | 683 | 137 | 220 | 178 | 150 | 25 | 8.3 | 6
Failure mode SAS breakdown | Loaded | 20 | 0.7 | 683 | 137 | 220 | 178 | 150 | 25 | 8.3 | 6
 | SAS breakdown | 20 | 0.7 | 0 | 27.4 | 220 | 178 | 150 | 25 | 0 | 6
 | PETS off | 20 | 0.7 | 0 | 27.4 | 55 | 0 | 150 | 25 | 0 | 1.5
 | Loaded | 20 | 0.7 | 683 | 137 | 220 | 178 | 150 | 25 | 8.3 | 6
 | Loaded | 40 | 0.7 | 683 | 137 | 220 | 178 | 150 | 25 | 8.3 | 6
 | SAS breakdown | 40 | 0.7 | 0 | 27.4 | 220 | 178 | 150 | 25 | 0 | 6
 | PETS off | 40 | 0.7 | 0 | 27.4 | 55 | 0 | 150 | 25 | 0 | 1.5
 | Loaded | 40 | 0.7 | 683 | 137 | 220 | 178 | 150 | 25 | 8.3 | 6
Failure mode PETS breakdown | Loaded | 20 | 0.7 | 683 | 137 | 220 | 178 | 150 | 25 | 8.3 | 6
 | PETS breakdown | 20 | 0.7 | 683 | 137 | 55 | 0 | 150 | 25 | 8.3 | 1.5
 | SAS off | 20 | 0.7 | 0 | 27.4 | 55 | 0 | 150 | 25 | 0 | 1.5
 | Loaded | 20 | 0.7 | 683 | 137 | 220 | 178 | 150 | 25 | 8.3 | 6
 | Loaded | 40 | 0.7 | 683 | 137 | 220 | 178 | 150 | 25 | 8.3 | 6
 | PETS breakdown | 40 | 0.7 | 683 | 137 | 55 | 0 | 150 | 25 | 8.3 | 1.5
 | SAS off | 40 | 0.7 | 0 | 27.4 | 55 | 0 | 150 | 25 | 0 | 1.5
 | Loaded | 40 | 0.7 | 683 | 137 | 220 | 178 | 150 | 25 | 8.3 | 6
* EDMS# 1332627
Elena Daskalaki, Alex Vamvakas, Anastasia Xydou