## Slide 1: News from RILIS group and new developments
Valentin Fedosseev - EN-STI-LP
ISOLDE Collaboration Committee meeting
24th June 2014

## Slide 2: RILIS layout
Fedosseev, V. N., Fedorov, D. V, Fink, D., Losito, R., Marsh, B. A., S.Rothe et al. (2012).
Upgrade of the RILIS at ISOLDE; Rev. Sci. Inst 83(2), 02A903. doi:10.1063/1.3662206
Dual laser system (TiSa and Dye) is now fully operational; LabView status monitoring and DAQ system;
NB mode for TiSa and Dye laser; Isobar suppression with ‘Laser Ion Source Trap’ device
Well represented at the EMIS 2012 conference in Matsue, Japan (4 articles in the proceedings)

## Slide 3: RILIS/LARIS projects for LS1 #1
Extension of RILIS cabin
  Enlarged entrance/storage and work area to maximize the useable laser laboratory space
GENERAL RILIS DEVELOPMENTS
RILIS machine protection system
  Installation of a machine protection and monitoring system to reduce reliance on shift-based operation
Space stabilization of laser beams
  Upgrade of existing commercial system to enable active stabilization of 3 beams and UV beams
GPS laser beam launch
  Replacement of prisms by high-reflectivity dielectric mirrors will reduce the losses of laser power in the beam transport to GPS mass separator
HRS laser window
  Extension tube for window mounting outside the 90o magnet will enable monitoring of window quality during operation and simplify its replacement
Improved motorization of Narrow-band TiSa
Laser developments
Laminar flow box containment of all laser tables
A dedicated, high power Nd:YVO laser for non resonant ionization
  High beam quality industrial laser could significantly improve efficiency for many schemes.
Ongoing TiSa R&D
Delivered today

## Slide 4: RILIS/LARIS projects for LS1 #2
RILIS R&D at ISOLDE offline separator and Mainz RISIKO
  Tests of high resistance cavity materials (graphite)
  Improved beam gating method
  LIST improvements/characterization
  RILIS @ VADIS
Develop RILIS power-meter target
  Summer student (Alexandra Zadvornaya) worked on this project and tested the unit offline
  The special target unit has been built and used at HRS during the start-up
New RILIS/LARIS dye handling/preparation laboratory
  Under construction in 252-R-002 (next to LARIS lab).
  Proper equipment, storage and safety measures – as requested by HSE
Installation of a reference cell at RILIS
Improved motorization of Narrow-band TiSa
Ionization of refractory metals
  Study of laser ionization in VADIS cavity
New and improved RILIS schemes for the Dual RILIS system
  According to requests from ISOLDE users: Ba, Li, Cr, Er, …
SPECTROSCOPY
and IONIZATION SCHEMES
Off-line R&D
In progress
Almost completed

## Slide 5: Part 1
Development of RILIS facility

## Slide 6: RILIS room extension
254 cm
320 cm
28 m2
6 m2
REX EBIS
RILIS
IS COOLER
HV cage
100 cm
Required for:
Safety
Reference cell installation
Dye handling
Upgrade of beam observation system
Improved ventilation system
Comfort/ergonomics
Installation of extra YAG laser
Existing laser room + SAS
Extended
part (SAS)
DESK
REF
40W at 10 kHz
17ns Pulse
Much better transmission efficiency to ion source
Higher efficiency and reduced setup time for many elements
STATUS
Work competed in
December 2013

## Slide 7
New GPS laser beam launch system
RELATED projects/tasks:
New reference beam area
New beam stabilization system
Reference cell installation
Benefits:
4 beams to GPS
Fewer power losses
Improved ergonomics
STATUS:
Designed by
Sebastian Rothe (Fellow)
Installed and operational

## Slide 8: Machine protection
Dye Leak: Fire hazard; laser damage risk
Up to 6 dye circulators each containing up to 3 L of ethanol flowing at 7 L/min.
Water cooling for Ti:Sa crystals. Water cooling network for each dye circulator.
Up to 40 W pump beam focused on dye cell. Almost immediate dye cell damage if dye flow stops.
Dye flow interruption: Fire hazard; laser damage risk
Water leak: Equipment damage risk; electrical safety hazard
Action required: Alert the laser operator.
Action required: Block pump beam to dye laser, alert the laser operator.
Action required: Stop pump laser, alert the laser operator.
Non invasive
dye flow sensor
(ULTRASONIC)
+
NI CompactRIO
MPS
+
Laser beam shutter
Flip mirror/ beam
dump assembly
with controller
+
Pump laser control by
Hyper-terminal commands
and access to laser operator
alert system (LABVIEW based)
Solution to be tested:
Install water leak sensor cables on laser table and RILIS cabin floor
Include sensor data logger in RILIS monitoring system
Organic solvent
detector
(breathalyzer)
+
NI CompactRIO
MPS

## Slide 9: RILIS machine protection: installed and being tested
Preparation for
‘on-call’
RILIS operation
  Hardware to control multiple laser interlocks and shutters is assembled by STI-ECE
  Laser dye leak detection
  Offline testing has begun
  Installation in January 2014
In collaboration with EN-STI-ICE (Sergio Batuca and Mark Butcher)

## Slide 10: Beam transport in separator area
Dust protection of optics needs to be improved
UV induced optics coating should be prevented
Assessment of magnet window and
faster replacement if necessary
  Power meter target
  Window extension with port aligner and CF viewport
reference
Quartz plate
Broadband optics
Quartz window
  RILIS TABLE
INACCESSIBLE
ZONE
HRS
GPS
>2
Sv/h
New GPS
prism mount
Old HRS window change tool
New HRS window tube, port aligner and prism mount

## Slide 11: HRS window upgrade
Proposed and designed by Sebastian Rothe
Laser beam window was mounted inside the HRS magnet -> exchange is difficaul
Installed in April - June 2014

## Slide 12: Independent laser for non resonant ionization
Blaze laser installed for testing at RILIS in Dec 2012
40W at 10 kHz
17ns Pulse
Low Jitter
Gaussian beam
Much better transmission
efficiency to ion source
A similar efficiency improvement should be expected for the 18 RILIS elements that use non-resonant ionization for the final step!
Laser | Laser Power (on table) | Reference beam power in 3 mm aperture | Transport efficiency
Edgewave | 43 W | 370 mW | 33 %
Blaze | 15 W | 350 mW | 88%
Blaze | 40 W | 800 mW | 76%
Power dependent thermal lensing in the beam transport optics is to be eliminated
B. Marsh et al., Suitability test of a high quality Nd:YVO industrial laser for the ISOLDE RILIS installation.
CERN-ATS-Note-2013-007 TECH
Can be used for Dye and Ti:Sa pumping as a back-up laser
Delivered today

## Slide 13: Part 2
Off-line development

## Slide 14: RILIS cavity tests at off-line mass separator
A simplified laser system is setup at the off-line ISOLDE mass separator – producing Ga ion beams for testing RILIS cavities
RILIS Ti:Sa Laser System
pA – meter
Faraday cup and
MCP detector
on movable holder
SHG/THG/FHG
l – meter
Ti:Sa
Nd:YAG
Nd:YAG
10 kHz Master clock
Delay generator
Behlke switch
DC
V-source
Vertical deflector

## Slide 15: 5 us beam gating test
Narrow laser-ion bunch width + micro beam gate tests
Laser-ion
time structure:
5 μS FWHM!
Ga mass
marker
High Ω cavities:
Thin graphite 
Pyrolytic graphite – being tested 
Sigradur ‘glassy’ graphite ☐ – under construction
Pulsed heating for higher voltage ☐ -under investigation
Ga
The fast beam gate is capable of a1μs beam gate!
This would give a 100 x
surface ion suppression!
Challenge : make a 1μs wide laser ion bunch.
Required pulsed cavity heating and possibly ToFLIS technique
RILIS
ionization
scheme
Solid-state switch
~ 500 V @ 10 kHz

## Slide 16: Inverted line as an ion repeller
Pre-peak:
Ions created at exit of cavity
Main peak
(laser ions from cavity)
has disappeared
Suppression factor
still has to be measured:
Is it as good as the LIST repeller?
No surface ion background
Standard cavity heating polarity

## Slide 17
Laser ionization inside an arc discharge ion source for the first time!
First VADLIS demonstration
RILIS ionized gallium inside a modified VADIS
Laser ionization efficiency for Ga is higher than VADIS efficiency under the test conditions
Easy switching between VADIS and RILIS mode
Pulsed anode enables new modes of operation to be investigated
Long laser ion survival/residence time indicates suitability for 2+ ionization or even optical pumping
RILIS in VADIS is the one step towards developing laser ionized refractory metal beams

## Slide 18: Two modes of operation
Tom Day Goodacre VADLIS 11
RILIS MODE
VADIS MODE

## Slide 19: Part 3
RILIS test during ISOLDE start-up

## Slide 20: RILIS tests during start-up period
Test of Ba ionization
Test of Ba+ ionization
Test of Li ionization
Test of Li ionization with Blaze laser
Test of Cr scheme
Test of Er scheme – no time left
Test of Hg ionization
Test of Ge ionization
GPS target 1
GPS target 2
HRS target 1
Test of power meter target
Optics alignment
Test of Hg ionization in VADIS
ISCOOL ion-laser overlap test
HRS target 2

## Slide 21
RILIS laser alignment target unit
Mounted as first target on HRS after LS1. Lasers successfully aligned. Unit Functioning as expected.
 facilitates laser alignment - normally only possible with ion beam
 helps to clarify laser beam transport issues (thermal lensing)
 enables remote check of status of magnet windows when in doubt, reducing interventions to separator areas
Thanks to: Bernard, Ermanno & our 2013 summer student Sasha
Tungsten ionizer acts as light source for pre-alignment after shutdown
Laser power meter measures power delivered through ion source
readout via existing thermocouple infrastructure
RILIS lasers
Magnet window
HRS/GPS
Target Unit

## Slide 22: New barium scheme
Tom Day Goodacre : PhD work
Tested at LARIS
Confirmed with RILIS on GPS
In June 2014
RILIS Ti:Sa
RILIS Dye
RILIS ionization efficiency ≈ surface ionization efficiency

## Slide 23: 2+ Ba ionization at RILIS
Removes possible Caesium contamination
Tested with RILIS at GPS just last night!
Laser ON
Laser OFF
Laser OFF
Mass = 69

## Slide 24: Laser ionization of Lithium
IP = 5.39 eV -> surface ionization efficient
532 nm
25 W
RILIS ionization efficiency = ½ surface ionization efficiency
Could be improved by ~ 40% using new Blaze laser

## Slide 25: RILIS ion beams