## Slide 1: Anomalies associated with radiation effects and the role of space agencies
Robert Ecoffet, CNES
CERN Seminar, June 10, 2014

## Slide 2
Radiation belts
Protons
Electrons
keV- 500 MeV eV ~ 10 MeV
Ions
Solar flares
Protons
keV- 500 MeV few 1-10 MeV/n
Cosmic rays
Ions
max ~ 300 MeV/n
Space environment radiation sources
CERN Seminar, June 10, 2014

## Slide 3: Hazard zones in LEO : SAA and poles
~ 400 km
Declination
Geographic equator
South-Atlantic anomaly
Magnetic dipole axis
Rotation axis
Magnetic equator
Radiation belts
Polar LEO orbit
CERN Seminar, June 10, 2014

## Slide 4: Space environment and components
An environment specific to space applications
A major dimensioning constraint for on-board systems
Very fast evolution of electronic technologies
Performance often leads to cutting edge designs
A strong economic drive toward margin reductions
More exposed missions
Smaller satellites (less shielding)
Today’s components features
Dimensions : 0.1 µm² Time : 1 ps Charge : 1 µV
More transistors now in a single chip than in whole 1980’s spacecraft designs
(GALILEO Jupiter probe for example)
CERN Seminar, June 10, 2014
Notes: Introduction. Spécificité de l’environnement spatial, impact de la contrainte. Facteurs d’impact internes : évolution techno rapide, performance embarquée, réduction des marges. Facteurs externes : missions, masse.

## Slide 5
Main radiation effects
Parametric drift
Function loss
Lifetime
SET : transient
SEU : upset
SEL : latch-up
SEB : burn-out
SEGR : rupture
Hot pixels
RTS
Operating safety
Dependability
Performances
Single event effects
Ion
Ionisation
+ - +
- + + -
+ - - +
+ + +
Oxide
Silicon
p+
Ion 2nd
Ionising dose
+ + + + + + + + +
+ - - + - + - + - - -
Oxide
Silicon
Trapped charges
Interface traps
p+
e-
Atomic displacement
Interstitials
Vacancies
Oxide
Silicon
p+
(e-)
CERN Seminar, June 10, 2014

## Slide 6
Single event effects classes
Turning on parasitic SCR
SEL
Effects in nominal active structures
Effects in parasitic structures
SET : transient
SEU : upset
Transient latch
Analog
Digital
CMOS
Power MOSFETs
Turning on parasitic BJT
SEB
Power MOSFETs
SEGR
Exceeding gate oxide breakdown field
CERN Seminar, June 10, 2014

## Slide 7: Space environment vs. CERN
> 10 MeV proton yearly proton fluence (outside spacecraft)
50 MeV yearly equivalent fluence (3 mmAl spherical shield)
CERN Seminar, June 10, 2014

## Slide 8: Yearly doses in sample equipment
LEO Observation Constellations
MEO Navigation
GEO
LEO Constellations
Outer electron belt
Proton belt and inner electron belt
Circular Orbits
CERN Seminar, June 10, 2014
Notes: Cartographie de la dose annuelle sur CARMEN que l’on situe sur diverses orbites circulaires (altitude, inclinaison) dans sa configuration JASON-2. Exemples de doses annuelles typiques sur un équipement.

## Slide 9: Spacecraft anomalies
Radiation-induced spacecraft anomalies have been observed since the very beginning of the space era
Single event effects now represent the major part of anomalies (60 to 90%)
1957
1962
1963
1975
1991
Discovery of the radiation belts
Nuclear blasts in space
First satellite failures due to radiation (dose)
First reported SEUs (GCR) in satellites
First proton latch-up in space
~1978
First proton SEUs
CERN Seminar, June 10, 2014

## Slide 10: Classical SEE effects
Memory corruption : single errors to error bursts
Processor crash
Mode swapping
Reset
Switch-off
ADC conversion errors
ADC swapping to autocal. mode
Gain change
Reference voltage change
VCO output frequency change
Transient PLL lock loss
False signals
Star pattern loss
Image corruption
…….
Equipment loss
CERN Seminar, June 10, 2014
Notes: Exemples d’effets classiques SEE

## Slide 11: Examples of system effects
Electrical Architecture (Generic) Equipment loss Self switch-off, disjunction, reset, reboot, redundancy swapping | Dose, Latch-up (SEL) SET
On-board energy Solar panel degradation | Dose, Displacements
Attitude and orbit control system Possible attitude loss Star tracker out of AOCS loop Inertia wheels disturbances Self switch-off of ion thruster | SEU Proton transients (SAA, flares) SET SET
On board management On board computer, resets, mode refusal, safe-hold mode Mass memory | SEU – SET SEU
Imaging systems « UFOs » Hot pixels, RTS Dark current, non linearity,… etc | Proton transients Displacements Displacements, dose
Time references Frequency jumps | Dose on SAA passes or flares
CERN Seminar, June 10, 2014

## Slide 12: Cumulated effects (published)
Telstar, 1963
Artificial radiation belt
Telstar - 1963
Artificial radiation belts
Starfish experiment, 1962
Hipparcos - 1993
Apogee motor failed
Degraded mission
Galileo - 2002
Jupiter radiation belts
TID degradation of bipolar PROMs and optocouplers
Design lifetime was 5 years in GEO
Actual lifetime was 5 years in GTO
Diode failed in command decoder
7 other satellites failed
Many systems affected
But outstanding success !

## Slide 13: SEE : GCR and SPE (published)
SOHO (L1) – 2001
GCR : self switch-of, reset, reboot, latch-up
SPE : mass memory errors spikes
SEUs in 93L422 bipolar RAMs
Possible satellite tumbling
GCR ~ 20 events / week
Oct. 89 flare : 249 events / 7 days
30% p+, 70% ions
TDRS-1 (GEO) – 1991
SPOT-1, 2, 3 (800 km, 98°) - 1995
GCR : SEUs in HEF4736 SRAMs
MAP (L1) – 2002
5 Nov. 2001, switch to safe-hold condition
SET on PM139 from processor reset circuitry
3-7 November 2001 : large solar event
Attributed to SPE ion

## Slide 14: SEE : trapped protons (published)
SAMPEX – 2001
(512 km x 687 km, 81.7°)
Solid State Recorder upsets
MIL-1773 fiber optics bus retries
Transients in the photoreceptor
TOMS / METEOR-3 – 2001
(1183 km x 1205 km, 82.6°)
Solid State Recorder upsets
ERS-1 (780 km, 98°) - 1991
Latch-up on CMOS SRAM
after 5 days Instrument lost
ISS, Space Shuttle, LANDSAT, TERRA, AQUA, AURA, HST, GALEX, GLAST, TRMM, ORBVIEW, ENVISAT, ERS-2, METOP, SMOS, CRYOSAT-2, HERSCHEL, INTEGRAL, XMM, SPOT-4, SPOT-5, JASON-1, JASON-2, CALIPSO, COROT, DEMETER, PARASOL, PICARD, Myriade µSATs,

## Slide 15: DDD : trapped protons (published – expt *)
TOPEX / POSEIDON – 2002
(1336 km, 66°)
GLOBALSTAR-1 - 2010
(1441 km, 52°)*
4N49 optocouplers
Status circuits
Earlier but not mission-critical
Thruster command circuits
Failures occurred at 8.75 years
Design lifetime was 3 years
48 operational satellites
and 4 spares.
Original constellation deployment in 1998-2000.
In the 2002-2004,
24 receivers
on 21 satellites affected,
3 satellites failed
Radiation design lifetime of individual satellites was 9 years
LT RH1014 bipolar devices

## Slide 16: Effects of a major SW event (oct-nov 03)
SMART-1
SOHO ACE WIND GENESIS
MAP
MARS ODYSSEY
GOES-9, 10, 12, 8 DMSP-16 KODAMA INMARSAT
INTEGRAL CHANDRA CLUSTER
AQUA TERRA LANDSAT TOMS
TRMM POLAR FEDSAT ICESAT GALEX MER-1, 2 XTE RHESSI CHIPSAT NOAA-17
MIDORI
STARDUST
SIRTF
www.sat-index.com

## Slide 17
Blurring of VIS camera on NASA / POLAR
NASA image
CERN Seminar, June 10, 2014

## Slide 18
Solar protons “filmed” by SOHO
CERN Seminar, June 10, 2014

## Slide 19
CERN Seminar, June 10, 2014
Solar protons “filmed” by SOHO

## Slide 20: Galileo at Jupiter
Image of a Sodium volcanic plume on the moon Io contaminated by speckles due to Jupiter radiation belts, JPL image
CERN Seminar, June 10, 2014

## Slide 21: Radiation activities in project phases
Phase 0
Mission analysis
Orbit analysis
Environment specification
Phase A
Feasibility
Phase B
Preliminary design
Phase C/D
Detailed design Qualification
Phase E
Utilisation
Calculations on simple structures
Generic specification of received dose
Hardness assurance specification
Pre-evaluation of critical components
Evaluation of component radiation performance
Interaction structural and system design
Risk estimation
Component list analysis
Radiation lot verification testing (RVT)
Application conditions
Radiation levels on actual satellite
Local shielding
Lessons learned
Anomaly analysis
Space weather
Complex structural modelling
Satellite is a sphere
?
+
+
+
+
+
+
-
-
-
-
-
-
Simple geometrical simulations
Components are evaluated
Functions and application conditions
Analysis and specification of radiation environment
Sector analysis
Flight lots testing
ON
OFF
ON
OFF
T°
CERN Seminar, June 10, 2014

## Slide 22: Implementation at CNES
“Radiation engineer” function
  Single entry point for radiation issues
  Continuity from phase 0 to phase E (design to exploitation)
  Leads calculations and tests
  Interfaces with component procurement engineers (qualification procedures)
  Interfaces with designers (functional, electrical, mechanical, thermal,…)
  Iterative and concurrent (2-way) process
  Interfaces with satellite operators
Similar implementation for satellite prime contractors and main equipment providers
Radiation engineer
Dose levels
Tests
Function
Mechanical
Reliability - dependability
Thermal
Electrical
Operations
Anomalies - failures
Mission analysis
CERN Seminar, June 10, 2014
SEE rates

## Slide 23: Implementation at CNES
Radiation engineer function
  set-up after first SPOT-1 on board computer SEUs (1986) : 50% of these SEUs resulted in 24h mission outage
  sad to say, new organizations come often as aftermaths of problems
A long run
  I started working on SPOT-5 radiation qualification in 1994
  20 years after, I’m still recording on-board SEUs !
How many people ?
  5 radiation engineers for 2406 employees
  (ESA : 2254 employees, 4 radiation engineers, 2 technicians)
  (Thales Alenia Space and Airbus Satellites : each 15-20 rad. engineers for 6000-7500 staff)
  Most of the tests are now subcontracted to test houses (TRAD, ALTER/HIREX…)
Key words : single point, continuity over project lifetime, interaction with designers
CERN Seminar, June 10, 2014

## Slide 24: CNES, ESA, RADECS
CNES and ESA
  CNES manages the French contribution to ESA
  For components and radiation
    ESCC, ECSS – space standards
    CTB : agencies – industry network
      Radiation Working Group
      Agencies, primes, providers, test houses, component manufacturers
    R&D harmonization
Larger networks
  IEEE NSREC
    NSREC 2014, Paris (merged with RADECS)
  RADECS
    University, research, agencies, industry
    Conferences, thematic workshops
    RADECS 2017 at CERN !
CNES
2000 M€
755 M€
ESA
4000 M€
Member States
2900 M€
E. U.
1100 M€
CERN Seminar, June 10, 2014

## Slide 25
Basic Mechanisms of Radiation Effects in Electronic Materials and Devices
  Single-Event Charge Collection Phenomena and Mechanisms
  Radiation Transport, Energy Deposition and Dosimetry
  Ionizing Radiation Effects
  Materials and Device Effects
  Displacement Damage
  Processing-Induced Radiation Effects
Radiation Effects on Electronic and Photonic Devices and Circuits
  Single-Event Effects
  MOS, Bipolar and Advanced Technologies
  Isolation Technologies, such as SOI and SOS
  Optoelectronic and Optical Devices and Systems
  Methods for Hardened Design and Manufacturing
  Modeling of Devices, Circuits and Systems
  Particle Detectors and Associated Electronics for High-Energy Accelerators and Nuclear Power Facilities
  Cryogenic or High Temperature Effects
  Novel Device Structures, such as MEMs and Nanotechnologies
Space, Atmospheric, and Terrestrial Radiation Effects
  Characterization and Modeling of Radiation Environments
  Space Weather Events and Effects
  Spacecraft Charging
  Predicting and Verifying Soft Error Rates (SER)
Hardness Assurance Technology and Testing
  New Testing Techniques, Guidelines and Hardness Assurance Methodology
  Unique Radiation Exposure Facilities or Novel Instrumentation Methods
  Dosimetry
New Developments of Interest to the Radiation Effects Community
www.nsrec.com

## Slide 26
Thanks for your attention

## Slide 27: Back-up

## Slide 28: Compared SEU sensitivities 1 Mbit SRAMs
- No standard behaviour within a technology “generation” - No scaling factor between generations

## Slide 29: Example of complex SEU response : DRAM 16M IBM LUNA-C

## Slide 30: Example of complex SEU response : DRAM 16M Texas Instruments

## Slide 31: A designer’s nightmare
The op-amp outputs SET parasitic signals of many volts lasting a few 10 µs
The comparator changes state on its own
The DAC outputs voltage swings of many volts
The ADC does conversion errors and switches on its own to auto-calibration mode during 1 s.
The FIFO TM buffer memory does addressing conflicts and scrambles write and read pointers
The DRAM storage array does row and line bursts of multiple errors
The program SRAM does multiple errors
The program FlashEPROM exhibits read errors and switches on its own to status mode
The µP does calculation errors, program errors, and crashes
SRAM
FlashEPROM
FIFO
µP
ADC
DAC
AMP
COMP
DRAM
Orange components are latch-up sensitive
Lim
The limiter /switch used as a « de-latching » device is itself sensitive to latch-up