## Slide 1: Particle Tracking for Orbit-Bump Quench Tests at LHC
Workshop on Beam-Induced Quenches, 15-16 September 2014
V. Chetvertkova, on behalf of B. Auchmann, T. Baer, W. Hofle, A. Lechner, A. Priebe, M. Sapinski, R. Schmidt, N. Shetty, A. Verweij, D. Wollmann.

## Slide 2: Quench Test Analysis What is the energy deposition in the coil at the moment of quench?
Particle Shower
FCBM: loss rate
QPS: moment of quench
Particle tracking: spatial distribution
BLM signals
Validation
Input
Analysis
Electro-Thermal Estimate (MQED)
BLM: normalized time distribution
P. shower: norm. space distribution
Quench test
QPS: moment of quench
Subscale
experiments
Quench Level
Upper bound or estimate
Lower bound
quench
no quench
Particle Tracking
Settings: bump amplitude etc.
Beam parameter measurements: ε, Q, etc.
BLM normalized time distribution
BPM signals

## Slide 3: Orbit bump quench test
How to lose the beam:
Increasing the bump amplitude (Dynamic bump test)
Exciting the beam
  Non-coherent excitation (Steady-state orbit bump)
  Coherent excitation (Millisecond timescale test)
Aperture
Beam
Reference orbit
Bump amplitude
Kick

## Slide 4: Methodology
Beam
Magnets of interest
Sliced into ~ 1cm lenses
MADX, thin-lens tracking:
1 cm resolution for further FLUKA simulations
Aperture
Aperture: black absorber (no scattered projectiles)

## Slide 5
  Beam parameters
    Energy
    Profile
    Tune, Chromaticity
  Orbit bump amplitude
  Transverse kick
    MKQ kick strength
    ADT kick strength
Input parameters / Validation
BPM data

## Slide 6
  Beam profile:
    Tail population
  β-function in the magnet
    β beat is <10%
  Aperture restrictions
    Surface roughness
    Misalignments
Other parameters influencing loss distribution
Beam
    β-function along the magnet
1-2%
Aperture
Aperture restriction
Aperture restriction:
Height: 30 μm
Length: 10 ÷ 30 cm

## Slide 7
7
Beam size:
  εx = 5.195e-7
  εy = 1.409e-5
Bump amplitude:
  4.3σnom
Qx = 64.(3)
Qx = 64.28
Qx = 64.28
Qx = 64.3330
Qx = 64.274
Qx = 64.268
3CB
matching
3CB
Matching – correcting tune
after establishing bump
Dependence on the tune
Conclusion:
Tune variation influences longitudinal loss distribution, however the maximum for realistic cases varies ~ 20%
Nominal tune spread < 1e-3
Not realistic!!!
Nominal
-6e-3
Tune:
Millisecond timescale test

## Slide 8
8
Bump amplitude:
  4.3σnom
Tune:
  Qx = 64.28
  Qy = 59.31
ε n,x = 5.19e-7
ε nom,x = 3.5e-6
Dependence on the beam size
Conclusion:
Influence of beam size on longitudinal loss distribution is small in case of fast losses
Experimental
Nominal (extreme case)
Beam size:
  εy = 1.409e-5
Millisecond timescale test

## Slide 9
9
Beam size:
  εx= 5.195e-7
  εy= 1.409e-5
4.3σnom
1.66σnom
Tune:
  Qx = 64.28
  Qy = 59.31
8.3σnom
Dependence on the bump amplitude
Conclusion:
Size of orbital bump has only small influence on maximum of lost-particles distribution in case of fast losses
Experimental
Extreme case (-)
Extreme case (+)
Bump amplitude:
Millisecond timescale test

## Slide 10: Dynamic orbit bump
Beam size:
  εx= 6.1e-6
  εy= 7.1e-6
Initial bump amplitude:
3.5σnom
Step: every 50 turns
Conclusion:
Slow increase of the orbital bump leads to the compression of the lost-particle distribution in case of slow losses

## Slide 11
11
Conclusion:
Decrease of diffusion rate leads to compression of longitudinal distribution
11
Dependence on diffusion rate
Steady-state orbit bump
Beam size:
  εx= 1.9e-6
  εy= 1.4e-5
Bump amplitude:
2.5σnom
ADT gain, % | Kick strength, sigma
15 | 1.15E-05
60 | 4.60E-05
125 | 9.58E-05
185 | 1.42E-04
285 | 2.18E-04

## Slide 12: Millisecond timescale test Steady state orbit bump test Dynamic orbit bump
12
Aperture limitations
Conclusion:
Presence of the aperture limitation of 30 μm shifts the longitudinal distribution and therefore changes the average impact angle.

## Slide 13: Summary
Spatial loss distribution was calculated for orbit bump quench tests.
Integrated over time this distribution was provided for further particle-shower simulations.
Particle Shower
Particle Tracking
Aperture
Beam
Reference orbit
Bump amplitude
Kick

## Slide 14: Conclusions
Spatial loss distribution varies depending on the scenario.
Impact angle does not depend on the scenario, but only on the integral magnetic field seen by the particles.
Weighted average angle changes with the spatial distribution.
Results of the FLUKA simulations depend both on the spatial and angular loss distributions (see talks of A. Lechner and B. Auchmann).

## Slide 16: Time structure
Fast losses
Slow losses
Experimental BLM signal