## Slide 1: Conceptual Layout and Integration in High Luminosity Insertions
V. Baglin (TE-VSC)
6th HL-LHC Technical Committee
CERN – 10th June 2014

## Slide 2: Outline
Vacuum performances
Layout generalities
Key areas:
  Experiments
  TAS-Q1
  IT
  Q3-D1
  LRBB
  TAN-D2
  D2, Q4, Q5, Q6
  Crab cavities
  Masks
Conclusions

## Slide 3: Vacuum Performances
Layout must ensure vacuum performances
Vacuum stability: beam current, ion desorption
Low background to the experiments
 | H2_eq / m3 | mbar
<LSS1 or 5> | ~ 5 1012 | 10-10
<ATLAS> | ~ 1011 | 10-11
<CMS> | ~ 5 1012 | 10-10
A. Rossi, CERN LHC PR 783, 2004.

## Slide 4: Layout Generalities
Sectorisation at each cold to warm transition:
    Lowest unbaked length at RT required
    Decoupling RT and cryogenic systems
Instrumented sector valve assembly
Cryogenic system with perforated beam screen
Room temperature system with NEG coating
    Fully bakeable 200/250 deg, 50 deg/h
    A roughing system every ~ 20 m
    Instrumentation
    Ion pumps every 28 m (to be review for HL-LHC)
    Dedicated pumping for uncoated chambers
    ID 80, 212 are standard aperture (100, 130 )
Integration studies must take into account mobile systems (bakeout, pumping groups) and installation/desinstallation of components.

## Slide 5: Experiments
Complex and dedicated vacuum chambers: Be, Al (ATLAS) and stainless steel (CMS).
NEG coated
Minimised thickness flanges with helicoflex gaskets
Adapted/dedicated supporting system
Dedicated remote tooling at TAS
Q1R5
IP5
CMS forward chamber
TAS
TAS remote tooling
Inside FIN (fin iron nose)
RF bridge repair 18-1-2012

## Slide 6: Experiments for HL-LHC
For HL-LHC:
    Be, Al material
    NEG coated, no RF bridges
    Issue with flange connection, robustness and radiation.
    Impose “quick” flange concept
    Review/redesign TAS remote tooling
    Mechanical supporting system to be compatible with detector maintenance (no personnel intervention must be required)

## Slide 7: TAS-Q1
2 sectors valves to decouple the experiments and allow pumping, Ne venting
NEG coated
IT
TAS
BPM
To be redesigned for HL-LHC to allow remote tooling
No room for personal to work !
(even to take a picture !)
VAX area

## Slide 8: IT
Perforated shielded beam screen
a-C coated beam screen
Active cooling (~ 40-60 K)
Cold/warm transition
Interconnects length to be compatible with vacuum stability
Under study, definition

## Slide 9: Q3-D1
Longest unbaked length in LHC : ~ 1.3 m !
Weak area
HL-LHC has the sector valve assembly at D1
DFBX-Q3
D1
HL-LHC layout

## Slide 10: LRBB
Do not exist in LHC.
Already sectorised
Must be bakeable
Material and layout to be studied and designed
Must be compatible with background to experiments

## Slide 11: TAN-D2
Short distance between TAN-D2 to accommodate all components (7.43 m)
Integration of all components (collimators, BPM, vacuum system) not properly done during LHC construction
Redesign of collimator’s envelope taking into account mobile equipment : bake out + pumping groups

## Slide 12: TAN-D2 for HL-LHC
This version must allow 5th axis and remote tooling
Current layout with added mask (TCA)

## Slide 13: D2,Q4, Q5,Q6 for HL-LHC
Re-use sector valve assembly
a-C coated beam screen (5 – 20 K ?)
1. 9 K cold mass
R-use Q4LHC cold warm transition for Q5HL-LHC

## Slide 14: Crab cavities between D2-Q4
Collimation must be in the same sector as the 2nd beam to use it as a cryotrap protecting the cavities
Q4 and Q5 sectorised
Collimation sectorised
Module sectorised

## Slide 15: Crab cavities between D2-Q4
Layout study and design
Impact of electron cloud and synchrotron radiation on crab modules ?
Vacuum valves inside insulation vacuum: not inserted into sector valve chain
Interconnects: one sector valve + instrumentation + cavity roughing
2nd non accelerated beam at cryogenic temp (2.0 K) => need beam screen / shadowing
Examples of HL-LHC crab cavities

## Slide 16: Other Masks and Collimators
Re-use of standard equipments
Room temperature
Bakeable to 250 deg, 50 deg/h
Room is available
TCLIM -6R2
TCL -6L1

## Slide 17: Conclusions
Conceptual layout well advanced
Objective to:
    Have vacuum performances compatible with HL-LHC (1.12 A per beam, 2.2 1011 ppb, 2748 b)
        2.24 A in the IP instead of 1.16 A for LHC !
        Above vacuum stability design margin !
    Review/redesign and develop along the LSS the remote tooling
    Re-use vacuum equipments from LHC

## Slide 18: Thank you for your attention