## Slide 1: The Radiation Hard GBTX Link Interface Chip
Paulo Moreira
26 November 2013
CERN, Switzerland

## Slide 2: GBTX People
The GBTX is the product of the imagination and work of many people going from the basic ideas through the specifications, design and testing. These people are:
  Sophie Baron
  Sandro Bonacini
  Pedro Cardoso
  Jorgen Christiansen
  Ozgur Cobanoglu
  Xavi Cudie
  Federico Faccio
  Sebastian Feger
  Diego Figueiredo
  Rui Francisco
  Tullio Grassi
  Ping Gui
  Pedro Leitao
  Alessandro Marchioro
  Paulo Moreira
  Christian Paillard
  Karolina Poltorak
  David Porret
  Rafael Sune
  Filip Tavernier
  Guoying Wu
  Ken Wyllie
  (At some point the list must end but, if you feel you should be in it please let me know…)

## Slide 3: Outline
Radiation hard optical Link
The GBT system
The GBTX up-link
The GBTX down-link
Phase-shifter
xPLL
ePLL
Controlling the GBTX
Interfacing with the GBLD
Built-in test features
SEU tests
Power consumption
Testing Status
GBTX future

## Slide 4: Radiation Hard Optical Link
On-Detector
Radiation Hard Electronics
Off-Detector
Commercial Off-The-Shelf (COTS)
GBTX
GBTIA
GBLD
PD
LD
Custom ASICs
Timing & Trigger
DAQ
Slow Control
Timing & Trigger
DAQ
Slow Control
FPGA
GBT
GBT
Versatile Link
Development of an high speed bidirectional radiation hard optical link:
GBT project:
  ASIC design
  Verification
  Functionality testing
  Packaging
Versatile link project:
  Opto-electronics
  Radiation hardness
  Functionality testing
  Packaging

## Slide 5: The GBT System
FE Module
FE Module
Phase – Aligners + Ser/Des for E – Ports
FE Module
E – Port
E – Port
E – Port
GBT – SCA
E – Port
Phase - Shifter
E – Port
E – Port
E – Port
E – Port
CDR
DEC/DSCR
SER
SCR/ENC
I2C Master
I2C Slave
Control Logic
Configuration
(e-Fuses + reg-Bank)
Clock[7:0]
CLK Manager
CLK Reference/xPLL
External clock reference
control
data
One 80 Mb/s port
I2C
Port
I2C (light)
JTAG
JTAG
Port
80, 160 and 320 Mb/s ports
GBTIA
GBLD
GBTX
e-Link
clock
data-up
data-down
ePLLTx
ePLLRx
clocks

## Slide 6: GBTX Data Bandwidth
The GBTX supports three frame types:
  “GBT” Frame
  “Wide Bus” Frame
  “8B/10B” Frame
“GBT” Mode
  User bandwidth: 3.28 Gb/s
    Up/down-links
“Wide Bus” and “8B/10B”frames are only supported for the uplink
  The downlink always uses the “GBT” frame.
“8B/10B” Mode
  Downlink data 8B/10B encoded
  No FEC
  User bandwidth: 3.52 Gb/s
“Wide Bus” Mode:
  Uplink data scrambled
  No FEC
  User bandwidth: 4.48 Gb/s
GBT Frame:
Frame Synchronization:
  DC balanced and “redundant” header
Forward Error Correction:
  Interleaved Reed-Solomon double error correction
  4-bit symbols (RS(15,11))
  Interleaving: 2
  Error correction capability:
    2 Interleaving × 2 RS = 4 symbols = 16-bits
  Code efficiency: 88/120 = 73%

## Slide 7: GBTX Functionality (1/4)
e-Links
40 bi-directional e-Links
  Up to 40 @ 80 Mb/s
  Up to 20 @ 160 Mb/s
  Up to 10 @ 320 Mb/s
e-Port data rate can be set independently for:
  each group
  Input / output ports
1 bi-directional e-Link:
  80 Mb/s
40 e-Link clocks (fixed phase) programable in frequency:
  40/80/160/320 MHz (per group)
  (independently of the bit rate)
Automatic, semi-automatic or user controlled phase alignment of the incoming serial data embedded in the e-Ports
  Automatic alignment
    Tracks temperature and voltage variations
    Transparent to the user
    Works on any type of data:
      DC balanced / un-balanced
      A few “occasional” transition enough to ensure correct operation
Phase – Aligners + Ser/Des for E – Ports
Phase - Shifter
E – Port
E – Port
E – Port
E – Port
CDR
DEC/DSCR
SER
SCR/ENC
I2C Master
I2C Slave
Control Logic
Configuration
(e-Fuses + reg-Bank)
CLK Manager
CLK Reference/xPLL
JTAG
GBTX
ePLLTx
ePLLRx

## Slide 8: GBTX Functionality (2/4)
e-Links Special cases
8B/10B mode:
  44 input (max @ 80 Mb/s)
  36 output (max @ 80 Mb/s)
    (Four outputs reused as inputs)
Wide-Bus mode:
  56 input (max @ 80 Mb/s)
  24 output (max @ 80 Mb/s)
    (16 “outputs” reused as inputs)
e-Links electrical characteristics
Drivers:
  SLVS signaling
Receivers:
  SLVS/LVDS signaling
Phase – Aligners + Ser/Des for E – Ports
Phase - Shifter
E – Port
E – Port
E – Port
E – Port
CDR
DEC/DSCR
SER
SCR/ENC
I2C Master
I2C Slave
Control Logic
Configuration
(e-Fuses + reg-Bank)
CLK Manager
CLK Reference/xPLL
JTAG
GBTX
ePLLTx
ePLLRx

## Slide 9: GBTX Functionality (3/4)
Phase-Shifter
8 independent clocks
Programable in frequency:
  40 / 80 / 160 / 320 MHz
Programable in phase:
  0 to 360◦
  Phase resolution: 50 ps
    (for all frequencies)
Clock driver electrical levels:
  SLVS
Reference clock:
On package crystal
Built-in crystal oscillator
Built-in VCXO based PLL (xPLL)
External reference can used as well
Phase – Aligners + Ser/Des for E – Ports
Phase - Shifter
E – Port
E – Port
E – Port
E – Port
CDR
DEC/DSCR
SER
SCR/ENC
I2C Master
I2C Slave
Control Logic
Configuration
(e-Fuses + reg-Bank)
CLK Manager
CLK Reference/xPLL
JTAG
GBTX
ePLLTx
ePLLRx

## Slide 10: GBTX Functionality (4/4)
Chip Control
e-Fuse register bank for burn in configuration
  Standalone operation
  Ready at power up
Dynamic configuration and control
  I2C Slave interface
  IC control channel trough the optical link
Watchdog circuit for chip operation supervision.
GBLD Control
GBLD dedicated I2C master interface
  Copies configuration burned in the GBTX into the GBLD at start-up
  Allows to program the GBLD either through the IC channel or through the I2C slave port
Phase – Aligners + Ser/Des for E – Ports
Phase - Shifter
E – Port
E – Port
E – Port
E – Port
CDR
DEC/DSCR
SER
SCR/ENC
I2C Master
I2C Slave
Control Logic
Configuration
(e-Fuses + reg-Bank)
CLK Manager
CLK Reference/xPLL
JTAG
GBTX
ePLLTx
ePLLRx

## Slide 11: GBTX In Numbers
½ million gates
Approximately:
  300 8-bit programable registers (all TMR)
  300 8-bit e-Fuse memory
Clock tree (chip wide):
  9 clock trees (all TMR)
  Frequencies: 40/80/160/320 MHz
7 PLLs:
  RX: CDR PLL + Reference PLL (2.4 GHz)
  Serializer PLL (4.8 GHz)
  Phase-Shifter PLL (1.28 GHz)
  xPLL (VCXO based PLL, 80 MHz)
  (2x) ePLL (320 MHz)
17 master DLLs:
  9 for phase alignment of the e-links
  8 for clock de-skewing
56 replica delay lines:
  For phase alignment of the e-links
7 power domains:
  Serializer (1.5V)
  DESerializer (1.5V)
  Clock Manager (1.5V)
  Phase shifter (1.5V)
  Core digital (1.5V)
  I/O (1.5V)
  Fuses (3.3V)
17 mm
17 mm
Total height including solder balls: ~3 mm
4.3 mm
4.3 mm

## Slide 12: GBTX – Floor Plan and Modelling
10 “Macro-cells”:
Serializer:
  Full custom
  “Analogue-Verilog" modelling
Clock Manager:
  Standard cells
  Verilog modelling
DESerializer
  Full custom
  + “custom” digital
  + standard cells
  “Analogue-Verilog" + Verilog modelling
XPLL
  Full custom
  “Analogue-Verilog" modelling
EPLL (x2)
  Full custom
  “Analogue-Verilog" modelling
Phase-Shifter
  Full custom
Phase Aligners (x8)
  Full custom
  “Analogue-Verilog" modelling
Prompt (x3)
  Full custom
  Verilog modelling
Power on reset
  Full custom
  Verilog modelling
e-Fuses (x300)
  Foundry IP
  Verilog modelling
SER
ePLL
Phase-Aligners
Phase-Aligners
Phase-Aligners
I/O Cells
Phase-Shifter
E-Fuses
PROMPT
xPLL
PON-RST
CLK-MAN
DES
Standard Cells: “everywhere”

## Slide 13: The GBTX up-link
Each eLink is associated with a specific set of bits in the frame
Front-end modules are thus “geographically” addressed:
  By being physically connected to an eLink
  No module address is required
Frontend
Module
Frontend
Module
Frontend
Module
Frontend
Module
GBT-SCA
IC Control
GBTX
eLinks: 80 /160 / 320 Mbps
Data and clock line (optional)
GBT-Frame
4.8 Gbps
optical-fibre link

## Slide 14: Transmitter Architecture
40 + 1 Rx eLinks
56 + 1
Phase Aligners
28 + 1 DeSerializers
1/2, 1/4 and 1/8
16 BiDir eLinks
Scrambler
FEC
Interleaver
8B10B
Encoder
Scrambler
Header
Insertion
Header
Insertion
Comma
Insertion
Serializer
/ Driver
Wide - Bus
GBT - Frame
8B10B - Frame
Bus Mode
“Conceptual”
40 + 1 Clocks

## Slide 15: Up eLink – Phase Alignment
The phase of the incoming data signals is “unknown” in relation to the internal sampling clock!
There are up to 57 eLink inputs (potentially) all with random phase offsets
The solution:
  “Measure” the phase offset of each eLink input
  Delay individually each incoming bit stream to phase align it with the internal sampling clock
eLink “i”
eLink “j”
Good sampling instants
GBTX internal clock
Bad sampling instants

## Slide 16: Phase Aligner
One master DLL and eight replica delay lines
Three modes of operation:
  Static phase selection:
    A system calibration must be done
  Training with learned static phase:
    1st a training pattern is sent to the GBTX over the e-Link
    2nd after training the phase is fixed:
  Automatic phase tracking:
    No system calibration required
    No need for DC balanced data
Unused channels can be powered Off
Power: 4 mW (for 8 channels)
(The above picture is just for “easy representation”. In reality the sampling clock phase is fixed and the data phase is adjusted.)
The total delay line delay is equal to 7/4 Tbit
The delay line is divided into 14 equal delay intervals Tbit /8
In the automatic mode the circuit can tolerate jitter which is ±3/8 Tbit

## Slide 17: eLink Data Latency
0
0
1
2
1
{Data(n-2)[0], Data(n-1)[1]}
{Data(n-1)[0], Data(n)[1] }
0
1
0
0
1
3
2
1
0
1
0
3
2
1
0
7
6
5
4
3
2
1
0
7
6
5
4
3
2
1
2
1
x4 Mode
x8 Mode
1
1
0
1
0
x2 Mode
0
3
2
1
0
2
1
0
3
{Data(n)[0], Data(n+1)[3:1]}
0
Important note:
A “word” might (it most likely will) span across a 40 MHz clock cycle boundary! (De-Serializer doesn’t know about the data structure!)
How the words will split depends on the link “return path” delay and on the phase programmed on the phase aligner.
{Data(n-1)[0], Data(n)[3:1]}
0
7
6
5
4
3
2
1
0
7
6
5
4
3
2
3
2
1
{Data(n)[0], Data(n+1)[7:1]}
0
{Data(n-1)[0], Data(n)[7:1]}
CLK 40 MHz
Shift CLK = 160 MHz
Phase Aligner Channel:
Shift register:
Parallel data:
CLK 40 MHz
Shift CLK = 80 MHz
Phase Aligner Channel:
Shift register:
Parallel data:
CLK 40 MHz
Shift CLK = 320 MHz
Phase Aligner Channel:
Shift register:
Parallel data:
0
Note1:
In all cases, the shift clock (80/40 /160 /320 MHz) is always “180°” out of phase with the 40 MHz reference clock.
Note2:
If data “splitting” is to be avoided this has to be done either at the frontend or the backend. In this case a latency of 1 LHC clock cycle has to be accounted
for.

## Slide 18: Tx eClock Jitter
“Absolute jitter”
  Scope triggered by the FPGA transmitter reference clock
  SLVDS driver with maximum current settings
eLink Clocks | Simplex Tx Operation | 
Frequency | Jitter s | Jitter P-P
[MHz] | [ps] | [ps]
40 | 6.0 | 47.8
80 | 5.9 | 45.0
160 | 5.6 | 49.4
320 | 5.7 | 44.4
320 MHz eClock
(all eLink signals on)

## Slide 19: Serializer: Architecture
Serializer:
  4.8 Gb/s
  120-bit shift register
    3 × 40-bit shift register (f=1.6 GHz)
    3-to-1 fast multiplexer (f=4.8 GHz)
Data path:
  No SEU protection
  SEUs handled by the Reed-Solomon CODEC
Clock divider:
  Divide by 120
  f = 4.8 GHz
  Triple voted for SEU robustness
PLL:
  SEU hardened VCO
  SEU hardened Clock Divider
    Based on “custom” dynamic flip-flop
  The PLL clock is used a the transmitter master clock (and not the reference clock)

## Slide 20: Fast-Mux / Line Driver
Pre-discharge switches to minimize pattern-dependent jitter
Three non-overlapping phases: 1/3 of 4.8 GHz
Pseudo differential output stage
Data inputs: 1/3 4.8 Gb/s

## Slide 21: Tx Eye-Diagram
GBTX
GBT-SerDes
 | GBTX | GBT-SerDes
TJ (1e-12) | 73.2 ps | 53.8 ps
RJ (rms) | 2.6 ps | 2.4 ps
PJ (d-d) | 24.1 ps | 19.4 ps
PJ (rms) | 6.6 ps | 4.6 ps
DJ (d-d) | 36.0 ps | 19.0 ps
DDJ (p-p) | 17.8 ps | 4.8 ps
DCD | 1.6 ps | 0.64 ps
ISI (p-p) | 17.5 ps | 4.8 ps
tr / tf | 100 ps | 80 ps
Max Data Rate | 5.4 Gb/s | 6.0 Gb/s
The same driver in the GBTX and GBT-SerDes!
However the clock phases were rotated to allow operation at 2.4 Gb/s
Simulations have not yet reveal the cause of the degradation!!!

## Slide 22: The GBTX down-link
As for the up link, each eLink is associated with a specific set of bits in the frame
Front-end modules are thus “geographically” addressed:
  By being physically connected to an eLink
  No module address is required
Frontend
Module
Frontend
Module
Frontend
Module
Frontend
Module
GBT-SCA
IC Control
GBTX
eLinks: 80 /160 / 320 Mbps
Data and clock line (optional)
GBT-Frame
4.8 Gbps
optical-fibre link

## Slide 23: Receiver Architecture
20 + 1 Serializers
x2, 1/4 and 1/8
Scrambler
Interleaver
FEC Decoder
Header
Detection
Line Receiver
DeSerializer
GBT - Frame
24 + 1 Tx eLinks
16 BiDir eLinks
40 + 1 Clocks

## Slide 24: Down eLink – Phase Alignment
Data and clock phases are aligned at the output of the ePort drivers
The system designer must ensure that clock and data phases “track each other” in the frontend modules
eClocks frequency can be programed independently of the eLink data rate
It is possible avoid the eLink clocks but clock recovery must be used in the frontend
  In this case the data transmitted over the eLinks must be DC balanced

## Slide 25: Rx eClock Jitter
“Absolute jitter”
  Scope triggered by the FPGA transmitter reference clock
  SLVDS driver with maximum current settings
eLink Clocks | Simplex Rx Operation | 
Frequency | Jitter s | Jitter P-P
[MHz] | [ps] | [ps]
40 | 7.2 | 60.5
80 | 6.8 | 56.7
160 | 5.9 | 45.6
320 | 5.8 | 47.8
80 MHz eClock
(all eLink signals on)
eLink Clocks | Duplex Rx Operation | 
Frequency | Jitter s | Jitter P-P
[MHz] | [ps] | [ps]
40 | 7.2 | 58.9
80 | 6.7 | 55.0
160 | 5.9 | 47.2
320 | 5.7 | 43.9

## Slide 26: eLink eye-diagrams
80 Mb/s
160 Mb/s
320 Mb/s
 | 80 Mb/s | 160 Mb/s | 320 Mb/s | Units
TJ (1e-12) | 105.3 | 150.8 | 166.5 | ps
RJ (rms) | 6.7 | 6.9 | 6.9 | ps
PJ (d-d | 5.6 | 19.0 | 59.0 | ps
PJ (rms) | 1.3 | 6.8 | 17.2 | ps
DJ (d-d) | 9.6 | 52.8 | 79.7 | ps
DDJ (p-p) | 12.3 | 44.8 | 31.7 | ps
DCD | 5.1 | 26.3 | 20.0 | ps
ISI (p-p) | 8.4 | 23.7 | 13.0 | ps

## Slide 27: System Latency

## Slide 28: DESerializer Architecture
1/3
(SKC)
Up
Down
S0
Sp
CK1/2
dataOdd
dataEven
phCntClock2400MHz
dataIn
rxOddReg[59:0]
rxEvenReg[59:0]
Data Re-Sampler
Phase/Freq
Detector
Charge
Pump
Loop
Filter
VCO
1-to-3
SREG
3-to-15
SREG
15-to-60
SREG
60
REG
1/5
1/4
1-to-3
SREG
3-to-15
SREG
15-to-60
SREG
60
REG
clock40MHz
3
3
15
15
60
60
skipCycle
(240 MHz)
(800 MHz)
(160 MHz)
(40 MHz)
clock80MHz
rxSelectDataInPhase
CDR PLL
DES 2/120
clock160MHz
Fast dynamic logic
“Macro Cell”
Full custom logic: DFF, gates, …
Characterized in ELC
“Hand” net list
Verilog Simulation
P&R in Encounter
Timing extracted
Back annotation
Verilog simulation
Spice simulation

## Slide 29: Phase Shifter
Main features:
8 – channels
Clock frequencies: 40, 80, 160 and 320 MHz
Phase resolution: 48.8 ps
Phase span: 0 to 2p
1 PLL + Counter generates frequencies: 40, 80, 160, 320, 640 and 1280 MHz
1 DLL per channel
Mixed digital/analogue phase shifting technique:
  Coarse deskewing – Digital
  Fine deskewing – Analogue
Differential non-linearity: < 6.7% LSB
Integral non-linearity: INL < 6.5% LSB
Power consumption: 5.6 mW/channel
Resolution = 1/(1.28GHz) = 781.25 ps
Resolution = 1/(16X1.28GHz) = ~49 ps

## Slide 30: Phase-Shifter Performance (1/3)

## Slide 31: Phase-Shifter Performance (2/3)
Non-Linearity |  | Integral |  |  | Differential |  | 
Frequency | Dt [ps] | s [ps] | Max [ps] | Min [ps] | s [ps] | Max [ps] | Min [ps]
40 MHz | 50 | 14.8 | 51.6 | -30.1 | 16.9 | 28.5 | -31.5
80 MHz | 50 | 11.8 | 35.6 | -23.2 | 8.2 | 20.3 | -14.6
160 MHz | 50 | 12.8 | 39.8 | -22.9 | 8.7 | 18.5 | -16.0
320 MHz | 50 | 15.7 | 47.1 | -30.7 | 17.0 | 29.7 | -30.6

## Slide 32: Phase-Shifter Performance (3/3)
Jitter |  | Min Delay (0 ns) |  | Max Delay (25 ns) | 
Frequency | Mode | s [ps] | P-P [ps] | s [ps] | P-P [ps]
40 MHz | Simplex Tx | 3.8 | 37.0 | 4.4 | 40.7
80 MHz | Simplex Tx | 3.4 | 36.7 | 3.8 | 37.5
160 MHz | Simplex Tx | 4.8 | 36.2 | 8.5 | 48.6
320 MHz | Simplex Tx | 13.5 | 63.0 | 15.2 | 67.3
40 MHz | Duplex | 3.9 | 40.9 | 4.4 | 45.0
80 MHz | Duplex | 3.6 | 35.0 | 3.8 | 37.5
160 MHz | Duplex | 5.4 | 42.3 | 8.9 | 49.5
320 MHz | Duplex | 13.4 | 65.7 | 15.3 | 70.6

## Slide 33: xPLL
Phase-Locked Loop based on a Quartz Crystal Oscillator (VCXO)
On package Quartz Crystal tailored to the LHC frequency
Three main functions:
  Clock reference (for systems without clock reference)
  Jitter cleaning PLL for systems with a “noisy” system clock
  Watchdog clock source

## Slide 34: xPLL Performance – VCXO Mode
VCXO Mode | 40 MHz | Units
TJ (1e-12) | 126.9 | ps
RJ (rms) | 5.4 | ps
PJ (d-d | 50.5 | ps
PJ (rms) | 11.7 | ps
DJ (d-d) | 50.5 | ps

## Slide 35: xPLL Performance – PLL Mode
VCXO Mode | 40 MHz | Units
TJ (1e-12) | 184.4 | ps
RJ (rms) | 8.8 | ps
PJ (d-d | 58.5 | ps
PJ (rms) | 19.0 | ps
DJ (d-d) | 58.5 | ps

## Slide 36: ePLL
Two ePLLs are used to generate the 160 and 320 MHz clocks needed to run the ePorts at 160 and 320 Mb/s respectively
It allows phase shifting the internal clocks with 200 ps resolution
  This is only for internal timing, can’t be used for phase adjust of the eLink clocks
The operation of the ePLLs is transparent to the users.
The performance of the device is reflected on the ePort clocks at 160 and 320 MHz

## Slide 37: Controlling the GBTX
eFuse Register Bank
(~300 8-bit words)
Configuration Registers
(~300 8-bit registers)
Copied into the configuration registers if the eFuses are enabled
I2C Interface
IC Channel
If the eFuses are not enable then the configuration registers must be written through the I2C slave interface
Configuration registers are TMR protected
Use of the IC channel to control the ASIC requires duplex operation
A “special” eFuse indicates if the I2C or eFuse bank are in use

## Slide 38: Interfacing with the GBLD

## Slide 39: Built-in Test Features
A series of “loopbacks” allow to test the chip with different levels of depths:
  Fast-serial to fast-serial
  ePort to ePort
  ePort – driver to ePort – receiver
Tx high speed test patterns:
  Header + AAA_BBBB_AAAA_BBBB_AAAA_BBBB_AAAA_BB
  Header + counter[25:0] + counter[29:0] + counter[29:0] + counter[29:0]
  Header + 4’h0 + prbs[6:0] x 16
Rx bit error counter:
  Works with the fixed pattern
ePort patterns to validate the GBTX to Frontend timing

## Slide 40: SEU TEST – Louvain-la-Neuve
Heavy Ion Irradiation Facility (HIF)

## Slide 41: SEU Test Setup
Ion type:
  Ar – 372
    LETeff = 10.2 MeV/ mg cm2
  Ne – 235
    LETeff = 3 MeV/ mg cm2
8 hour time slot:
  22 “test” runs
Faced some problems with the test setup:
  “Fixed” latency FPGA Rx needs to be used
  Robust lock tracking FPGA Rx must be used
Tested Cases:
  High Speed loopback
  Simplex Tx:
    80 and 160 Mb/s ePorts
    Max and min phase-aligner delay
  Simplex Rx:
    80 Mb/s ePorts
  Duplex:
    80 Mb/s ePorts
  “Special” duplex
    Both Tx and Rx clocked by the reference clock

## Slide 42: Duplex, ePorts 160 Mb/s , Ne: LETeff = 3 MeV/ mg cm2, flux 15.4k i/cm2 s
Rx
Tx
sevent = 18.6 mm2
sevent = 18.6 mm2

## Slide 43: Duplex, ePorts 160 Mb/s , Ar: LETeff = 10.2 MeV/ mg cm2, flux 8k i/cm2 s
Rx
Tx
Tx Reset?
FPGA receiver desynchronized
Shouldn’t have an only register “A”
Registers errors should be corrected in a fraction of a second!!!

## Slide 44: GBTX Power Consumption (1/2)
All power supplies voltages = 1.5V except EfusePower = 3.3V
I/O (gndIO/vddIO):
  P = 41 × 8.2 mW (Data SLVS-Tx) + 41 × 8.2 mW (CLK SLVS-Tx) + 41 × 0.65 mW (SLVS-Rx) = 698 mW, I = 466 mA
TX (gndTx/vddTx):
  P = 456 mW, I = 304 mA
RX (gndRx/vddRx):
  P = 330 mW, I = 220 mA
CORE (GND/VDD):
  P = 305 mW (Standard cells) + 8 × 3.5 mW (Phase-Aligners) = 333 mW, I = 222 mA
PS (gndPS/vddPS):
  P = 42 mW (PLL) + 8 × 16 mW (channel) + 8 × 8.2 mW (SLVS-Tx) = 236 mW, I = 157 mA
CM (gndCm/vddCm):
  P = 2 × 41.5 mW (E-PLL) + 100 mW (XPLL) = 183 mW, I = 122 mA
E-Fuses (EfusePower):
  P = 465 mW , I = 141 mA
  (Only during e-fuse programming. Not added to the total power figure below.)
Total:
  P = 2.2 W
  (This is worst case power consumption: all functions ON, worst case simulations)
Chart: 
| I/O | TX | RX | CORE | PS | CM
 | 698 | 456 | 330 | 333 | 236 | 183

## Slide 45: GBTX Power Consumption (2/2)
Case study:
Hypothetical CMS Tracker upgrade configuration:
  E-Links:
    20 × Data-In @ 160 Mb/s
    1 × Clock @ 160 MHz
    2 × Data-Out @ 160 Mb/s
  Phase-Adjustable clocks:
    2 × Clock @ 40 MHz
    2 × Clock @ 160 MHz
Mode: |  |  |  | TRANSCEIVER
E-Links: |  |  |  | 
 | Data rate [Mb/s]: |  |  | 160
 | # Data outputs: |  |  | 2
 | # Clock outputs: |  |  | 1
 | # Data inputs: |  |  | 20
EC-Channel: |  |  |  | 
 | State: |  |  | Disabled
Phase-Shifter: |  |  |  | 
 | State: |  |  | Enabled
 | # Channels |  |  | 4
Circuit: |  |  |  | Power
 |  |  |  | [mW]
 | Transmitter: |  |  | 
 |  |  |  | 456
 | Receiver: |  |  | 
 |  |  |  | 330
 | Clock Manager |  |  | 
 |  | E-PLL: |  | 83
 |  | XPLL: |  | 100
 |  | Total: |  | 183
 | Phase-Shifter: |  |  | 
 |  | PLL: |  | 42
 |  | Channel: |  | 64
 |  | SLVS-TX: |  | 33
 |  | Total: |  | 139
 | I/O: |  |  | 
 |  | Data SLVS-Tx: |  | 16
 |  | CLK SLVS-Tx: |  | 8
 |  | Data SLVS-Rx: |  | 13
 |  | Total: |  | 38
 | CORE: |  |  | 
 |  | Standard Cells: |  | 305
 |  | Phase-Aligners: |  | 14
 |  | Total: |  | 319
Total Power [mW]: |  |  |  | 1464

## Slide 46: GBTX Future
Q4 – 2013
  Finalize chip characterization: November– December
  Total dose irradiation tests: December
  Samples available for prototyping: December
    Only small quantities available (< 30)
Q1 – 2014
  Second run of SEU tests: February
  Depending on the SEU test results small changes might be required to improve the robustness of the circuit
  Although the circuit is fully functional a “a few small corners need to be rounded” to make it “plug-and-play” for the users
Q2 – 2014
  Additional 100 GBTX samples available
  Split Engineering Run to produce in quantities:
    GBTX
    GBTIA
    GBLD V4/V5
    GBT-SCA
Q3 – 2014
  Chips available from the foundry
  ASIC Packaging
Q4 – 2014
  ASIC production testing
  First production ASICs distributed to the users

## Slide 47: Backup Slides
Additional Slides

## Slide 48: GBTx latency measurement
Has to include
  Back end: GBT-FPGA IP core (Rx or Tx)
  Front End: E-links IP core (Serializer or Deserializer)
  To allow pattern detection for flag rising
We used a test system presented at TWEPP, including:
  BE: GLIB
  GBTX: SAT board
  FE: ML605 (virtex6) equipped with an HDMI-FMC
We removed all the system specific delays (cables, PCB, etc)

## Slide 49
BACK END
(GLIB)
GBTx SAT
board
FRONT END
(ML605 + HDMI FMC)

## Slide 50
E-LINK SERDES
GBT-FPGA TX
MGT TX
GBT-FPGA RX
MGT RX
SFP
GBTx
GBT-FPGA
SFP
CV
HDMI
HDMI
HDMI
HDMI
FE EMULATOR
HDMI
HDMI
HDMI
HDMI
GBTx SAT board
ML605
GLIB
GBT SERDES
E-LINK SERDES
CDR
CDR
CLOCK
Automatic Phase alignment (one value per e-link, transparent to the user)
Sub-frame alignment (add 1 BC)
E-links 0, 2, 4, 6 only
are connected, allowing:
4 e-links of group0 @ 80MHz
Full group0 @ 160MHz
Flag3,
latched with e-link clock
Flag4,
latched with e-link clock
Flag1,
latched with e-link clock
Flag2,
latched with e-link clock
BACK END
FRONT END
Sub-frame alignment (add 1 BC)
189 ns
280 ns
Downstream
Upstream

## Slide 51
E-LINK SERDES
GBT-FPGA TX
MGT TX
GBT-FPGA RX
MGT RX
GBTx
GBT-FPGA
FE EMULATOR
GBTx SAT board
ML605
GLIB
GBT SERDES
E-LINK SERDES
CDR
CDR
CLOCK
Bit alignment per group (add 1 BC)
Flag3,
latched with e-link clock
Flag4,
latched with e-link clock
Flag1,
latched with e-link clock
Flag2,
latched with e-link clock
BACK END
FRONT END
Bit alignment per group (add 1 BC)
189 ns
280 ns
5 ns
11 ns
1 ns
Core latency : 280 -1 -5 – 11 - 9 = 254 ns
Core latency: 189 + 1 -5 – 11- 8 = 166 ns
Downstream
Upstream
9 ns
8 ns

## Slide 52: Total
Architecture: GBT encoding scheme and e-links @ 160 MHz,
Downstream Core Latency:
GBT-FPGA Tx + GBTx + FE GBT deserializer =
166ns = 6.65 BC
Upstream Core Latency:
FE GBT serializer + GBTx + GBT-FPGA Rx (latency optimized) =
254 ns = 10.1 BC
Without the bit alignment (per group), to be done either in the Front End or in the Back End:
=> you should add 1 BC (for bit alignment) to have a realistic value, plus the length of your cables and PCB traces

## Slide 53: GBTX Frames
H(3:0)
IC(1:0)
EC(1:0)
D(63:48)
D(47:32)
D(31:16)
D(15:0)
FEC(31:16)
FEC(15:0)
D(79:64)
G0
G1
G2
G3
G4
GBT Frame (for up and down links)
EC
H(3:0)
IC(1:0)
EC(1:0)
D(63:48)
D(47:32)
D(31:16)
D(15:0)
D(111:96)
D(95:80)
D(79:64)
G5
G6
G0
G1
G2
G3
G4
Wide Bus Frame (for up-links only)
EC
G5 (1/2)
G6 (not used)
G0
G1
G2
G3
G4
8B/10B Frame (for up-links only)
8B/10B
8B/10B
8B/10B
8B/10B
8B/10B
8B/10B
8B/10B
8B/10B
8B/10B
8B/10B
8B/10B
8B/10B
“Out of order” bit sequence for compatibility with the GBT frame