## Slide 1: TDC and PLL work
Jeffrey Prinzie

## Slide 2: Previous work
Thesis
  Low jitter clock generator
PhD
  Radiation tolerant TDC

## Slide 3: Low jitter clock generator Concept
Equivalent-time sampling clock
  Tref + Ts
UWB imaging (Tx / Rx)
  Requires accurate clock
Low jitter
51.2 GSa/s eq. time

## Slide 4: Low jitter clock generator Architecture

## Slide 5: Low jitter clock generator PLL
3rd order PLL
2.8 ps RMS jitter
8 phase generation
Maneatis load VCO
Charge pump PFD
No multiplier
90nm UMC CMOS

## Slide 6: Low jitter clock generator DTC
0-1.25ns Delay control
6 bit
PVT insensitive
2nd Phase lock

## Slide 7: Low jitter clock generator Results
19,5 ps
3.2 ps jitter
(system)
4 mW power consumption

## Slide 8: Low jitter clock generator Discrete component version

## Slide 9: Low jitter clock generator Discrete component version

## Slide 10: Previous work
Thesis
  Low jitter clock generator
PhD
  Radiation tolerant TDC

## Slide 11: TDC chip 1
DLL based TDC
  DLL → gain/resolution
  Td = Tref/N
  DLL corrects TID radiation
  DLL reduces mismatch effects

## Slide 12: TDC chip 1
Delay line
  Resistive interpolation
  5.8ps resolution
    Tref/5N
  Mismatch
    156 fs/√ps
Coding
  Thermometer code → Binary
    Bubble correction
    Priority detection
    ROM

## Slide 13: TDC chip 1
DLL control loop
  Radiation
    TID → offset in PD
    SEE → lock loss
  Combination PFD and Bangbang PD
    Speed/Recovery→ PFD
    Low offset (calibration) → Bangbang PD

## Slide 14
PFD
Deadzone (20ps)
High bandwidth
SEE recovery
Large SPO
Bangbang PD
Low bandwidth (fine adjustment)
Low SPO (1.2 ps 3σ) (TID)
Trade-off: speed vs. ripple (spur)

## Slide 15: Progress Chopped phase detector
Bang-Bang-PD: Chopping
  Minimizes SPO through radiation
  Time domain
Principe
  Inject calibration-clock in both inputs
  Measure phase difference (offset)
  Correct PD
  Effective DLL measurement
Calibration

## Slide 16: Progress: chip 1
  Inject calibration-clock in both inputs
  Measure phase difference (offset)
  Correct PD
  Effective DLL measurement

## Slide 17: Progress: chip 1
  Inject calibration-clock in both inputs
  Measure phase difference (offset)
  Correct PD
  Effective DLL measurement

## Slide 18: Progress: chip 1
  Inject calibration-clock in both inputs
  Measure phase difference (offset)
  Correct PD
  Effective DLL measurement

## Slide 19: Progress: chip 1
  Inject calibration-clock in both inputs
  Measure phase difference (offset)
  Correct PD
  Effective DLL measurement

## Slide 20: Progress: chip 1
Mismatch between 2 Mux
  → SPO ( 1.2ps 3σ including measurement)
Reduction of 1/f noise in PD
  Increases with radiation
Future improvements
  Interleaved BB-PD
  Individual calibration of DLL elements

## Slide 21
1.75mm
0.95mm
370 µm
130 µm
45 nm TSMC CMOS RF 10 layer

## Slide 23: Conclusion
2 year work on
  Time based systems / control loops
    PLL, TDC, DTC …
  nm CMOS implementation
  Jitter / Phase noise optimization
1 year work on
  Radiation effects
Research group
  Multiple PhD on radiation tolerant ICs
    Amplifier , ΣΔ TDC …

## Slide 24: Thank you