## Slide 1: Overview of CMS Forward Muon Upgrade
Brian L. Dorney on behalf of the CMS Collaboration

## Slide 2: The CMS Detector
CMS Collaboration, Lucas Taylor, “CMS detector design,” http://cms.web.cern.ch/news/cms-detector-design 2011.

## Slide 3: The CMS Trigger
Two level system
  Hardware level: on-detector electronics, Level 1 (L1)
  Software level: underground CPU farm, High Level Trigger (HLT)
Significant rate reduction
  LHC collision rate is O(10 MHz)
  L1 trigger readout rate ~100 kHz
  HLT rate ~1 kHz
~400 different trigger paths select pp collision events for offline analysis

## Slide 4: CMS Muon Performance: Run I
Muon-trigger demonstrated superb performance over very wide pT range!
A = {ω, ϕ, J/ψ, ψ*, Bs, ϒ(ns), Z0}

## Slide 5: CMS Muon Performance: Run I
Exceptionally high muon-reconstruction and identification efficiency has been demonstrated!!

## Slide 6: CMS Physics Results: Run I
Fantastic physics results!!!
Phys. Rev. Letters, 112, 191802 (2014)
Phys. Rev. Letters, 111, 101804 (2013)
CMS Collaboration, CMS PAS TOP-14-001, 2014.

## Slide 7: CMS Physics Results: Run I
Producing fantastic physics results
Phys. Rev. Letters, 112, 191802 (2014)
Phys. Rev. Letters, 111, 101804 (2013)
CMS Collaboration, CMS PAS TOP-14-001, 2014.
Phys. Rev. D, 89, 0920077 (2014)
Not possible w/o state-of-the-art muon system

## Slide 8: The Future
Muon-triggers in CMS from |η|>1.6 arrive solely from cathode strip chambers (CSC)
CSC system is at the limit of its performance
No redundancy!!!
  Potential problem for physics data taking
Sole System!
No Redundancy!!!

## Slide 9: The Future
The rate flattening problem
  Low-pT “soft” muons scatter in the steel return yoke
  Tracks are incorrectly reconstructed as high-pT “hard” muons
Rare occurrence but very high number of soft muons
  Causes large tail in L1 muon-trigger pT resolution
Flattening of L1 trigger rate at high-muon pT values due to this large tail
Rate flattening!!!

## Slide 10: Solution: GEM-CSC Bending Angle
Additional muon chambers before first CSC station offers significant improvement
Bending angle:
acts as powerful discriminator between soft and hard muons

## Slide 11: GEMs Solve Rate Flattening
Studies show triple-GEM detectors are the L1 trigger rate savior of CMS
Additional advantages
  Low cost
  High rate capability
  Radiation hard:
    Dose > 9mC, no degradation
    See Jeremie’s talk!!!!
  Good spatial/time resolution:
    ~100μm; ~4-5ns
  High Efficiency (~98%)
  Nonflammable gas mixture
  Rapid manufacturing time
    See Antonio’s talk!!!
Improvement!!!

## Slide 12: The CMS GEM Project
Create redundancy in muon system
Robust tracking
Reduce L1 muon-trigger and HLT rates by improving muon pT resolution
Ensure ~100% trigger efficiency in post LS2 pp collision environment
  High pile up!
    LS2 (LS3) <PU> = 70(140)
Proposal to install triple-GEM detectors in the forward region of CMS

## Slide 13: ME0 System
2.0 < |η| < 3.5
  20° wedges affixed to back of upgraded CMS HCAL endcap
Six layers of triple-GEM detectors
  Design ongoing
Significantly increases muon acceptance for high profile analyses
  e.g. H->ZZ->4μ
Total foil area ~144m2
Dz = 30 cm
2.5 borated polyethylene plus 1.2 Pb for n shielding
2.5 borated polyethylene plus 1.2 Pb for n shielding
f direction →
2
3
4
5
1
6
Sliding Rail
& Services Pocket
For package of 6
9
20 degree
Chambers
10
18 degree
Chambers
Thicknesses cm:
2.5 Borated Poly
1.2 Pb
3.2 Single Chamber 1
3.2 Single Chamber 2
3.2 Single Chamber 3
3.2 Single Chamber 4
3.2 Single Chamber 5
3.2 Single Chamber 6
3.2 Sliding Rail
1.2 Pb
2.5 Borated Poly
------------------------
28.8cm
Mechanical
Supports
ME0
Services
& Support

## Slide 14: Current Focus: GE1/1 System
1.55 < |η| < 2.18
  Short and long chambers for maximum coverage
36 superchambers (SC) per side of CMS
  Each chamber spans 10° in ϕ
  2 chambers/SC
  144 chambers total
Total foil area ~140m2
Four years of R&D has given us five prototype generations; each an improvement of the last!!!

## Slide 15: GE2/1 System
1.55 < |η| < 2.45
Each chamber spans 20°
Design on-going
Targeting two rings of double-layered triple-GEM detectors
Total foil area ~145m2
GE1/1
GE2/1

## Slide 16: Current Prototype: GE1/1-V5
Triple-GEM foils 5:50:5μm for Cu:Kapton:Cu
  70μm diam.; 140μm pitch
Gap configuration (in mm): 3/1/2/1
NS2 assembly technology; no spacers or glue!
NS2
GND
Epoxy frame
O-rings
Internal screws to adjust stretching
Gas volume
Free to slide
Drift electrode
GEM attaching structure (4 pieces defining gaps)
External screws
Washers
Embedded nut
GND
Readout connector

## Slide 17: Assembly of GE1/1-V5 Prototype
Brass pullout
New external frame without holes

## Slide 18: Assembly of GE1/1-V5 Prototype

## Slide 19: GEM DAQ

## Slide 20: GEM DAQ – Status
Version 2 production launched
Firmware development ongoing

## Slide 21: GEM DAQ – Status
Switching to MP7
Firmware under development
Being developed by CERN microelectronics group

## Slide 22: GEM DAQ – Status
Integration work ongoing at CERN in B904

## Slide 23: On-going Activities
Prototype production
X-ray station
CMS GEM Training School
Cosmic stand
CSC-GEM integration stand
Fall 2014 Test Beam
GE1/1 Slice Test in 2016

## Slide 24: Prototype Production
See Sinem’s talk regarding status of production sites!!!

## Slide 25: X-Ray Station: Gain Uniformity
APV
SRS
Amore SRS
DATE
master
master
slave
slave
DATA
Latency
Nb of APVs
Internal rate
Veto
Trigger type
Pulse from the bottom of the last GEM
Ar
CO2
CF4
Mixture 5l/h
exhaust
Xrays // 8 keV
Current
Voltage
ON/OFF
1,20 m
Need two FECs and 24 APVs to scan the entire prototype.
MiniX
MFC viewer
Trigger
Amplifier
CFD

## Slide 26: X-Ray Station: Gain Uniformity
APV
SRS
Amore SRS
DATE
master
master
slave
slave
DATA
Latency
Nb of APVs
Internal rate
Veto
Trigger type
Pulse from the bottom of the last GEM
Ar
CO2
CF4
Mixture 5l/h
exhaust
Xrays // 8 keV
Current
Voltage
ON/OFF
1,20 m
Need two FECs and 24 APVs to scan the entire prototype.
MiniX
MFC viewer
Trigger
Amplifier
CFD

## Slide 27: TIF Cosmic Stand
Additional layer of quality control
Construction on going
Aluminum superstructure completed
Assembling scintillators and trigger logic presently

## Slide 28: CMS GEM Training School
Introduce new members of the collaboration to principals of triple-GEM detectors
  Leakage current
  Assembly
  HV stability
  Gain calibration
Train expert collaborators in the use of SRS+APV system for gain calibration measurements
  Critical to large scale production of GE1/1 system

## Slide 29: CSC-GEM Integration Stand
Goal: Slice test readiness
  CSC track finding algorithm commissioned before slice test
Full ME1/1 CSC chamber present in B904
Plan to add GE1/1 prototype in tandem
  Position as if they were in CMS
Use cosmics to develop cross chamber communication and trigger logic
HV
Computer for μTCA
μTCA Crate
CMS GE1/1

## Slide 30: Fall 2014 Test Beam

## Slide 31: Fall 2014 Test Beam Setup
H2 Test Beam w/Magnet
October 13th – Nov 2nd
Charge sensitive performance measurements in high B field
Test version one of GEM electronics
H4 Test Beam w/Magnet
Nov 26th – Dec 15th
Timing sensitive performance measurements with B=0
Study impact of radiation dose on performance
Test of version two of GEM electronics
μ
Magnet
Magnet
1st Tracker
(RD51 Collab.)
2nd Tracker
(CMS GEM Collab.)
GE1/1-V5
GE1/1-V4
μ
GE1/1-V5
GE1/1-V4
GE1/1-V4 GIF
RD51 Tracker
GE1/1-V6-L1
CMS Tracker
No Tracker!!!

## Slide 32: GE1/1 Slice Test
GE1/1-Slice TEST
SLOTS 1-2; 35-36
Gas Racks
40° wedge
4 superchambers
8 chambers total

## Slide 33: On-going Activities
X-ray station
CMS GEM Training School
Cosmic stand
CSC-GEM integration stand
Fall 2014 Test Beam
GE1/1 Slice Test in 2016
You can get involved! Ask how!!!
  Discoveries around the corner!!!

## Slide 34: Conclusion
Post LS2 presents a challenging pp collision environment
To maintain ability to perform competitive physics measurements CMS must adapt
Muon upgrade based on triple-GEM detectors is an ideal solution for post LS2 operations

## Slide 35: Back-up slides

## Slide 36: Muon Reconstruction in CMS
Tracks independently reconstructed in:
  Silicon tracker, referred to as tracker tracks
  Muon chambers, referred to as standalone-muon tracks
Global muon reconstruction via outside-in approach
  Attempts to match a standalone-muon track to a tracker track
Tracker muon reconstruction via inside-out approach
  Tracker tracks extrapolated to muon chambers
  Attempt to match to track stub in muon chambers

## Slide 37: CMS Coordinate System
CMS Collaboration, Detector Drawings, CMS-PHO-GEN-2012-002.