## Slide 1: FIELD QUALITY UPDATE
E. Todesco
CERN, Geneva Switzerland
Thanks to Susana, Xiarong, Gianluca
Tsukuba, 20th November 2014
Hi-Lumi meeting

## Slide 2: CONTENTS
Triplet
  Field quality variation with operational current
  Spread in integrated gradient
  Non allowed multipoles
D1
  Field quality variation with operational current
D2
  Field quality variation with operational current

## Slide 3: TRIPLET
Spread in the integrated gradient
  Orders of magnitude of integrated gradient spread (one sigma) in previous productions
    MQ, MQM: 13 units
    MQXA/MQXB: less than 10 units
A variation of 0.1 mm in coil position gives of the order of 10 units difference in integrated gradient
  So 1 s = 10 unit this is the best guess we can give today
  To have 100 units difference (1%) one would need 1 mm, which is a lot
So I would propose to remove the trim on Q2a from the baseline and keep it in the options

## Slide 4: TRIPLET
Dependence of field quality on operational current
  All field quality optimized at top field (7 TeV)
  Going to 6.5 TeV we add a fraction of unit of b6
  Having 10% less on the top of this (ABP request) would give a 1 systematic unit of b6
  Optimization at 6.5 TeV instead of 7 TeV being considered
b6 versus current in QXF [S. Izquierdo Bermudez]
7 TeV

## Slide 5: TRIPLET: NON ALLOWED MULTIPOLES
The most critical paramter is the size of non allowed multipoles (a3, b3, a4, b4)
  This parameter is difficult to estimate (you need an homogeneous set of few magnets)
  First data on HQ shows we are a factor two-three off
    Similar results on the first MQXC Nb-Ti magnet (so it is not specific to Nb3Sn technology)
    Good result considering that we are on a short model, first iteration
    In case we don’t manage to go there, we have a plan B: magnetic shimming

## Slide 6: TRIPLET
Shimming strategy to correct low order non allowed multipoles is effective at 7 TeV
  Saturation makes the correction nonlinear
  Also in this case optimizing at 6.5 TeV guarantees effective correction from 90% of 6.5 TeV to 100 % of 7 TeV
Shim effect versus current [P. Hagen]
90% of 6.5 TeV
100% of 7 TeV

## Slide 7: D1
D1
  Fine tuning of b3 presently done at 7 TeV
    Running at 6.5 TeV will give 2 units of b3 – probably we should optimize at 6.75 TeV
b3 versus current in D1 [Q. Xu, T. Nakamoto]
6.5 TeV
100% of 7 TeV

## Slide 8: D2
D2
  Fine tuning of b3 presently done at 7 TeV
    Running at 6.5 TeV will give 1 unit of b2, 2 units of b3 – probably we should optimize at 6.75 TeV
Multipoles versus current in D2 [P. Fabbricatore]
6.5 TeV
7 TeV

## Slide 9: SUMMARY
Integrated gradient uniformity
  10 units estimate - proposal to remove the trim on Q2a from the baseline
Main concern is not allowed multipoles
  On the way to reach the ambitious target
  Plan B magnetic shimming
Optmization of field quality for QXF should be done at 6.5 TeV
  We can guarantee good field from 90% of 6.5 TeV to 100% of 7 TeV
Optmization of field quality for D1 and D2 should be done at 6.75 TeV
  We can guarantee good field from 6.5 TeV to 7 TeV