## Slide 1: Design of the new D1 and relevant R&D
Click to edit Master title style
Click to edit Master text styles
  Second level
    Third level
      Fourth level
        Fifth level
The HiLumi LHC Design Study is included in the High Luminosity LHC project and is partly funded by the European Commission within the Framework Programme 7 Capacities Specific Programme, Grant Agreement 284404.
M. Sugano, T. Nakamoto, S. Enomoto, H. Kawamata, Q. Xu,
N. Higashi, N. Okada, R. Okada, Y. Ikemoto,
M. Iio, T. Ogitsu, K. Sasaki, N. Kimura, M. Yoshida, A. Yamamoto,
E. Todesco
4th Joint HiLumi LHC-LARP Annual Meeting
17-21 November 2014, KEK, Tsukuba

## Slide 2
Contents
My talk
Design parameters
Magnet design
Mechanical analysis
Magnetic design
Quench protection study
3. Report on 2-m test coil fabrication
Next talk by Dr. Nakamoto
Plans
Procurement
Insulation
Quench protection heaters
Collars, yokes
Test facilities

## Slide 3
Lay out around interaction points, ATLAS and CMS
HL-LHC
Nominal LHC
NC D1
IT Quads. w/ Nb3Sn
SC D1
HL-LHC
Nominal LHC
IT Quads.& D1
Long Straight Section
Crab Cavity
D2
Q4
Corrector
Package
Q1
Q2a
Q2b
Q3
Aperture increase in IT Quads:70mm150mm Large bore also for the new D1
Replacement of current NC D1 by SC D1: Shortening magnet length by 15m
Making room for new crab cavities

## Slide 4
19
13
8
4
Stress management
High saturation, stray field
Radiation resistance, cooling capability
44 turns
Coil ID: 150 mm
Integrated field:35 T m (26 Tm at present LHC)
  5.58 T at 12 kA. Lcoil=6.3 m
Top: 1.9 K by HeII cooling
Load line ratio (SS): 75 %
Coil layout: 1 layer of 15.1 mm cable
  Better cooling. Saving space for iron yoke.
Conductor: Nb-Ti LHC MB outer cable
Structure: Collared yoke structure by keying
  RHIC dipole, LHC MQXA, J-PARC SCFM
  Enhancing iron material for stray field issue
Field quality: < 10-4 at Rref = 50 mm
Cold mass OD: 550 +10 x 2 = 570 mm
Cryostat OD: 914 mm, same as MB cryostat
Radiation, energy deposition:
Latest design parameters of D1
135 W in total, 2 mW/cm3 at local peak, Radiation dose >25 MGy

## Slide 5
Comparison btw production mag. and 2-m model
Design parameters | Production | 2-m model
Field integral | 35 T•m | 10.3 T•m
Magnetic length | 6.27 m | 1.85 m
Coil mechanical length | 6.46 m | 2.00 m
Magnet mechanical length | 6.96 m | 2.50 m
Cold mass weight | 12 tons | 3.8 tons
Cable unit length per coil | 568 m | 175 m

## Slide 6
Magnet design of new D1

## Slide 7
Mechanical analysis
Mechanical analysis during the assembly process, cooling and excitation using ANSYS has been completed
Highest stress arisen at key slots in the yoke < 220 MPa
 The assembly scheme would be feasible
UX = 0
UY = 0
Collar
Coil
Yoke
0.5 unit
thickness
Remove load from the yoke shoulder and insert the load-key; The gap between top and bottom yokes keep closed at both ends.
Stress in the yoke
Key insertion

## Slide 8
Coil stress
UX = 0
UY = 0
Collar
Coil
Yoke
Pole
Mid-plane
Coil stress during yoking: 100 MPa
Excitation

## Slide 9
Magnetic design by ROXIE
Impact of possible design changes
Diameter and position of HX holes (-5.1 units)
Shape of cryostat (Elliptical cryostat option)
(-2 units)
Systematic errors
Packing factor of iron yoke (-1.2 units)
Relative permeability of stainless steel collar (-0.6 units)
Mispositioning of coil blocks during yoking
(-1 unit)
Random geometric error
Consideration on possible error sources
ID890 mm x 1112 mm,
t=12 mm, elliptical
Thanks to Susana Izquierdo Bermudez
for her technical support in ROXIE
(Change of b3 by each factor)
A
B
C
D
55mm
12mm
33mm
32mm
33mm
9mm
5mm
54mm
20mm
Yoke
Collar

## Slide 10
Impact of possible design changes on field quality
Diameter and position of HX holes(f50~70 in diameter)
f50  f60 : Db3=+2.0 units
R185  R195 with keeping f50 : Db3=-5.1 units
These errors can be corrected by small re-arrangement of the coil blocks
 NO significant design changes in wedges, collars, and the number of blocks
and cables are needed
f50
f60
f70
Const.
R185
R190
R195
Now the diameter and position of the HX holes have been fixed to
f60 at R190

## Slide 11
Packing factors (PFs) of iron yoke
Assembly of yoke stacks
Main body (PF=0.98)
Slot region:
3.4% lower packing factor
than main body
Spacer yoke（t=6）
Fixing yoke（t=5.6）
PF=0.98 for whole parts 
PF=0.98 for main body, 0.95 for slot region: Db3=-1.2 units
Systematic error

## Slide 12
Random geometric error
r direction
f(position angle)
direction
a(inclination angle)
direction
f
a
r
Coil block displacement in 3 degrees of freedom was considered
Df
Da
Dr
Bellesia et al,
Proc. EPAC 2006, 2601
w
Displacement, d (mm) | Stand. dev. of b3 (unit)
100 | 2.067
50 | 1.033
25 | 0.516
10 | 0.206
Given d
 A thousand sets of (Dr, Df, Da) are given
by Monte-Carlo method
 Calculation of standard deviation of bi and ai
d : assumed displacement, r : coil aperture, w : cable width
1 unit

## Slide 13
Coil block re-optimization with full iron model
Main body of
iron yoke (PF=0.98)
Slot region (PF=0.95)
Keys(PF=0.96)
Stack tubes
(PF=1)
SUS collar
(mr=1)
Circular cryostat
Coil blocks
Main field (T) | 5.573
b3 (unit) | -0.059
b5 (unit) | -0.097
b7 (unit) | -0.111
b9 (unit) | 0.284
b11 (unit) | 0.360
HX hole
(f60, R190)
Coil block re-optimization in 2-D model
has been completed

## Slide 14
Variation of multipole coefficients
Nominal current
Nominal
current
b3
b3
b5 ~ b13

## Slide 15
Transfer function
Nominal current
Transfer function starts to decrease at 6 kA and the value at the nominal
current is lower by 10% than one at low field

## Slide 16
Coil end design
Old version
Coil end found in practice
winding
(2-m test coil)
Modified design
End spacer
made using a 3-D
printer
Due to insufficient length between straight section to end,
cables at the coil end tend to be inclined
to relieve strain energy
 Difference in height between end spacer and cables
Coil end will be modified to have longer length
Length of each coil block is being optimized to minimize multipole coefficients

## Slide 17
Quench protection study with Rdump=75 mW
Rdump=75 mW: Already implemented for the MB circuit in the LHC
Quench detection threshold: 0.1 V, 10 msec
Cable resistance was neglected in calculation of detection time & time constant of
current decay, t  A conservative scenario
Quench starts around lead out (B ~ 0 T)  Worst case
Peak temperature at Bpeak
(at Imax=13kA) = 305 K
Further study will be made with 3D field map soon.
QPH would not be necessary in the production magnet, but it will be decided after quench test using 2-m model magnet.
Calculation condition

## Slide 18
Fabrication of a test coil
for the 2-m model

## Slide 19
Purposes of test coil fabrication 1
To verify the following items
Toolings for winding (Mandrel, Forming block, …)
Operation test for winding machine, hydraulic press, heater,…
Design of end spacers, winding and measurement of coil end
Confirmation of curing cycle (temperature profile and homogeneity, pressure)
Practice for quality assurance
electrical tests of coil (ground fault, cable resistance, turn-turn insulation,…)
Once test coil fabrication is completed, it will be used for
Commissioning of coil size measurement
Practice for attaching voltage leads
200mm-long mechanical model

## Slide 20
Purposes of test coil fabrication 2
- Radiation resistant GFRP end spacers and wedges
End spacers and wedges made of
BT resin + S2 glass fibre were used for
the first time
Can newly developed hard GFRP
end spacers be accommodated to
the cable by curing ?
- Curing with radiation resistant cyanate ester adhesive
Curing temperature around 200oC is needed, while it should not influence
on contact resistance between the strands
(lower than melting point of Ag-Sn coating)
To consider compromised heat treatment condition
and check if bonding strength is strong enough even for a single layer coil
End spacers were machined in house

## Slide 21
Coil structure
Cable: NbTi MB cable with APICAL and PIXEO insulation supplied by CERN
Coil configuration:
- Single layer coil
- 44 turns, 4 coil blocks
- Coil length: 2020 mm (between the end saddles)
- 2D cross-section optimized for HX-hole of 50 mm (old version)
Wedge(GFRP)
MP shim(GFRP)
Pole shim (GFRP)
Ramp box
Center post
Mandrel
Pushing bar

## Slide 22
Coil end
Lead end
Return end
Practice winding
The cable angle was inclined too much and
large gap between the cable and end spacer remained
End spacer was re-designed to accommodate to the inclined cable
(but further modification for the 2m-model coils
should be needed)
Inner 2 blocks were subdivided to reduce peak field

## Slide 23
Layer jump
2D cross-sections of the layer jump
Coil layer at the straight section
Collar layer at the lead end
Pole turn
Ramp box was designed in such a
way that the layer jump turn go out uprightly
Ramp box
A
B
C
A
B
C

## Slide 24
Tensioner
Feeder
Turn table
Winding mandrel
Coil winding
Winding machine
Measurement of cable positions and
angles
Winding tension: Started from 40.9 kgf,
decreased by 0.25 kgf/turn

## Slide 25
Fitting of end spacer to cable
Gap between the end saddle and the cable remained
 We checked if the gap can be closed after curing

## Slide 26
Preparation for curing
SUS liner + Midplane shim
SUS protective liner
Pushing bars
Alignment pin

## Slide 27
Transfer of coil into forming block
Insertion tooling
Pushing the coil
into the groove
by screwing the bolts
Forming block
The coil was successfully inserted to the
forming block using the alignment pin
and jigs

## Slide 28
How much should coil be compressed in curing ?
Final size of coil is determined by yoking
Pressure applied to coil
Curing: 50 MPa
Yoking: 100 MPa (max)  80 MPa
From the results of 10 stack measurement (22 cables),
coil after curing should be larger by 0.9 mm
than the final size
Forming block
Mandrel
Pushing bar
Curing pressure
0.9mm-thick shim
0.9 mm-thick shims were inserted
and coil was compressed until the gap
was closed
Gap

## Slide 29
Curing press
Thickness gauge
Vertical load was applied incrementally
until the gap was closed
Longitudinal load
(5.2 tonf)
90 ton hydraulic rams x3x7 over the length of 2m-coil
Hydraulic ram

## Slide 30
Determination of curing pressure
1
2
3
4
5
6
Mandrel
Forming
block
Gap was closed at hydraulic pressure of 23 MPa
Pressure in curing
Pressure pattern
by pushing bars
Check by Fuji paper
Gap
Coil pressure:
50 MPa

## Slide 31
Configuration of heater and thermometers
Heaters in forming block
Heaters in mandrel
Mandrel
Form-block
Heater
Thermocouples
(Both sides)
1m-long cartridge heater
4 in forming block
2 in winding mandrel
Thermocouples
10 in forming block
5 in winding mandrel
2 at cartridge heater for mandrel
Used for heater control

## Slide 32
Actual temperature trend in curing
Max. temperature could be controlled at 190 - 210oC (< 220oC)
150oC
180oC
190oC
Expected temperature profile was realized
F-E
M
F-W
NN
N
M
S
SS
Temperature profile to harden cyanate ester (150oC x 4h + 180oC x 8h) was obtained
as expected
Bonding of polyimide insulation
Hardening of cyanate ester

## Slide 33
Coil after curing
The gap between the end saddle and
the cable was closed after curing
Hard BT resin + S2 glass GFRP can
be accommodated to the cable
Bonding between the cable and
the wedges is sufficiently strong
Effectiveness of heat treatment
profile is verified

## Slide 34
Electrical tests after curing
No ground fault throughout winding and curing
No change of cable resistance (for 44 turn)
No damage of cable insulation checked
by a bundle of fine Nb-Ti filaments
No turn-turn insulation failure at least
up to 1 kV (Surge test)
Coil inductance: 2.26 mH
(calc. value = 2.28 mH)
Electrical soundness of the coil
was confirmed
After winding | 242.9 mW
Under curing pressure, before curing | 242.5 mW
After curing | 242.2 mW
Surge test

## Slide 35
Issues to be modified 1
The protective liner deformed plastically after curing
Additional support is needed for the layer jump
to make the width of the groove narrower
Slit for the layer jump
Protective liner
Groove for the layer jump
Protective liner
Bottom surface of the
ramp box
Ramp box is slightly
popping up
Forming block

## Slide 36
Issues to be modified 2
There is difference in height at the boundary of the end spacer and the cable
To make the cable more upright by elongating the length of coil end
The leads for the QPH could be damaged
Approach 1: Modification of coil end shape
Approach 2: Filling the gap with shoe

## Slide 37
Preparation for coil size measurement
Pushing bars with strain gauges
50 ton hydraulic press
Coil pressure up to 90 MPa
Continuous measurement using the 5.4 m-long bench
Two pushing bars each having 5 x 20mm-wide fingers
4 x linear gauges to measure coil deformation
Same system as CERN (Thanks to G. Kirby)
R5
R4
R3
R2
R1
L5
L4
L3
L2
L1
Maximum pressure to compress the coil to the final size was measured

## Slide 38
Preliminary
Coil size measurement
Measured maximum pressure: 80 – 92 MPa
(After correction considering machine
deformation: 90 – 100 MPa)
The size of our test coil is almost
as designed
Coil pressure – deformation
Results for adjacent 5 sections
Final size
Oversize
Coil stress at the final size along the coil length
Dot: Results for each 20 mm
Line: Average for every100 mm
R
L
R5
R4
R3
R2
R1
1-m Straight section

## Slide 39
Summary
Iron model for ROXIE 2-D calculation was refined to include possible error sources.
Arrangement of 2-D coil blocks has been optimized for HX holes with a diameter of
f60mm at R190.
Quench protection studies were started. Peak temperature was estimated to be 305 K in a conservative scenario using Rdump=75 mW with quench detection threshold of 0.1 V and 10 msec.
Fabrication of 2-m test coil was completed successfully. We confirmed that new radiation resistant GFRP can fit the cable after curing and tested curing temperature profile can work to obtain sufficient bonding strength for the single layer coil.
Coil size measurement was started. The coil size of the test coil was suggested to be almost as designed.
200-mm mechanical short model will be assembled using the straight section of the test coil to verify collaring and yoking process.