## Slide 1: SixTrackLib
Kartikeya Singh (student)
Riccardo De Maria (mentor)

## Slide 2: SixTrack - Introduction
-SixTrack is a single particle six-dimensional symplectic tracking code used for beam dynamics in circular accelerators, like the Large Hadron Collider.
Why a particle tracking code: -
- To analyze beam properties and the long-term stability of a particle in accelerators.
- The orbit stability data is used to count how many particles are lost into the vaccum pipe walls—if this happened too often in actual running, this would cause damage to the accelerator which would need repairs.
The Six Dimensions of particle coordinates: -
- Refers to the six degrees of freedom of a tracked particle.
- The horizontal and vertical motion - four degrees of freedom.
- The longitudinal coordinates related to the energy and position along the accelerator with respect a reference particle trajectory - the other two degrees of freedom.

## Slide 3: What SixTrack actually does
- It contains maps for every beam line element type which modify coordinates of moving charged particles from the entrance to the exit of the element.
- In one work unit, 60 particles are simulated travelling 100,000 or 1,000,000 loops.
- Initial and final coordinates of particles for each turn are saved in the output and post processed.
Input to SixTrack :-
- Description of every element.
- Location of elements in accelerator.
Output :-
- Starting time and date of the simulation.
- Description of accelerator settings.
- A list of the initial coordinates of all the particles.
- Turn-by-turn print of all the coordinates of the particles.

## Slide 4: SixTrackLib
This project is about creating a standalone particle tracking library written in C and refactoring the existing module using newly created library.
Main purpose of the new API :-
- The API and the module would open the way to GPU calculations.
- New runs will rely only on the newly written library to perform tracking simulations.
- Increased readability, so new developers can easily understand the code.
New code will contain :-
- C Functions which represent the maps how a particle will change its coordinates when passing through the respective element.
- These functions take particle’s initial coordinates and element’s properties as arguments and modify the particle coordinates accordingly.
Software technologies used -:
- Languages :- C, Fortran, Python
- Operating System :- Linux

## Slide 5: API code example for horizontal dipole :-
extern int thin6d_map_horizontal_dipole_(double *coord, double *argf, double *argi)
{
double xp = coord[2],yp = coord[3]; // xp is yv(1,j) yp is yv(2,j)
double LengthElementTiltCos = argf[0], LengthElementTiltSin = argf[1]; // first one is strackc(i) and second one is stracks(i)
double RatioPtoPj = coord[4]; // it's oidpsv(j)
coord[2] = xp + LengthElementTiltCos * RatioPtoPj;
coord[3] = yp + LengthElementTiltSin * RatioPtoPj;
return 1;
}

## Slide 6: Refactoring example of fortran code :-
50 argf(1)=strackc(i)
argf(2)=stracks(i)
do 60 j=1,napx
coord(3)=yv(1,j)
coord(4)=yv(2,j)
coord(5)=oidpsv(j)
call thin6d_map_horizontal_dipole(coord,argf,argi)
yv(1,j)=coord(3)
yv(2,j)=coord(4)
60 continue

## Slide 7: Description of example code :-
Description of C code :-
It takes three arrays as parameters coord, argf, argi
- coord contains particle coordinates
- argf contains element property floating values
- argi will contain integer properties if needed and other structural information
- According to the element properties, the code modifies the particle’s initial coordinates, and then fills coord array with updated values.
Description of fortran code :-
- First argf array is filled with element properties
- In every turn :-
1) First the coord array is filled with particle coordinates
2) Then new C functions is called which modifies coord array accordingly
3) Finally the particle coordinates are updated from modified coord array.

## Slide 8: Next Steps
- Complete few missing maps from thin6d
- Testing all the maps
- documentation of work done so far
- writing maps in CUDA kernels
- documentation of work done so far
- Add code to replace particle and elements loops
- Testing all the maps for all routines
- documentation of work done so far

## Slide 9: References
- Sixtrack web site: http://cern.ch/sixtrack
- SixTrack developer manual https://twiki.cern.ch/twiki/bin/view/LHCAtHome/SixTrack
- Work done so far :-
https://github.com/SixTrack/SixTrackLib/tree/master/kartikeya/sixtrack_lib