## Slide 1
Future Circular Collider (FCC) Study Status
http://cern.ch/fcc
Michael Benedikt

## Slide 2
Motivation & scope
Parameters & design challenges
Study organization, study time line
Summary
Outline

## Slide 3
with emphasis on proton-proton and electron-positron high-energy frontier machines.
These design studies should be coupled to a vigorous accelerator R&D programme, including high-field magnets and high-gradient accelerating structures,
in collaboration with national institutes, laboratories and universities worldwide.
http://cds.cern.ch/record/1567258/files/esc-e-106.pdf
….“to propose an ambitious post-LHC accelerator project at CERN by the time of the next Strategy update”:
d) CERN should undertake design studies for accelerator projects in a global context,
Summary: European Strategy Update 2013
Design studies and R&D at the energy frontier

## Slide 4
Future Circular Collider Study - SCOPE
CDR and cost review for the next ESU (2018)
Forming an international collaboration to study:
pp-collider (FCC-hh)  defining infrastructure requirements
e+e- collider (FCC-ee) as potential intermediate step
p-e (FCC-he) option
80-100 km infrastructure in Geneva area
~16 T  100 TeV pp in 100 km
~20 T  100 TeV pp in 80 km

## Slide 5
Conceptual design report by end 2018
  Parameter optimisation and baseline development
  Conceptual design of machines, experiments and infrastructure
  Launch R&D in SC magnet and SRF areas
  Identification of technical challenges and R&D needs and R&D planning
  Cost model and estimation, project schedule estimation
  Preparation and planning for a technical design phase (TDR phase)
  Preparation of global FCC collaboration
Goals CDR phase 2014-2018

## Slide 6
Hadron collider FCC-hh parameters
Energy 100 TeV c.m.
Circumference ~ 100 km (base line) [80 km option]
Dipole field (top energy) ~ 16 T (base line) [20 T option]
Dipole field (injection) ~ 1 T (base line) [1.2 T option]
Bunch spacing 25 ns [5 ns option]
Bunch population (25 ns) 1x1011 p
#bunches 10500
Stored beam energy 8.2 GJ/beam
Luminosity 5x1034 cm-2s-1
b* 1.1 m [2 m conservative option]
#IPs 2 main (tune shift) + 2
Synchroton radiation arc 26 W/m/aperture (filling fact. 78% in arc)
Longit. emit damping time 0.5 h

## Slide 7
FCC-hh: high-field magnet targets
FHC baseline is 16T Nb3Sn technology for ~100 TeV c.m. in ~100 km
Develop Nb3Sn-based 16 T dipole technology (at 4.2 K?),
with sufficient aperture (40 – 50 mm) and
accelerator features (margin, field quality, protect-ability, cycled operation).
conductor developments
Goal: 16T short dipole models by 2018/19 (America, Asia, Europe)
Goal: Demonstrate HTS/LTS 20 T dipole technology in two steps:
a field record attempt to break the 20 T barrier (no aperture), and
a 5 T insert, with sufficient aperture (40 mm) and accelerator features
In parallel HTS development targeting 20 T.
HTS insert, generating o(5 T) additional field (EuCARD2), in an outsert of large aperture o(100 mm) (FRESCA2 or other)

## Slide 8
Energy in beam & magnets, dump, collimation, quench protection
  Stored beam energy and losses critical: 8 GJ/beam (0.4 GJ LHC)
  Collimation, losses, radiation effects are very important
  Magnet and machine protection to be considered from early phase
High synchrotron radiation load on beam pipe (inside cold-mass)
  Up to 26 W/m/aperture in arcs, total of ~5 MW for the collider
  (LHC has a total of 1W/m/aperture from different sources)
  LHC-type beam screen
    Cooling efficiency depends on screen temperature, higher temperature  larger impedance  40-60 K?
  Open midplane magnets
    Synergies with muon collider developments
  Photon stops
    dedicated warm photon stops for efficient cooling between dipoles, as developed by FNAL for VLHC
FCC-hh: some other design challenges
http://inspirehep.net/record/628096/files/fermilab-conf-03-244.pdf
Also P. Bauer et al., "Report on the First Cryogenic Photon Stop Experiment," FNAL TD-03-021, May 2003

## Slide 9
Ph. Lebrun
contributions: beam screen (BS) &
cold bore (BS heat radiation)
total cryo power for cooling of SR heat
D Schulte
Optimum BS temperature range: 50-100 K ;
40-60 K favoured by impedance & vacuum considerations

## Slide 10
Lepton collider FCC-ee parameters
Design choice: max. synchrotron radiation power set to 50 MW/beam
  Defines the max. beam current at each energy.
  4 Physics working points
  Optimization at each energy (bunch number & current, emittance, etc).
For TLEP-H and TLEP-t the beam lifetime of ~few minutes is dominated by Beamstrahlung (momentum acceptance of 2%).
Parameter | TLEP-Z | TLEP-WW | TLEP-H | TLEP-ttbar | LEP2
E/beam (GeV) | 45 | 80 | 120 | 175 | 104
I (mA) | 1450 | 152 | 30 | 6.6 | 3
Bunches/beam | 16700 | 4490 | 170 | 160 | 4
Bunch popul. [1011] | 1.8 | 0.7 | 3.7 | 0.86 | 4.2
L (1034 cm-2s-1) | 28.0 | 12.0 | 4.5 | 1.2 | 0.012

## Slide 11
FCC-ee: RF parameters and R&D
Synchrotron radiation power: 50 MW per beam
Energy loss per turn: up to 7.5 GeV (at 175 GeV, t)
System dimension compared to LHC:
  LHC 400 MHz  2 MV and ~250 kW per cavity, (8 cavities per beam)
  FCC-ee: ~600 cavities 20 MV / 180 kW RF  12 GV / 100 MW
R&D Goal is optimization of overall system efficiency and cost!
  Power source efficiency, low loss high gradient SC cavities, operation temperature vs. cryogenic load, total system cost and dimension.
  1. SC cavity R&D  large , high gradient, acceptable cryo power!
  Recent promising results at 4 K with Nb3Sn coating on Nb at Cornell,
  heat treatment JLAB, beneficial effect of impurities FNAL.
2. High efficiency RF power generation from grid to beam
  Amplifier technologies
  Klystron efficiencies >65%, alternative RF sources: Solid State Amplifier, etc.
3. High reliability

## Slide 12
Other SC magnet R&D for FCC
Nb3Sn quadrupoles for regular arc hadron collider
IR magnets and special magnets in collimation regions
  in high radiation zones, larger aperture
  HTS
Transmission line magnet (injectors, TLs)
  SC cable in warm iron yoke (SF magnet), double aperture magnets
Pulsed SC magnets (injectors, TLs)
  SC cable in warm iron
SC septum magnets for beam dumping (injection?)
  Beam losses, quench per design?
Current leads
  Overall optimization of powering and energy distribution system

## Slide 13
Global collaboration based on general MoU between CERN and individual partners.
Addenda for each participant describing specific contributions and conditions.
Presently discussions with potential collaborators to conclude MoUs and establish collaboration.
First international collaboration board meeting on 9. and 10. September 2014 at CERN.
FCC study status

## Slide 14
EU H2020 FCC Design Study proposal
HH Interaction region design
HH Arc design
HH Cryo-magnet-vacuum-beam pipe
HH high-field magnet design
Collider functional
machine design
Key technological
aspects
Management, Coordination and Implementation
Coordination, CDR,
Strategy, Cost
Focused on hadron collider design (main emphasis of study)

## Slide 15
FCC work plan study phase
2014 |  |  |  | 2015 |  |  |  | 2016 |  |  |  | 2017 |  |  |  | 2018 |  |  | 
Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4
Kick-off, collaboration forming,
study plan and organisation
Release CDR & Workshop on next steps
Workshop & Review
 contents of CDR
Workshop & Review identification of baseline
Ph 2: Conceptual study of baseline “strong interact.”
Workshop & Review, cost model, LHC results  study re-scoping?
Ph 3: Study
consolidation
Report
Prepare
4 large FCC Workshops distributed over participating regions
Ph 1: Explore options
“weak interaction”
Explore options, now – spring 2015:
Investigate different options in all technical areas, taking a broad view
Deliverables: description and comparison of options with relative merits/cost, Develop schedules, understand relative impact of options on overall schedule (physics operation time, machine installation time, etc.)
FCC workshop to converge to common baseline with small number of options
Proposed WS date 23 – 27 March 2015 (presently no known collisions…)
Followed by review ~2 months later, begin June 2015

## Slide 16
today
Project
Kick-off meeting: 11th Nov. 2013 (Daresbury)
CDR and Cost Review 2018
FCC study milestones
ESU
Kick-off meeting
12th-14th February 2014
CDR and Cost Review for 2018
Study
FCC

## Slide 17
There are strongly rising activities in energy-frontier circular colliders worldwide. CERN is setting-up an international study for the design of Future Circular Colliders (FCC).
Worldwide collaboration in physics, experiments and accelerators will be essential to advance and reach the goal of a CDR by 2018.
FCC presents challenging R&D requirements for SC magnets in many different areas:
  Main focus is the 16 T Nb3Sn program as hadron collider baseline, representing a natural continuation of HL-LHC developments
  HTS for special magnets and as option to the 16T program
  SF and pulsed SC magnets as potential options for injectors, TLs.
  SC septum magnets
  HTS current leads for power distribution systems.
Need your collaboration and use all synergies to move forward!
Conclusions

## Slide 18
Work/meeting structures established based on INDICO, see:
FCC Study: https://indico.cern.ch/category/5153/
FCC-hh Hadron Collider VIDYO meetings
  https://indico.cern.ch/category/5263/
  Contacts: daniel.schulte@cern.ch
FCC-hadron injector meetings
  https://indico.cern.ch/category/5262/
  Contacts: brennan.goddard@cern.ch
FCC-ee (TLEP) Lepton Collider VIDYO meetings
  https://indico.cern.ch/category/5264/
  Contacts: jorg.wenninger@cern.ch,
Work and organisation status (i)

## Slide 19
FCC infrastructure meetings
  https://indico.cern.ch/category/5253/
  Contacts: philippe.lebrun@cern.ch, peter.sollander@cern.ch
FCC-hh Hadron Collider Physics and Experiments VIDYO meetings
  https://indico.cern.ch/category/5258/
  Contacts: michelangelo.mangano@cern.ch, fabiola.gianotti@cern.ch, austin.ball@cern.ch
FCC-ee Lepton Collider (TLEP) Physics and Experiments VIDYO meetings
  https://indico.cern.ch/category/5259/
  Contacts: alain.blondel@cern.ch, patrick.janot@cern.ch
Work and organisation status (ii)