## Slide 1: The FCC Magnet Program seen from CERN
Luca.Bottura@cern.ch
Meeting at ASC-2014, Charlotte, August 13t, 2014

## Slide 2: Quick summary
The FCC-hh magnet program builds upon the HL-LHC magnet R&D and construction
We see three legs to the magnet R&D in support to the FCC-hh design study
We have to achieve a good cog-wheeling of many running, planned and collaborating programs into a coherent R&D

## Slide 3: HL-LHC (main) magnets
 | Type | Material | Field/Gradient (T)/(T/m) | Aperture (mm) | Length (m) | Units (-)
Q1,Q3 Q2 | Single aperture | Nb3Sn | (12.1) 140 | 150 | 8 6.7 | 40
D1 | Single aperture | Nb-Ti | 5.2 | 150 | 6.7 | 6
D2 | Twin aperture | Nb-Ti | 3.5…5.0 | 95…105 | 7…10 | 6
Q4 | Twin aperture | Nb-Ti | (5.9) 120 | 90 | 4.2 | 6
DS 11T | Twin aperture | Nb3Sn | 10.8 | 60 | 11 | 40
NOTE: Correctors not included

## Slide 4: A possible timeline (for an FCC @ CERN)
1980
1990
2000
2010
2020
2030
2040
construction
physics
upgrade
LEP
construction
physics
LHC
Design R &D
prototyping
construction
HL-LHC
Design R&D
prototyping
physics
CDR
Design R&D
prototyping
construction
physics
FCC

## Slide 5: FCC magnets – LTS option
 |  | B / G (T) / (T/m) | Bpeak (T) | dB/dt (mT/s) | Bore (mm) | Length (units x m)
FCC | MB | 16 | 16.8 | 16 | 40 | 4578 x 14.3
 | MQ | 375 | 10 | 10 | 40 | 762 x 6.6
 | QX | 200 | 12.5 | 12.5 | 90 | Optics ?
 | D1 | 12 | 13 | 13 | 60 | 4x2 x 12
 | D2 | 10 | 10.5 | 10.5 | 60 | 4x3 x 10
Booster in the FCC | MB | 1.1 | 2 | 2 | 50 | 4578 x 14.3
injector in the LHC | MB | 5 | 5.25 | 20 | 50 | 1232 x 14.3
injector in the SPS | MB | 12 | 12.5 | 100 | 50 | 892 x 4.7

## Slide 6: FCC magnets – HTS option
 |  | B / G (T) / (T/m) | Bpeak (T) | dB/dt (mT/s) | Bore (mm) | Length (units x m)
FCC | MB | 20 | 21 | 16 | 40 | 3662 x 14.3
 | MQ | 375 | 10 | 10 | 40 | 610 x 6.6
 | QX | 200 | 12.5 | 12.5 | 90 | Optics ?
 | D1 | 12 | 13 | 13 | 60 | 4x2 x 12
 | D2 | 10 | 10.5 | 10.5 | 60 | 4x3 x 10
Booster in the FCC | MB | 1.5 | 2.2 | 2.2 | 50 | 3662 x 14.3
injector in the LHC | MB | 5 | 5.25 | 20 | 50 | 1232 x 14.3
injector in the SPS | MB | 12 | 12.5 | 100 | 50 | 892 x 4.7

## Slide 7: Three directions for R&D
16 T dipole for the FCC-hh main arc
  Challenges: field level with a 40…50 mm bore, field quality, protection, cost
  Proposal: develop A15-based 16 T dipole technology, with sufficient aperture and accelerator features. Build short model(s) as a worldwide effort
20 T dipole for the FCC-hh main arc and special regions
  Challenges: feasibility, field level, protection, field quality
  Proposal: demonstrate HTS/LTS 20 T dipole technology in two steps:
    a field record attempt at breaking the 20 T barrier (no aperture)
    a 5 T insert, with sufficient aperture (40 mm) and accelerator features
1 T … 2 T injectors and booster magnets
  Challenges: power consumption, compatibility with other collider options (e.g. FCC-ee)
  Proposal: demonstrate low consumption, compact (HTS based ?) dipole technology
High awareness of potential and impact in other domains of magnet technology and applied superconductivity

## Slide 8: FCC Magnet Design and R&D
HH SC magnets
LTS magnets
Arc dipole designs
Arc quadrupole designs
IR magnets design
A15 material R&D (Nb3Sn, Nb3Al)
16 T dipole model(s) construction and test
H2020
Conceptual and engineering design of 16 T dipole
HTS magnets
Arc dipole designs as hybrid LTS/HTS
IR and collimation region magnet designs
HTS material R&D
20 T (no bore) insert R&D and test
5 T (40 mm) standalone and insert R&D and test
Injectors and booster
Compact, low consumption resistive magnets
Redundancy/fast connectivity, radiation hardness
Fast cycled 5 T magnets (LHC tunnel)
Fast cycled 12 T magnets (SPS tunnel)
Fast cycled 1.5 T magnets for an FCC-hh booster
EuCARD
6 T insert
EuCARD2
5 T dipole
H2020-FET ?
2 T HTS FCM with high energy efficiency

## Slide 9: H2020 proposal
EuroCirCol proposal (September 2014): “The objective of [the] proposal is to develop the conceptual design of a future high-energy frontier hadron collider infrastructure as an international, collaborative effort, to assess the feasibility of the accelerator key elements and to draft an implementation scenario”
≈15 beneficiaries, 5 work-packages
  WP1 management and coordination
  WP2 Interaction region design
  WP3 Arc lattice design
  WP4 cryogenic beam vacuum system concept
  WP5 High-field accelerator magnet design
“Horizon 2020 is the biggest EU Research and Innovation programme ever with nearly €80 billion of funding available over 7 years (2014 to 2020)”
Not to be confused with the Euro-Circus

## Slide 10: H2020 EuroCirCol WP5
Explore design options for an accelerator dipole magnet in the range of 16 Tesla, and produce the engineering design of the selected baseline configuration
7 partners (CERN,CEA, CIEMAT, INFN, TUT, UG, UT) and discussions with associated partners (US, J)
7 tasks:
  5.7: Management of Work Package
  5.1: Study accelerator dipole magnet design options
  5.2: Develop a cost model based on dipole magnets
  5.3: Develop electromagnetic design
  5.4: Develop mechanical engineering design
  5.5: Devise quench protection concept
  5.6: Produce manufacturing folder for a 16 T dipole short model