## Slide 1
Notes: Timing: XXX mins

## Slide 2
Why SCADA Security is NOT like Computer Centre Security
Finding vuln’s is easy ─ finding solutions is the challenge!

## Slide 3: Overview

## Slide 4: Control System in a Nutshell
Process Control System (PCS)
Safety System

## Slide 5: (R)Evolution of Control Systems

## Slide 6: (R)Evolution of Control Systems

## Slide 7: Typical Control Systems & Devices

## Slide 8: Critical (Cyber-)Infrastructures
COBB County Electric, Georgia
Middle European Raw Oil, Czech Republic
Athens Water Supply & Sewage
CERN Control Centre

## Slide 9: Overview

## Slide 10: Enter reality

## Slide 11: Natanz, we have a problem…

## Slide 12: The Workings of Stuxnet (I)
PC-Level:
Infiltration of infected USB stick into plant by malicious act or through social engineering.
Compromizing Windows PCs with 4(!) zero-day exploits (worth >$100k)
4-5 evolutions starting 6/2009
Infected 100.000 PCs (60% Iran,10% Indonesia)
Hiding using “rootkit” techno & two stolen certificates
Infecting other hosts and establishing connection “home”
So far, nothing new: A standard, but expensive virus!

## Slide 13: The Workings of Stuxnet (II)
PLC Level:
Checking local configuration for Siemens PCS7/STEP7/WINCC
If found, copying into local STEP7 project folder (to propagate further).
Replacing S7 communication DLLs used for exchanging data with PLC
Stuxnet is now the “Man in the Middle” controlling the communication between SCADA & PLC.

## Slide 14: The Workings of Stuxnet (III)
Process Level:
“Fingerprinting” connected PLCs
If right PLC configuration, downloading/replacing code (between 17 and 32 FBs & DBs)
GAME OVER: varying rotational speed of centrifuges wearing them out and inhibiting Uranium enrichment. “Man in the Middle” made SCADA displays look fine.

## Slide 15: Cyber: Old Game, New Tools

## Slide 16: Overview

## Slide 17: The Lack of Patching

## Slide 18: The Problem of Patching
Safety!
Needs heavy compliance testing (vendor & utility)
Potential loss of warranties & certification (e.g. SIL)
Availability
Rare maintenance windows
Legacy
Old or embedded devices
Integrity
S/W development live-cycles
Thorough regression testing
Nightly builds
Full configuration management
Availability
Redundancy & virtualization
Exceptions
“One-offs”; stand-alone systems

## Slide 19: The Problem of Patching
Safety!
Needs heavy compliance testing (vendor & utility)
Potential loss of warranties & certification (e.g. SIL)
Availability
Rare maintenance windows
Legacy
Old or embedded devices
Integrity
S/W development live-cycles
Thorough regression testing
Nightly builds
Full configuration management
Availability
Redundancy & virtualization
Exceptions
“One-offs”; stand-alone systems
Security at CERN has been delegated.
We (work hard to) enable & assist our people to fully assume that responsibility!
They decide when to install what and where.

## Slide 20: The Lack of Access Controls

## Slide 21: The Problem of Access Control
Safety!
Access always to be guaranteed
Shared accounts
Encryption too “heavy”
Legacy
Default passwords
Undocumented backdoors
Impossible IdM integration
No ACLs, iptables, etc.
Security
Split of AuthN & AuthZ
SSO, LDAP & AD
Kerberos, x509 & 2-factor AuthN
Laziness
We still deal with people
Password vs. Phishing
Complexity
WLCG: a network of computer centres

## Slide 22: The Problem of Access Control
Safety!
Access always to be guaranteed
Shared accounts
Encryption too “heavy”
Legacy
Default passwords
Undocumented backdoors
Impossible IdM integration
No ACLs, iptables, etc.
Security
Split of AuthN & AuthZ
SSO, LDAP & AD
Kerberos, x509 & 2-factor AuthN
Laziness
We still dealing with people
Password vs. Phishing
Complexity
WLCG: a network of computer centres
CERN strives to bring IT to the plant floor. CERN IT provides general services.
CERN CERT provides general protections.
CERN controls experts run the show.

## Slide 23: The Lack of Robustness

## Slide 24: The Problem of Robustness
Robustness
Use-cases and abuse-cases
Not always compliant to standards
No certification (yet?)
Security
Not integral part… …or through obscurity
Low priority, low knowledge
Unwillingness to share incidents
No laws; too many guidelines
Robustness
(Externally sponsored) penetration testing & vulnerability scanning
Security
Decades of experience & knowledge
CSIRT: Protection, detection & response
Responsible disclosure

## Slide 25: The Problem of Robustness
Robustness
Use-cases and abuse-cases
Not always compliant to standards
No certification (yet?)
Security
Not integral part… …or through obscurity
Low priority, low knowledge
Unwillingness to share incidents
No laws; too many guidelines
Robustness
(Externally sponsored) penetration testing & vulnerability scanning
Security
Decades of experience & knowledge
CSIRT: Protection, detection & response
Responsible disclosure
Asset inventories are key to CERN: Devices, websites, S/W, dependencies.
CERT pen tests everything(we can get hands on). (IPv6 is our next nightmare.)

## Slide 26: SmartMeters: Nothing learned!
Confidentiality:
Customer data available to others
Integrity:
Manipulation of reading data
Misuse of meter as an attack platform
Availability:
Data not available in a timely manner…

## Slide 27: Summary
P.S. Why do I have to do due diligence (and bear the costs) instead vendors shipping out insecure applications/devices?
PCS are (still) not designed to be secure. They fulfil use-cases and abuse cases.
Defence-in-Depth is the key. Make security part as functionality, usability, availability, maintainability, performance!
Hack the box!
Buy any PCS on ebay and throw your favourite pen suite at it. Push vendors & start responsible disclosure
Align Control System Cyber-Security with IT security! Patch procedures, access protection, robustness, certification & documentation need significant improvement.

## Slide 28: Literature