## Slide 1: The European XFEL Project – lasers for user experiments
Hamburg, November 12, 2014
Max Lederer, Laser Group European XFEL
max.lederer@xfel.eu
Notes: How to edit the title slide
Upper area: Title of your talk, max. 2 rows of the defined size (55 pt)
Lower area (subtitle): Conference/meeting/workshop, location, date, your name and affiliation, max. 4 rows of the defined size (32 pt)
Change the partner logos or add others in the last row.

## Slide 2: European XFEL mission
International multi-user facility for FEL research by a multi-disciplinary science community using ultrashort soft & hard X-ray FEL pulses.
  User proposed experiments: peer-review, invitation, support
  Basic science: establish the foundations for future high-tech applications
  Multidisciplinary: physics, chemistry, biology, materials sciences, geo-sciences, ...

## Slide 3: European XFEL as international project
Partner countries
  GmbH under German law
Total project cost
  Construction (2009-2017) 1.15 B€(2005)
  Operation (≥2017) ~100 M€/yr
    ~4800 hrs/yr x-ray FEL beam delivery
Partners & In-Kind contributions (~50%)
  About 30 different contributions
  Accelerator is biggest object
    DESY: coordinator of the Accelerator Consortium
  Responsibilities construction and operation:
    DESY  Accelerator & tech. Infrastructure;
    XFEL.EU  X-ray units & scientific user program

## Slide 4: X-ray Free-Electron Laser (XFEL)
Light generation in
the undulator:
SASE:
Self-Amplified Spontaneous Emission
Micro-bunching
≙ ca.100fs
lx-ray
≙ ca.100fs
e- - bunch
Synchrotrons vs. XFELs
  103-104×shorter light pulses
  106×higher flux density
  Full transverse coherence
Electron-
injector
Super-conducting
electron accelerator
Undulator
(periodic magnet arrangement)
X-ray FEL
beam
Micro-bunching
Electron beam
Electron
beam
Time
Intensity
Synchrotron
X-ray sources
X-ray
FELs
New scientific applications

## Slide 5: New science capabilities
Imaging and structure determination
  Use high coherence & flux
  Nano-scale objects
  Single molecules or cells
Ultrafast processes
  Use extremely short x-ray pulses
  Photo- & reaction chemistry
  Condensed-matter phase transitions
Non-linear processes and extreme states
  Higher order x-ray processes
  X-ray excitation of matter
High peak & average flux applications
Au nanocrystals
Clark et al.,
Science 341, 56 (2013)
Non-linear mixing
Glover et al.,
Nature 488, 603 (2012)
Insulator-metal-transition
De Jong et al.,
DOI: 10.1038/NMAT3718

## Slide 6: Facility overview
Schenefeld campus:
Experiment hall and main building
Osdorfer Born campus:
Kicker
DESY-Bahrenfeld campus:
Injector
Schenefeld campus: underground experiment hall with main building

## Slide 7: LINAC-Tunnel with infrastructure

## Slide 8: Bird’s eye view of Schenefeld campus, Juli 2014

## Slide 9
Experiment hall, June 2013
24 April 2013

## Slide 10: X-ray FEL delivery to 6 science instruments
Provision to add 2 more FEL sources and additional scientific instruments

## Slide 11
Lasers for European XFEL user experiments

## Slide 12: European XFEL experimental laser plans
SQS
SCS
SPB
FXE
HED
Types of experimental lasers:
PP (pump-probe):
  sub-15…100fs, 0.2mJ, 10Hz burst, 0…4.5MHz, 800nm
MAL (molecular alignment):
  sub-20fs, 3…10mJ, 10Hz burst, 800nm („kick“)
  or
  1J-class, 10Hz or burst, ns („adiabatic“)
TUNE (tuning, freq. conversion):
  UV…mid-IR, THz
TW (Terawatt):
  <30fs, >1Hz, 100 Terawatt–class laser, Ti:sapphire
SHOCK (high energy):
  100J … kJ-class ns-laser, exponential ramp
PW (Petawatt):
  30fs, 1Hz, Ti:sapphire
Baseline
HIBEF User Consortium
SASE 3
SASE 1
U2
U1
SASE 2
Experiment Hall
MID
PP
TW
TUNE
MAL
SHOCK
PW
PP
TUNE
MAL
PP
TUNE
PP-type
high rep-rate
HE/HI-type
PP
MAL
PP
TUNE
MAL
PP
TUNE
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 13: HE / HI – type lasers
Carsten Baehtz
  HiBEF contributions:
    HI-laser: 100 TW / 10 Hz laser system (industry, Ti:sapphire)
    HE (ramped compression): 100 J / 10 Hz laser system (RAL, DiPOLE 100-X)
    External laser building, chamber, spectrometers, diagnostics, etc.
Helmholtz international Beam-line for Extreme Fields (HiBEF)
  XFEL groups:
    Integration effort

## Slide 14: Pump-probe laser
European XFEL pulse timing
100 ms
t
10Hz electron bunch trains
(with up to 2700 bunches à 0.1…1 nC) => eff. rep-rate: 27kHz
100 ms
t = 220 ns
t
600 s
t
≈ 100 fs
t
100 fs
Photon pulses
FEL
process
4.5 MHz
Pump-probe laser development goals as set in 2010:
Synchronized few-cycle laser pulses with energy up to the few mJ-level
10 Hz bursts (600µs) with intra-burst rep. rate up to 4.5MHz
    What is the development strategy with highest likelihood for success?

## Slide 15: European XFEL pump-probe laser concept: NOPA
A. Dubietis, G. Jonusauskas, and A. Piskarskas, “Powerful femtosecond pulse generation by chirped and stretched pulse parametric amplification in BBO crystal,” Opt. Commun. 88, 437–440 (1992)
G. Cerullo and S. De Silvestri, “Ultrafast optical parametric amplifiers,” Rev. Sci. Instrum. 74, No. 1 (2003)
R. Riedel, A. Stephanides, M. J. Prandolini, B. Gronloh, B. Jungbluth, T. Mans, and F. Tavella “Power scaling of supercontinuum seeded megahertz-repetition rate optical parametric chirped pulse amplifiers,” Opt. Lett, 39, 1422-1424 (2014)
M.J. Lederer, M. Pergament, M. Kellert, and C. Mendez, “Pump–probe laser development for the European X-Ray Free-Electron Laser Facility,“ Paper 8504-20, SPIE Conference on Optics and Photonics 2012, 12–16 August 2012, San Diego, invited talk.
1030nm
Soliton
seeder
Dt =
0-5ns
burst-mode
all-fiber CPA
front-end
super-
continuum
var.
prechirp
AOM
PC
SHG
NOPA 1
NOPA 2
NOPA 3a
Compressor
SHG
SHG
SHG
NOPA 3b
sync via fiber
and OBC
x-ray - optical
laser overlap
sub-ps
1030nm, 4 … 100mJ, 4.5 … 0MHz
sub-ns
800nm, 0.2 … 3mJ,
4.5 ... 0MHz,
15 … 100 fs
Yb-booster 1
(burst-mode)
7 kW
Yb-pre-amp
(burst-mode)
400 W
Yb-booster 2
(burst-mode)
20 kW
4.5MHz
1MHz
200kHz
4W @
4.5, 1 or 0.2MHz
20W @
4.5MHz
Compressor
control
system
XF2
XF1
Dt
DQ
    Complex (sub-)systems with challenging requirements
    Scientific user facility: ideally combine high flexibility with high up-time
    System aspects: integrated control system, reliability
    No commercial off-the-shelf solutions, high risk, highly customized
    Project constraints (time line, resources, …)
    Multiple installations

## Slide 16: XFEL PP-laser development strategy
PP-Laser specification goals
Ti:Sapphire OPA
System level (in)
NOPA OPCPA
InnoSlab Cryo-Yag Thin-Disk
Yb-all-fiber Yb-Rod-type fiber Yb-Regen
TiSa Super-continuum
Yb-fs-oscillator TiSa
Pump-pulse power amplifier (ex/in)
Front-end amplifier (ex/in)
Seeder front-end amplifier (ex)
Seeder NOPA (in)
µ-TCA, Beckhoff, Karabo
Control hard and software (in)
AOM, PC
Pulse on demand (in/ex)
    Select technologies and define in- and ex-house efforts (2011)
    Choose SME for long-term and close OEM-type collaboration
        e. g. Laser Impulse GmbH / IDIL, OneFive, Amphos GmbH, Adamietz, Layertec, …
        Two-way know-how transfer
        Influence design solutions
        Participate in development
    Strictly project-focussed approach
        XFEL laser group: 10 Scientists and engineers
        Cover all aspects of project:
          laser development
          industry and intra-project interfacing
          lab-, facility- and operations-planning
          Installation, commissioning, operation, experiment facilitation

## Slide 17: Example: InnoSlab high power burst-mode amplifiers
    Goal: 20kW burst power, 10Hz (20Hz), 600µs, 0.1…4.5MHz
    SME: Amphos GmbH
Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4
Evaluation and debugging of 20kW booster chain at XFEL laser-lab
2011
2013
Feasibility
Prototype development
Follow-up development with XFEL involvment
2014
Production of 3 systems (5kW)
2017
2015
2012
Start of installation at SASE 1
2016
Production of 3 systems (20kW upgrade)
SASE 1
first x-ray
    Timeline: consistent with facility plans

## Slide 18
System installed
20kW (during burst) is reached
20kW
Measured slope of booster stages 1 and 2
Remaining issues: mainly beam quality => require follow-up development.
Example: InnoSlab high power burst-mode amplifiers
Mitigation: NOPA experiments continue with 5kW beam from booster 1.

## Slide 19: Status of pump-probe laser NOPA R&D
Some features:
180µJ per pulse, 34W average power during burst
Nearly transform limited pulses: 15fs … 75fs
100nm tuning for longer pulses
200kHz and 4.5MHz intra-burst operation
Identical performance from BBO and LBO
15fs
600µs burst
Arb. sequence
diff. lim.
High power burst-mode optical parametric amplifier with arbitrary pulse selection
Optics Express, Vol. 22, Issue 18, pp. 22202-22210 (2014)

## Slide 20: Laser locations in Experimental Hall
SASE 2
SASE 1
SASE 3
PP-Laser
Hutches
Instrument Laser
Hutches

## Slide 21: SASE 1: Laser area (PP, FXE, SPB)
SPB - laser
hutch
SFX instrument
PP - laser
hutch
SPB instrument
SFX - laser
hutch
FXE - laser
hutch
FXE instrument

## Slide 22: Laser hutch for SASE 1
Different climate zones:
  Air-condition in preparation/rack area (+/- 0.5 K)
  Precision climatisation in laser area (+/- 0.1 K)

## Slide 23: Summary I
Start-up of European XFEL is in full swing
  Civil construction completed
  Installation of accelerator started
  First x-rays: end of 2016
  Early users: 2017
  Ramp-up x-ray delivery to ~4.800 hrs per annum
  Dedicated instruments and trained staff support users in complex FEL exp.

## Slide 24: Summary II
Lasers for European XFEL user experiments
  Pump-probe laser highly specialized => development at European XFEL
  Strategy: mixed in- and ex-house developments, involving suitable SMEs and OEM-style collaborations
  Development and installation schedule in agreement with current facility plans
  HE/HI lasers planned to be contributed by user consortium „HIBEF“
    Laser group to coordinate integration into HED-instrument
    RAL: DiPOLE 100-X (10Hz, 100J, ns-laser for ramped compression)
    Industry: 100TW, 10Hz, Ti:sapphire

## Slide 25
Thank you!!