## Slide 1: Beam Halo Measurement using Diamond Sensor at ATF2
S. Liu, P. Bambade, F. Bogard, P. Cornebise, V. Kubytskyi, C. Sylvia, A. Faus-Golfe, N. Fuster-Martínez, T. Tauchi, N. Terunuma

## Slide 2
Outlines
Motivations
Conclusions and Prospects
Issues of beam halo @ATF2
Characterization of Diamond Sensor
Beam Halo Measurements
Main Goals for 2014 Run @ ATF2

## Slide 3
Shintake Monitor
Diamond Sensor
Compton
Probe Compton recoil electron (prepare future investigations of higher order contribution to Compton process)
Motivations
Beam halo transverse distribution unknown → investigate halo model
Damping Ring
Old
IP
Diamond sensor

## Slide 4
[3] S. Liu, N. Fuster et al., ATF-14-01 report
New EXT Line
Post-IP WS
16-April-2013
4
Issues of Beam Halo @ATF2
Diamond sensor
Damping Ring
Post-IP WS
Old
26m
MW2X
Cherenkov detector
5m
New EXT Line
Analytical estimation of horizontal beam halo distribution with different vacuum pressure (effect of beam gas scattering) [1]
[1] D. Wang et al., arXiv:1311.1267v2(2014)
[2] T. Suehara et al., arXiv:0810.5467v1(2008)
[2]
Old EXT Line
Notes: Measurement of beam halo distribution using wire scanner is quit limited by the background photons generated by the beam halo hitting the vacuum chamber and the apertures.

## Slide 5
• Large band-gap⇒ low leakage current
• High breakdown field
• High mobility⇒ Fast pulse (several ns)
• Large thermal conductivity
• High binding energy⇒ Radiation hardness
ADVANTAGES
Diamond Sensor (DS) Characteristics
5
FWHM ≈4ns
1 MIP With 40dB amplifier
electron beam
HV
Readout
Charge generated by 1 MIP for 500 µm diamond (with 100% CCE): 2.88 fC
Dynamic range: 1 ->108 e-
4.5mm X 4.5mm X 500µm
 | Total N | Min.～Max. N/mm2 @ DS | Charge signal/mm2
Beam | 1010 | 6.16×108 | 1.6887μC
Halo | 107 | 1.14×104～2.24×104 | 31.236pC～61.376pC
Compton | 28340 | 30～520 | 82.2fC～1.4284pC

## Slide 6
Signal: Bremsstrahlung photons
Dynamic range limited by:
Background level
14 bit ADC counts
PMT high voltage
Background sources:
Beam halo hitting the beam pipe
Beam halo hitting another wire
Data Taking :
Difficult to combine data
Difficult to avoid beam position jitter
Wire Scanner
Signal: Ionized e- hole pairs
Dynamic range:
⇒ 1～ >108 e- (adding amplifier or attenuator)
Possible background:
Beam halo hitting B-Dump bending magnet
⇒ can be collimated by collimators upstream
-> N.Fuster’s talk
Back-scattered neutrons from dump
⇒ slow neutrons can be separated in time
Bremsstrahlung photons
⇒ can be neglected?
Data Taking :
Different channel for beam core and halo
⇒ possible to do overall scan
Diamond Sensor

## Slide 7
In Vacuum Diamond Sensor @ATF2
@CIVIDEC
The first Diamond Sensor is installed horizontally at ATF2 in Nov. 2014
A second unit will be installed vertically in 2015 for vertical halo measurements

## Slide 8
Data Acquisition System
Tests of the system were done with beam at PHIL (photoinjector beamline at LAL) in Oct. 2014 before installation at ATF2
RG58 coax cable
2.5 m
Heliax 1/4 inch coax cable 21 m
Coax cable
0.6 m
feedthrough
Vacuum cable
0.64 m
Vacuum chamber
HV
Power supply
CH1 CH2 CH3 CH4
Ext. Trigger
Agilent 6104 Oscilloscope
4Gs/sec, 1GHz bandwidth
50
5
Diamond Sensor
Ethernet 1
Data acquisition
using Matlab
Ethernet 3
PC
Motor control
@ Post-IP
@ IP laser room
@ Control room
Ethernet 2

## Slide 9
Commission and characterize DS
Main Goal for 2014 Run
Initial measurement of horizontal beam halo distribution
Pick-up study
Study of correlation between DS, ICT and BPM data
Beam core and halo scan with different HV
Background study (background signal from cables observed)
Vertical alignment (VA) applied
Tests of auto vertical range setting
Charge Collection Efficiency (CCE) study with attenuators(with different HV)
Beam halo scan for different beam intensity (1.1*109,2.5*109,4.9*109)
Beam halo scan for different beam optics
Study the background from cables
Study the cut of beam halo by upstream apertures
First try to measure Compton recoil electrons
November Run (5 shifts)
December Run (6 shifts)

## Slide 10
Lower limit of DS : pick-up study
Higher limit of DS : linearity study
Characterization of Diamond Sensor (DS)

## Slide 11
Signal Pick-up Study
Charge, [nC]
Pick-up scan w/o applying HV on DS
Signal pick-up by the strip lines on the PCB was observed as the PCB is not shielded
Residual signal?
Background from Pick-up ≈ 500 e-

## Slide 12
Charge Collection Efficiency
Charge collection efficiency (CCE) depends on the “effective” bias voltage (EBS) on DS
EBS = applied HV – voltage drop on the 50Ω
electron beam
HV
Readout
50Ω
Oscilloscope
HV= 400V
Typical life time of e-h pairs:
τe,h ≈40 ns
HV= 400V

## Slide 13
Linearity of DS Response
Response is linear when the voltage drop is not significant
In the beam core we observed an obvious non-linear response due to large voltage drop
Preliminary
Preliminary

## Slide 14
Beam size verification
Beam halo scan and beam halo distributions
Beam core scan and beam core distributions
Beam Halo Measurements

## Slide 15
Waveforms and Integrated Charge during Scan
Total Beam intensity: 1.2*109
Voltage on DS: -40V
Charge, [nC]
Collected charge during beam scan
The beam core is scanned by DS by applying low voltage
The charge of waveform at each position is integrated to get the distribution

## Slide 16
Beam Core Scan
We move the AQD0FF magnet mover vertically to find the max. charge collected on DS
Before Alignment
After Alignment
Charge, [C]
Charge, [nC]
Charge, [nC]
Vertical Alignment

## Slide 17
Beam Size Verification
12-12-14 data
 | BX10BY0.5 (12-12-14) | 
 | σx (m) | σy (m)
Post-IP WS calculated | 1.564e-04 | 2.892e-04
Post-IP WS measured | 2.174e-04 | 5.57e-04
DS calculated | 1.394e-03 | 1.787e-03
DS expected | 1.938e-03 | 3.442e-03
DS measured (CH2) | 1.498e-03 | Non
Vertical beam size is extrapolated from the Post-IP WS measured beam size

## Slide 18
LE
HE
Beam Halo Scan
Charge, [nC]
2014/12/18 - Day Shift
65mm
Low Energy (LE)
High Energy (HE)
Preliminary
Present Dynamic
Range: 106
76mm

## Slide 19
After fixing
Before fixing
Issue with cables
Before
After

## Slide 20
After Normalization
Before Normalization
Beam Halo Distribution for Different Beam Intensity
Measurements were done for BX10BY0.5 optics with
N= 1.1*109,2.5*109,4.9*109
No change in horizontal beam halo distribution was observed
-> We expect to see the changes on the vertical beam halo distribution

## Slide 21
Beam Halo Distribution for Different Optics
No obvious change observed in the horizontal beam halo distribution between BX10BY1 and BX10BY0.5 optics
For BX100BY1000 optics, beam halo seems less than other optics -> binning is needed
Preliminary

## Slide 22
Conclusions and Prospects
In Nov. and Dec. Run at ATF2 we performed:
Studies to characterize the in vacuum DS performance
Initial measurements of horizontal beam halo distribution
We can use DS to scan both the beam core and beam halo with a dynamic range of 106 (from 5*102 to 5*108 e-) with a 30dB attenuator -> saturation of charge collection will be studied in detail-> improvements on the PCB (shielding etc.) will further improve the dynamic range
Horizontal beam halo distribution was measured -> will be compared with the measurements done in 2013 using the Post-IP WS -> will be useful to see effects from collimators soon to be installed
Asymmetry of horizontal beam halo distribution was observed -> origin of this asymmetry will be studied
Dependence on beam intensity and beam optics will be checked for the vertical beam halo distribution using the 2nd unit of DS -> will be installed in April 2015
Further study to check the possibility of measuring Compton recoil electrons is ongoing

## Slide 23
Thank you!

## Slide 24
Back up …

## Slide 25
High Energy (HE) side
Low Energy (LE) side
Old ATF2 line in 2007
Asymmetry of Horizontal distribution
LE
HE
We can see the asymmetry of horizontal beam halo distribution from the data taken in 2007

## Slide 26
WS signal
Tapered beam pipe (TBP)
Post-IP WS
Cherenkov detector
Diamond Sensor
LE side
HE side
LE side
HE side
Diamond sensor 18-Dec-2014
LE
HE
Charge, [nC]
LE
HE
Post-IP WS 16-April-2013
This asymmetry was observed also in the data taken in 2013 using Post-IP WS and in 2014 using DS
Asymmetry of Horizontal distribution

## Slide 27
Signal FWHM distribution
Typical life time of e-h pairs[1] : τe,h≈40 ns
[1] H. Pernegger et al., J.Appl.Phys. 97, 073704(2005) [2] M. Pomorski et al., phys. Stat. sol. (a) 203, No. 12 (2006)
HV= 40V
HV= 400V
τe,h
Hecht formula: =(]

## Slide 28
Information from ICT and BPMs
ICT after IP, [106 ]
BPM after IP on X
BPM after IP on Y
ICT correction and beam position jitter (4-6 µm) can be taken into account in data analysis
We read the data from Epics via SSH, but it is possible to use Labca to get data directly from Matlab
In the future we can also input data from DS to the Epics system

## Slide 29
Charge Collection Efficiency

## Slide 30
Signal at each channel is a convolution of beam (Gaussian) with strip (rectangular shape)
Fit function: F(d1,a1,b1,s1) = d1+a1*(erf(((x+0.75-b1)/(sqrt(2)*s1)))-erf(((x-0.75-b1)/(sqrt(2)*s1))))
Beam Core Scan
Scan direction

## Slide 31
FFT of Pick-up
1-20mm
20-50mm
90-110mm
70-90mm
50-70mm
(center)
Asymmetry in frequency domain observed

## Slide 32
Background from cables
Move the beam step by step
Cable 1
Cable 2
Cable 3
Cable 1
2
3

## Slide 33
 | CH1 | CH2 | CH3 | CH4
Measured σx | 1.70 mm | 1.49 mm | 1.53 mm | 1.61 mm
Ratio of collected e- | 13.34% | 1.04% | 1.02% | 14.07%
Expected full charge (3fC/MIP) | 1.88µC | 147.21nC | 143.68nC | 1.98µC
Max. charge collected | 442.72nC | 151.79nC | 158.11nC | 600.8nC
Corresponding CCE | 23.55% | 101% | 101% | 30.35%
Scan_Run60_12-12-2014_143616_core_400V
Data taken with 30dB attenuator
Total e- number: 4.8*109
Expected signal (400V)

## Slide 34: Compton recoil electrons study
Perform simulations in CAIN and Mad-X for different optics
Compare the estimated signal level with the background/pick-up signal level
Charge, [nC]
Charge, [nC]
2014/12/20 - OWL Shift
2014/12/18 - DAY Shift