## Slide 1: HCal Barrel Optimization: Status and Updates
Nikiforos Nikiforou
CERN/PH-LCD
CLICdp Detector Optimization Meeting
CERN, Sep 23rd 2014

## Slide 2: Introduction - Reminders
We have continued the work on optimizing the HCal Barrel
  Absorber material (Tunsgten Vs Steel)
  Various combinations of absorber thickness and # Layers
Aim also to have a realistic update on the outer radius
Assumed an active layer cassette with realistic thickness and layout
STEEL
PCB~0.7 mm
SCINTILLATOR (polysterene)
STEEL
RADIATOR (W alloy or Fe)
RADIATOR (W alloy or Fe)
2.7 mm AIR AIR AIR AIR
10 mm
10 mm
3 mm
0.5 mm
0.5 mm
(Steel cassette)
17.5 mm
7.5 mm
PCB (0.7 mm) + Cu (0.1 mm)
(ignore electronics)
Generous 2.7 mm air gap
(called “Fiber gap” in Mokka ILD driver)
Stack on top for simplicity
Could also accommodate some thickness for electronics
(slit size)
(layer thickness for W)
Kept ILD_o1_v06 thicknesses, added cassette, removed 1 mm from Steel absorber thickness

## Slide 3: Various Model Options
Try variations around depth of 7.5 λΙ
Set additional absorber plate at the end, 1 mm steel in cassette
Depth calculations assume particle traversing layer perpendicularly to its face, assume no gaps/dead regions (no cassette joints etc).
Try to gauge performance of various models:
  Single Particle Response
  Jet Energy Resolution: for now
  Have to Calibrate each model
Detector | # Layers | Abs Thick | Cass. Thick | Air | Total Depth | Total Thickness | Inner R | Outer Face Position | Outer Radius
 |  | mm | mm | mm | #λΙ | mm | mm | mm | mm
CLIC_ILD_CDR | 75 | 10 | 5* (*Scint) | 1.5 | 7.42 | 1237.5 | 2058 | 3295.5 | 3341.2
CLIC_SID_CDR |  |  |  |  |  | 1237.5 | 1447 | 2684.5 | 2721.7
W + cassette | 75 | 10 | 4.8 | 2.7 | 7.92 | 1322.5 | 1750 | 3072.5 | 3115.1
W + cassette | 70 | 10 | 4.8 | 2.7 | 7.40 | 1235 | 1750 | 2985 | 3026.4
Fe + cassette | 60 | 19 | 4.8 | 2.7 | 7.55 | 1609 | 1750 | 3359 | 3405.6
Fe + cassette | 70 | 16 | 4.8 | 2.7 | 7.93 | 1661 | 1750 | 3411 | 3458.3

## Slide 4: Outline of Calibration Procedure and JER study
Modify ILD_o1_v06 model in Mokka
    , 4.5 T field (constant for all variations, rest same as ILD)
    Vary absorber material and thickness in HCal Barrel
Simulate events in Mokka/G4 (QGSB_BERT_HP):
    γ (10 GeV), μ (10 GeV), K0L(1,2,5,10,20,50,100,200,500 GeV) [G4 GPS]
    Also generate events () [stdhep files]
Hit-level, digitization calibration:
    Dump root ntuples from LCIO files with sum of energies per layer
    Use γ events to set CalibrEcal (do once, assume same then)
    Use 50 GeV K0L to set CalibrHCalBarrel (do for every variation of HCal). Do once for CalibrHCalEndcap and keep the same (not varying endcap)
    Use μ to set EcalToMip (verified that remains ~the same) and HcalToMip
    Assume CalibrMuon, CalibrOther, same as ILD

## Slide 5: Outline of Calibration Procedure - II
PandoraPFA calibration:
    Run PandoraPFA over the γ events to get ECALToEM , HCALToEM (actually set both to 1 for these studies)
    Run Calibration procedure over the Kaon events to obtain ECALToHAD, HCALToHAD at 50 GeV
    Obtain Non-Linearity Corrections (NLC):
      Measure response for 1,2,5,10,20,50,100,200,500 GeV Kaons and calculate scaling factor (extrapolate in-between)
Recalibrate when changing Readout Window Timing Cut
Having these numbers, we can study the Jet Energy Resolution
Use AnalysePerformance (from PandoraAnalysis-v00-06)
Study the performance various models
  Also look at different Timing Cuts

## Slide 6: JER Results
Chart: 
| 91 | 200 | 360 | 500 | 1000 | 2000 | 3000
10W 70L HP TC 100 ns 7.4 λΙ | 4.2613 | 3.4165 | 3.3666 | 3.388 | 3.5198 | 3.6493 | 3.786
10W 75L HP TC 100 ns 7.92 λΙ | 4.3452 | 3.451 | 3.2734 | 3.3656 | 3.3015 | 3.4179 | 3.5154
19Fe 60L HP TC 10 ns 7.55 λΙ | 4.4689 | 3.7219 | 3.722 | 3.8995 | 4.2312 | 4.3733 | 4.7099
16Fe 70L HP TC 10 ns 7.93 λΙ | 4.3845 | 3.7049 | 3.6708 | 3.7824 | 3.8984 | 4.4076 | 4.4091
19Fe 60L HP TC 100 ns 7.55 λΙ | 4.4181 | 3.6088 | 3.5223 | 3.5821 | 3.5672 | 3.9985 | 4.207
10W 75L HP TC 10 ns 7.40 λΙ | 4.5276 | 3.9215 | 4.1815 | 4.3903 | 5.0558 | 5.4127 | 5.4998
16Fe 70L HP TC 100 ns 7.93 λΙ | 4.2682 | 3.5808 | 3.4961 | 3.4973 | 3.4957 | 3.9346 | 4.0548
Drop from Steel @ 100 ns
Drop

## Slide 7: JER Results For Just Two Models
Chart: 
| 91 | 200 | 360 | 500 | 1000 | 2000 | 3000
10W 70L HP TC 100 ns 7.4 λΙ | 4.2613 | 3.4165 | 3.3666 | 3.388 | 3.5198 | 3.6493 | 3.786
19Fe 60L HP TC 10 ns 7.55 λΙ | 4.4689 | 3.7219 | 3.722 | 3.8995 | 4.2312 | 4.3733 | 4.7099
19Fe 60L HP TC 100 ns 7.55 λΙ | 4.4181 | 3.6088 | 3.5223 | 3.5821 | 3.5672 | 3.9985 | 4.207
10W 75L HP TC 10 ns 7.40 λΙ | 4.5276 | 3.9215 | 4.1815 | 4.3903 | 5.0558 | 5.4127 | 5.4998

## Slide 8: Residuals with Proper Calibration
Chart: 
| 91 | 200 | 360 | 500 | 1000 | 2000 | 3000
10W 70L HP TC 100 ns 7.4 λΙ | 0.13714 | -0.177 | -0.90056 | -1.3198 | -2.3347 | -2.529 | -2.4657
10W 75L HP TC 100 ns 7.92 λΙ | -0.10637 | -0.0795 | -0.77139 | -1.276 | -2.2198 | -2.474 | -2.1927
19Fe 60L HP TC 10 ns 7.55 λΙ | 0.17374 | 0.038 | -0.83694 | -1.4432 | -2.7309 | -2.9875 | -2.951
16Fe 70L HP TC 10 ns 7.93 λΙ | 0.14879 | -0.041 | -0.78889 | -1.4266 | -2.6936 | -2.9975 | -3.059
19Fe 60L HP TC 100 ns 7.55 λΙ | 0.23538 | 0.15 | -0.48139 | -0.9154 | -1.5997 | -1.872 | -1.7967
10W 75L HP TC 10 ns 7.40 λΙ | -0.31813 | -0.628 | -1.7339 | -2.778 | -4.951 | -6.1525 | -6.3143
16Fe 70L HP TC 100 ns 7.93 λΙ | 0.23275 | -0.0675 | -0.47528 | -1.0568 | -1.7757 | -1.5855 | -1.6063
Residual non-linearity to be investigated more
See next slides for single particle response

## Slide 9: Single particle response (K0L)
No errors on plots
Fits to energy distributions from calibration procedure
After application of NLC
Some small discrepancies at low and high ends of the energies
However, taking all plots into consideration and comparing with JER plots, it seems unlikely this is driving the JER performance
I would say that nothing looks extremely suspicious here
Chart: 
| 1 | 2 | 5 | 10 | 20 | 50 | 100 | 200 | 500
10W 70L HP TC 100 ns | 53.4455 | 41.1319 | 25.1259 | 18.8377 | 12.8288 | 9.436 | 8.1291 | 7.31 | 6.4945
10W 75L HP TC 100 ns | 45.709 | 41.5005 | 25.5284 | 18.8692 | 12.4846 | 9.486 | 8.4554 | 7.2969 | 6.5354
19Fe 60L HP TC 10 ns | 53.376 | 44.8649 | 26.8559 | 19.7758 | 14.541 | 11.4432 | 10.9225 | 10.8616 | 11.0546
16Fe 70L HP TC 10 ns | 49.3102 | 41.9089 | 25.9674 | 19.2271 | 13.8233 | 11.3399 | 10.9642 | 10.4432 | 11.036
19Fe 60L HP TC 100 ns | 44.9636 | 42.6298 | 25.9296 | 19.3997 | 14.1597 | 10.7601 | 9.6931 | 9.5024 | 8.8127
10W 75L HP TC 10 ns | 47.3385 | 42.6074 | 27.3031 | 20.7546 | 14.2421 | 12.6601 | 13.6412 | 14.1581 | 14.9253
16Fe 70 L HP TC 100 ns | 50.3094 | 41.3245 | 25.4888 | 18.5021 | 13.4808 | 10.7809 | 9.8808 | 8.9224 | 9.0464
Chart: 
| 1 | 2 | 5 | 10 | 20 | 50 | 100 | 200 | 500
10W 70L HP TC 100 ns | -5.8208 | -0.6745 | 0.481 | 0.756 | 0.6705 | 0.4566 | 0.327 | 0.237 | 0.2786
10W 75L HP TC 100 ns | -4.8987 | -1.196 | 0.5514 | 0.692 | 0.6295 | 0.4082 | 0.227 | 0.1665 | 0.1602
19Fe 60L HP TC 10 ns | -9.9901 | -2.2355 | 0.0814 | 0.618 | 0.6685 | 0.554 | 0.37 | 0.427 | 0.231
16Fe 70L HP TC 10 ns | -6.8708 | -1.461 | 0.1704 | 0.669 | 0.6275 | 0.57 | 0.53 | 0.1625 | 0.3834
19Fe 60L HP TC 100 ns | -5.131 | -0.541 | 0.341 | 0.745 | 0.622 | 0.6352 | 0.523 | 0.442 | 0.3934
10W 75L HP TC 10 ns | -4.9375 | -1.578 | 0.637 | 0.653 | 0.8705 | 0.3812 | 0.035 | -0.4565 | -1.274
16Fe 70 L HP TC 100 ns | -7.6334 | -1.4435 | 0.0416 | 0.747 | 0.624 | 0.4908 | 0.436 | 0.2575 | 0.7332
Look at timing cut response in more detail (next two slides)

## Slide 10: Tungsten and Steel Response to 50 GeV K0L for various Timing Cuts: Fraction of Reconstructed Energy
Chart: 
| 1 | 2 | 5 | 10 | 20 | 30 | 40 | 50 | 60 | 80 | 90 | 100 | 120 | 140 | 160 | 180 | 200 | 400 | 600 | 800 | 1000 | 2000 | 5000 | 10000
19Fe 60L Cut-dependent calibration | 100.6862 | 100.6056 | 100.6066 | 100.5674 | 100.6004 | 100.603 | 100.5978 | 100.6064 | 100.6182 | 100.6206 | 100.624 | 100.6336 | 100.5876 | 100.5896 | 100.5972 | 100.592 | 100.598 | 100.5688 | 100.5802 | 100.579 | 100.578 | 100.5468 | 100.5518 | 100.5828
19Fe 60L Fixed calibration (10000 ns) | 89.8528 | 91.942 | 93.6586 | 94.4706 | 95.0392 | 95.2492 | 95.3986 | 95.5042 | 95.5828 | 95.5928 | 95.6492 | 95.7018 | 95.7484 | 95.8334 | 95.894 | 95.95 | 95.994 | 96.035 | 96.1248 | 96.1948 | 96.3048 | 96.3898 | 96.4628 | 96.5896 | 96.696 | 97.5886 | 98.1762
10W 75L Cut-dependent calibration | 100.5348 | 100.4406 | 100.3868 | 100.3812 | 100.3674 | 100.3938 | 100.4312 | 100.3594 | 100.3886 | 100.4124 | 100.4342 | 100.4086 | 100.4404 | 100.4076 | 100.4006 | 100.3946 | 100.3836 | 100.4044 | 100.4178 | 100.4216 | 100.4454 | 100.4086 | 100.4124 | 100.414
10W 75L Fixed calibration (10000 ns) | 82.8496 | 84.899 | 86.0364 | 86.9266 | 87.522 | 89.2454 | 90.6516 | 91.4776 | 92.0544 | 92.5036 | 92.8932 | 93.22 | 93.5228 | 93.7798 | 93.978 | 94.376 | 94.692 | 94.9706 | 95.2072 | 95.4086 | 95.8842 | 96.2084 | 96.7212 | 97.0728 | 97.3414 | 97.5688 | 97.7506 | 98.0398 | 98.823 | 99.3852 | 99.6936
Readout Window Timing Cut [ns]
Tighter timing cut = Smaller Fraction of reconstructed energy
  Tungsten is more sensitive
  Calibration procedure adapts to correct for the lost energy

## Slide 11: Tungsten and Steel Response to 50 GeV K0L for various Timing Cuts: Energy Resolution (normalized to 50 GeV)
Chart: 
| 1 | 2 | 5 | 10 | 20 | 30 | 40 | 50 | 60 | 80 | 90 | 100 | 120 | 140 | 160 | 180 | 200 | 400 | 600 | 800 | 1000 | 2000 | 5000 | 10000
19Fe 60L Cut-dependent calibration | 13.6979 | 12.7 | 12.0312 | 11.5048 | 11.2592 | 11.154 | 11.0616 | 10.9989 | 10.9565 | 10.8869 | 10.8561 | 10.8366 | 10.8919 | 10.8585 | 10.8315 | 10.8107 | 10.7916 | 10.6752 | 10.5819 | 10.5344 | 10.496 | 10.2001 | 10.0073 | 9.8547
19Fe 60L Fixed calibration (10000 ns) | 11.0857 | 10.6172 | 10.3071 | 10.1105 | 9.9024 | 9.8191 | 9.7547 | 9.7194 | 9.6903 | 9.7607 | 9.7335 | 9.708 | 9.6853 | 9.6522 | 9.6272 | 9.5975 | 9.5739 | 9.5548 | 9.5089 | 9.4815 | 9.4396 | 9.4126 | 9.391 | 9.3431 | 9.3186 | 9.1695 | 8.9922
10W 75L Cut-dependent calibration | 17.2777 | 15.9465 | 14.0164 | 12.7084 | 11.6519 | 11.0603 | 10.6775 | 10.2816 | 10.0466 | 9.7349 | 9.6204 | 9.5247 | 9.3649 | 9.1474 | 9.0537 | 8.9527 | 8.865 | 8.4927 | 8.3317 | 8.2251 | 8.1772 | 8.0755 | 7.9976 | 7.9776
10W 75L Fixed calibration (10000 ns) | 12.8386 | 12.3531 | 11.9658 | 11.568 | 11.343 | 10.5634 | 9.8082 | 9.4013 | 9.0742 | 8.8515 | 8.6878 | 8.5605 | 8.4175 | 8.3319 | 8.272 | 8.1572 | 8.0824 | 7.9734 | 7.8836 | 7.8439 | 7.857 | 7.7931 | 7.6506 | 7.6041 | 7.5704 | 7.5506 | 7.5446 | 7.5354 | 7.5625 | 7.5232 | 7.5186
Readout Window Timing Cut [ns]
First attempt to reproduce previous studies by M. Thomson and J. Marshall (see backup)
Similar conclusion to JER study:
Tungsten@100 ns “outperforms” Steel at 10 ns and 100 ns

## Slide 12: Conclusions and Next Steps
JER: “Fe does not appear to perform better than W, assuming the same timing window of 100 ns or larger”
  If there is a strong argument for a small readout window (), Fe will perform better than W
    However, any effect (increased background/pileup) due to a large HCal timing window can be mitigated by PFO-level timing cuts ( )
  At the very least, one can say that at 100 ns, Fe can perhaps have a comparable (within ~5-10%) JER performance with W
  Some residual non-linearities/systematics to be investigated more
The single particle response results appear to agree with JER conclusions
Next steps: Study more realistic physics events with two jets
  and
  Study JER in these events
  Study overlap of and dijet-invariant mass peaks

## Slide 13: Bonus material – OLDER PLOTS

## Slide 14: JER for various HCal timing cuts from last week
Chart: 
| 91 | 200 | 360 | 500 | 1000 | 2000 | 3000
10W 75L | 4.029 | 3.2176 | 3.0292 | 2.9362 | 3.0949 | 3.005 | 3.3399
19Fe 60L | 4.2209 | 3.3895 | 3.295 | 3.2496 | 3.5419 | 3.4139 | 3.5434
10W 75L HP | 4.0891 | 3.2 | 3.0841 | 3.0566 | 2.8641 | 2.9377 | 3.059
19Fe 60L HP | 4.2566 | 3.4061 | 3.2346 | 3.2291 | 3.3764 | 3.2226 | 3.5861
10W 75L HP TC 150 ns | 4.0709 | 3.5588 | 3.7128 | 3.7999 | 3.8785 | 3.8446 | 4.0611
19Fe 60L HP TC 150 ns | 4.2525 | 3.6609 | 3.7321 | 3.7939 | 3.8853 | 4.2325 | 4.4142
10W 75L HP TC 100 ns | 4.0972 | 3.6614 | 3.881 | 4.0731 | 4.3764 | 4.2193 | 4.3433
19Fe 60L HP TC 100 ns | 4.2588 | 3.6793 | 3.7916 | 3.8621 | 4.1363 | 4.4019 | 4.4461
10W 75L HP TC 10 ns | 4.5138 | 4.586 | 5.3938 | 5.8866 | 6.8672 | 7.3342 | 7.5509
19Fe 60L HP TC 10 ns | 4.2826 | 3.8194 | 4.1509 | 4.317 | 4.6914 | 4.9398 | 5.7861
Using same calibration for same model, different timing cuts! The calibration was performed without timing cuts

## Slide 15: Residuals for the same sets from last week
Chart: 
| 91 | 200 | 360 | 500 | 1000 | 2000 | 3000
10W 75L | 0.40989 | 0.097 | -0.29028 | -0.6542 | -1.2406 | -1.353 | -1.2393
19Fe 60L | 0.70143 | 0.4375 | -0.14028 | -0.2708 | -0.8511 | -0.822 | -0.74567
19Fe 60L HP | 0.88648 | 0.7535 | 0.27667 | 0.1806 | -0.1872 | 0.1015 | 0.362
10W 75L HP | 0.33462 | 0.0675 | -0.31306 | -0.8492 | -1.3524 | -1.4675 | -1.2063
19Fe 60L HP TC 150 ns | 0.33 | -0.4525 | -1.3931 | -2.2206 | -3.9338 | -7.1125 | -5.8527
10W 75L HP TC 150 ns | -0.21747 | -0.9955 | -2.0164 | -2.9414 | -5.1612 | -6.7735 | -6.8083
10W 75L HP TC 100 ns | -0.46824 | -1.1255 | -2.2758 | -3.454 | -6.0795 | -7.6935 | -8.176
19Fe 60L HP TC 100 ns | 0.14846 | -0.5415 | -1.5444 | -2.3092 | -4.2774 | -5.4175 | -6.1597
10W 75L HP TC 10 ns | -1.2435 | -2.2645 | -4.1814 | -5.9402 | -9.9555 | -14.024 | -15.6693
19Fe 60L HP TC 10 ns | -0.14319 | -0.901 | -2.0656 | -3.1202 | -5.753 | -7.6295 | -8.893
Using same calibration for same model, different timing cuts! The calibration was performed without timing cuts

## Slide 16: Reminder: Readout Windows
See talks by M. Thompson:
  http://indico.cern.ch/event/115459/contribution/14/material/slides/0.pdf (slides 3,4)
  https://agenda.linearcollider.org/getFile.py/access?contribId=13&sessionId=1&resId=0&materialId=slides&confId=5134 (slides 16,17…)
Further timing cuts (mainly for background/pileup suppression) are applied at the PFO level. NOT CONSIDERED IN THE STUDY PRESENTED TODAY
  We will apply cuts at the digitization level

## Slide 17: Plots from CDR
CDR Fig. 6.1, see also Ref. [1]
Numbers indicate
CDR Fig. 6.2 and Refs. [3,4]
These studies drive the aim for an HCal depth of at
Right: Pandora PFA study by A. Lucaci Timoce
  Modiﬁed CLIC01_ILD model
  Older Pandora version (not expected to be significantly relevant to the results)
  New studies underway (Cambridge, CERN)
Bottom: Toy (testbeam stack) calorimeter study by C. Grefe and P. Speckmeyer
Single (Slic)
Hit based
TMVA calibration
Determined performance of Tungsten and Steel (see next slide)

## Slide 18: Material Scan of W-HCAL (CLIC_SID_CDR)
Try to verify material budget in current detector geometry implementations
See whether we can squeeze some more the HCal outer radius
Scan using Slic/Geant4 (see backup)
Geometry Parameters:
(www.lcsim.org/detectors/clic_sid_cdr.html)
Chart: 
HCAL BARREL | 
Number Of Layers | 75
Number Of Sides | 12
Inner Radius | 1419 mm
Outer Radius | 2656.5 mm
Z Length | 3530 mm
Section Phi | 0.52 radians
Cell Size U | 30.0 mm
Cell Size V | 30.0 mm
Layers 0 - 74 | 
10 mm | Tungsten
5 mm (sensor) | Polystyrene
1.5 mm | Air

## Slide 19: CLIC_SID_CDR Material Scan in θ
Chart: cos(θ)
| 6.1257422745431001E-17 | 1.7452406437283376E-2 | 3.489949670250108E-2 | 5.2335956242943966E-2 | 6.9756473744125455E-2 | 8.7155742747658138E-2 | 0.10452846326765346 | 0.12186934340514749 | 0.13917310096006569 | 0.15643446504023092 | 0.17364817766693041 | 0.19080899537654492 | 0.20791169081775945 | 0.22495105434386492 | 0.2419218955996679 | 0.25881904510252074 | 0.27563735581699916 | 0.29237170472273677 | 0.30901699437494745 | 0.32556815445715676 | 0.34202014332566882 | 0.35836794954530038 | 0.37460659341591196 | 0.39073112848927394 | 0.40673664307580021 | 0.42261826174069944 | 0.43837114678907746 | 0.4539904997395468 | 0.46947156278589086 | 0.48480962024633711 | 0.50000000000000011 | 0.51503807491005438 | 0.5299192642332049 | 0.5446390350150272 | 0.55919290347074679 | 0.57357643635104616 | 0.58778525229247314 | 0.60181502315204838 | 0.61566147532565829 | 0.6293203910498375 | 0.64278760968653936 | 0.65605902899050728 | 0.66913060635885824 | 0.68199836006249848 | 0.69465837045899737 | 0.70710678118654757 | 0.71933980033865119 | 0.73135370161917057 | 0.74314482547739424 | 0.75470958022277213 | 0.76604444311897801 | 0.7771459614569709 | 0.78801075360672201
Hcal λΙ | 7.4626 | 7.4638 | 7.4672 | 7.4729 | 7.4809 | 7.4911 | 7.5037 | 7.5187 | 7.536 | 7.5557 | 7.5778 | 7.6023 | 7.6294 | 7.6589 | 7.6911 | 7.7259 | 7.7634 | 7.8036 | 7.8467 | 7.8926 | 7.9416 | 7.9936 | 8.0487 | 8.1071 | 8.1689 | 8.2341 | 8.3029 | 8.3755 | 8.452 | 8.5324 | 8.6171 | 8.7062 | 8.7998 | 8.8982 | 8.7498 | 8.1344 | 7.546 | 6.977 | 6.4397 | 5.9085 | 5.4213 | 4.8891 | 4.4151 | 3.9391 | 3.4535 | 2.9551 | 2.5007 | 2.0371 | 1.559 | 1.0617 | 0.61366 | 0.14737 | 0
Ecal λΙ | 0.97207 | 0.97222 | 0.97267 | 0.97341 | 0.97445 | 0.97579 | 0.97743 | 0.97937 | 0.98163 | 0.98419 | 0.98707 | 0.99027 | 0.99379 | 0.99764 | 1.0018 | 1.0064 | 1.0112 | 1.0165 | 1.0221 | 1.0281 | 1.0345 | 1.0412 | 1.0484 | 1.056 | 1.0641 | 1.0726 | 1.0815 | 1.091 | 1.1009 | 1.1114 | 1.1225 | 1.1341 | 1.1462 | 1.1591 | 1.1725 | 1.1867 | 1.2015 | 1.2172 | 1.2336 | 1.2508 | 1.269 | 1.288 | 1.3081 | 1.3291 | 1.3513 | 1.3747 | 1.3994 | 1.4253 | 1.4527 | 1.4817 | 1.5123 | 1.5446 | 1.2758 | 0.7032 | 0.19161 | 0
Hcal X0 | 191.7508 | 191.78 | 191.8677 | 192.014 | 192.2191 | 192.4833 | 192.807 | 193.1908 | 193.6353 | 194.141 | 194.7089 | 195.3398 | 196.0347 | 196.7947 | 197.621 | 198.5151 | 199.4783 | 200.5123 | 201.6187 | 202.7996 | 204.057 | 205.3929 | 206.8099 | 208.3105 | 209.8974 | 211.5736 | 213.3423 | 215.207 | 217.1712 | 219.2391 | 221.4148 | 223.7029 | 226.1084 | 228.6366 | 225.0254 | 209.1089 | 193.9737 | 179.2732 | 165.468 | 151.854 | 139.4772 | 125.6459 | 113.5259 | 101.3681 | 88.8475 | 75.9294 | 64.3782 | 52.4742 | 40.1917 | 27.2792 | 15.9008 | 4.0449 | 0
Ecal X0 | 25.6959 | 25.6998 | 25.7116 | 25.7312 | 25.7587 | 25.7941 | 25.8374 | 25.8889 | 25.9484 | 26.0162 | 26.0923 | 26.1768 | 26.27 | 26.3718 | 26.4825 | 26.6024 | 26.7314 | 26.87 | 27.0183 | 27.1765 | 27.345 | 27.524 | 27.7139 | 27.915 | 28.1277 | 28.3523 | 28.5893 | 28.8392 | 29.1024 | 29.3795 | 29.6711 | 29.9777 | 30.3001 | 30.6389 | 30.9949 | 31.3689 | 31.7619 | 32.1748 | 32.6086 | 33.0645 | 33.5436 | 34.0474 | 34.5772 | 35.1347 | 35.7215 | 36.3395 | 36.9907 | 37.6774 | 38.4019 | 39.1671 | 39.9757 | 40.8312 | 33.612 | 18.3256 | 4.9808 | 0

## Slide 20: CLIC_ILD_CDR Material Scan in φ
Chart: 
Scan using Mokka/Geant4 (see backup)
Geometry Parameters:
(from CDR and http://www-flc.desy.de/ldcoptimization/tools/mokkamodels.php?model=CLIC_ILD_CDR)
HCAL BARREL | SHcalSc02
Number Of Layers | 75
Number Of Sides | (8) 16
Inner Radius | 2058 mm
Outer Radius | 3296 mm
Z Length | 4700 mm
Section Phi | 0.52 radians
Cell Size U | 30.0 mm
Cell Size V | 30.0 mm
Layers 0 - 74 | 
10 mm | Tungsten
5 mm (sensor) | Polystyrene
1.5 mm | Air

## Slide 21: ILD AHCAL Assembly (from ILD TDR)
Active Element Cassette |  | ILD
Material | Thickness | Thickness
 | mm | mm
Steel | 2 | 0.5
PCB | 1.4 | 1
Cu (etching) | 0.1 | 0
Electronics (30%) | 1.5 | 1
Scintillator | 5 | 3
Sum (per layer) | 10 | 5.5
#λΙ (per layer) | 0.02 | 0.01
NB: ILD TDR also mentions “The active layers will contribute 4 mm of steel to each absorption layer”
Not shown in diagram?
16 mm (absorber layer) +
4 mm = 20 mm steel
+0.5 mm bottom plate?
Not clear what is done in code (comment says ignored)