## Slide 1: Beam Diagnostics at Free Electron Lasers
Gero Kube
DESY / MDI
gero.kube@desy.de
Introduction
Beam Position (Intensity)
Transverse Profile Diagnostics
Longitudinal Profile Diagnostics
Timing and Synchronization
Laser Applications at Accelerators Conference 2015
25-27 March 2015
Son Caliu Hotel

## Slide 2: Free Electron Lasers (FELs)
Gero Kube, DESY / MDI
linac (single pass) based 4th generation light sources
Linac based Self Amplification of Spontaneous Emission (SASE) FELs
electron bunch modulated with
its own synchrotron radiation field
micro-bunching
more and more electrons radiate in
phase until saturation is reached
European X-FEL @ DESY
LCLS @ SLAC
SACLA @ SPring8
Swiss FEL @ PSI
FLASH @ DESY
SPARC @ INFN-Frascati
…
SASE FEL projects
(→ no matter for diagnostics which FEL type)
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015

## Slide 3: FLASH @ DESY
Gero Kube, DESY / MDI
FLASH accelerator, FLASH I/II SASE FELs
first lasing FLASH II:
→ August 20, 2014
FEL radiation parameters 2012
lasing @ FLASH:
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015

## Slide 4: The European XFEL @ DESY
Gero Kube, DESY / MDI
3.3 km
HERA
DESY
Hamburg
City Centre (7 km)
FLASH
PETRA III
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015

## Slide 5: E-XFEL @ DESY
Gero Kube, DESY / MDI
photo-injector RF electron gun
injector linac
two-stage bunch compression
collimation and beam distribution
undulator sections
photon beamlines
maximun energy: 17.5 GeV
normalized emittance: 1-2 mm mrad
typical rms beam sizes: 20-200 μm
bunch charge : 0.1-1 nCb
min. bunch spacing: 222 nsec
max. macro pulse length: 600 μsec
bunches within macro pulse: 1-2700
bunch pattern: arbitrary
RF repetition rate: < 30 Hz
λmin 0.1 nm (12.4 keV)
injector commissioning: mid 2015
linac commissioning: 2016
user operation: 2017
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015

## Slide 6: Beam Properties (1)
Gero Kube, DESY / MDI
high current density
sufficient energy transfer from electron beam to radiation field
natural scale: number of electrons per wavelength
Ü
requires additional bunch compression in order to increase current density
Ü
extremely short bunch lengths O(10-100 fsec)
single or few bunches, typically with large separation
Ü
requires single bunch measurements
charge per bunch: pCb up to about nCb
new trend: short pulse operation, requires lower and lower charges…
signal to noise problems at low charge, even for kA peak currents
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015

## Slide 7: Beam Properties (2)
Gero Kube, DESY / MDI
Ü
high demands on 6-dimensional phase space
high electron beam quality
energy spread
for resonant energy exchange and good overlap with radiation field
transverse emittance
(→ high energy helps)
beam gets extremely small, often weird shape
emittance is no equilibrium property, many effects can spoil it
optics errors propagate through entire machine (linac is open loop system)
coherent effects due to short pulses and instabilities
short bunches require complicate longitudinal diagnostics
new methods required to verify pulse lengths of electron and laser bunch
transverse phase space
longitudinal phase space
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015

## Slide 8: Beam Properties (3)
Gero Kube, DESY / MDI
comment: transverse emittance
electrons slip back in phase with respect to photons by lr each undulator period
FEL integrates over slippage length → slice emittance of importance
x
x´
lr
slice emittance
x
x´
projected emittance
stability
energy stability → wavelength stability
arrival time stability → pump probe experiments
example: XFEL @ DESY
length of undulator section: 100-150 m
BPM position resolution:
1 μm (single bunch), 100 nm (average over bunch train)
position stability
→ overlap between beam and radiation in undulators
LLRF feedback
high level synchronisation
high resolution BPMs, orbit feedback
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015

## Slide 9: Standard FEL Diagnostics @ FLASH
Gero Kube, DESY / MDI
and a lot of additional special diagnostics…
 |  | FLASH1 | FLASH2
Charge | Toroids | 12 | 5
 | Dark Current Monitor | 1 | 
 | Faraday Cups | 3 | 
 | BPMs | 6 | 33
Transverse Size | OTR-Screens | ~30 | 
 | Scintillating-Screens | 1 | 7
 | Wire scanners (MDI) | 10 | 
 | Wire scanners (Zeuthen) | 9 | 
Transverse Position | Button-BPMs | 26 | 12
 | Stripline-BPMs | 33 | 4
 | Cold Cavity BPMs | 6 | 
 | Cavity BPMs |  | 17
 | HOM-based monitors | 39 | 
Beam Loss | BLMs | >70 | ~55
 | Cherenkov Fibers | 2 | 1
 | Beam Halo Monitors | 1x4 | 1x4
 | Ionization Chambers | 4 | 4
about ~ 400 monitors
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015

## Slide 10: Standard FEL Diagnostics @ E-XFEL
Gero Kube, DESY / MDI
Monitor (Standard Diagnostics Only) | Number
BPMs (cold) | 120
BPMs (Striplines, Pickups) | 250
Undulator BPMs (Cavity, 1µm Resolution) | 140
Charge Monitors (Toroids, Faraday Cups) | 40
Beam Size: OTR, Wirescanners | 77
Dark Current | 10
Loss Monitors (PM Systems, Fibers) | 320
Phase | 15
Other | about 50
Total | about 1000
and a lot of additional special diagnostics…
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015

## Slide 11: Beam Position Monitors
 | Number | Beam Pipe | Length | Type | Single Bunch Resolution (RMS) | Train Averaged Resolution (RMS) | Optimum Resolution Range | Relaxed Resolution Range | x/y Crosstalk | Bunch to Bunch Crosstalk | Trans. Alignment Tolerance (RMS)
 |  | mm | mm |  | μm | µm | mm | mm | % | μm | μm
Standard BPM | 219 | 40.5 | 200/ 100 | Button | 50 | 10 | ± 3.0 | ± 10 | 1 | 10 | 200
Cold BPM | 102 | 78 | 170 | Button/ Re- entrant | 50 | 10 | ± 3.0 | ± 10 | 1 | 10 | 300
Cavity BPM Beam Transfer Line | 12 | 40.5 | 255 | Cavity | 10 | 1 | ± 1.0 | ± 2 | 1 | 1 | 200
Cavity BPM Undulator | 117 | 10 | 100 | Cavity | 1 | 0.1 | ± 0.5 | ± 2 | 1 | 0.1 | 50
IBFB | 4 | 40.5 | 255 | Cavity | 1 | 0.1 | ± 1.0 | ± 2 | 1 | 0.1 | 200
Gero Kube, DESY / MDI
short version of E-XFEL BPM specification
specified charge range: 0.1 – 1nC
courtesy: D.Nölle (DESY)
different BPM types to meet different requirements
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015

## Slide 12: Beam Position Monitors
Gero Kube, DESY / MDI
operation principle of (capacitive) button pickup
electric field induces image charge on pick-up
→ pick-up mounted isolated inside vacuum chamber
→ amount of induces charge depends on distance between beam and pick-up
LHC button pickup
courtesy: R.Jones (CERN)
x
y
beam
x = Kx
P1 – P3
P1 + P3
y = Ky
P2 – P4
P2 + P4
processing example: Δ/Σ method
beam position information
Courtesy: M. Gasior (CERN)
amplitude modulated on large (common mode) beam intensity signal
signal subtraction to obtain position information
→ difficult to do electronically without some of the intensity information leaking through
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015

## Slide 13: Cavity BPM
Gero Kube, DESY / MDI
collect directly position information
bunch excites several resonating modes while passing a
pillbox-like cavity
→ short bunches deliver wide spectrum of frequencies
monopole mode TM01(0): beam intensity
→ maximum at center
→ strong excitation
dipole mode TM11(0): beam position
→ minimum at center
→ excitation by beam offset
→ slightly shifted in frequency wrt. monopole mode
antenna for outcoupling of dipole mode
amplitude: position information
→ only absolute value !
phase (wrt. monopole mode): sign information
→ simultaneous measurement required !
t / ns
U / V
antenna signal: time domain
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015

## Slide 14: Cavity BPM
f / GHz
U / V
TM01
TM11
TM02
U~q
U~q∙|r|
U~q
cavity frequency spectrum
Gero Kube, DESY / MDI
problem: monopole mode (TM01) leakage into dipole mode (TM11)
→ suppression of monopole mode required
q: beam charge, r: beam offset
courtesy: D.Lipka (DESY)
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015

## Slide 15: Cavity BPM
Gero Kube, DESY / MDI
suppresion of monopole mode
dipole mode (TM11) signal coupled out via waveguide
→ choose outcoupling at position of large TM11 electric field amplitude
design waveguide with cutoff frequency above f01 (monopole mode) resonance
Monopole Mode
Dipole Mode
courtesy: D.Lipka (DESY)
influence of outcoupling waveguide
narrow-band electronics for signal processing
→ B.Keil, Proc. DIPAC’09, Basel (Switzerland) 2009, TUOC01, p.275
→ D.Lipka, Proc. DIPAC’09, Basel (Switzerland) 2009, TUOC02, p.260
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015

## Slide 16: Cavity BPMs for SASE Machines
Gero Kube, DESY / MDI
Undulator intersection @ LCLS
Cavity BPM @ LCLS
Low Q Cavity BPM @ SCSS
E-XFEL Cavity BPM Test @ FLASH
courtesy: D.Nölle (DESY)
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015

## Slide 17: Cavity Monitor for Bunch Current
Gero Kube, DESY / MDI
E-XFEL design
parameters:
→ fres = 1.3 GHz, QL = 198.4
→ 40.5 mm diameter tube, 9 cm length
achieved sensitivity:
→ S = 11.83 V/nCb
D.Lipka et al., Proc. DIPAC 2011,
Hamburg (Germany) 2011, WEOC03
Cavity vs. Toroid
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015
μr
N
P. Forck, “Lecture Notes on Beam Instrumentation and Diagnostics”, JUAS 2011
Toroid principle

## Slide 18: Transverse Profile / Emittance
Gero Kube, DESY / MDI
advantage: fast single shot measurement
linear response (neglect coherence !)
disadvantage: high charge densities may destroy radiator → limitation on bunch number
working horse: Transition Radiation
electromagnetic radiation emitted when a charged
particle crosses boundary between two media with
different optical properties
visible part: Optical Transition Radiation (OTR)
beam diagnostics: backward OTR
typical setup: image beam profile with optical system
→ virtual photon reflection at boundary
(perfect conductivity)
radiation generation
→ reflected and incident
field are the same
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015

## Slide 19: OTR Monitor Resolution
Gero Kube, DESY / MDI
calculation of point spread function in image plane
parameters of calculation
G. Kube, TESLA-FEL Report 2008-01
E = 1 GeV
λ = 500 nm
f = 250 mm
a = b = 500 mm (1:1 imaging)
lens-Ø = 50.8 mm
OTR resolution
resolution definition according to classical optics:
first minimum of PSF (→ diameter of Airy disk)
Ri0
M: magnification
θm: lens acceptance angle
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015

## Slide 20: OTR Monitors at FLASH
Gero Kube, DESY / MDI
Camera
3 Lenses
3 Filters
Mirror
K. Honkavaara et al., Proc. PAC 2003, p.2476
2 Screens
Calibration Marks
Mover
optical system
magnification f / mm a / mm b / mm
1 250 500 500
0.382 200 724 276
0.25 160 800 200
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015

## Slide 21: Example of Beam Images (matched)
4DBC2
6DBC2
10DBC2
8DBC2
1 bunch, 1 nC, Solenoid 277 A, ACC1 on-crest
4.8 mm
6.4 mm
Gero Kube, DESY / MDI
courtesy: K. Honkavaara (DESY)
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015

## Slide 22: COTR and possible Mitigation
Gero Kube, DESY / MDI
R. Akre et al., Phys. Rev. ST Accel. Beams 11 (2008) 030703 H. Loos et al., Proc. FEL 2008, Gyeongju, Korea, p.485.
unexpected Coherent OTR observation during LCLS commissioning
measured spot is no beam image!
strong shot-to-shot fluctuations
doughnut structure
change of spectral contents
courtesy:
H. Loos (SLAC)
interpretation of coherent formation in terms of “Microbunching Instability”
E.L. Saldin et al., NIM A483 (2002) 516
Z. Huang and K. Kim, Phys. Rev. ST Accel. Beams 5 (2002) 074401
G. Stupakov, Proc. IPAC 2014, Dresden, Germany (2014), p.2789.
alternative schemes for transverse profile diagnostics
long term perspective: TR imaging at smaller λ
L.G. Sukhikh, G. Kube, S. Bajt et al., Phys. Rev. ST Accel. Beams 17 (2014) 112805
proof of principle experiment @ λ = 19.6 nm:
additional advantage of better resolution
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015
short term perspective: scintillating screen monitors

## Slide 23: Screen Station for E-XFEL
optical resolution
Scheimpflug observation geometry
10.5 μm average resolution
(dot → optical „step“ function)
Optical Axis
BEAM
f = 180mm for 1:1
f = 120mm for 1:2
Gero Kube, DESY / MDI
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015
200µm thick LYSO screen (on-axis)
2 half 200µm thick LYSO screens (off-axis)
dot grid target(spot Ø .50mm)
monitor setup
BEAM
Optics Axis
FLASH II installation

## Slide 24: Longitudinal Profile Diagnostics
Gero Kube, DESY / MDI
electro-optical (EO) techniques
principle idea:
statement about bunch profile via longitudinal extension of particle bunch Coulomb field
→ good approximation for ultra-relativistic beam energies (1/γ opening angle)
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015
O. Grimm, Proc. PAC 2007, Albuquerque, USA, p.2653
standard method for radiation based bunch length diagnostics
Coherent Radiation Diagnostics (CRD)
long bunch (l<sz)
short bunch (l>sz)
opt. intensity variation → laser + polarizer + analyzer
task:
detection of transient Coulomb field → electro-optical detection in THz region
- imprint influence of Coulomb field onto electro-optical crystal
- convert action in crystal into detectable signal
following 2 talks by Andrii Borysenko and Mateusz Tyrk
st ≈ 100 fsec
st ≈ 30 fsec
Transverse Deflecting Structure (TDS)
intra-beam streak camera
→ potential for sub-fsec resolution
→ access to slice parameters

## Slide 25: RF Cavity Manipulation
Gero Kube, DESY / MDI
Transverse Deflecting Structures (TDS)
iris loaded RF waveguide structure
designed to provide hybrid deflecting modes (HEM1,1)
→ linear combination of TM1,1 and TE1,1 dipole modes, resulting in transverse force that act on
synchronously moving relativistic particle beam
used for beam separators and RF deflectors
Input coupler
courtesy D. Alesini (INFN-LNF)
traveling wave RF deflector ”LOLA-type”
→ SLAC design
standing wave RF deflector
→ SPARC-INFN design
“LOLA”: G.A. Loew, R.R. Larsen, O.A. Altenmueller
G. A. Loew et al., SLAC Technical Report SLAC-PUB-135 (1965)
D . Alesini et al., NIM A568 (2006) 488
L. Ficcadenti, Proc. PAC‘07, Albuquerque, (2007), p.3994
E-field configuration
2π/3 phase shift per cell
2856 MHz (S-band)
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015

## Slide 26: TDS Working Principle
Gero Kube, DESY / MDI
TDS as intra-beam streak camera
electron beam
CCD camera
screen
transverse density distribution
horizontal
vertical
courtesy C. Behrens (DESY)
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015

## Slide 27: TDS Working Principle
Gero Kube, DESY / MDI
TDS as intra-beam streak camera
electron beam
CCD camera
screen
transverse density distribution
horizontal
vertical
vertical
longitudinal
courtesy C. Behrens (DESY)
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015

## Slide 28: TDS Working Principle
Gero Kube, DESY / MDI
TDS as intra-beam streak camera
electron beam
CCD camera
screen
transverse density distribution
horizontal
vertical
vertical
longitudinal
courtesy C. Behrens (DESY)
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015

## Slide 29: TDS Working Principle
Gero Kube, DESY / MDI
TDS as intra-beam streak camera
electron beam
CCD camera
screen
transverse density distribution
horizontal
vertical
vertical
longitudinal
courtesy C. Behrens (DESY)
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015

## Slide 30: TDS Measurements
Gero Kube, DESY / MDI
effect of TDS on observation screen
current profiles with (left) and without (right) magnetic compression
courtesy C. Behrens (DESY)
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015

## Slide 31: TDS Properties
TDS for slice profile (emittance) diagnostics
camera at view screen (OTR) delivers 2D information
→ vertical beam size: bunch length information
→ horizontal beam size: transverse profile information
streaked image
→ transv. profile as function of long. position (slice) ζ
→ access to slice emittance
Gero Kube, DESY / MDI
resolution limit
deflected spot size σdefl equals un-deflected beam size σbeam : σζ → σζ,res = c ∙ σt,res
good resolution:
→ Ψ = 0 zero-crossing for bunch centroid
→ βtds as large as possible for most effective kick
→ ΔΦ 90/270° ideal for phase advance
→ V0 high deflecting voltage (high RF power)
→ fRF high RF frequency
X-band TDS @ LCLS: fRF = 11.424 GHz → σt,res = 1 – 4 fsec (rms)
C. Behrens et al., Nature Communications 5:3762 (2014), DOI:10.1038/ncomms4762
example:
XFEL design parameters for TDS behind first BC
fRF = 3 GHz V0 = 18 MV (P = 45 MW)
βtds = 20 m ε = 1 nm.rad @ 500 MeV
→ σt,res = 10.5 fsec / sinΔΦ
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015

## Slide 32: TDS @ LCLS, FLASH, SPARC, …
Gero Kube, DESY / MDI
low energy TW RF deflector @ LCLS
TW RF deflector @ FLASH
X-band TDS @ LCLS
SW RF deflector @ SPARC
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015

## Slide 33: Beam Synchronous Timing (BST)
Gero Kube, DESY / MDI
BST tasks
T. Korhonen , Proc. ICALEPCS’99 , Trieste, Italy (1999) p.167
generate and remotely distribute phase reference
trigger fast sub-systems
trigger slow systems
interface to the control system
two levels of timing
fast timing → level of individual bunches
slow timing → level of revolution clock (circ. accelerator) or bunch (train) repetition rate (linac)
synchronization
local task → implemented at different clients of timing system
BST building blocks (expected timing jitter)
reference oscillator → phase reference for all sub-systems (≈ ps to fs)
master time-base (event system) → trigger, bunch clock, injection/extraction, experiment triggers (≈ ns to ps)
distribution system (coaxial vs. fiber optics) → phase reference (down to fs ), trigger (100ps to <10ps)
interface to the control system
courtesy M. Ferianis (Sincrotrone Trieste)
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015

## Slide 34: fs-Synchronization System @ FLASH
Gero Kube, DESY / MDI
distribution of synchronization reference
courtesy M. Felber (DESY)
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015
star topology
repetition rate 216.7 MHz
→ 6th subharmonic of accelerator RF
optical reference pulse train
mode-locked Erbium Doped Fiber Laser
long term: < 3.5 fsec
→ rms values, measured out-of-loop with
independent detector
point-to-point stability over several km:
short term: < 1 fsec
Bunch Arrival Time Monitor (BAM)
→ beam based arrival time feedback
applications:
laser synchronisation
→ e.g. pump-probe, seed, injector,…
RF reference stabilization or generation
→ LLRF stability
→ user driven (pump-probe)

## Slide 35: Fiber Link Stabilization
Gero Kube, DESY / MDI
interferometric method
courtesy M. Felber (DESY)
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015
based on balanced optical cross-correlation
→ fast actuator: piezo stretcher
→ coarse actuator: motorized delay
Schulz, S. et al., Nat. Commun. 6:5938 doi: 10.1038/ncomms6938 (2015).
C. Sydlo et. al. Femtosecond timing distribution for the European XFEL, FEL 2014, August 25-29, 2014

## Slide 36: Synchronization System @ FLASH
Gero Kube, DESY / MDI
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015
S. Schulz et al., “Femtosecond all-optical synchronization of an X-ray free-electron laser” Nat. Commun. 6:5938 doi: 10.1038/ncomms6938 (2015).

## Slide 37: Beam-based Arriv. Time Stabilization
Gero Kube, DESY / MDI
Bunch Arrival Time Monitor (BAM)
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015
F. Loehl et al., Phys. Rev. Lett. 104, 144801 (2010)
uncorrelated jitter
over 2000 shots:
8.4 fs (rms)
electro-optical arrival time measurement:
→ < 10 fsec precision (> 300 pCb)
BAMs
FLASH:
Feedback
Feedback
courtesy M.K. Czwalinna, S. Pfeiffer (DESY)
fast feedback to LLRF station before bunch compressor (2 μsec latency, settling within 7 μsec)
arrival time stability:
→ arrival time stabilization to < 20 fsec precision
12 fsec (rms)

## Slide 38: Laser Synchronization
Gero Kube, DESY / MDI
e.g. Ti:Sa pump-probe laser
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015
twofold sum frequency generation in BBO
pure timing sensitive response
courtesy S. Schulz (DESY)
balanced optical cross correlation
balanced detection scheme
elimination of amplitude changes by
subtraction of both detector signals
conventional RF lock:
35 fs rms
optical lock:
6 fs rms

## Slide 39: Laser RF Phase Detector
Gero Kube, DESY / MDI
for RF synchronization or laser-to-RF lock
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015
2.44 fsec integrated jitter
measured out of loop
(10 Hz to 1 MHz)
3.3 fsec peak-peak drift
over 24 hours
courtesy E. Janas (DESY)
T. Lamb et. al. “Femtosecond stable laser-to-RF phase detection for optical synchronization systems”, IBIC 2013

## Slide 40: Summary
Gero Kube, DESY / MDI
many thanks ….
for your attention
to my DESY colleagues M. Felber, D. Lipka, D.Nölle, K.Wittenburg for their help in the preparation
and many stimulating discussions
special thanks to C. Welsch, R. Ashworth for organizing the LA3NET conference and their invitation
overview of diagnostic systems at modern 4th generation light sources
machine parameters and the requirements are challenging
monitor design offers the combination of various fields
lasers in beam diagnostics play important role
fancy monitor concepts
physics → radiation physics, interaction with matter, el.magn. theory, laser technology,…
electrical engineering → analog/digital signals, communication technology, control theory,…
mechanical engineering → material science,…
optical engineering → classical optics, lens design, wave optics, electro-optics,…
IT technology → computer science,…
laser wire scanners, EO techniques, timing and synchronization issues,…
LA3NET Conference, Son Caliu Hotel (Spain), 27. March 2015