## Slide 2: Proposal for ground motion in Point 5
Mechanical Measurements Laboratory M. Guinchard – P. Grosclaude

## Slide 3: Goal of the measurements
    Measure spatial correlation of ground motion (<100 Hz) with geophones between left/right of the cavern
    Measure spatial correlation of ground motion (<100 Hz) with geophones along the triplet positions

## Slide 4: Technique of measurements
    Synchronous ground motion measurements up to 1 km done by optical fibre connection
    Phase shift below 0.1° on the bandwidth between two spectrum analyser
ICP42S G2 features:
• 24-bit resolution, 204.8 kSa/s sampling rate per channel, 90 kHz bandwidth
• <0.1° @ 10 kHz phase accuracy between channels of the same or any other Modules

## Slide 5: Technique of measurements
    Six geophones :
      CMG-T60-0004 from Guralp Systems
      Three directions measurements V, NS and EW
      Sensitivity of about 2000 [V/(m/s)]
      Frequency range between 30 [s] and 100 [Hz].

## Slide 6: Technique of measurements
2 Spectrum Analyzers
3 x 1 km of optical fiber
    Installation in the tunnel (from previous measurements)
Geophones

## Slide 7: Typical measurements in LHC
PHYSICAL REVIEW SPECIAL TOPICS - ACCELERATORS AND BEAMS 13, 072801 (2010)
Seismic response of linear accelerators
C. Collette, K. Artoos, M. Guinchard, and C. Hauviller

## Slide 8: Sensors positions at point 5
    Measure spatial correlation of ground motion (<100 Hz) with geophones between left/right of the cavern
Geophone_54_0
Geophone_54_1
Geophone_54_2

## Slide 9: Sensors positions at point 5
    Measure spatial correlation of ground motion (<100 Hz) with geophones between left/right of the cavern
Geophone_56_0
Geophone_56_1
Geophone_56_2

## Slide 10: Sensors positions at point 5
    Measure spatial correlation of ground motion (<100 Hz) with geophones between left/right of the cavern
Sensors around Q2 should be placed at the same distance of the magnet foot both sides !

## Slide 11: Sensors positions at point 5
Set 2 of measurements
Set 1 of measurements
    Measure spatial correlation of ground motion (<100 Hz) with geophones along the triplet positions
Geophone_54_1 (Reference point)

## Slide 12: Comments
  Geophones at position 0 can be installed before cryogenic filling of the triplets;
  Final positions of the sensors will be adjusted on site depending of the quality of the slab and the position of services;
  Measurement time :
    ½ day to install sensors (left and right of CMS) ;
    One night of measurements
    ½ day to move sensors in 4-5 sector
    One night of measurements
    ½ day to remove equipment
  Measurement cost :
    Measurements between left/right of CMS : 10 460 CHF
    Coherence measurement between Q1 and Q3 : 18 000 CHF