## Slide 1
Magnetic Sweet Spots and the eh Machine Detector Interface
Brett Parker, BNL/SMD
?
eRHIC Q1 Sweet Spot Septum Quadrupole
Schematic of an 80-100 km Long FCC Tunnel at CERN

## Slide 2: Magnetic Sweet Spots & Machine Detector Interface
Review of eRHIC IR design challenges.
Demonstrate the creation of a generic sweet spot coil in a few simple steps.
Review the eRHIC Q1 and B1 magnets as two specific design examples.
Finish up with discussion of some eh IR design challenges / opportunities.
Note to cover these slides in 15 minutes means having to gloss over many details.
Offline discussion is most welcome if this material is of interest to you. 
3
5
2
2

## Slide 3: eRHIC IR Machine Detector Interface Summary
Hadrons
Electrons
Synrad
The hadron beta functions are symmetric but the bending is antisymmetric.
Electron bending comes after the IP in order to avoid synrad background.
IP
Cryostat
Cryostat
Cryostat
Cryostat
Cryostat
Cryostat
Crab Cavities
Crab Cavities
Crab Cavities
Crab Cavities
Warm Quad
Warm Quad
4.5m Region
10 mrad total crossing angle
10 mrad additional electron bending
16 mrad hadron dogleg
16 mrad hadron dogleg has spectrometer function for forward going particles
ZDC
Yellow boxes outline the cold beam tube apertures.

## Slide 4: eRHIC IR Forward Region Layout Details
Note that the coordinate system in these figures is aligned with the center of the 4 mrad neutron cone (neutral vector) indicated by the hatched region on the plot.
Main Beam 3 mrad
4 mrad neutron cone
Q1
Q0
B1
Dp/p = 20% Po
3 mrad
ZDC
Forward
Detector
Roman
Pots
Dp/p = 50% Po
Measure as much as possible before the next cold accelerator region.
Q2, has HERA style “butterfly shape chamber”
Q2 Front

## Slide 5: eRHIC IR, Version 2.5, Forward Layout Details
Strong quadrupole focusing takes place in these, Q1 & Q2 apertures
Strong dipole bending in this B1 aperture
Low field “sweet spot” shielded
regions for incoming electrons in these apertures.
Note that the coordinate system in these figures is aligned with the center of the 4 mrad neutron cone (neutral vector) indicated by the hatched region on the plot.
4 mrad neutron cone acceptance

## Slide 6: Generic Septum Quadrupole Sweet Spot Example
¼ Symmetry Bare Quadrupole Coil
The longest range field external field component from a quadrupole falls off as (Rcoil/R)3.
So the external field “remembers” the size of the coil structure.
Higher order harmonics cause the field magnitude in the vicinity of the coil to be even larger.
The quadrupole coil thickness grows according to ln(Router/Rinner) gradient dependence (high field = thick coil).
For yoke fields more than say 2 T, the yoke saturates and field will leak into cutout regions (cannot hide there).
However, note that there is a zero in the coil field distribution close to the middle of the coil structure.
R = 100 mm
Average R = 55.5 mm
For this figure we plot |#Scaled_B|, the field distribution in the coil structure divided by the maximum field in the coil. At the 100 mm indicated spot #Scaled_B is about -0.2.
B»0 Region
TQS03 Inspired Coil Geometry
G = 230 T/m for this coil & later plots
Bmax Spot

## Slide 7: Generic Septum Quadrupole Sweet Spot Example
¼ Symmetry Simple Sweet Spot Coil
R = 100 mm
Scaled Vertical Field at Coil Midplane
By/BMAX
X, Y (mm)
Linear on the
inside
Reversed in the coil
Now have zero at X=100 mm
Adding the second outer quadrupole coil show here contributes an additional 11% to overall magnetic field efficiency and slightly decreases the peak field.
But now we have created a field reversal “sweet spot” at the desired, X = 100 mm, location.
The field magnitude grows with distance from the zero crossing sweet spot point. It depends on how large the electron region we must shield as to whether or not we can use a passive iron shield for the final field reduction.
High field coil
Low field coil
G = 230 T/m

## Slide 8: Generic Septum Quadrupole Sweet Spot Example
Scaled Vertical Field at Coil Midplane
By/BMAX
X, Y (mm)
Zero field inside the passive iron shield
Adding racetrack coils above and below the desired sweet spot region further enhances magnetic field efficiency and decreases the coil peak field.
But having conductor above/below the region of interest can dramatically reduce local field non-linearities and expand the size of the low-field sweet spot region.
This coil configuration has good field quality with little influence from the passive iron shield. Unlike active shielding, the sweet spot coils have the same polarity for greater efficiency. Optimizing the coil ends is the major remaining challenge.
¼ Symmetry Final Sweet Spot Coil
Racetrack Coil
Racetrack Coil
G = 230 T/m

## Slide 9: Generic Quadrupole Active Shielding Counter Example
Scaled Vertical Field at Coil Midplane
By/BMAX
X, Y (mm)
Reduced efficiency because coils “fight” each other. Efficiency goes as 1 – (R1/R2)4.
There is a net 57% increase in operating current and 14% peak field increase with respect to the previous sweet spot coil.
The good new is that there is now a large external region with very low field.
Having no magnetic material this method works while embedded in detector field.
This coil configuration dramatically reduces the external field at the cost of returning all the flux between the inner and outer coils. Works best with more space between inner and outer coils (original ILC IR). We still need to very carefully optimize the coil ends to avoid large local field overshoot/undershoot.
¼ Symmetry Actively Shielded Coil
R = 100 mm
Small field outside the active shield
New spot for the peak field
Reverse polarity coil
Flux returns between coils
2% increase here
G = 230 T/m
R1
R2

## Slide 10: Generic Quadrupole Yoke Shielding Counter Example
Scaled Vertical Field at Coil Midplane
By/BMAX
X, Y (mm)
Similar peak field to that of sweet spot coil but operating current is now 5% higher.
For 230 T/m, B > 1 T in the cutout region.
Moving cutout region closer to coil will only make things worse!
Could consider making the cutout larger and inserting an active compensation coil? (going this road is full of complications)
For a low field magnet, sending beam through a small cutout is the easiest solution. But this highly saturated yoke is ineffective at shielding field from penetrating into the cutout region. There are also significant transition fields (3d end effects) where the yoke terminates.
¼ Symmetry Coil with Close In Yoke
R = 100 mm
-9% of #BMAX inside cutout
Saturated Yoke
G = 230 T/m
#BMAX = 12 T
Linear on the
inside
Reversed in the coil
Yoke
Yoke

## Slide 11: eRHIC IR Q1 with Sweet Spot Barely Outside Main Coil
Q1 Version 2.5 Parameters
Magnetic Length = 1.975 m
Main Gradient = 136.9 T/m
Field @ e-Beam < Few Gauss
Note that the Q1 sweet spot region comes much closer to the main coil than the previous generic solution.
The Q1 outer coils contribute »36% of the total gradient and the peak field reaches 6.2 T on the inner main coil
Field quality is close to 1 x 10-4 at Rref = 20 mm (i.e. about 1 Unit).
Field inside elongated shielded region is less than 1 gauss in the main body.
These Q1 parameters would be very hard to achieve by any other means.
Q1, Version 2.5 Optics, Full Model
Coil ends do not preserve the body cross section, so we must carefully optimize end turns. Combining magnetic and superconducting materials, “magnetic cloaking,” may be helpful. https://wiki.bnl.gov/eic/index.php/Magnetic_Cloak

## Slide 12: eRHIC IR B1 with Sweet Spot Barely Outside Main Coil
B1 Version 2.5 Parameters
Magnetic Length = 2.9 m
Dipole Field = 4.6 T
Field @ e-Beam < Few Gauss
For those already familiar with the RHIC DX magnet, this is in effect a septum version of that magnet.
Since the external field for a dipole falls off more slowly than from quad, (Rcoil/R)2, and the B1 coil radius is so large, we expected that it would be hard to make the sweet spot this close.
But the slower fall-off led to smaller residual field non-linearity over the sweet spot region and there is no need for any Q1-style racetrack coils.
We are constructing a 1 m long Direct Wind version of the inner coil now in FY’15 using BNL LDRD funding.
B1, Version 2.5 Optics, ¼ Symmetry Model
With a full 3d model we find that because the B1 end-fields change much less rapidly than for Q1, it is much easier to preserve the sweet spot throughout the magnet ends.
Passive, sweet spot shield is located just outside the main coil
Field Magnitude, |B|, Mapping at the coil in Tesla

## Slide 13: Septum Magnet Experience from HERA-II
Beam is off-axis; so if Q1 set is strong enough to focus p-beam, then there should be some deflection seen here.
LHeC (CDR) 60 GeV *7 TeV Interaction Region
HERA-II Septum Quadrupole
LHeC Septum Quadrupole
Magnetic Septum Quadrupoles (MSQ), whether HERA-II (warm) or the LHeC (cold) version, focused beam passes off-axis and is deflected. MSQ aperture is surprisingly limited. Maybe IR sweet spot coil configurations could be useful? And also for pp injection?
Off-axis Beam Spot
Parker et.al.
A sweet spot quad has double the gradient with the same aperture or for same gradient twice as much aperture.

## Slide 14: Experimental Background Experience from HERA-II
FCC-he (ERL) 60 GeV * 50 TeV Interaction Region
Synrad Albedo
Even given a perfectly functioning machine, the early HERA-II luminosity was limited by the tolerable levels of experimental background in the ZEUS and H1 detectors.
The albedo backscatter radiation from sufficiently high critical energy synchrotron radiation is profuse, nearly isotropic and very difficult to collimate close to the detector.
The experiment probably wants some amount of dipole field in the forward/backward directions but maybe we can still keep the e-beam bending as small as possible?
Again using sweet spot coil septum magnet configurations may be helpful for this.