## Slide 1
The new CERN IRRAD Facility and its user infrastructure
Maurice Glaser, Blerina Gkotse, Pedro Lima, Michael Moll, Federico Ravotti
CERN PH/DT, IRRAD Facility Team
… presenting the work of many contributors to the East Area Upgrade construction project at CERN
EN holds the overall projects leadership
Core teams: EA Upgrade Project: D. Brethoux, R. Froeschl, L. Gatignon, M. Lazzaroni, et al.
R2E Project: M. Brugger & J. Mekki, et al.
CERN groups:
EN-MEF and EN-STI (core teams), HSE and EN-HDO (Projects Safety), DGS-RP, EN-CV (EA-IRRAD ventilation), EN-HE (exp. areas transports), GS-ASE (access control), BE-BI and TE-CRG (EA-IRRAD cryogenic system), …
AIDA Final Meeting @ CERN

## Slide 2: Contents
Overview (and evolution) of Irradiation Facilities at CERN
PS East Area Irradiation Facilities until 2012
New PS East Area Irradiation Facilities (EA-IRRAD)
  IRRAD Proton Facility
  CHARM Mixed-Field Facility
  IRRAD Proton Facility Layout
Conclusion

## Slide 3: CERN Irradiation Facilities until 2012
Proton Energy
LHC 7 TeV
SPS 450 GeV
PS 23 GeV
PSB 1.4 GeV
Linac 50 MeV
SPS: CERF CERN Reference Facility mixed-field
CNRAD mixed-field test area (parasitic operation)
SPS: H4IRRAD mixed-field test area
PS: IRRAD proton & mixed-field facilities, 24 GeV/c, slow extraction
HiRadMat proton test area, 440 GeV, fast extraction
GIF Gamma Irradiation Facility (no more particle beam)
(West Area)

## Slide 4: CERN Irradiation Facilities from 2014
Proton Energy
LHC 7 TeV
SPS 450 GeV
PS 23 GeV
PSB 1.4 GeV
Linac 50 MeV
SPS: CERF CERN Reference Facility mixed-field
PS: IRRAD & CHARM proton & mixed-field facilities, 24 GeV/c, slow extraction
SPS: GIF++ new GIF with muon beam
HiRadMat proton test area, 440 GeV, fast extraction

## Slide 5: PS-EA Irradiation Facilities until 2012
24 GeV/c protons
Mixed-field irradiations (T8)
  Mixed field produced in cavity after C (50cm) - Fe (30cm) - Pb (5cm) ‘target’ (IRRAD2)
from 1992 - until 2012
Proton irradiations (T7)
  Primary 24 GeV/c proton beam (IRRAD1, IRRAD3, IRRAD5, …)
157
24 GeV/c protons
PS
13
slow-extraction
(~400ms)

## Slide 6: Proton Irradiation Facility (2012)
  Beam spot
  12×12 mm2 (FWHM)
  Beam momentum
  24 GeV/c
  Proton flux
  ~1×1016 p  cm-2 20days-1
  (year average)
p+ (T7)
Iron DUMP
Counting Room
IRRAD3, IRRAD5, … Tables
p+
Radiation Shielding
IRRAD1 Shuttle
40×25cm2, ~15m length

## Slide 7: IRRAD1 Shuttle & IRRADx Tables
IRRAD1 Shuttle
Vmax=5×5×15cm3
IRRAD3 & IRRAD7 Tables
Vmax=20×20×50cm3
scanning over surface

## Slide 8: Mixed-field Irradiation Facility (2012)
Secondary particles in a cavity (IRRAD2)
  24 GeV/c proton beam on a C/Fe/Pb target
  Small volume (max ~30×30×30cm3) behind DIRAC
  Spectrum & flux of n, p+, p+, p-, g simulated & measured
  ~1×1013 n(E>1MeV) cm-2 5d-1 @ 50cm from beam axis
IRRAD2 Shuttle
p+
Particle flux at 10cm [CMS-IN-2001/012]

## Slide 9: Past Irradiation Experiments
     IRRAD user community!

## Slide 10: Past Irradiation Experiments
     IRRAD user community!
IRRAD facilities in numbers …
  from 1999 to 2012 (no beam in 2005)
  more than 8300 “pieces” irradiated (~650 per year)!
  about 5800 dosimeters (Al foils) measured!
  Statistics for 2012 …
  40 users
  from 20 institutes belonging to several experiments/projects
  main users: ATLAS, CMS, LHCb, ALICE, RD39, RD50, LHC (BE and TE)
  649 objects irradiated
  358 dosimeters measured
  223 days of beam time (~8.5×1016 protons delivered to IRRAD)

## Slide 11: Drawbacks & Shortcomings
Proton IRRAD Facility
  Located in primary radiation area (limited access: stop all beam lines of East Area for access)
  Limited space (ALARA, difficult to scan beam over big objects, backscattered particles)
  Limited flux of primary protons (weakness of the shielding)
  Safety standards to be improved!
Mixed-field IRRAD Facility (behind DIRAC)
  No irradiation positions lateral to target (missing an important ‘particle mix’ component)
  Limited intensity (present flux not interesting for inner detector community)
  Too little space and limited accessibility (access only via shuttle system!)
  Parasitic to DIRAC operation
IRRAD Facilities were located in different beam lines: competing for beam!
(of the old facilities / test areas with respect to future needs)
Mixed-field H4IRRAD/CNRAD Test Areas
  CNRAD not operational after 2012
  Limited accessibility (“ad-hoc installations”, lack of flexibility, access required shielding removal)
  Limited control on beam intensity

## Slide 12: Towards a new EA Irradiation Facility
July 2013: dismantling DIRAC & old IRRAD1 and IRRAD2 Facilities
Nov. 2013: removal of IRRAD2 target & beginning of construction
    R2E project: Cern High-energy AcceleRator Mixed-field facility (CHARM)
    CERN-PH & AIDA: proton IRRADiation facility (IRRAD)
10 Oct. 2014: first pilot beam in the new EA-IRRAD facility for commissioning
17 Nov. 2014: first irradiation experiments
  19 Nov. 2012: first technical meeting on upgrade
    R2E project (LHC machine): Mixed-field facility & infrastructure design
    CERN-PH & AIDA: Proton facility & infrastructure design
2012: CERN management agrees on EA facilities upgrade
  CERN-EN is charged and funded to design and construct the irradiation beam line in the framework of the EA renovation plan during LS1 (PL: Lau Gatignon)
  CERN-PH through AIDA EU FP7-funded project (Task 8.3)
26 Nov. 2012: last day of operation for the DIRAC experiment

## Slide 13: OLD East Area Layout
157
13

## Slide 14: NEW East Area IRRAD Layout
Proton Facility
(IRRAD)
Mixed-field Facility
(CHARM)
T8 beam line
Beam dump
     drawings provided by EN-MEF

## Slide 15: 24 GeV/c Proton Beam Parameters
Here dimensions are mm (RMS)
Beam dimensions
  several optic variants possible on T8
  standard size: 12x12 mm2 (FWHM)
  spot size from 5x5 mm2 to 20x20 mm2 (FWHM)
Beam intensity (estimations)
  p+ are delivered in “spills” of ~5×1011 p
  number of spills/frequency depends on CPS
  Typical CPS from 2014: 30s
  Typical figures (High Intensity): 3 spills per CPS
    ~1  1016 p cm-2 5days-1 (12x12 mm2 FWHM)
    ~4x more than the old facilities
  Design figures (maximum): 6 spills per CPS
    ~1  1017 p cm-2 4days-1 (5x5 mm2 FWHM)
IRRAD
CHARM
     L. Gatignon, preliminary calculations (EDMS 1270807)

## Slide 16: Ventilation System
Ventilation system (CERN EN/CV)
  area confinement (under-pressure) for air activation, ozone formation, temp. control, etc.
  air re-circulated during operation (through filters) and flushed before access
  integration of ducts through the shielding:
Ventilation Ducts
Ventilation Unit
     drawings provided by EN-MEF

## Slide 17: Proton IRRAD Facility (PH)
24GeV/c p+
Chicane
Counting Room
Zone 1
Zone 2
Zone 3
Shuttle System
Access
Point
Cryogenic System
detectors
electronics
calorimeter
samples
Zone 4
partially shielded
     drawings provided by EN-MEF

## Slide 18: Proton IRRAD Shuttle System
mainly “passive” samples
possibility to irradiate samples under bias

## Slide 19: IRRAD Remote-controlled Tables
  3 tables per IRRAD zone; DUTs powered and cooled
  1 stand-alone control unit per table (on UPS)
Temp. Control: -20 ºC / 40 ºC
q
x
y
beam
  prototype (AIDA MS31)
Temp. Control: -20 ºC / RT
Vmax=10×10×30cm3
  cold boxes from AIDA (WP8.3.2 QMUL/Sheffield)

## Slide 20: IRRAD Beam Instrumentation & DAQ
New Beam Position Monitors (Metal Foil Detectors)
New Web-application
  display Beam Profile Monitor data (for IRRAD users and CERN CCC)
  new database for data storage (ORACLE); can display multiple BPM devices
  flexible display also for other IRRAD data: SEC counters, table/shuttle positions, T., …
 E. Matli (BE-OP)
BPM Display

## Slide 21: “CryoBLM” Setup
Setup for irradiation in cryogenic conditions (1.8K/4.2K)
  clone of the system used for “CryoBLM” (BE-BI) experiment in 2012
  cryogenic line “embedded” in the shielding; bigger cryostat
Cryogenic system operated by TE-CRG
  manual refilling; dewar outside rad. area
  installed on a movable irradiation table
p+
     Bernd Dehning (BE-BI)
    Marcin Ryszard Bartosik (BE-BI)
    Christoph Kurfuerst
    Thomas Eisel and TE-CRG
Samples position

## Slide 22: New IRRAD Facility
Counting Room
Zone 2
Zone 1
Zone 4
Zone 3

## Slide 23: East Area EA-IRRAD Infrastructure
IRRAD1B
Buffer Zone
Storage Area
Counting Rooms
24GeV/c p+
IRRAD
CHARM
     drawings provided by EN-MEF

## Slide 24: Proton IRRAD Infrastructure
Fixed cabling/piping infrastructure
  4 Patch-Panels installed along IRRAD
  twisted-pairs, coaxial, power HV/LV, …
  space for custom users-cabling
  (optical fibers, etc..)
Storage area
  shielded zones for cool-down and storage at room and low temperature of IRRAD (and CHARM) irradiated equipment
  workspace to handle and perform (setup) measurements on irradiated equipment
IRRAD1 B
Workspace
RP Buffer Zone
Storage Areas
Chillers
Cables length from ~13m to ~20m

## Slide 25: Mixed-field CHARM Facility (EN)
Hot
Buffer
Zone
Movable Target
Beam
Catcher
Movable
shielding
Access chicane
Cablings
Beam dump
24GeV/c p+
Conveyer path
Contacts
  www.cern.ch/charm
    Markus.Brugger@cern.ch (EN-STI)
    Julien.Mekki@cern.ch (EN-STI)
     drawings provided by EN-MEF

## Slide 26
EA-IRRAD Aerial View
Proton Facility
(IRRAD)
Mixed-field Facility
(CHARM)
T8 beam line

## Slide 27: Summary
  New EA-IRRAD facility is now being commissioned (fully operational in 2015)
  Experimental community (PH): Proton facility (IRRAD)
  Accelerator community (EN): Mixed-field facility (CHARM)
  IRRAD Proton Facility in 2014
  2 Tables operational (no cooling): IRRAD 7 & IRRAD 9
  Limited time/space (16 experiments registered!)
  More to come in 2015
  IRRAD1 Shuttle System
  Additional tables, cooling systems
  Users space for testing irradiated samples
  Storage area being assembled
  …
  New web-site
  www.cern.ch/ps-irrad

## Slide 28: Ongoing Experiments
CryoBLM experiment (IRRAD15)
Small samples (IRRAD7)
Detector Prototypes (IRRAD9)