## Slide 1: Coping with Emittance Measurement Challenges in the LHC after LS1
Gentner Day October 2014
An Overview of Control and Data Flow Related to LHC Emittance Measurements
Maria Kuhn – October 15, 2014

## Slide 2: My Background
Accelerator physicist from University of Hamburg
  Technical student at CERN in 2012
Enrolled in the Gentner Program since May 2013
Working in BE-OP-LHC:
Emittance Preservation at the LHC

## Slide 3: CERN Accelerator Complex
Beam 1
TI2
Beam 2
TI8
LHC proton path
The LHC needs most of the CERN accelerators...

## Slide 4: The LHC Timeline
After a successful LHC Run 1 the machine is currently shut down until 2015
  Now preparing for LHC Run 2
2013
2008
2009
2010
2011
Sept 10, 2008
First beams around
Sept 19, 2008
Disaster Acci- dental release of 600 MJ
November 7, 2010
First ion collisions
March 30, 2010
First collisions at 3.5 TeV
1380
June 28, 2011
1380 bunches
2012
July 4, 2012
Higgs like discovery
March 14, 2013
Higgs discovery
2014
Long Shutdown 1 (LS1) until 2015
After LS1:
Higher collision energy (6.5 TeV)
October 8, 2013
Nobel Price
March 13, 2012
First collisions at 4 TeV
Sept 13, 2012
First p - Pb collisions
2015
March 2015
LHC Restart

## Slide 5: The LHC Layout and the LHC Cycle
2012 LHC cycle:
4 TeV collision energy
11 to 0.6 m b* squeeze at ATLAS/CMS
50 ns bunch spacing
1380 bunches per beam
Injection energy: 450 GeV
Collisions in 4 points in the LHC. ATLAS & CMS are the 2 large multi purpose detectors.
2015 LHC cycle (preliminary):
6.5 TeV collision energy
Longer ramp (~ 20 min)
25 ns bunch spacing
More bunches in the machine (~ 2800)

## Slide 6: Introduction: Luminosity
Performance of a collider is measured in luminosity
  Combines cross section and number of interactions per second
    Assuming two identical Gaussian shaped beams that collide head on
To maximize luminosity a small transverse emittance is needed!
Injectors produce high brightness beams with small emittances.
Goal: preserve emittance in the LHC!
  In 2012 the emittance could not preserved during the LHC cycle
  Sources and solutions of emittance blow-up could only partly be tackled due to problems with beam instrumentation
k …. Number of bunches
N …. Number of protons per bunch
f …. Revolution frequency
g …. Relativistic gamma (beam energy)
F …. Luminosity reduction factor
b*…. Beta function at interaction point
e …. Normalized transverse emittance

## Slide 7: Transverse Emittance
Normalized transverse emittance:
b function is measured during the LHC cycle
Transverse profiles are obtained for instance from wire scanners
  A carbon wire passes through the beam and measures the bunch-by-bunch transverse profiles
  In the LHC: 4 operational wire scanners B1H, B1V, B2H, B2V
dispersion negligible
Amplitude [a.u.]
Position [μm]
Beam parameter: beam size from Gaussian fit to transverse profile (5 parameter Gauss fit)
Machine parameter: b fct. at location of profile monitor
Beam energy
(at location of transverse profile monitors in the LHC)

## Slide 8: LHC Wire Scanner
Voltage on wire
Device properties accessed by the operator in the control room
Acquired data displayed in the control room

## Slide 9: Operational Tools
An operator in the control room needs a tool to communicate easily with the wire scanner  wire scanner application
Objectives:
Set scanner properties: voltage on wire and optical filter
Perfom scan
Constantly monitor the status of the wire scanners
  Wire position and voltage, filter, ...
Acquire scan data
  Display transverse profiles
  analyse scans: fit profiles
Send data to logging DB and LHC logbook
Get data from logging DB
...

## Slide 10: Control System and Data Acquisition
BE-CO maintains CERN accelerator control system
Controls software infrastructure:
Front End Layer (FE)
Business Layer
Presentation Layer
General purpose and specific application servers
 accelerator control, monitoring & diagnostics, machine protection
Device servers
 equipment integration
Graphical interactive applications, fixed displays
Wire scanner in the LHC ring
Wire Scanner Application

## Slide 11: CERN Control Center – LHC Island
Fixed Displays
Operational Consoles

## Slide 12: Fixed Display: LHC Page 1

## Slide 13: Control and Data Flow
Front End Layer (FE)
Business Layer
Presentation Layer
LHC Software Architecture (C/C++)
 Settings management system
Front End Software Architecture (FESA)
Integrates the equipment into control system
CCC applications (Java)
Wire scanner in the LHC ring
Application:
Set properties
Get information

## Slide 14: Key Points For LHC Applications
User friendly applications
  No expert knowledge needed
  Everyone in the control room should be able to use it
Time is precious
  Be prepared – know “good” wire scanner settings
  Setting scanners and performing scans needs to be quick
Online analysis
  Quality of measurements can be judged immediately
Avoid breaking wires!
  Cannot extensively use wire scanners
  Only scan at low intensity (very few bunches in the machine)
Do not disturb the beam or cause beam dumps!
  Application needs to be linked to machine protection

## Slide 15: Wire Scanner Application
Main improvements:
Load settings for certain scenarios
  To avoid saturated profiles
Monitor wire position, voltage and filter
  Display saturation information
Scanners are launched automatically in series, multiple scans possible
Online analysis

## Slide 16: Summary & Conclusion
Working in LHC operations is challenging but very interesting
Problems with measuring beam sizes and beta functions dominated the emittance analysis in 2012
  The transverse normalized emittance was not preserved during the LHC cycle in 2012!
  Not all causes for emittance blow-up could be discovered and eliminated
During LS1 intensive work was done to improve transverse profile monitors and beta function measurements
  Improved algorithms
  New operational applications
    Simplifies operation of the devices
    Shorter measurement periods
    Online analysis
We are well prepared for emittance measurements in 2015!

## Slide 17: Additional Slides

## Slide 18: Reminder: Emittance Preservation
Liouville’s Theorem:
  Normalized emittance is conserved during acceleration!
Effects that can cause emittance growth (in a hadron collider):
  Mismatch at injection
  Intra beam scattering (IBS)
  Noise
  Instabilities
  Coupling between horizontal and vertical plane
  Collective effects, e.g. electron cloud, impedance
  Beam-beam effects
  Wake fields
  Space charge effects
  …

## Slide 19: Previous Problems and Improvements
Problems | Improvements
Saturated profiles Wire voltage and photomultiplier filters influenced the measured beam size | Monitor wire voltage and filter Have saturation information displayed before the scan
Voltage and filter always set manually Operators didn‘t know „good“ settings | Load settings for certain scenarios To avoid saturated profiles
Every scanner was launched individually Time consuming | Scanners are launched automatically in series, also multiple scans possible
Offline analysis | Online analysis Time evolution of scans, fitting, saturation information