## Slide 1: Introduction to Proton Therapy JAI Octoberfest, 3rd October 2014
Claire Timlin
Particle Therapy Cancer Research Institute, University of Oxford

## Slide 2: Introduction to Radiotherapy and Proton Therapy

## Slide 3: The Evolution of External Beam Radiation Therapy
High resolution IGRT
Multileaf Collimator
Dynamic MLC
and IMRT
1950’s
1970’s
1980’s
1990’s
2000’s?
Cerrobend Blocks Electron Therapy
Functional
Imaging
The First Cobalt Therapy Unit and Clinac
Computerized 3D CT Treatment Planning
Standard Collimator
Particle
Therapy
Slide courtesy of Prof. Gillies McKenna
Notes: Key points to make:
Completely new carriage and leaf design to
Other improvements made:
Reduced Head Diameter by 10 cm from previous “Standard” MLC

## Slide 4: Goal of RT
Radiation Induced Toxicity:
  Central Nervous System: blindness, deafness, paralysis, confusion, dementia
  Bowel: colostomy, chronic bleeding.
  Lung: shortness of breath, pneumonias
  Kidney: renal failure and hypertension
  Reproductive organs: sterility
  Everywhere: severe scarring in medium to high dose regions, possible increase in induced cancers in low-medium dose regions
Maximise Tumour Dose
Minimise Normal Tissue Dose

## Slide 5: Photons/X-rays dose deposition
Depth-dose curve – single beam
Multiple Beams:
Reduced dose to organs at risk
  Fewer complications
Increased tumour dose
  Higher probability of tumour control
However:
  Large volumes of low-intermediate dose
RT dose plan – multiple beams beam

## Slide 6: History of Proton Therapy
1946: Therapy proposed - Robert R. Wilson, Harvard Physics
1955: 1st Proton Therapy - Lawrence Tobias University of California, Berkeley
1955-73: Single dose irradiation of benign CNS lesions - Uppsala, MGH, St Petersburg, Moscow

## Slide 7: The Bragg Peak
Components of the proton depth dose curve:
  Bethe-Bloch formula
    Coulomb interactions with atomic electrons
  Scattering, energy spread and interactions with atomic nuclei
Illustrations from M. Goitein “Radiation Oncology: A Physicist’s-Eye View” © Springer, 2007
Dose
Depth

## Slide 8: Proton dose deposition
Incident energy is modulated to form Spread Out Bragg Peak the cover the tumour
Unnecessary dose
Unnecessary dose
The Daily Telegraph Australia

## Slide 9: Medulloblastoma in a Child
100
60
10
X-rays
With Protons
With X-rays

## Slide 10: Orbital Rhabdomyosarcoma
Courtesy T. Yock, N. Tarbell, J. Adams
X-Rays
Protons/Ions

## Slide 11: Proton Therapy in Action Anaplastic Ependymoma Brain Tumour http://news.bbc.co.uk:80/1/hi/england/7784003.stm http://news.bbc.co.uk/1/hi/england/7795909.stm http://news.bbc.co.uk/1/hi/england/7906084.stm
CPC, Friedmann, NEJM, 350:494, 2004
Pre-treatment
During-treatment
Post-treatment
Slide courtesy of Prof. Gillies McKenna

## Slide 12: Number of treatment centres worldwide
> 93,000 patients
> 10,000 patients
Protons:
40 operational,
~ 40 in development
carbon:
8 operational,
4 in development

## Slide 13: Proton Therapy Centre World Map
Protons - low energy
Protons – high energy
Carbons
Notes: Philadelphia

## Slide 14: Proton Therapy Centre Europe Map
Protons - low energy
Protons – high energy
Carbons

## Slide 15: Many more in the planning stages….

## Slide 16: Proton Therapy in UK
Clatterbridge
  1989: First hospital based proton therapy at Clatterbridge, near Liverpool
  ~2500 patients with ocular melanoma; local control ~97%.
  Targets the cancer
  Avoids key parts of eye (optic nerve, macula, lens)
Simon to talk about UCLH and Manchester….

## Slide 17: Production and Delivery of Medical Proton Beams

## Slide 18: Beam Production and Acceleration
Ion source
  Plasma accelerated in electric field
Acceleration
  Cyclotron
    Fixed magnetic field
    Fixed energy
    Constant frequency
  Synchrotron
    Fixed radius
    Variable magnetic field
    Synchronous frequency
  Future accelerators that do the job better?
HIT, Germany
Notes:   Hydrogen gas
  Plasma created via interaction with electrons form cathode

## Slide 19: Beam Transport
Gantries
Fixed Beams
Clinical Indications
Flexibility
Space
Cost

## Slide 20: Beam Delivery - Scattering
Courtesy of T. Lomax, PSI, Switzerland.

## Slide 21: Beam Delivery - Scanning
  Exploiting depth control
  Exploiting charge
Beam direction
Beam direction
Patient
Patient
Target
Target

## Slide 22: Some challenges in Proton Therapy
Acceleration and Beam transport:
  Faster spot scanning
  More compact accelerators and gantries
  Beam switching and splitting
Uncertainty in planned vs. delivered dose:
  Range uncertainties
  Relative biological effectiveness
Treatment delivery
  Organ motion
  Hypo-fractionation
Which clinical indications?
  Cost-effectiveness
  Ethics
Lack of data and models to predict late effects e.g. second cancers

## Slide 23: Some possible solutions
Accelerator development
Radiobiological modelling and experiments
Advanced treatment planning and delivery techniques
  Novel, high resolution, minimally damaging imaging
  Dose validation/online dosimetry
Consistent data recording and data sharing
Clinical studies with long-term follow-up

## Slide 24: University of Oxford’s hope for Protons

## Slide 25: Targeted cancer treatment pathway
Early Stage Cancer Patient
Molecular Stratification
Precision Cancer
Medicine Institute
Big Data
Institute
Oxford Cancer Imaging Centre
Structural
Genomics
Consortium
Population Health Science
Experimental Cancer Medicine Centre
Increased Cures
Target Discovery Institute
Courtesy of Gillies McKenna

## Slide 26: Precision Cancer Medicine
Physically Targeted
  Robotic Surgery
  Proton Therapy
  HIFU
Physiologically Targeted
  Molecular Imaging
Molecularly Targeted
  Deep Genomic Sequencing
  Biomarker Driven
  Biologically targeted
Courtesy of Gillies McKenna

## Slide 27
Oxford Precision Medicine Institute
Genomics
Particle Therapy
Robotic Surgery
Functional and Molecular Imaging
Targeted
Agents
Courtesy of Gillies McKenna

## Slide 28: The Evolution of Cancer Therapy
1980 1990 2000 2010 2020
Molecular Imaging
Nanotechnology
Proton
Therapy
Robotics
HIFU
CT, MRI,
PET
Targeted
Agents
(CF3)180
Genomics
Courtesy of Gillies McKenna
Increased Effectiveness, Reduced Toxicity

## Slide 29
Thank you….
            ……….any questions?

## Slide 30: Extra Slides

## Slide 31: Induction and cell kill
Induction
Cell killing
What is the form of the induction function? Linear, quadratic?
Form of cell killing function known with some certainty at clinical energies, the parameters are tissue dependent and can have large uncertainties.
Risk needs to be
  accurately modelled
  confirmed experimentally
  taken into account when deciding on the optimal treatment plan
Probability of transforming a cell
Probability of inducing a potentially malignant mutation
Probability the cell survives

## Slide 32: Second cancer risk
IMRT
IMPT

## Slide 33: Second cancer risk
IMRT
IMPT

## Slide 34: Multiscale, voxelised TCP calculation for GBM
Cell Level
Voxel Level
Patient Level
Cellularity
Tumour microenvironment: P02
Genetic heterogeneity: Stem vs. non-stem
Dose matrix
Structure matrix
Post treatment CCD
Tumour recurrence time
Clinical Data
Number of fractions
Radiobiological parameters e.g. ,
Treatment plan DICOM files
Cell automaton model
Pre-treatment clonogenic cell density (CCD)
Predicted TCP

## Slide 35: Relative Biological Effectiveness
Photons and protons (at clinical energies) have similar biological effects
  Clinically a modifier (RBE) of 1.1 is applied to physical dose for protons
For heavier ions (e.g. C) RBE has large uncertainties
RBE needed* to calculate physical dose to administer to achieve prescribed biological dose
*maybe there is a better way?
New treatment regimes requiring new methods of optimisation?

## Slide 36: RBE vs. Dose for Protons
Paganetti et al.: Int. J. Radiat. Oncol. Biol. Phys. 2002; 53, 407
Where does the 1.1 come from?