## Slide 1: CGBM Data Transfer/Handling and Reduction
Taka Sakamoto, Satoshi Nakahira,
Kazumasa Senuma
On behalf of CGBM team

## Slide 2
Scheme of CGBM Data Flow

## Slide 3
CALET
JAXA Tsukuba Space Center
Level 1 Data
Waseda CALET Operations Center
Once an hour
Real time downlink (~70%)
Gamma-ray burst Coordinated Network (GCN)
CGBM Real time Data Analysis (prepare by AGU)
Real time
On-board trigger
Ground trigger
Level 0 Data
Light curve data (WCOC server)
Data server
Level 0 data
Raw data
Trigger information
TH data
Level 2 Data
Level 3 Data
CGBM institutions
Level 1.1 Data
Raw
Data

## Slide 4
CALET
JAXA Tsukuba Space Center
Level 1 Data
Waseda CALET Operations Center
Once an hour
Real time downlink (~70%)
Gamma-ray burst Coordinated Network (GCN)
CGBM Real time Data Analysis (prepare by AGU)
Real time
On-board trigger
Ground trigger
Level 0 Data
Light curve data (WCOC server)
Data server
Level 0 data
Raw data
Trigger information
TH data
Level 2 Data
Level 3 Data
CGBM institutions
Level 1.1 Data
Raw
Data

## Slide 5
CALET
JAXA Tsukuba Space Center
Level 1 Data
Waseda CALET Operations Center
Once an hour
Real time downlink (~70%)
Gamma-ray burst Coordinated Network (GCN)
CGBM Real time Data Analysis (prepare by AGU)
Real time
On-board trigger
Ground trigger
Level 0 Data
Light curve data (WCOC server)
Data server
Level 0 data
Raw data
Trigger information
TH data
Level 2 Data
Level 3 Data
CGBM institutions
Level 1.1 Data
Raw
Data

## Slide 6
Plan for GRB alerts

## Slide 7: Gamma-ray burst Coordinated Network (GCN)
Gamma-ray burst Coordinated Network (GCN)
Swift
Fermi
MAXI
Etc.
Radio telescope
IR telescope
Optical telescope
X-ray telescope
TeV telescope
Within a few second to a few minutes after the trigger
Follow up observations start a few minutes up to days after the trigger
CGBM must contribute this part
GRB detection by spacecraft
Follow-up observation from space and ground
All the big discoveries of GRBs can not be achieved without GCN!

## Slide 8: Status of Currently operating GRB instruments
 | Automatic distribution | Delivering Products | Distribution
MAXI | Y | Trigger time, Position | GCN
Fermi | Y | Trigger time, Position | GCN
Swift | Y | Trigger time, Light curve, Position | GCN
INTEGRAL | Y | Trigger time, Position | GCN
Konus-Wind | Y | Trigger time, Light curve | GCN
Suzaku | Y | Trigger time, Light curve | GCN
AGILE(*) | Y | Trigger time, Position | GCN
All the currently operating GRB instruments deliver the alert through GCN automatically (no-human-in-the-loop)

## Slide 9: CGBM Trigger Alert (1)
On-board triggered event (CGBM: Flight GRB Notice)
Ground triggered event (CGBM: Ground GRB Notice)
(Running the ground triggering code on TH data in near real-time)
Contents (plan):
GRB trigger time (UT)
GRB trigger number
ISS Location
Trigger significance (sigma)
Foreground integration time (s)
Background integration time (s)
Energy band
Note: we only obtain “triggered flag” info from the real-time data (raw data) for the on-board trigger.
Goal: Within 10 seconds after the event

## Slide 10: CGBM Trigger Alert (2)
Publically available CGBM Light curve
Put the CGBM light curve data from T0-50 s (TBD) to T0+300 s (TBD) using TH data for the triggered events at the publically accessible web page
png or jpg image and ascii data of the light curve
Single energy band light curve (HXM and SGN)
Three different time resolutions (e.g., 0.125 s, 1.25 s, 12.5 s)
ascii data in 0.125 s resolution in single energy band
Web site: WCOC public web page
Goal: Within 10 minutes after the event

## Slide 11: Real-time Telemetry of ISS
Example of MAXI
Frequency distribution
Data completeness
~75% of real-time data (black) within 10 second delay
101
102
103
104
105
100
Time Delay(s)

## Slide 12: Current Status
Done:
Delivered two CGBM computers (GRB alert and QL) to WCOC
Sign-up for the GCN socket connection account
Need to be done:
“Receive only” socket connection test with GCN
Software to extract required info from the raw data
Communication with GCN (Scott Barthelmy) to finalize the GCN Notice format
“Receive and send” packet test with GCN

## Slide 13
Current Status of Software

## Slide 14: CGBM Data Format
CGBM analysis data are in FITS (Flexible Image Transport System) format.
  Following the standard FITS format to be able to use already available software
  Easy for archiving the data in a future (e.g., NASA/GSFC HEASARC archives the data in the FITS format)
(FITS is a standard data format in astronomy community)

## Slide 15
Level 1 binary Data (@ Waseda CALET Operations Center)
Level 2 FITS file
(C) Event data FITS conversion
(D) TH data FITS conversion
(E) PH data FITS conversion
(A) Aspect data FITS conversion
(a) Time conversion
New
New
New
New
Reuse MAXI library
Reuse MAXI library
ISS information
Inst FOV, etc.
(B) HK data FITS conversion
New
FITS aspect file
FITS HK file
FITS event file
FITS TH file
FITS PH file
(F) PI column conversion
Energy calibrated FITS event file
(G) Energy conversion PHA rebin
Energy calibrated FITS PH file
Level 2 FITS file
New
New

## Slide 16: Level 3: Light curve file

## Slide 17: Level 3: PHA (spectral) file
- Energy response FITS file

## Slide 18: 1. CGBM Event FITS Conversion
- Python (pyfits, numpy)
Sensor
0 : HXM1 1 : HXM2 2 : SGM
TIME
PHA_HIGH
PHA_LOW
TIME
S
PHA_HIGH
CHANNEL
PHA_LOW
CHANNEL
Input: ascii file (PI calibration’s trigger test)

## Slide 19: 1. CGBM Event FITS Conversion
> ~/work/CALET/cgbm_tool/fits_conversion_ver2.py cgbm_evt_good.txt
> ls
cgbm_evt_good.txt cgbm_evt_good.txt_hxm2.evt
cgbm_evt_good.txt_hxm1.evt cgbm_evt_good.txt_sgm.evt
> extractor cgbm_evt_good.txt_hxm1.evt NONE timefile=NONE gti=GTI imgfile=NONE phafile=NONE fitsbinlc=cgbm_1s_hxm1.lc binlc=1.0 regionfile=NONE gtinam=GTI xcolf=NONE ycolf=NONE tcol=TIME ecol=PHA_LOW xcolh=NONE ycolh=NONE
> extractor cgbm_evt_good.txt_hxm1.evt NONE timefile=NONE gti=GTI imgfile=NONE phafile=cgbm_low_hxm1.pha fitsbinlc=NONE regionfile=NONE gtinam=GTI xcolf=NONE ycolf=NONE tcol=TIME ecol=PHA_LOW wtmapb=no

## Slide 20: 1. CGBM Event FITS Conversion
cgbm_1s_hxm1.lc
Light curve and spectrum created by standard ftools “extractor” from CGBM FITS event file
cgbm_low_hxm1.pha

## Slide 21: 2. Light curve background subtraction
- Python (pyfits, numpy)
Interactive tool:
Input FITS light curve
Specify a burst interval
Automatic polynomial fit (1-5 orders)
Background subtracted FITS light curve
Raw FITS light curve
Background subtracted
FITS light curve

## Slide 22: 3. Background PHA file
- Input event FITS data
Input background subtracted FITS light curve
Fit the multi-channel light curves using the same burst interval and the order of polynomial function.
Estimate the background counts for each channel.
Write the results to the FITS PHA file.
Background spectrum

## Slide 23
4. Gain Correction
Currently under development….
1.4 MeV = 1007 ch @26℃
1.4 MeV = 1624 ch @ -28℃
Count
Count
Channel
Channel
SGM BBM: ISAS thermal vacuum test data
Instrument’s gain changes due to the temperature variation.
Python script to find a peak channel from the background spectra

## Slide 24: 4. Gain Correction
Currently under development….
Peak channel of 1.4 MeV
Investigating the coefficient of heat transfer between thermocouple and the temperature of crystal.

## Slide 25
Level 1 binary Data (@ Waseda CALET Operations Center)
Level 2 FITS file
(C) Event data FITS conversion
(D) TH data FITS conversion
(E) PH data FITS conversion
(A) Aspect data FITS conversion
(a) Time conversion
New
New
New
New
Reuse MAXI library
Reuse MAXI library
ISS information
Inst FOV, etc.
(B) HK data FITS conversion
New
FITS aspect file
FITS HK file
FITS event file
FITS TH file
FITS PH file
(F) PI column conversion
Energy calibrated FITS event file
(G) Energy conversion PHA rebin
Energy calibrated FITS PH file
Level 2 FITS file
New
New
Done
Working

## Slide 26: Level 3: Light curve file
Done

## Slide 27: Level 3: PHA (spectral) file
- Energy response FITS file
Done

## Slide 28: Future Plan
Development of FITS converter as the highest priority
Provide the example of CGBM FITS files and developed software to the team
We will communicate to the team member using cgbm_int@phys.aoyama.ac.jp