## Slide 1: Summary of US CALET M&S Group Activities
John Krizmanic (for US CALET M&S group)
CRESST/USRA/NASA/GSFC
October 2014
1
Action Item Summary
Summary of CALET M&S Epics-based simulation software status.
Synopsis of US CALET M&S group’s activities.
  Continue validation & benchmarking studies as the Epics-based code and CALET CAD models are evolving.
  Production run status via LSU HPC cluster.
  Supporting analysis development.
  Work in progress.

## Slide 2: Action Items
Japan to 1) provide new mass model and support getting it running and 2) provide benchmark data for comparison. US will download model, run it in new version of EPICS and verify. Also will test in old version of mass model in new version of EPICS.
Status: Done
LSU will look into implementation of quenching modeling in the new version of EPICS. What is the most appropriate model.
Status: Evaluated Quenching in Rev 15, reported problems
JFK will finalize FEE notes and distribute to collaboration after discussion with Torii.
JFK will go back to HEASARC do discuss when to archive and what level data after discussions with JWM and JPW.
JFK will test use of NASA computing resources for simulation.
LSU will look into using HPC systems there.
2

## Slide 3: US CALET M&S Group
NASA/GSFC:
John Krizmanic, Alex Moiseev, Makoto Sasaki, Thomas Hams
Washington University at St. Louis:
Brian Rauch, Bob Binns
LSU:
Greg Guzik, Amir Javaid, Nick Cannady, Bethany Broekhoven, Doug Granger, Michael Stewart
University of Denver:
Jonathan Ormes, Aaron Worley
3

## Slide 4: CALET M&S Simulation Software Status
4
  Cosmos/Epics-based Physics modeling:
  Current version Cosmos9.645/Epics9.165
    Epics9.165 corrects a problem with the modeling of the LPM effect for E > 5 TeV in ‘heavy’ materials such as W (which is in CALET). It should be paired with Cosmos7.645. These versions should be used for HE gamma simulations.
    Libraries compiled with higher level of optimization (Opt –O3 vs Opt –O0) leads to ~x1.8 speed improvement on Linux machines (I get x5 improvement on my Mac)
  Hadronic modeling Benchmarks demonstrate stable results since Cosmos7.622 & Epics9.13, sans X-position asymmetry issue fixed since Cosmos7.641/Epics9.160 see CALET-PisaModel-Response_dpmjet3-vs-Version-Oct14-JFK.pdf, which completes comparisons through Cosmos7.645/Epics9.165 using Pisa-distribution CALET model.

## Slide 5: CALET CAD Model Software Status
Current CALET CAD model Rev18 (released to group):
  penultimate version Rev15
  fixes one detector numbering problem left over from Rev14 to Rev15 fix.
  scintillator quenching model updated:
    GSFC/LSU studies showed previous ad hoc model actually gave anti-quenching (EQuench >Z2) for light Z nuclei.
  CHD positions in the normal direction have moved up by ~300 um (Kenji/Yosui may have more comments).
  significant difference in data output format.
  CALET CAD Rev18 requires Cosmos7.645/Epics9.165.
  Rev 18 supports higher level of compiler optimization (-optO3).
Hadronic modeling benchmarks show different response between Pisa-distribution mass model and CAD models, with response between Rev15 and Rev18 very similar (see later talk: CALET-CadModel-Response_dpmjet3-vs-Version-Oct14-JFK.pdf).
5

## Slide 6: INTEL fortran compiler version dependence
First ‘discovered’ by WashU, certain versions of Cosmos/Epics will either build or run some versions of the INTEL fortran compiler.
  Ifort –v -> 12.0.4 (WashU)
    Cosmos7.644/Epics9.161: libraries build, but CALET models do not build.
    Cosmos7.645/Epics9.165: libraries build and CALET models build and run.
  ifort –v : 12.0.2 (GSFC):
    Cosmos7.644/Epics9.161: libraries build and CALET models build and run.
    Cosmos7.645/Epics9.165: libraries build but CALET models do not build.
  ifort –v : 12.1.4 (LSU):
    Cosmos7.644/Epics9.161: libraries build and CALET models build and run.
    Cosmos7.645/Epics9.165: libraries build and CALET models build and run.
  Installed trial version of ifort –v -> 14.0.3 on my Mac to get around this.
  Reported to KK, who has acknowledged the problem and determined the cause.
  See CALET-IntelCompilerVersion-Dependence-inUS.pdf for description of ifort version dependencies determined in the US.
6

## Slide 7: CALET High Statistics Runs
The LSU group (Bethany Broekhoven & Doug Granger) has secured significant High Performance Computing (HPC) resources and have been performing high-statistics runs using electrons, protons, and Z>1 nuclei:
Cosmos7.644/Epics9.161
CALET CAD Model Rev15
Starting point generation on a sphere
    Radius 78 cm; origin at (0,0,24.53 cm)
    Max Zenith angles 110°
    “ InputA ‘cos 1’ ”, e.g. generation flat in cos2(q), flat in f.
    “ CosNormal (0., 1.0) “
Events generated in E-1 spectra in various energy ranges, eg 1 to 10 TeV.
Goal is to generate 10^4 -> 10^5 events, in each energy range that traverse the entire depth of CALET (see Mike Stewart’s talk) .
7

## Slide 8: Supporting Software Status
UnifiedDataFormat:
  We have successfully installed and built the latest version of the UnifiedDataFormat (see Nicola Mori’s email of 12-Feb-14) but needed to modify root paths (results reported to Nicola, who modified the installation scripts to solve the problem).
  Also have build Nicola’s event viewer.
CALET CAD Epics-based Data  UnifiedDataFormat:
  Software included in CALET CAD model Rev15 and Rev18 based upon different UnifiedDataFormat definitions:
  Yosui has written a beta-version of the software (not all variables populated yet) and it is under evaluation at GSFC.
  Once evaluation complete, will convert HPC production data into root unified format.
8

## Slide 9: Work in Progress
9
Further Validation Studies:
  Electron benchmarks vs Cosmos/Epics version and CALET mass models (data generated and Paw-based ntuples populated).
  CALET Geometry Factor Calculations: JFK has performed this for CAD models. Presentation can be given at this TIM if time allows.
Moving from validation to analysis:
  Alex Moiseev (GSFC) developing “science analysis variables” or “merit variablex based upon his Fermi experience (see Alex’s talk).
  Aaron Worley (Denver) is developing event reconstruction techniques based upon Multivariate Analysis developed for Fermi analysis (see Aaron’s talk).
  Amir Javaid (LSU) continues to develop Epic-based code to efficiently track and determine Edep from individual particles for detailed back-splash studies. Amir has recent effort focused on on-orbit calibration rate calculations (see Amir’s talk on 16-Oct-14).
  Nick Cannady (LSU) is studying the response of CALET to gamma-rays.
  Brian Rauch (WashU) has been supporting the validation effort and is beginning high-statistics heavy nuclei runs using CALET CAD model Rev18.
  Once HPC production data transformed into UnifiedDataFormat, US group will perform an independent e/p separation analysis.