## Slide 1: Comparison of proton and carbon response in CALET CAD model as a function of Cosmos & Epics Version
John Krizmanic (for US CALET M&S group)
CRESST/USRA/NASA/GSFC
October 2014
  Procedure: use normal incident mono-energetic protons (10, 100, 1000 GeV) and 12C (100 GeV/nuc) in center 4×4 cm2 of CALET.
    Start with Cosmos7.644 & Epics9.161 on Linux platform
      Compare Pisa-distribution model to CAD model Rev15
    End with Cosmos7.645 & Epics9.165 on Mac platform
      Compare CAD model Rev15 to CAD model Rev18
    Comparison of hadronic shower properties in CALET using protons and carbon using Epics/Cosmos (with and without ‘fixes’ where appropriate).
      Investigate effects of epCal.f ‘bug’ in CAD Model Rev15
      Compare results to see how EDEP, longitudinal profile, Lateral Profile for hadronic showers scales in CAD models (due to separation between PWO logs).
1

## Slide 2: CALET Mass Models
Pisa-distribution CALET Model
CALET CAD Model in 78 cm sphere
2

## Slide 3: CALET Proton & Carbon Response vs Cosmos/Epics Version with and without dpmjet3 fix
Simulated response of 10, 100, and 1000 GeV protons and 100 GeV/nuc Carbon in CALET
  COMPARE with CALET Mass model from Pisa Distribution (May 2011)
  Cosmos7.644 and Epics9.161
    dmpjet.inp and dmpjet.GLB updated via 'fordpmjet dummyconfig’
    IntModel = '"dpmjet3”’
    AutoEmin=2
  CAD Model Rev 15
    Cosmos7.644 & Epics9.161
    Cosmos7.644 & Epics9.161, correcting index error in epCal.f (see next slide)
    Cosmos7.645 & Epics9.165 (on Mac, with OPT-O3)
  CAD Model Rev 18
    Cosmos7.645 & Epics9.165 (on Mac, with OPT-O3)
    Cosmos7.645 & Epics9.165 (on Mac, with OPT-O0)
STUDY GOAL: Assess the change in measurement parameters in CALET as a function of Cosmos, Epics, and CALET CAD model versions.
3

## Slide 4: Index error in epCal.f CAD Model Rev 15
Lines 409 – 415 of epCal.f
c *** initialize *******
do i=0, Ncomp
ElossAll(i) = 0;
ElossAllEff(i) = 0;
ElossAll_prim(i) = 0;
ElossAllEff_prim(i) = 0;
enddo
ISSUE: arrays defined from i=1 to Ncomp
  Fixed by Akaike-san in CAD Model Rev 18
  CAD Model Rev 15 builds and runs fine using Cosmos7.644/Epics9.161 on Unix platform
  CAD Model Rev 15 builds fine using Cosmos7.645/Epics9.165 on Mac, but dies when running
    forrtl: severe (408): fort: (3): Subscript #1 of the array ELOSSALL has value 0 which is less than the lower bound of 1
  Need to fix problem to run with Cosmos7.645/Epics9.165 on Mac.
  Running on Linux only issue appears to be ~20% increase in processing time for ‘efficient’ event generation.
4

## Slide 5: Selection Definitions
No Hit Fraction: fraction of events with no EDep in CHD and (since CAD models have gaps between detectors). Note that always have EDep in CHD or IMC.
Non-Interacting Events: fcolz<0
Interact in CHD:
  Pisa-Distributed Model: 0 ≤ z ≤ 2.0 cm
  CAD Model Rev 15: 0 ≤ z ≤ (1.8665+1.0) cm (note top of CHD at z=0.7315)
  CAD Model Rev 18: 0 ≤ z ≤ (1.8535+1.0) cm (note top of CHD at z=0.7005)
Interact in IMC:
  Pisa-Distributed Model: 3.0 ≤ z ≤ 17.2 cm
  CAD Models: 5.047≤ z ≤ (21.287+0.096) cm
Interact up to 4th TASC Layer:
  Pisa-Distributed Model: 0 ≤ z < 27.2 cm
  CAD Models: 0 ≤ z ≤ (31.587+2.0) cm
Interact within top 4 TASC Layers:
  Pisa-Distributed Model: 19.2 ≤ z < 27.2 cm
  CAD Models: 24.927 ≤ z ≤ (31.587+2.0) cm
Interact within bottom 8 TASC Layers:
  Pisa-Distributed Model: 27.2 ≤ z ≤ 43.2 cm
  CAD Models: 33.807 ≤ z ≤ (49.347+2.0) cm
5

## Slide 6: Description of Analysis Metrics
Proton results for 10, 100, and 1000 GeV:
  Interaction statistics, eg fraction of non-interacting events, fraction of events interacting in CHD, IMD, or TASC  relative comparison of cross-sections.
  Energy deposited in TASC for events that interact up to the first 4 TASC layers  relative comparison of energy deposition for well-contained hadronic showers.
  Longitudinal and lateral size of hadronic showers for interacting events  relative comparison of hadronic shower profiles.
Carbon results for 100 GeV/nuc:
  Similar analysis as performed for protons.
6
6

## Slide 7: Proton Interaction Statistics
Procedure: Evaluate interaction fractions in each of the CALET sub-systems, i.e. CHD, IMC, and TASC.
7
7

## Slide 8: 10 GeV Interaction Statistics (%)
Epics Settings | No hit fraction | Non- Interact | Interact in CHD | Interact in IMC | Interact in 1st 4 TASC LayersCHD | Interact in last 8 TASC LayersCHD | Interacting up to 1st 4 TASC Layers
Pisa Model Cosmos7.644/Epics9.161 | - | 27.27 | 2.09 | 10.76 | 27.55 | 32.32 | 40.40
CAD Rev 15 Cosmos7.644/Epics9.161 | 0.01 | 26.91 | 2.96 | 14.85 | 24.24 | 28.04 | 44.94
CAD Rev 15 Cosmos7.644/Epics9.161 FIXDepCal Bug | 0 | 26.86 | 3.05 | 14.40 | 24.35 | 28.35 | 44.67
CAD Rev 15 Cosmos7.645/Epics9.165 FIXDepCal Bug | 0.01 | 27.11 | 2.88 | 14.46 | 24.64 | 28.29 | 44.45
CAD Rev 18 Cosmos7.645/Epics9.165 | 0 | 27.11 | 2.80 | 14.45 | 24.44 | 28.22 | 44.43
CAD Rev 18 Cosmos7.645/Epics9.165 OPT-O0 | 0 | 26.64 | 3.33 | 14.90 | 24.37 | 27.97 | 45.20
8
≈ 3 s
Slightly less non-interacting events in CAD models  slightly more matter in beam.
~50% more interactions in the CHD.
~4% more interactions in IMC (W layer thicknesses identical).
~4% more interactions up to 1st 4 TASC layers in CAD models.
~3% less interactions in TASC in CAD models.

## Slide 9: 100 GeV Interaction Statistics (%)
Epics Settings | No hit fraction | Non- Interact | Interact in CHD | Interact in IMC | Interact in 1st 4 TASC LayersCHD | Interact in last 8 TASC LayersCHD | Interacting up to 1st 4 TASC Layers
Pisa Model Cosmos7.644/Epics9.161 | - | 27.27 | 2.09 | 10.76 | 27.55 | 32.32 | 40.40
CAD Rev 15 Cosmos7.644/Epics9.161 | 0.01 | 26.03 | 3.11 | 14.87 | 24.62 | 28.36 | 45.49
CAD Rev 15 Cosmos7.644/Epics9.161 FIXDepCal Bug | 0 | 26.46 | 3.05 | 14.93 | 24.18 | 28.51 | 44.85
CAD Rev 15 Cosmos7.645/Epics9.165 FIXDepCal Bug | 0 | 26.22 | 2.37 | 15.56 | 25.11 | 27.91 | 45.71
CAD Rev 18 Cosmos7.645/Epics9.165 | 0 | 25.70 | 2.96 | 15.32 | 24.38 | 29.00 | 45.10
CAD Rev 18 Cosmos7.645/Epics9.165 OPT-O0 | 0 | 27.00 | 2.81 | 15.16 | 24.14 | 27.79 | 45.00
9
Slightly less non-interacting events in CAD models.
~50% more interactions in the CHD.
~4% more interactions in IMC.
~5% more interactions up to 1st 4 TASC layers in CAD models.
~3% less interactions in TASC in CAD models.

## Slide 10: 1000 GeV Interaction Statistics (%)
Epics Settings | No hit fraction | Non- Interact | Interact in CHD | Interact in IMC | Interact in 1st 4 TASC LayersCHD | Interact in last 8 TASC LayersCHD | Interacting up to 1st 4 TASC Layers
Pisa Model Cosmos7.644/Epics9.161 | - | 26.89 | 2.33 | 10.90 | 27.29 | 32.58 | 40.52
CAD Rev 15 Cosmos7.644/Epics9.161 | 0 | 25.48 | 3.22 | 15.21 | 24.62 | 28.49 | 45.90
CAD Rev 15 Cosmos7.644/Epics9.161 FIXDepCal Bug | 0 | 25.58 | 3.05 | 15.04 | 25.23 | 28.23 | 46.05
CAD Rev 15 Cosmos7.645/Epics9.165 FIXDepCal Bug | 0 | 24.54 | 3.00 | 15.76 | 25.24 | 28.91 | 46.47
CAD Rev 18 Cosmos7.645/Epics9.165 | 0 | 25.07 | 2.71 | 15.50 | 25.74 | 27.96 | 46.82
CAD Rev 18 Cosmos7.645/Epics9.165 OPT-O0 |  |  |  |  |  |  | 
10
Slightly less non-interacting events in CAD models.
~50% more interactions in the CHD.
~4% more interactions in IMC (W layer thicknesses identical).
~5% more interactions up to 1st 4 TASC layers in CAD models.
~3% less interactions in TASC in CAD models.

## Slide 11: Proton Energy Deposition in TASC
Procedure: Evaluate energy deposition in TASC for interacting protons.
  Interact up to 1st 4 TASC Layers
  Mean and s obtained from Gaussian fit (reduced c2 values presented as a measure of goodness-of-fit)
11

## Slide 12: Energy deposited in TASC by interacting protons: 10 GeV Interact up to 1st 4 TASC Layers
gen E = 10 GeV | <E> (GeV) | σ (GeV) | σ/<E> | <E>/gen E | χ2
Pisa Model Cosmos7.644/Epics9.161 | 4.119 | 1.405 | 34.1% | 0.414 | 0.882
CAD Rev 15 Cosmos7.644/Epics9.161 | 3.784 | 1.459 | 38.6% | 0.378 | 1.061
CAD Rev 15 Cosmos7.644/Epics9.161 FIXDepCal Bug | 3.635 | 1.469 | 40.4% | 0.364 | 0.958
CAD Rev 15 Cosmos7.645/Epics9.165 FIXDepCal Bug | 3.795 | 1.404 | 37.0% | 0.380 | 1.340
CAD Rev 18 Cosmos7.645/Epics9.165 | 3.768 | 1.423 | 37.8% | 0.377 | 1.378
CAD Rev 18 Cosmos7.645/Epics9.165 OPT-O0 | 3.748 | 1.446 | 38.6% | 0.375 | 1.200
12
~9% less <EDEP>, s slightly larger, s/<E> ~12% larger in CAD models

## Slide 13: Energy deposited in TASC by interacting protons: 100 GeV Interact up to 1st 4 TASC Layers
gen E = 100 GeV | <E> (GeV) | σ (GeV) | σ/<E> | <E>/gen E | χ2
Pisa Model Cosmos7.644/Epics9.161 | 38.257 | 14.241 | 37.2% | 0.383 | 1.107
CAD Rev 15 Cosmos7.644/Epics9.161 | 36.960 | 14.004 | 37.9% | 0.370 | 1.321
CAD Rev 15 Cosmos7.644/Epics9.161 FIXDepCal Bug | 35.421 | 14.175 | 40.0% | 0.354 | 1.194
CAD Rev 15 Cosmos7.645/Epics9.165 FIXDepCal Bug | 35.878 | 13.996 | 39.0% | 0.359 | 1.326
CAD Rev 18 Cosmos7.645/Epics9.165 | 36.057 | 14.124 | 39.2% | 0.361 | 0.965
CAD Rev 18 Cosmos7.645/Epics9.165 OPT-O0 | 36.413 | 14.243 | 39.1% | 0.364 | 0.881
13
~6% less <EDEP>, s similar, s/<E> ~5% larger in CAD models

## Slide 14: Energy deposited in TASC by interacting protons: 1000 GeV Interact up to 1st 4 TASC Layers
gen E = 1000 GeV | <E> (GeV) | σ (GeV) | σ/<E> | <E>/gen E | Reduced χ2
Pisa Model Cosmos7.644/Epics9.161 | 326.91 | 140.12 | 42.9% | 0.327 | 1.442
CAD Rev 15 Cosmos7.644/Epics9.161 | 312.27 | 139.26 | 44.6% | 0.312 | 1.466
CAD Rev 15 Cosmos7.644/Epics9.161 FIXDepCal Bug | 310.64 | 142.17 | 45.8% | 0.311 | 1.509
CAD Rev 15 Cosmos7.645/Epics9.165 FIXDepCal Bug | 312.71 | 143.25 | 45.8% | 0.313 | 1.272
CAD Rev 18 Cosmos7.645/Epics9.165 | 315.32 | 142.42 | 45.2% | 0.315 | 1.426
CAD Rev 18 Cosmos7.645/Epics9.165 OPT-O0 |  |  |  |  | 
14
~4% less <EDEP>, s similar, s/<E> ~5% larger in CAD models

## Slide 15: Proton Longitudinal Profiles in TASC
Procedure: Evaluate longitudinal TASC profiles of interacting protons.
  All protons, Interact up to 1st 4 TASC Layers, Interact only in TASC.
  Mean and RMS obtained from layer number distributions
15

## Slide 16: Longitudinal Profile in TASC by 10 GeV protons
 | All Protons |  | Interacting Protons Up to 1st 4 TASC Layers |  | Interacting Protons In 1st 4 TASC Layers | 
Run Params | <Layer> | rms (Layer) | <Layer> | rms (Layer) | <Layer> | rms (Layer)
Pisa Model Cosmos7.644/Epics9.161 | 6.080 | 3.271 | 4.811 | 2.993 | 5.143 | 2.870
CAD Rev 15 Cosmos7.644/Epics9.161 | 5.861 | 3.308 | 4.724 | 3.024 | 5.193 | 2.856
CAD Rev 15 Cosmos7.644/Epics9.161 FIXDepCal Bug | 5.880 | 3.299 | 4.761 | 3.033 | 5.247 | 2.872
CAD Rev 15 Cosmos7.645/Epics9.165 FIXDepCal Bug | 5.904 | 3.282 | 4.776 | 3.023 | 5.239 | 2.849
CAD Rev 18 Cosmos7.645/Epics9.165 | 5.880 | 3.294 | 4.736 | 3.017 | 5.220 | 2.849
CAD Rev 18 Cosmos7.645/Epics9.165 OPT-O0 | 5.867 | 3.308 | 4.758 | 3.042 | 5.246 | 2.872
16

## Slide 17: Longitudinal Profile in TASC by 100 GeV protons
 | All Protons |  | Interacting Protons Up to 1st 4 TASC Layers |  | Interacting Protons In 1st 4 TASC Layers | 
Run Params | <Layer> | rms (Layer) | <Layer> | rms (Layer) | <Layer> | rms (Layer)
Pisa Model Cosmos7.641/Epics9.161 | 6.636 | 3.137 | 5.677 | 2.953 | 6.210 | 2.706
CAD Rev 15 Cosmos7.644/Epics9.161 | 6.410 | 3.199 | 5.571 | 3.027 | 6.317 | 2.720
CAD Rev 15 Cosmos7.644/Epics9.161 FIXDepCal Bug | 6.468 | 3.173 | 5.633 | 3.017 | 6.402 | 2.694
CAD Rev 15 Cosmos7.645/Epics9.165 FIXDepCal Bug | 6.408 | 3.197 | 5.603 | 3.031 | 6.330 | 2.724
CAD Rev 18 Cosmos7.645/Epics9.165 | 6.456 | 3.192 | 5.616 | 3.028 | 6.372 | 2.716
CAD Rev 18 Cosmos7.645/Epics9.165 OPT-O0 | 6.381 | 3.187 | 5.586 | 3.022 | 6.318 | 2.706
17

## Slide 18: Longitudinal Profile in TASC by 1000 GeV protons
 | All Protons |  | Interacting Protons Up to 1st 4 TASC Layers |  | Interacting Protons In 1st 4 TASC Layers | 
Run Params | <Layer> | rms (Layer) | <Layer> | rms (Layer) | <Layer> | rms (Layer)
Pisa Model Cosmos7.644/Epics9.161 | 7.096 | 2.955 | 6.367 | 2.828 | 6.981 | 2.507
CAD Rev 15 Cosmos7.644/Epics9.161 | 6.865 | 3.045 | 6.207 | 2.926 | 7.060 | 2.544
CAD Rev 15 Cosmos7.644/Epics9.161 FIXDepCal Bug | 6.873 | 3.024 | 6.248 | 2.902 | 7.112 | 2.512
CAD Rev 15 Cosmos7.645/Epics9.165 FIXDepCal Bug | 6.837 | 3.038 | 6.193 | 2.918 | 7.069 | 2.518
CAD Rev 18 Cosmos7.645/Epics9.165 | 6.847 | 3.030 | 6.235 | 2.915 | 7.072 | 2.535
CAD Rev 18 Cosmos7.645/Epics9.165 OPT-O0 |  |  |  |  |  | 
18
All Protons & Int Protons up to 1st 4 TASC Layers: SMAX in TASC ~3% shallower in CAD models.
Int Protons within 1st 4 TASC layers: SMAX in TASC ~1% deeper in CAD models.

## Slide 19: Proton Lateral Profiles in TASC
Procedure: Evaluate lateral TASC profiles of interacting protons.
  All protons, Interact up to 1st 4 TASC Layers, Interact only in TASC.
  Lateral profile determined in layer with maximum energy deposit: defined as shower maximum.
  Lateral distributions calculated and centered on channel with maximum energy deposit  mean ≈ 0 for lateral distributions
    Note: used 17 bins each with 2 cm size (Pisa Model), 2.042 cm (CAD models)
Mean and RMS obtained from spatial distributions
19

## Slide 20: Lateral Profile @ Smax in TASC by 10 GeV protons
 | All Protons | Interacting Protons Up to 1st 4 TASC Layers | Interacting Protons In 1st 4 TASC Layers
Run Params | rms (cm) | rms (cm) | rms (cm)
Pisa Model Cosmos7.644/Epics9.161 | 2.533 | 2.804 | 2.322
CAD Rev 15 Cosmos7.644/Epics9.161 | 2.917 | 3.233 | 2.552
CAD Rev 15 Cosmos7.644/Epics9.161 FIXDepCal Bug | 3.001 | 3.276 | 2.601
CAD Rev 15 Cosmos7.645/Epics9.165 FIXDepCal Bug | 2.886 | 3.186 | 2.540
CAD Rev 18 Cosmos7.645/Epics9.165 | 2.893 | 3.211 | 2.594
CAD Rev 18 Cosmos7.645/Epics9.165 OPT-O0 | 2.947 | 3.271 | 2.554
20

## Slide 21: Lateral Profile @ Smax in TASC by 100 GeV protons
 | All Protons | Interacting Protons Up to 1st 4 TASC Layers | Interacting Protons In 1st 4 TASC Layers
Run Params | rms (cm) | rms (cm) | rms (cm)
Pisa Model Cosmos7.644/Epics9.161 | 1.793 | 1.891 | 1.749
CAD Rev 15 Cosmos7.644/Epics9.161 | 2.049 | 2.154 | 1.926
CAD Rev 15 Cosmos7.644/Epics9.161 FIXDepCal Bug | 2.131 | 2.244 | 2.024
CAD Rev 15 Cosmos7.645/Epics9.165 FIXDepCal Bug | 2.051 | 2.156 | 1.948
CAD Rev 18 Cosmos7.645/Epics9.165 | 2.069 | 2.187 | 1.975
CAD Rev 18 Cosmos7.645/Epics9.165 OPT-O0 | 2.080 | 2.189 | 1.963
21

## Slide 22: Lateral Profile @ Smax in TASC by 1000 GeV protons
 | All Protons | Interacting Protons Up to 1st 4 TASC Layers | Interacting Protons In 1st 4 TASC Layers
Run Params | rms (cm) | rms (cm) | rms (cm)
Pisa Model Cosmos7.644/Epics9.161 | 1.396 | 1.446 | 1.415
CAD Rev 15 Cosmos7.644/Epics9.161 | 1.531 | 1.588 | 1.541
CAD Rev 15 Cosmos7.644/Epics9.161 FIXDepCal Bug | 1.607 | 1.660 | 1.614
CAD Rev 15 Cosmos7.645/Epics9.165 FIXDepCal Bug | 1.520 | 1.572 | 1.521
CAD Rev 18 Cosmos7.645/Epics9.165 | 1.527 | 1.578 | 1.533
CAD Rev 18 Cosmos7.645/Epics9.165 OPT-O0 |  |  | 
22
Lateral Width ~10% larger in CAD models.

## Slide 23: 100 GeV/nuc Carbon Results
Procedure: Analysis similar to proton analysis.
23

## Slide 24: 12C 100 GeV/nuc Interaction Statistics (%)
Epics Settings | No hit fraction | Non- Interact | Interact in CHD | Interact in IMC | Interact in 1st 4 TASC LayersCHD | Interact in last 8 TASC LayersCHD | Interacting up to 1st 4 TASC Layers
Pisa Model Cosmos7.644/Epics9.161 | - | 5.99 | 9.51 | 20.46 | 38.76 | 25.28 | 68.73
CAD Rev 15 Cosmos7.644/Epics9.161 | 0 | 5.80 | 10.79 | 27.21 | 30.36 | 20.13 | 73.93
CAD Rev 15 Cosmos7.644/Epics9.161 FIXDepCal Bug | 0 | 5.36 | 10.62 | 27.16 | 30.93 | 19.84 | 74.56
CAD Rev 15 Cosmos7.645/Epics9.165 FIXDepCal Bug | 0 | 5.70 | 10.05 | 27.56 | 30.65 | 19.82 | 74.28
CAD Rev 18 Cosmos7.645/Epics9.165 | 0 | 5.20 | 10.77 | 26.77 | 31.55 | 19.71 | 74.88
CAD Rev 18 Cosmos7.645/Epics9.165 OPT-O0 |  |  |  |  |  |  | 
24
Slightly less non-interacting events in CAD models  slightly more matter in beam.
~7% more interactions up to 1st 4 TASC layers in CAD models.
~6-8% less interactions in TASC in CAD models.

## Slide 25: Energy deposited in TASC by interacting 12C: 100 GeV/nuc Interact up to 1st 4 TASC Layers
gen E = 1200 GeV | <E> (GeV) | rms (GeV) | rms/<E> | <E>/gen E | Reduced χ2
Pisa Model Cosmos7.644/Epics9.161 | 317.1 | 121.2 | 38.2% | 0.264 | 6.26
CAD Rev 15 Cosmos7.644/Epics9.161 | 301.4 | 112.9 | 37.5% | 0.251 | 6.15
CAD Rev 15 Cosmos7.644/Epics9.161 FIXDepCal Bug | 291.7 | 113.3 | 38.8% | 0.243 | 5.74
CAD Rev 15 Cosmos7.645/Epics9.165 FIXDepCal Bug | 303.5 | 114.2 | 37.6% | 0.253 | 7.62
CAD Rev 18 Cosmos7.645/Epics9.165 | 299.9 | 113.9 | 38.0% | 0.250 | 6.23
CAD Rev 18 Cosmos7.645/Epics9.165 OPT-O0 |  |  |  |  | 
Note1: <E> taken from histogram (not Gaussian fit)
Note2: Gaussian fit c2 given as a measure of non-Gaussian nature of distribution.
25
~5% less <EDEP>, s smaller, s/<E> similar in CAD models

## Slide 26: Longitudinal Profile in TASC by 100 GeV/nuc 12C
 | All 12C |  | Interacting 12C Up to 1st 4 TASC Layers |  | Interacting 12C In 1st 4 TASC Layers | 
Run Params | <Layer> | rms (Layer) | <Layer> | rms (Layer) | <Layer> | rms (Layer)
Pisa Model Cosmos7.644/Epics9.161 | 6.696 | 3.115 | 6.286 | 3.080 | 6.825 | 2.790
CAD Rev 15 Cosmos7.644/Epics9.161 | 6.510 | 3.175 | 6.192 | 3.141 | 6.912 | 2.781
CAD Rev 15 Cosmos7.644/Epics9.161 FIXDepCal Bug | 6.538 | 3.157 | 6.213 | 3.122 | 6.939 | 2.758
CAD Rev 15 Cosmos7.645/Epics9.165 FIXDepCal Bug | 6.491 | 3.172 | 6.175 | 3.135 | 6.890 | 2.774
CAD Rev 18 Cosmos7.645/Epics9.165 | 6.509 | 3.172 | 6.206 | 3.138 | 6.910 | 2.799
CAD Rev 18 Cosmos7.645/Epics9.165 OPT-O0 |  |  |  |  |  | 
26
All 12C & Int 12C up to 1st 4 TASC Layers: SMAX in TASC ~3% shallower in CAD models.
Int 12C within 1st 4 TASC layers: SMAX in TASC ~1% deeper in CAD models.

## Slide 27: Lateral Profile @ Smax in TASC by 100 GeV/nuc 12C
 | All 12C | Interacting 12C Up to 1st 4 TASC Layers | Interacting 12C In 1st 4 TASC Layers
Run Params | rms (cm) | rms (cm) | rms (cm)
Pisa Model Cosmos7.644/Epics9.161 | 1.811 | 1.864 | 1.757
CAD Rev 15 Cosmos7.644/Epics9.161 | 2.076 | 2.130 | 1.952
CAD Rev 15 Cosmos7.644/Epics9.161 FIXDepCal Bug | 2.145 | 2.199 | 2.034
CAD Rev 15 Cosmos7.645/Epics9.165 FIXDepCal Bug | 2.070 | 2.125 | 1.951
CAD Rev 18 Cosmos7.645/Epics9.165 | 2.083 | 2.136 | 1.961
CAD Rev 18 Cosmos7.645/Epics9.165 OPT-O0 |  |  | 
27
Lateral Width ~10% larger in CAD models.

## Slide 28: Summary
Comparing the hadronic modeling of the Epics-based CALET CAD models Rev 15 and 18 via evaluating:
  the interaction versus location factions,
  energy deposited in the TASC for interacting events,
  longitudinal profile in the TASC for interacting events,
  lateral profile in the TASC for interacting events.
All CAD model results are consistent with one another regardless of CAD model revision or using Cosmos7.644/Epics9.161 vs Cosmos7.645/Epics9.165.
Comparing the CAD model results to those from the Pisa-distribution CALET mass model show that for the CAD models:
  Slightly more material in the depth of CALET.
  ~5% More events interact up to the 1st 4 TASC layers:
    CHD: corresponds to 1 mm Al box thickness.
    IMC: corresponds to 0.5 mm Al box thickness.
  <EDEP> in TASC for interacting events is ~5% less; assumed to be due to gaps in log spacing.
  Longitudinal profile has slightly shallower SMAX for events interacting up to 1st 4 TASC layers and slightly deeper for events interacting in TASC, the latter assumed to be due to spacing between layers.
  Lateral profile is ~10% larger; assumed to be due to spacing between logs.
28