## Slide 1: CALET Level 1 Data Format Comments and Questions
Michael Stewart, Nicholas Cannady
Louisiana State University
Oct. 2014 CALET TIM (Japan)

## Slide 2: Purpose
The purpose of this presentation is to provide feedback on the Level 1 Data Format as provided in revision 140831.
We understand that some changes will not be possible. We make requests with this understanding in hope that they will be taken into consideration.
These topics are discussed in greater detail in the accompanying documents for the CAL and COM volumes.

## Slide 3: General questions
How often will we receive these data volumes?
  How variable is this timing?
What are the current estimated sizes of the Level 1 data volumes?
Are “Test Pulse” and “Charge Injection” the same thing?

## Slide 4: CAL: Event Data Ordering
It is our understanding that the event data will be grouped such that the data from all hit IMC channels will be together, followed by all hit TASC-PMT data, followed by all TASC-PD/APD data, with all CHD data at the end.
  Is this correct? It is ambiguous to have Ni referring back to the record start, but not referenced to other event data.
  It would be helpful to add counters or offsets to these different data to the Event Data (Scalar) volume.

## Slide 5: CAL: Event Data Contents
It is our understanding that all gain channels of a detector component that has at least one gain channel that surpasses zero suppression will be present in the CAL data volume.
  Is this correct?
  What data values are loaded into those gain channels that do not surpass the threshold?

## Slide 6: CAL: LD Patterns
The bit patterns (E.g. scalar data no. 14 and 19) between these two data entries are different and cannot be quickly bit compared for consistency.
  It would be very convenient if these patterns were identical between the data fields.
  One would be able to OR the hit pattern with the mask pattern and AND the result with the trigger as a verification.

## Slide 7: CAL: Event ID
In Scalar Data No. 9, a 64-bit ULL would serve well as an overall mission event counter.
  This would allow easy and clear communication between collaborators in regards to specific events
  In the case that this change is not possible, how often will this counter be reset? Will it roll over or be reset at the beginning of each data volume?

## Slide 8: CAL: Zero-suppression files
It would be useful to have clear definition for the indices listed in the data format.
We do not have a file format for the zero-suppression threshold files.
  It would be useful to have MDC File Interface Specification Rev. F (WK-111572F) made available to us.
  When will these data be available?

## Slide 9: CAL: Timing
What is the difference between “Event Timing in GPS corrected UTC” and “Event Timing in MDC Time (Trigger Time)”?
  The phrase “Trigger Time” is causing some confusion
  Is the only difference that one is GPS corrected and the other isn’t?
  If these are different times, how do we relate the Trigger Time to GPS time?

## Slide 10: COM Volume (1)
Data No. 2, Attribute for Periodic Data,
  Why might the data not be available?
Data No. 14, Identification Flag for the Use of Internal Time,
  What is this?
Data No. 15, PPS Correction Flag in GPSR,
  What is this?
Data No. 16-23, Time of Equal-Time Pair,
  Are these for correcting MDC time to GPSR time?
Data No. 24-25, Non-reset time,
  What is non-reset time?

## Slide 11: COM Volume (2)
Data No. 27, 29, 30, 31, RPC…
  What does RPC stand for?
Data No. 32, Periodic Data Acquisition Setting,
  Does this refer to IMC, CHD and TASC data acquisition and if so can the detectors be run independently?
Data No. 41-79, LD Counters, Trigger Counters
  Are the LD counters cumulative; allowed to roll over?
  Are they any different than those in the CAL volume?
  Are these hardware counters?

## Slide 12: COM Volume (3)
Data No. 80, CAL Observation Dead Time,
  Is this re-initialized or is it allowed to roll over?
Data No. 81-91, CGBM…
  What are these times?
Data No. 132, 133, Dispatch Coefficient of CAL Event in Low / Medium-rate down link,
  What are these used for?
Data No. 140-145, … File Number,
  What are these files?

## Slide 13: COM Volume (4)
Data No. 278, Inhibit Settings…,
  What does it mean by inhibited?
  How are the fibers routed to the MaPMTs?
    Is the a fiber to MaPMT mapping that we can have?
Data No. 280, MaPMT Delay Time,
  What does VA (index 2) stand for?
Data No. 284, Operation Setting,
  What do these operation settings indicate?
Data No. 300, Trigger Setting,
  What does this mean?

## Slide 14: COM Volume (5)
Data No. 301-304, LD Mask Pattern,
  Are these different than the mask patterns in the CAL volume?
Data No. 333, Double Command Status,
  What is a double command status?
Data No. 336-337, Schedule File,
  What are the schedule files for?
We need the reference document for the Auxiliary records (A8-1)
  When will this document be made available?