## Slide 1: CALET Heavy Ion Beams March 2014
John W. Mitchell
NASA Goddard Space Flight Center

## Slide 2: CERN Accelerator Complex

## Slide 3: CERN Accelerator Complex
SPS 6.3 km diameter
LHC 27 km diameter

## Slide 6
5.8 Km of beam lines
About 1000 beamline components
CALET in “LHCB” Area

## Slide 7: H8 Beam Optics
CALET
CALET test location is at at a focal point about 480 m from the T4 target.
  Focus of Quad 14 and Quad 15
  Beam location controlled by Trim 3 and Trim 4 dipole magnets

## Slide 8: T4 Target Configuration
T4 Targets Available:
Beryllium 300 mm
Beryllium 200 mm
Beryllium 100 mm
Lead 40 mm

## Slide 9
CERN Injector Accelerator Schedule 2015

## Slide 10: SPS Heavy-Ion Schedule 2015

## Slide 11: Ion Beams for CALET - 1
Beam energies are determined by NA61/SHINE.
  Successor to NA49
  Main goal is study of p-p and p-nucleus physics with focus on quark-gluon plasma and the phase boundary between hadron “gas” and QGP.
  NA61 is the reason the SPS heavy-ion run is taking place. NA61 chooses beam species, energy and duration. All other users (e.g. CALET) are secondary.
Maximum beam rigidity is limited by SPS magnets to 400 GV/c (really 450 GV/c but that is rarely used now) – for nuclear beams A/Z has to be considered.
Beams planned for NA61 in 2015: Ar at 13A GeV/c, 19A GeV/c, 30A GeV/c, 40A GeV/c, 75A GeV/c, 150A GeV/c
Run schedule (2015 CERN Injector Schedule) 16 February – 6 April.
CALET scheduled in H8 beamline (used in 2012 proton run and 2013 heavy ion run) 2-17 March.
CALET has requested highest energy, but that is uncertain as other users (e.g. DAMPE) have same request.
SPS Coordinator (Henric Wilkins) has scheduled CALET “away from 13A GeV/c.”
CALET will use beams resulting from fragmentation in the T4 target.

## Slide 12: Ion Beams for CALET - 2
Peripheral fragmentation takes place when a beam particle (projectile) impacts a target nucleus (target).
Fragmentation results from a combination of two processes:
  Simple removal of nucleons by scattering interaction between projectile and target nucleons
  Emission of nucleons or groups of nucleons (e.g. alpha particles) from the (possibly unstable) remnant projectile nucleus.
  Most probable (highest cross-section) interaction is removal of a single nucleon.
  Next most probable is emission of an alpha.
Fragments are emitted approximately in the direction of the projectile and travel at approximately the velocity of the projectile.
  The fragment is affected by the net vector Fermi momentum (momentum of the nucleons in the nucleus) of the removed nucleons (250 MeV/c per nucleon).
  The direction is altered by the ratio of the transverse component of the Fermi momentum to the total momentum and by multiple scattering. Both effects are small at these energies.
  The velocity is altered by the longitudinal component of the Fermi momentum.

## Slide 13: Ion Beams for CALET - 3
Relatively thick targets available in T4 make multiple interactions likely.
  Final fragment momentum depends on the net effect of all Fermi momentum dispersion as well as differential energy loss in the target, depending on the interaction depth.
Investigating possibility of using a thinner target (e.g. few cm of polyethylene) to reduce multiple interactions.
Beamline is a highly selective (<1% momentum resolution) magnetic spectrometer. This is mainly driven by the “big bends” that bring the beam from the underground SPS tunnel and T4 target area to the surface.
Beams are selected by magnetic rigidity (momentum/charge). Because the velocity is approximately the same for all particles, this effectively selects A/Z.
Normally we run A/Z=2 to span full range of fragment Z from Z=1 (deuterons) to the primary beam (depending on the A/Z of primary).
However, the momentum dispersion resulting from multiple fragmentation and energy loss dispersion makes selectivity less effective than might be expected.
Experience in 2013 showed that we cannot get isotope resolution from beamline except for light elements.