## Slide 1: CALET Calibration on ISS Orbit Using Cosmic Ray Protons & Helium
2014. 10. 16
T. Niita

## Slide 2
Calibration on the ISS orbit
For continuous high performance of the detector, on-orbit calibration considering detector condition is required.
We use the measured response to MIP (Minimum Ionizing Particle) for the calibration. Applicability of the basic method has been confirmed in several beam tests using muons.
There are few muons in space, so we use protons and helium nuclei for on-orbit calibration.
What we should confirm :
number of penetrating events obtained during 1 orbit
efficiency and accuracy of off-line event selection
expected calibration error
Notes: 2

## Slide 3
1. Simulation data
1.1. Interstellar flux
AMS-01 (M. Aguilar et al., Phys. Rep., 366, (2002), 331-405)
flight: June 1998, altitude: 320-390 km
the data in high rigidity region can be fitted to a power law Φ = Φ0 R-γ
Proton
Φ0 = 17.1 [GV2.78/m2/s/sr/MV]
γ = 2.78
Helium
Φ0 = 2.52 [GV2.74/m2/s/sr/MV]
γ = 2.74
Notes: 3

## Slide 4
1.2. Solar modulation effect
extrapolate the power law to the lower energy region
calculate the solar modulation effect by Force-Field approximation
(L. J. Gleeson et al., ApJ, 154, (1968), 1011-1026)
Proton
He
when creating simulation data, we assume φ as
φ = 0.591 [GV]
1. Simulation data
Notes: 4

## Slide 5
1.3. Effect of geomagnetic field on primary particles
It takes time to calculate the geomagnetic effect on all particles at a long distance (most of them wouldn’t reach to the ISS orbit), so we use the following method.
Prepare a data set of protons and helium nuclei
(considering solar modulation effect as in p.5)
Invert the sign of the charge (p->p, He->He), and inject them from an altitude of 400km toward the outside.
If the antiparticle (p, He) escape from the geomagnetic field, the original particle (p, He) with opposite direction is supposed to be able to reach to the altitude from the outside. So we select those event.
Rearth+400km
Rearth×10
1. Simulation data
Notes: 5

## Slide 6
1.3. Effect of geomagnetic field on primary particles
It takes time to calculate the geomagnetic effect on all particles at a long distance (most of them wouldn’t reach to the ISS orbit), so we use the following method.
Prepare a data set of protons and helium nuclei
(considering solar modulation effect as in p.5)
Invert the sign of the charge (p->p, He->He), and inject them from an altitude of 400km toward the outside.
If the antiparticle (p, He) escape from the geomagnetic field, the original particle (p, He) with opposite direction is supposed to be able to reach to the altitude from the outside. So we select those event.
Rearth+400km
Rearth×10
1. Simulation data
Amount of data
number of events : N0 = 4×108 (protons), 2×107 (He)
integral flux : F = 3083 [/m2/sr/s] (proton), 262.8 [/m2/sr/s] (He)
geometrical factor : S0Ω0 = 4π (Rearth+400,001 m)2×π = 1.81×1015 [m2sr]
corresponding time :
T0 = N0 / F / S0Ω0 = 7.15×10-11 [s] (proton), 4.20×10-11 [s] (He)
Notes: 6

## Slide 7
Proton
He
1.4. Flux of primary & albedo particles on the ISS orbit
Simulation code : ATMNC3
Atmospheric structure model : US-standard 1976
Geomagnetic field model : IGRF2010
Minimum energy of incident particles : 10 MeV (p), 100 MeV/n (He)
Minimum hadron/elemag interaction energy : 20 MeV (p), 200 MeV/n (He)
Incident altitude : 400.001 km
Output : momentum, position (x, y, z)
of particles which reach to the altitude of 400.000 km
1. Simulation data
Notes: 7

## Slide 8
1.5. Calculation of the detector-response
Simulation code : EPICS
Incident surface : sphere around the detector (radius 0.48 m)
Incident direction : as recorded by ATMNC3
Incident position :
as the particle pass a random point in a cross section of the sphere
1. Simulation data
θ
r = 48 cm
Φ
R = Rearth + 400 km
θ
Notes: 8

## Slide 9
1.5. Calculation of the detector-response
Simulation code : EPICS
Incident surface : sphere around the detector (radius 0.48 m)
Incident direction : as recorded by ATMNC3
Incident position :
as the particle pass a random point in a cross section of the sphere
1. Simulation data
θ
r = 48 cm
Φ
R = Rearth + 400 km
θ
incident area in ATMNC3 calculation :
S0(Φ) = 2 × (Rearth+400,001m)2 × 2π(sinΦ’-sinΦ)
incident area in EPICS calculation :
S = π(0.48)2 × cosθ
corresponding observation time : t = T0 ・ S0 / S
S0
Notes: 9

## Slide 10
1.5. Calculation of the detector-response
Simulation code : EPICS
Incident surface : sphere around the detector (radius 0.48 m)
Incident direction : as recorded by ATMNC3
Incident position :
as the particle pass a random point in a cross section of the sphere
1. Simulation data
θ
r = 48 cm
Φ
R = Rearth + 400 km
θ
incident area in ATMNC3 calculation :
S0(Φ) = 2 × (Rearth+400,001m)2 × 2π(sinΦ’-sinΦ)
incident area in EPICS calculation :
S = π(0.48)2 × cosθ
corresponding observation time : t = T0 ・ S0 / S
S0
Latitude [deg] | S0×1013 [m2] | ISS transit time [s] | t (p) [period] | t (He) [period]
0.00-5.16 | 5.19 | 395 | 13.0 | 7.61
5.16-10.32 | 5.15 | 397 | 12.8 | 7.61
10.32-15.48 | 5.07 | 402 | 12.5 | 7.31
15.48-20.64 | 4.94 | 409 | 11.9 | 7.00
20.64-25.80 | 4.78 | 420 | 11.2 | 6.59
25.80-30.96 | 4.57 | 438 | 10.3 | 6.06
30.96-36.12 | 4.33 | 465 | 9.20 | 5.40
36.12-41.28 | 4.06 | 513 | 7.81 | 4.58
41.28-46.44 | 3.75 | 617 | 6.00 | 3.52
46.44-51.60 | 3.41 | 1343 | 2.51 | 1.47
Notes: 10

## Slide 11
2. Rate estimation
2.1. Trigger rate
Latitude [deg] | proton [/s] | He [/s]
0.00-5.16 | 36.6 | 6.53
5.16-10.32 | 38.2 | 7.01
10.32-15.48 | 40.9 | 7.83
15.48-20.64 | 46.8 | 8.93
20.64-25.80 | 57.4 | 11.5
25.80-30.96 | 73.8 | 15.4
30.96-36.12 | 100 | 20.6
36.12-41.28 | 143 | 28.2
41.28-46.44 | 202 | 37.1
46.44-51.60 | 273 | 45.9
Counts / period | 7.34×105 | 1.32×105
 | High Energy Shower | Low Energy Shower | Calibration
CHD | - | > 0.7 MIP | > 0.7 MIP
IMC layer 1-6 | - | > 0.7 MIP | > 0.7 MIP
IMC layer 7-8 | > 7.5 MIP | > 2.5 MIP | > 0.7 MIP
TASC layer 1 | > 55 MIP | > 7 MIP | > 0.7 MIP
Notes: 11

## Slide 12
Proton
He
all
top to bottom
all
top to bottom
2.2. Angular distribution of triggered events
Latitude [deg] | proton | He
 | B/A | B/A
0.00-5.16 | 0.182 | 0.125
5.16-10.32 | 0.181 | 0.123
10.32-15.48 | 0.176 | 0.126
15.48-20.64 | 0.170 | 0.126
20.64-25.80 | 0.170 | 0.120
25.80-30.96 | 0.182 | 0.125
30.96-36.12 | 0.194 | 0.137
36.12-41.28 | 0.205 | 0.154
41.28-46.44 | 0.225 | 0.168
46.44-51.60 | 0.241 | 0.178
Condition
triggered
(A) & meet the geometrical condition (top to bottom i.e. CHD layer1 to TASC layer12)
2. Rate estimation
Notes: 12

## Slide 13
2.3. Interaction probability
Proton
latitude : 46.44-51.60°
He
latitude : 46.44-51.60°
Below 4 GeV, elastic scattering is treated as “interaction” in current EPICS.
Latitude [deg] | proton |  | He | 
 | C/B | D/C | C/B | D/C
0.00-5.16 | 0.860 | 0.232 | 0.999 | 0.123
5.16-10.32 | 0.868 | 0.234 | 0.995 | 0.115
10.32-15.48 | 0.891 | 0.230 | 0.994 | 0.114
15.48-20.64 | 0.926 | 0.226 | 0.993 | 0.112
20.64-25.80 | 0.930 | 0.234 | 0.981 | 0.117
25.80-30.96 | 0.920 | 0.239 | 0.958 | 0.110
30.96-36.12 | 0.884 | 0.236 | 0.898 | 0.131
36.12-41.28 | 0.811 | 0.227 | 0.788 | 0.144
41.28-46.44 | 0.701 | 0.228 | 0.667 | 0.159
46.44-51.60 | 0.606 | 0.235 | 0.595 | 0.169
Condition
triggered
(A) & meet the geometrical condition (top to bottom)
(B) & reach to the bottom layer (without losing all its energy in upper layers)
(C) & penetrate the bottom layer without interaction
2. Rate estimation
※ Total depth of the detector :
1.3 m.f.p. for protons (in a vertical direction)
Notes: 13

## Slide 14
2.4. Rate of penetrating events
By selecting the events in condition (D) (i.e. penetrating the detector without interaction), we get the event rate as below.
Latitude [deg] | proton [/s] |  | He [/s] | 
 | per layer | per log | per layer | per log
0.00-5.16 | 1.33 | 0.049 - 0.096 | 0.10 | 0.0028 - 0.0070
5.16-10.32 | 1.41 | 0.066 - 0.097 | 0.099 | 0.0046 - 0.0085
10.32-15.48 | 1.48 | 0.066 - 0.099 | 0.11 | 0.0038 - 0.0090
15.48-20.64 | 1.67 | 0.072 - 0.11 | 0.12 | 0.0030 - 0.0063
20.64-25.80 | 2.12 | 0.083 - 0.16 | 0.16 | 0.0071 - 0.0099
25.80-30.96 | 2.95 | 0.12 - 0.20 | 0.20 | 0.010 - 0.012
30.96-36.12 | 4.06 | 0.17 - 0.29 | 0.33 | 0.012 - 0.020
36.12-41.28 | 5.40 | 0.22 - 0.35 | 0.50 | 0.021 - 0.036
41.28-46.44 | 7.28 | 0.30 - 0.52 | 0.66 | 0.027 - 0.046
46.44-51.60 | 9.37 | 0.37 - 0.67 | 0.82 | 0.030 - 0.073
Counts / period | 26287 | 1066 - 1856 | 2252 | 87 - 176
2. Rate estimation
Notes: 14

## Slide 15
2.4. Rate of penetrating events
Latitude [deg] | proton [/s] |  |  | He [/s] |  | 
 | trigger | geometry | single penetrating | trigger | geometry | single penetrating
0.00-5.16 | 36.6 (100 %) | 6.68 (18.2 %) | 1.33 (3.64 %) | 6.53 (100 %) | 0.82 (12.5 %) | 0.10 (1.54 %)
5.16-10.32 | 38.2 (100 %) | 6.92 (18.1 %) | 1.41 (3.69 %) | 7.01 (100 %) | 0.86 (12.3 %) | 0.099 (1.41 %)
10.32-15.48 | 40.9 (100 %) | 7.22 (17.6 %) | 1.48 (3.61 %) | 7.83 (100 %) | 0.98 (12.6 %) | 0.11 (1.43 %)
15.48-20.64 | 46.8 (100 %) | 7.98 (17.0%) | 1.67 (3.57 %) | 8.93 (100 %) | 1.12 (12.6 %) | 0.12 (1.40 %)
20.64-25.80 | 57.4 (100%) | 9.77 (17.0 %) | 2.12 (3.70 %) | 11.5 (100 %) | 1.37 (12.0 %) | 0.16 (1.37 %)
25.80-30.96 | 73.8 (100 %) | 13.4 (18.2 %) | 2.95 (4.00 %) | 15.4 (100 %) | 1.93 (12.5 %) | 0.20 (1.32 %)
30.96-36.12 | 100 (100 %) | 19.4 (19.4 %) | 4.06 (4.05 %) | 20.6 (100 %) | 2.82 (13.7 %) | 0.33 (1.61 %)
36.12-41.28 | 143 (100 %) | 29.3 (20.5 %) | 5.40 (3.78 %) | 28.2 (100 %) | 4.36 (15.4 %) | 0.50 (1.76 %)
41.28-46.44 | 202 (100 %) | 45.6 (22.5 %) | 7.28 (3.60 %) | 37.1 (100 %) | 6.22 (16.8 %) | 0.66 (1.78 %)
46.44-51.60 | 273 (100 %) | 65.9 (24.1 %) | 9.37 (3.43 %) | 45.9 (100 %) | 8.18 (17.8 %) | 0.82 (1.80 %)
Counts / period | 7.34×105 (100 %) | 1.62×105 (22.1 %) | 0.26×105 (3.58 %) | 1.32×105 (100 %) | 0.21×105 (16.1 %) | 0.023×105 (1.70 %)
2. Rate estimation
Notes: 15

## Slide 16
2.5. Rate of penetrating events for each PWO log (protons)
2. Rate estimation
1
2
3
4
5
6
7
8
9
10
11
12
1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16
Layer
Notes: 16

## Slide 17
2.5. Rate of penetrating events for each PWO log (He nuclei)
2. Rate estimation
1
2
3
4
5
6
7
8
9
10
11
12
1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16
Layer
Notes: 17

## Slide 18
3. Signal distribution
3.1. Signal distribution
x axis is normalized by MPV of deposited
energy by 2GeV muons (= 20.47 MeV).
incident axis geometrically pass the layer
penetrate the layer
penetrate the layer without interaction
deposited energy on the axis is largest in the layer
with correction of zenith angle
Notes: 18

## Slide 19
3.1. Signal distribution
y axis is normalized at the peak.
Layer #1 (PMT, S/N=30)
Layer #12 (APD, S/N=3.3)
incident axis geometrically pass the layer
penetrate the layer
penetrate the layer without interaction
deposited energy on the axis is largest in the layer
with correction of zenith angle
3. Signal distribution
Notes: 19

## Slide 20
3.2. Energy-dependence of deposited energy
Energy deposition vary with particle energy as described in Bethe-Bloch equation. Average energy of particles vary with geomagnetic intensity, so MIP value may shift as a function of geomagnetic latitude.
3. Signal distribution
We can use this function as a correction factor when we combine the data obtained at different geomagnetic latitudes.
Notes: 20

## Slide 21
3.3. Fitting the distributions
Fit the distribution to Landau Function convoluted with a Gaussian.
3. Signal distribution
 | proton |  | Helium | 
 | number of events (average of 16 logs) | calibration error | number of events (average of 16 logs) | calibration error
1 period | 1380 | 3.52 % | 117 | 1.76 %
5 period | 6899 | 1.57 % | 584 | 0.79 %
Fitting result (bottom layer)
Proton
He
Notes: 21

## Slide 22: End

## Slide 23
4. Event selection method
4.1. Track reconstruction using IMC
For all the single penetrating protons,
- Reconstruct rate : 99.9 %
- Percentage of hitting the most luminous PWO in the bottom layer : 96.2 %
- Angular resolution : 0.26 degree
all events
hit the most luminous PWO in layer #12
Notes: 23

## Slide 24
4. Event selection method
4.2. Rejection of interacted events using TASC
Cut by total deposited energy in TASC
Cut by likelihood
Notes: 24

## Slide 25
4. Event selection method
4.3. Distribution without any selection
single penetrating
interacted
dead in upper layer
total
Notes: 25

## Slide 26
4. Event selection method
4.4. Distribution after the cut by total deposit energy
single penetrating
interacted
dead in upper layer
total
Notes: 26

## Slide 27
4. Event selection method
4.5. Distribution after the cut by likelihood
single penetrating
interacted
dead in upper layer
total
Notes: 27

## Slide 28
4. Event selection method
4.6. If we require the PWO to have maximum dE..
single penetrating
interacted
dead in upper layer
total
Notes: 28