## Slide 1: Introduction to the LHCb detector
Paula Collins,
CERN

## Slide 2
Brief tour of the LHCb experiment
Focus on
  RICH system
  Silicon Vertex Detector
LHCb upgrade in preparation
Talk partly stolen from Vladimir Gligorov, Monica Pepe-Altarelli, Guy Wilkinson,

## Slide 3
L’expérience LHCb

## Slide 4: How to measure and identify particles?
Ideally we would like to measure the position, charge, speed, mass and energy of all particles produced in the collisions.
The particle detector is made up of several layers which all play a role in particle detection
Notes: There is not enough visible mass in rotating spiral galaxies to hold them together
4

## Slide 5
Traditionally colliding beam
experiments have this kind of layout
while fixed target experiments have
a forward geometry
Particle production roughly constant in units of rapidity

## Slide 7
Angular distribution of b and b quarks
forward (backward) and correlated

## Slide 8
700 members
52 institutes
15 countries
1100 members
52 institutes
15 countries
LHCb
Notes: Fundamental research (pursuit of knowledge, not making money)
Pooling resources (money and intellectual)
training

## Slide 9
Pour chaque collision, l’objectif du physicien est de caractériser toutes les différentes particules produites.
La trace laissée par la particule fournit de nombreuses informations utiles, surtout si le détecteur est placé dans un champ magnétique : la charge de la particule, par exemple, est clairement détectable, puisque les particules à charge électrique positive sont déviées dans un certain sens et celles à charge négative dans le sens opposé.
De même, il est possible de déterminer l’impulsion de la particule (la « quantité de mouvement » égale au produit de la masse par la vitesse) : les particules à impulsion élevée se propagent en ligne presque droite, tandis que les particules à faible impulsion décrivent des spirales serrées.
How to measure and identify particles?
Notes: There is not enough visible mass in rotating spiral galaxies to hold them together
9

## Slide 10: Detector Requirements
Key features:
  Highly efficient trigger for both hadronic and leptonic final states to enable high statistics data collection
  Vertexing for secondary vertex identification
  Mass resolution to reduce background
  Particle identification
bt
Bs
K
K
K

Ds
Primary vertex
Mass + pointing constraints to
reduce background
Good primary + secondary vertexing to measure proper time
Good K/ separation
Flavour Tagging
Example: Bs  Ds K

## Slide 11
Notes: 11

## Slide 12
VErtex LOcator
Notes: 12

## Slide 13
Notes: 13

## Slide 14
Ds
Bs
K
K
K

d~1cm
47 mm
144 mm
440 mm
Primary vertex
s(t) ~40 fs
Example: Bs → Ds K
Vertex Locator (Velo)
21 stations of silicon strip detectors (r-f)
~ 4 mm hit resolution
Trigger on large IP tracks
Measurement of decay distance (time)
Notes: 14

## Slide 15
Cherenkov Detectors
Notes: 15

## Slide 16
Cherenkov Detectors
Notes: 16

## Slide 17: Cherenkov light
    Radiation produced when a charged particle travels faster than the speed of light in the medium it is passing through (βc >c/n, with n=refractive index)
    By measuring θc ( radius of ring) the velocity β of the particle is found Then with knowledge of its momentum the mass of the particle can be found
    Light produced in a cone with cosθc=1/βn can be detected as a ring image

## Slide 18
Cherenkov Detectors

btag
Bs
K
K
,K

Ds
Primary vertex
KK : 96.77 ± 0.06%
pK : 3.94 ± 0.02%
Bs → Ds K
Notes: 18

## Slide 19: Tracking detectors
Notes: 19

## Slide 20: Momentum measurement
Inner Tracker
Trigger Tracker
4 layers Si: ~200 mm pitch
Outer Tracker
24 layer
Straws
shit~200mm
sp/p~0.5%
Notes: 20

## Slide 21: Momentum measurement
Inner Tracker
Trigger Tracker
4 layers Si: ~200 mm pitch
Outer Tracker
24 layer
Straws
shit~200mm
sp/p~0.5%

btag
Bs
K
K
p+, K

Ds
Primary vertex
Bs→ Ds K
Bs →Ds p
Mass resolution
s ~14 MeV
Notes: 21

## Slide 22: Calorimeters
Notes: 22

## Slide 23
Muon Detectors
Notes: 23

## Slide 24: Particle identification and L0 trigger
e
h
Calorimeter system :
Level 0 trigger: high ET electron and hadron
Identify electrons, hadrons, π0 ,γ
btag
Bs
K
K
K

Ds
Primary vertex
ECAL (inner modules): σ(E)/E ~ 8.2% /√E + 0.9%

## Slide 25: Particle identification and L0 trigger
m
Muon system:
Level 0 trigger: High Pt muons
Identify muon (also important for flavour tagging)
btag
Bs
K
K
K

Ds
Primary vertex
Multi Wire Proportional Chambers (MWPC)

## Slide 26: LHCb Trigger
Trigger is crucial as sbb is less than 1% of total inelastic cross section and B decays of interest typically have BR < 10-5
b hadrons are long-lived 
  well separated primary and secondary vertices
have a ~large mass
  decay products with large pT
Notes: Check trigger efficiencies

## Slide 27: LHCb trigger
The tracking and particle ID systems of the detector can only be read out at
1 MHz : must therefore start with Calorimeter/Muon based hardware trigger

## Slide 28: LHCb trigger
The tracking and particle ID systems of the detector can only be read out at
1 MHz : must therefore start with Calorimeter/Muon based hardware trigger

## Slide 29: LHCb trigger
The tracking and particle ID systems of the detector can only be read out at
1 MHz : must therefore start with Calorimeter/Muon based hardware trigger
For muons search for a track in all 5 muon system stations
(also momentum estimate from first two stations)
Trigger limitation comes from ability of front-end boards to collect and process information in time

## Slide 30: Trigger Latency
Maximum latency of L0 trigger is 4 ms
Half of this is time for particles to travel to the detector, and their signals to travel throught the cables in the readout system – the other half the time needed to make a decision
Need to be able to process 80 events in parallel
  Muon(s) with high transverse momentum
  Hadrons with high transverse energy etc..
20-30 ms

## Slide 31: ATLAS/CMS triggers vs LHCb

## Slide 32: Focus on RICH

## Slide 33
Cherenkov Radiation in a Nutshell
Fundamental Cherenkov relation:
Both a threshold
and thereafter, an
angular dependence
up to saturation (cosq=1)
Frank-Tamm relation:
So number of photons will also increase with velocity (up to saturation)
Notes: when the speed is above threshold emits photons at a characteristic angle which changes with beta

## Slide 34
Prediction of Cherenkov radiation: Heaviside 1888
Discovery (by accident) : Pavel Cherenkov 1936
Radiation seen when uranyl salts
exposed to radium source.
Sergey Vavilov was Cherenkov’s
supervisor, and hence Russians
refer to Vavilov-Cherenkov radiation
Explanation: Tamm and Frank 1937
Experimental exploitation in HEP
pioneered by Cherenkov himself
Cherenkov: 1905-1990
(Cherenkov, Tamm, Frank: Nobel Prize 1958)
History of Cherenkov Radiation

## Slide 35
Cherenkov :
1936 – discovery
Arthur Roberts: 1960 - first
to propose exploiting c
Tom Ypsilantis: 1977- driving
force behind practical RICH
1905-1990
1912-1994
1928-2000
Fathers of the RICH

## Slide 36
What is a RICH ?
Measurement of cosq from RICH, together
with p, from tracking system, allow
mass, and hence PID to be determined.
This is an excellent way of separating cosq from kaons and protons
The simplest way to exploit Cherenkov radiation is to choose n such
that heavy particles do not emit light. This works OK if p range narrow.
But if we want to do better, or if momentum is far from monochromatic,
→Cherenkov counter (not a RICH!)
then we need to measure cosqC . We have to image the ring. This is a RICH!

## Slide 37
Photodetectors, enclosed
in magnetic shielding box
(not shown) to protect vs
fringe field of dipole magnet
Spherical Mirror, tilted at 0.3
rad to keep photodetectors
outside acceptance
Flat Mirror
Aerogel
LHCb RICH 1: a two-in-one detector
Gas volume

## Slide 38
Hybrid Photo-Diodes (HPDs)
What kind of photodetector do
we need for high performance
PID at the LHCb? Requirements:
Good single photon
efficiency
Sensitivity in visible
Capacity to cover large
area (several m2)
Good spatial resolution
(order mm2)
High rate capabilities
Solution – the HPD:

## Slide 39
HPDs and Testbeam Results

## Slide 40
RICH 2
LHCb data
(preliminary)
Kaon ring
RICH 1
LHCb data
(preliminary)
Kaon ring
with PID
Φ  KK !
Φ  KK ?
No PID
LHCb RICH already performed well
with very first (2009) collision data

## Slide 41
Reconstructed Cherenkov angle vs momentum

## Slide 42
A performance plot

## Slide 43
+
-
B0→ππ
Bs→KK
Λb→pK
Λb→pπ
RICH needed to dig out contributing modes !
Deploy
RICH to
isolate
each
mode !
Two-body charmless B decays are central goal of LHCb physics. Significant
contribution of Penguin diagrams provides entry point for New Physics
B0→Kπ
LHCb preliminary
Inclusive spectrum,
ππ hypothesis
LHCb RICH: performance on ‘B→hh’

## Slide 44: Focus on VELO

## Slide 45: VELO: Current Design
2 retractable detector halves:
  7 (37) mm from beam when closed (open)
21 stations per half with an R and  sensor
Operated in secondary vacuum
300μm Al foil separates detector from beam vacuum
Bi-phase CO2 cooling system
45
RF foil
21 +2 modules
Base
Kapton cables
Cooling manifold
45
Notes: 45

## Slide 46: VELO sensors
46
Ф measuring sensors:
2 regions
Short/long strips
Pitch=36-97μm
Stereo angle.
46
silicon edge just 7 mm from beam!
R measuring sensors:
45o quadrants
Pitch=40-102μm
512
strips
512
strips
512
strips
512
strips
683 inner
strips
1385 outer
strips
300 mm n in n strip sensors (Micron Semiconductor)
Double metal layer for signal routing
Notes: 46

## Slide 47: Silicon very popular in HEP

## Slide 48: Large Systems
DELPHI 1990
DELPHI 1994
DELPHI 1996
CDF 2001
CMS 2007
 2 !

## Slide 49: Silicon sensors for HEP
Start with high resistivity silicon
More elaborate ideas:
n+ side strips – 2d readout
Integrate routing lines on detector
Floating strips for precision
make radiation hard
Hybrid Pixel sensors
Chip (low resistivity silicon)
bump bonded to sensor
Floating pixels for precision
CCD: charge collected in thin layer
and transferred through silicon
MAPS: standard CMOS wafer
Integrates all functions
chip
chip
chip
n+
n+
p
DEPFET:
Fully depleted sensor
with integrated preamp
Al strip
amplifier
SiO2/Si3N4
+ Vbias
+
+
+
+
-
-
-
n bulk
p+
n+
chip

## Slide 50: Basic Principles (1)
The probability of an electron jumping from the valence band to the conduction band is proportional to
e
-Eg
kT
where Eg, the band gap energy is about 1.1 eV and kT=1/40 eV at room temperature
Next step is to dope the silicon with impurities
Some numbers:
Intrinsic carriers: 1010cm-3
Doping concentration: 1012cm-3
Silicon Density: 5 x 1023cm-3
Phosphorus doping: electrons are majority carriers
Boron doping: holes are majority carriers

## Slide 51: Basic Principles (2)
Now we can construct a p-n junction

+
–
+

–
+
+
+
+
+
+
+
+
+
+

–

–

–
+
+
–
+
+
–
–
–
p
n

## Slide 52: Basic Principles (3)

+
–
+

–
+
+
+
+
+
+
+
+

–

–

–
+
+
–
+
+
–
–
–
p
n
When brought together to form a junction, the majority diffuse carriers across the junction. The migration leaves a region of net charge of opposite sign on each side, called the space-charge region or depletion region. The electric field set up in the region prevents further migration of carriers.


Dopant
concentration
Space charge
density
Carrier
density
Electric
field
Electric
potential
Now for the magic part!

## Slide 53: Basic Principles (4)
The depleted part is very nice, but very small
Apply a reverse bias to extend it
Electron-hole pairs created by the traversing particles drift in the electric field
Vd = d2 / (2)

## Slide 54: Basic Principles (5)
By segmenting the implant we can reconstruct the position of the traversing particle in one dimension
x
Typical values used are
pitch : 20 mm – 150 mm
bulk thickness: 150 mm – 500 mm
p side
implants
+
+
+
-
-
-

## Slide 55: Double Metal Technology

## Slide 56: Challenging, but elegant

## Slide 57: Irradiation – LHCb VELO most irradiated silicon so far at LHC
Good testing ground for future upgrades
Change of depletion/operation voltage
  Due to defect levels that are charged in the depleted region -> time and temperature dependent, and very problematic!
Increase of leakage current
  Bulk current due to generation/recombination levels
Damage induced trapping centers
  Decrease in collected signal charge

## Slide 58: Irradiation: strips for LHCb
LHCb vertex detector
1014
1013
neq/cm2 per year
radius [cm]
We expect the classic bulk damage effects
Increased Leakage Current
  Noise
  Hard to bias
Effective Doping Changes
  Depletion growing from n+ side
Annealing effects
  Buildup of negative space charge worsening in time
  Strongly temperature dependent
Depletion voltage [V]
Fluence
High and strongly non uniform irradiation

## Slide 59: Changes in depletion voltage

## Slide 60: LHCb textbook

## Slide 61: LHCb – new textbook
Landau shapes of R sensors are deteriorating
R
f
R sensors are showing inefficiencies at the outer parts which are inversely dependent on HV
Before irradiation
After irradiation
LHCb VELO Preliminary
LHCb VELO Preliminary
LHCb VELO Preliminary
LHCb VELO Preliminary
LHCb VELO Preliminary

## Slide 62: LHCb and VELO Upgrade
Current detector

## Slide 63: Upgrade overview
Current detector → upgraded detector
All sub-detectors read out at
40 MHz for software trigger
UT
SciFi
Pixel
VELO

## Slide 64: Upgrade overview
Current detector → upgraded detector
All sub-detectors read out at
40 MHz for software trigger
UT
SciFi
Pixel
VELO
Replacement of
full tracking system

## Slide 65: Upgrade overview
Current detector → upgraded detector
All sub-detectors read out at
40 MHz for software trigger
UT
SciFi
Pixel
VELO
Replacement of
full tracking system
RICH 1 redesigned; new photodetectors
installed for RICH 1 and RICH 2

## Slide 66: Upgrade overview
Current detector → upgraded detector
All sub-detectors read out at
40 MHz for software trigger
UT
SciFi
Pixel
VELO
Replacement of
full tracking system
Calorimetery and muons:
Redundant components of system removed;
new electronics added; more shielding included
RICH 1 redesigned; new photodetectors
installed for RICH 1 and RICH 2

## Slide 67: Challenges for VELO Upgrade
40 MHz readout (electronics)
Pattern recognition and trigger capabilities
Radiation hardness (and cooling)
How do I cope with having 10 quadrillion particles thrown at me?*
*1016 fluence / cm2 at 4cm SLHC

## Slide 68
VELO Upgrade
VELO halves closed
front view
projected view of sensors
52 modules
Module pitch:
N*25 mm

## Slide 69: Hybrid Pixels

## Slide 70: Hybrid Pixels

## Slide 71: Intelligent Pixels 4 LHCb
sensor
Analogue amplification
Digital processing
Chip read-out
Timepix design requestedand funded by EUDET collaboration
Conventional Medipix2 counting mode remains.
Addition of a clock up to 100MHz allows two new modes.
Time over Threshold
Time of Arrival
Pixels can be individually programmed into one of these three modes
Threshold
Time Over Threshold counts to the falling edge of the pulse
Threshold
Time of Arrival counts to the end of the Shutter

## Slide 72: Or As Results…
Time of Arrival
Strontium Source
Time over Threshold
Ion Beams at HIMAC
Charge deposition studies with various Isotopes
Space Dosimetry
Courtesy L. Pinsky, Univ. Houston

## Slide 73: Summary
LHCb is a very innovative, and so far very successful experiment with an exciting future
I hope that in the future you may join us!
ברוכים הבאים!
ביקור נעים!