## Slide 1: FPGA Use within the Detector Volume
Tullio Grassi (Univ. of Maryland)
ECFA High Luminosity LHC Experiments Workshop
21-23 October 2014
Disclaimer: difficult to cover all cases, this talk is a partial view.

## Slide 2: What are FPGAs ?
The data needed to set all programmable options of an FPGA is often called “Configuration data“.
The circuit realized with the Logic blocks and interconnects in an FPGA is called “User Logic”.
A Field Programmable Gate Array (FPGA) is a integrated circuit which contains lots of logic blocks.
Logic blocks can be connected together in a programmable way.
inputs and outputs are also programmable, in direction, strength and standard (CMOS, LVPECL, LVDS, etc).
Each logic block can be programmed to perform a boolean operation (in the LUT) and store a single bit in a Flip-Flop.
Logic Block

## Slide 3: Why do we care about that ?
In HEP detectors and accelerators, FPGAs have become extremely useful to build digital hardware tailored to specific requirements, including non-standard data processing and interfaces.
The advantages over traditional circuit boards with discrete components are that:
FPGAs are denser, cheaper, faster.
The advantages over Application-Specific Integrated Circuits are that:
part of the FPGA development is done by the vendor
FPGAs often can be bought in small quantities
FPGAs are programmable by the user
Being commercial circuits, they are not (necessarily) tolerant to ionizing radiations
 this point is the focus of the talk.
Many detector and accelerator subsystems use or will use FPGAs in radiation areas (but not in extreme radiation areas like central trackers).

## Slide 4: FPGAs in HEP: trends
in recent FEE systems, FPGAs (will/could) take advantage of newer functions: high-speed links for increased data readout, PLLs for clock management related to synchronization with the accelerator clock, etc.
Powering newer FPGAs becomes more complicate: need to provide higher currents at lower voltages.
initially FPGAs were simple boolean logic; later other blocks have been integrated: CPU, PLL, high-speed communication, etc.
in the HEP Front-End Electronics installed around 2005, FPGAs were mostly used for control and readout logic with external high speed links.

## Slide 5: FPGA types by market
Military and aerospace markets: FPGAs designed explicitly for radiation hardness. HEP projects normally cannot (afford to) buy them. Not covered here.
Commercial markets: all other applications. Accessible to HEP projects  covered in this talk.

## Slide 6: FPGA types by technology
User Logic : commonly built with CMOS fabrication processes (at least for commercial grade FPGAs).
Configuration memory : see table.
Technology of the memory element | Main Vendors
SRAM (Static RAM) | Altera, Atmel, Lattice, Xilinx
Anti-fuse: one-time-programmable | MicroSemi, Aeroflex, Quicklogic
Flash memory cells | MicroSemi

## Slide 7: Radiation effects on CMOS digital circuits (not limited to FPGAs)
7
7
TID = Total Ionization Dose. Measured in Grey = Gy (or in rad: 1 rad = 100 Gy)
SEE = Single-Event Effects :
SEL = Single-Event Latchup
SEU = Single-Event Upset
SET = Single-Event Transient
SEFI = Single-Event Functional Interrupt
SEGR = Single-Event Gate Rupture
SEB = Single-Event Burnout

## Slide 8: Radiation effects on commercial FPGAs at LHC (LET < 40MeV∙cm2/mg [8])
8
Memory cells | TID (degradation, then failure) | SEU on configuration | SET on configuration | SEL
SRAM | Virtex-6: ~3.8 kGy [1]. Arria GX: degrades from 1.7 kGy, still alive at 70 kGy [13] | Yes  need reconfiguration (partial or total) | Yes | No, on recent Xilinx families [12, 13].
Anti-fuse | Aeroflex Eclipse: 3 kGy [18] | No | Yes | No [12]
Flash | ProASIC3: fails at ~300 Gy. Igloo2: one sample failed at ~1000 Gy. SmartFusion2: one sample survived 380 Gy; reprogramming fails at ~20 Gy [10] | No | Yes | No on ProASIC3x [8]. Suspect non-destructive SELs on SmartFusion2 [10]
SEU and SET in the User Logic normally are mitigated by the user logic itself, not by the technology.
1 Gy = 100 rad
10 Gy = 1 krad

## Slide 9: How to proceed ?
FPGA are increasingly used in radiation areas.
Their behavior under radiation has to be qualified, but this is difficult because:
Modern FPGAs have many different blocks (previously mentioned)
These blocks can have a wide range of programmable options
FPGAs keep evolving
Batch-to-batch variations
Each case of User Logic should be qualified (TMR, safe FSM, EDAC codes on RAM, etc).
We could benefit from:
common qualification programs
common procurement strategies
An initial attempt has been the “Workshop on FPGAs for High-Energy Physics” held at CERN on March 2014.
Results should be shared between our community, but preferably not with the general public because of: undesirable attention, vendors less likely to share internal data, etc.
Initial attempt: https://twiki.cern.ch/twiki/bin/viewauth/FPGARadTol/

## Slide 11: Back-up slides

## Slide 12: FEE systems of CMS
12
12
Sub-system | Approx radiation | FPGAs in 2008-2012 | FPGAs after 2012 (radiation ~6x higher)
Tracker [2] | 200 kGy. 1014 n/cm2 | No FPGAs (ASICs only) | No FPGAs (ASICs only)
ECAL [3,4] | 25 kGy. | No FPGAs (ASICs only) | No FPGAs (ASICs only)
HCAL [5] | 3 Gy. 1011 n/cm2 | Actel anti-fuse FPGA, for control only | igloo2 (flash) for control, data processing, TDC and transmission from 2016
Muon detectors | 0.4 Gy. 5x1010n/cm2 | SRAM FPGAs [6, 7]. | igloo2 (flash) for control, data processing, TDC and transmission from 2014 [15]
CT-PPS | 200 Gy, 2x1012 n/cm2 per 100/fb integrated lumin. | Did not exist | igloo2 (flash) for control, data processing, TDC and transmission from 2018 ?

## Slide 13: FEE systems of ATLAS
13
13
Sub-system | Approx radiation | FPGAs in 2008-2023 | FPGAs after 2023 (radiation ~6x higher)
Tracker | Xx kGy. 1014 n/cm2 | No FPGAs (ASICs only) | 
Liquid Argon Calorimeter [16] |  |  | On chamber (3.4 kGy): probably no FPGAs. On sTGC (90 Gy): investigate with xilinx for processing and 10 Gbps readout links.
Tile calorimeter [17] | 15 Gy. 1011 n/cm2 | 640 Mb/s, severe errors in data transmission, loss of configurations | Demo project with xilinx for processing and 10 Gbps readout links
Muon detectors | xx Gy. 5x1010n/cm2 |  | 

## Slide 14: FEE systems of LHCb
14
14
Sub-system [9, 10] | Approx radiation in 2008-2018 | FPGAs in 2008-2018 | FPGAs after 2018 (radiation ~6x higher)
Inner Tracker | 60 kGy. 1014 n/cm2 | No FPGAs in the hot zone (ASICs only) | Under study (probably not required)
RICH | 240 Gy, 1012 n/cm2 | Actel AX (antifuse) + Actel ProAsicPlus (flash) for controls | Xilinx Kintex7
Outer Tracker | 70 Gy. 1012 n/cm2 | No FPGAs in the hot zone (ASICs only) | 
SciFi Tracker |  |  | Under study (Microsemi Igloo2)
Calorimeters | 50 Gy. 1012 n/cm2 | Actel AX (antifuse) for 80 MHz processing, Actel ProAsicPlus (flash) for 40MHz processing and control [9] | Under study (Microsemi Igloo2)
Muons [11] | 80 Gy. 1012 n/cm2 | Actel ProAsicPlus, for calibration system | Under study (Flash device)

## Slide 15: FEE systems of ALICE
Sub-system | Approx radiation | FPGAs in 2008-2012 | FPGAs after 2012 (radiation higher)
TPC [20] | 16 Gy. 1011 n/cm2 [21] | Virtex-II Pro (SRAM) for datapath, with its configuration verified and refreshed by an Actel ProASIC+ (flash) | Microsemi SmartFusion2 (flash). Links up to 5 Gbps. Problems observed. FPGA PLL loss of lock → use TTCrx instead [10]. ProASIC3 (flash) for radmon.
DDL (Detector Data Link, common to all subsystems) |  | Actel ProASIC+ (flash). 200 MB/s links | 
All others | ~0 at the FPGA location |  | 

## Slide 16: SEU prevention in FPGAs
16
16
SEU on Flip-flops  TMR, fault-tolerant FSM.
There are two commercial synthesisers that can do automatic TMR of flip-flops, in order to prevent SEU:
Synplify: http://www.actel.com/documents/SynplifyRH_AN.pdf It is in use in Cern by a few groups, so far so good (circuits not yet deployed).
Precision RT: http://www.mentor.com/products/fpga/synthesis/precision-rad-tolerant/ (ITAR limited)
SEU on memory  encoding

## Slide 17: SET prevention in FPGAs
17
17
Prevention of SETs:
TMR that includes combinatorial logic
filtering with guard-gate
Precision Rad-Tolerant can do TMR of combinatorial logic. Apparently this feature is not supported for Actel FPGA (as of today).
Commercially available tools are evolving rapidily wrt SEU and SET  keep watching.
In the Microelectronics Section of CERN, some designers have been using a custom script that generates automatically TMR on registers and combinatorial logic.
The script supports only Verilog 1995 designs.
The script is available to people registered on the CERN FPGARadTol web page.

## Slide 18: SEL prevention
18
18
A SEL is a latch-up caused by a particle crossing the circuit.
It can happen on the internal nodes (while normal latchups occur mostly on the I/Os due to ESD).
Most modern FPGAs are immune from SEL.
But other commercial components can be affected by SEL.
 external SEL protection circuit.

## Slide 19: SEL-protection circuits: a generic scheme
19
19
R (< 1 ohm)
VCC_IN
Voltage
threshold
Monostable circuit
 ~ 1 s
PMOS SWITCH
VCC
SEL-sensitive
circuit
When a SEL-sensitive circuit develop a SEL, it draws more current. An external circuit can detected this situation and cycle the power.
Problem: also the protection circuit can be affected by radiation. But being a simpler circuit, it is possible to design it so that it is very unlikely that it develops a problem.

## Slide 20: SEFI
20
SEFI = Single Event Functional Interrupt
The definition can vary according to the authors, but it normally indicates an SEE which affects the entire device, for instance:
power-on reset
global reset,
global tristate
problems in the circuit that program the rest of the FPGA
For an FPGA, it is difficult or impossible to mitigate SEFI within the FPGA design. SEFI could be mitigated at the system level.
20

## Slide 21: References
21
21
[1] Jano Gebelein, “An approach to system-wide fault tolerance for FPGAs”, http://microelectronics.esa.int/fiws/WFIFT_P11_Gebelein.pdf
[2] “Neutron damage studies of semiconductor lasers for the CMS tracker optical data links”, K. Gill et al.
http://cms-tk-opto.web.cern.ch/cms-tk-opto/tk/publications/wdocs/karl2.pdf
[3] “The Electromagnetic Calorimeter of CMS, Summary and Status”, Werner Lustermann
http://iopscience.iop.org/1742-6596/160/1/012044/pdf/jpconf9_160_012044.pdf
[4] “The MGPA Electromagnetic Calorimeter Readout Chip for CMS “, M.Raymond et al.
http://www.imperial.ac.uk/research/hep/preprints/03-6.pdf
[5] “Radiation Validation of CMS HCAL ESR” , internal presentation by Julie Whitmore
http://cmsdoc.cern.ch/cms/HCAL/document/www-ppd.fnal.gov/tshaw.myweb/CMS/presentations/Raddam_ESR.pdf
[6] “EMU DAQ MotherBoard”, internal presentation by Jianhui Gu
http://www.physics.ohio-state.edu/~cms/dmb/esr.pdf
[7] “TECHNICAL PROPOSAL FOR THE UPGRADE OF THE CMS DETECTOR THROUGH 2020”, version of 2011/01/14
[8] Private communication, Federico Faccio
https://twiki.cern.ch/twiki/pub/FPGARadTol/InformationOfInterest/SEL_on_ProASIC3_by_Faccio.pdf
[9] https://owncloud.lal.in2p3.fr/public.php?service=files&t=32382bebee98be725770e1e9fc465ddb
[10] https://indico.cern.ch/event/299180/session/5/contribution/73/material/slides/0.pptx
[11] “Muon Off Detector Electronics Board”, A. Balla, P. Ciambrone
https://indico.cern.ch/getFile.py/access?contribId=s1t15&resId=0&materialId=0&confId=a054562
[12] “Radiation Effects in FPGAs,” J. Wang, in 9th Workshop on Electronics for LHC Experiments, October 2003
http://cdsweb.cern.ch/record/712037/files/p34.pdf?version=1
[13] “Radiation tolerance tests of SRAM-based FPGAs for the potential usage in the readout
electronics for the LHCb experiment”, http://iopscience.iop.org/1748-0221/9/02/C02028/pdf/1748-0221_9_02_C02028.pdf
[14] ”RT ProASIC3: The Low-Power, Non-Volatile, Re-programmable and Radiation-Tolerant Flash-based FPGA”, Sana Rezgui, 2010 CMOS Emerging Technologies Workshop, http://www.cmoset.com/uploads/Sana_Rezgui_2010.pdf
[15] https://indico.cern.ch/event/336562/contribution/5/material/slides/0.pdf
[16] https://indico.cern.ch/event/300532/contribution/7/material/slides/1.pdf
[17] https://indico.cern.ch/event/299180/session/5/contribution/12/material/slides/0.pdf
[18] http://ams.aeroflex.com/pagesproduct/datasheets/RadTolEclipseFPGA.pdf
[20] https://indico.cern.ch/event/300532/contribution/11/material/slides/1.pdf
[21] https://cds.cern.ch/record/921042/