## Slide 1: Recent results from Test Beam of Hybrid THGEM – Micromegas Photon Detector
Shuddha Shankar Dasgupta
INFN Trieste and Trieste University
On behalf of:
Alessandria, Aveiro, Budapest, Calcutta, Freiburg, Liberec, Prague, Torino, Trieste
collaboration

## Slide 2: Outline
Hybrid THGEM + MM PD.
The new Hybrid PD equipped with capacitive anode.
Test Beam at CERN PS T10.
Results from analogue readout.
Results from digital readout.
Conclusion

## Slide 3: First Hybrid Photon Detector prototype: working principle and results
Hybrid detector
Drift wires
THGEM
Micro Mesh
Anode
UV LED Source
Kapton/Fused Silica Window
55Fe X–Ray Source.
128 mm
5 mm
15 mm
Bulk Micromegas: courtesy of Saclay COMPASS colleagues
FIRST SMALL SIZE PROTOTYPE
CAEN N471A High Voltage PSU
Charge Sensitive Pre amplifier CREMAT CR – 110/111
Normal Readout Chain
Double THGEM ∆V scan. Plateau represents the unitary THGEM gain, corresponding MM GAIN ~ 500. Gas: Ar:CH4 30:70
Preliminary test
55Fe source,
Gas used: Ar:CO2 70:30.
Chart: Channels
Hybrid with double THGEMs and tested with UV LED
Gain ≈ 9.5E5
Gas: Ar:CO2 70:30
105
Effective GAIN ~ 3E5

## Slide 4: 300X300mm2 Hybrid prototype with THGEM
Micromegas produced by Rui at CERN by Bulk technology
Anode Pads (12mm X 12mm)
THGEM with 6 Sectors

## Slide 5: 300 X 300 mm2 Hybrid prototype: Micromegas only
300X300 mm2 micromesh checked for uniformity with 55Fe source
Result obtained:
The Micro Mesh was produced by Rui de Olivera in CERN with BULK Technology.
Checked with Ar:CO2 70:30, CAEN N471A HV PS, CREMAT CR – 110/111 and Normal Readout chain.

## Slide 6: 300 X 300 mm2 Hybrid prototype: Micromegas + THGEM
Chart: ∆V Scan of Sectors of a 300X 300 mm2 THGEM. VMESH = 640V. Source used: 55Fe X – Ray source; Gas used Ar:CH4 30:70.
| 320 | 370 | 470 | 570 | 670 | 770 | 870 | 970 | 1070 | 1170 | 1270 | 1320 | 1370 | 1420 | 1470 | 1520 | 1570 | 1620 | 1670 | 1695 | 1720 | 1745 | 1770 | 1780 | 1790 | 1795 | 1800 | 1805 | 1810 | 1815 | 1820 | 1825 | 1830 | 1835 | 1840 | 1845 | 1850
Sector1 | 153 | 159 | 188 | 201 | 222 | 222 | 246 | 315 | 404 | 608 | 1007 | 1358 | 1898 | 2617 | 3779 | 5286 | 8246 | 13056 | 20430 | 25822 | 33486 | 41363 | 54710 | 58542 | 66999 | 70964 | 73607 | 78364 | 81800 | 85501 | 91975 | 96204 | 101887 | 107883 | 110741 | 118934 | 124088
Sector2 | 165 | 171 | 172 | 195 | 201 | 222 | 256 | 307 | 415 | 613 | 983 | 1340 | 1884 | 2595 | 3748 | 5471 | 8246 | 12766 | 21170 | 26271 | 33989 | 42023 | 53652 | 60788 | 66470 | 68981 | 71889 | 76382 | 80346 | 84840 | 87482 | 94486 | 96864 | 103076 | 110078
Sector3 | 124 | 153 | 174 | 201 | 209 | 225 | 259 | 304 | 389 | 579 | 943 | 1226 | 1665 | 2281 | 3285 | 4678 | 7110 | 11206 | 17021 | 22148 | 28095 | 34781 | 44005 | 49159 | 53388 | 56824 | 59995 | 66206 | 72417 | 80346 | 88011 | 101093
Sector4 | 109 | 118 | 133 | 156 | 161 | 173 | 199 | 238 | 325 | 454 | 753 | 991 | 1214 | 1682 | 2452 | 3620 | 5500 | 8583 | 13989 | 17808 | 21836 | 28843 | 35733 | 40754 | 45425 | 47527 | 50563 | 55468 | 60547 | 68371 | 74093 | 82034 | 91026 | 103696 | 104221
Sector5 | 161 | 201 | 201 | 222 | 241 | 267 | 330 | 455 | 677 | 1121 | 1528 | 2125 | 3008 | 4358 | 6475 | 9488 | 14986 | 24923 | 32006 | 41098 | 50349 | 68717 | 73475 | 84047 | 84575 | 91447 | 101622 | 103340 | 112194 | 123427 | 126334 | 136245 | 146687 | 150385 | 152367 | 165979 | 168622 | 168622 | 179590 | 180799 | 194659 | 201394 | 208002
Sector6 | 198 | 217 | 225 | 235 | 275 | 346 | 433 | 687 | 1072 | 1464 | 1953 | 2783 | 3962 | 5682 | 9039 | 13585 | 22095 | 28623 | 36394 | 44005 | 59599 | 66999 | 71625 | 74400 | 81139 | 88011 | 89465 | 96601 | 100169 | 106776
105
300 X 300mm2 THGEM + Micromegas provide the same response as the 30 X 30 mm2 prototype.
All the 6 sectors of the THGEM have been checked with different bias voltages.
Maximum effective gain achieved: 105 or larger with 55Fe X – Ray source.
Ar:CH4 30:70 is the reference gas mixture for compass THGEM photon detector.

## Slide 7: Hybrid Micromegas + THGEM
  55Fe main peak
   total gain
  55Fe escape peak
  55Fe main peak,
  MICROMEGAS only
   MICROMEGAS gain

## Slide 8: Hybrid with double THGEMs
Chart: Effective GAIN vs. VMESH Scan
| 39.0625 | 41.015625 | 42.96875 | 44.921875 | 46.875 | 48.828125 | 50.78125 | 52.734375 | 54.6875 | 54.6875
DV1 = 1550V; DV2 = 1450V; | 1287 | 1835 | 3211 | 5362 | 9300 | 15479 | 25984 | 50292 | 84601 | 84078
DV1 = 1450V; DV2 = 1550V; | 1195 | 1835 | 3321 | 5286 | 8350 | 16453 | 26822 | 46939 | 85120 | 76083
DV1 = 1550V; DV2 = 1550V; | 4248 | 7446 | 11304 | 20667 | 36017 | 61640 | 103805 | 194635
Chart: Effective GAIN vs. one of the ∆V Scan, keeping VMESH and other ∆V constant
| 1300 | 1350 | 1400 | 1450 | 1500 | 1550
DV2 = 1550V; V_MESH = 700V | 28493 | 40732 | 54934 | 85120 | 120933 | 194635
DV1 = 1550V; V_MESH = 700V | 26386 | 38024 | 44876 | 60609 | 84601 | 119895 | 194635
Staggered configuration
Source used: 55Fe, Gas used: Ar:CH4 30:70

## Slide 9: Improving the detector concept
At the test beam two hybrid detectors have been tested.
The first one has been described so far.
The second is identical but equipped with a capacitive anode architecture.
      Inspired by ATLAS MAMMA principle already presented by J. Wotschack.
      Positive voltage bias on anodic pads via external resistors.
      Mesh at ground (only not segmented electrode).
      Signal readout via capacitively coupled pads.

## Slide 10: Readout via capacitive anode
PCB
0.10 mm
fiberglass
Metallic pads
HV to blue pad through the hole of red pad
Readout Amplifier
  Scheme (not to scale)
    Only 1 single pad shown
  Principle
    Blue pad at HV via internal connection
    Resistive (individual pad resistor at the PCB rear surface)
    Red pad: signal induced by RC coupling

## Slide 11: Layout of the capacitive anode PCB
We already did extensive study with a small prototype to find out the optimal resistance.
The optimal resistance for <10% signal loss has been found = 1MΩ.
We use a resistor array for each 8 pads.
Resistor arrays
(from HV line to blue pads)
Signal connectors
(from red pads)
Section of the back part of the 300 X 300 mm2 anode PCB. It has 24 X 24 = 576 (12 X 12mm) pads. For each 16 pads we have this readout board which is used to read all of these 16 pads together through the LEMO female connector.
PCB
0.10 mm
fiberglass
Metallic pads
HV to blue pad through the hole of red pad

## Slide 12: Micromegas with capacitive anode
From now on all results refer to the capacitive Micromegas chamber.

## Slide 13: CsI Deposit at CERN
CsI deposition Plant
THGEMs to be coated
QE measurement

## Slide 14: Assembling the Photon Detector
Here this picture shows the delicate operation carried out in CERN in a controlled environment to assembles the CsI coated THGEM to the chamber.

## Slide 15: setup for Test Beam
We set up our prototype in CERN PS T10 beam line.
We used a truncate cone fused silica radiator for Cerenkov photons.
For trigger we use 2 finger cross in front + 2 finger cross in back+ a Paddle.
CERN PS, T10
Trigger = Front Finger cross X Back Finger cross X Paddle.
Beam area setup

## Slide 16: Beam area installation

## Slide 17: Analog Read – Out
TRG
Input
Channels
Gandalf
Cremat Pre – Amplifier Box
Test Input
Output to Amplifier
Physics Trigger
Pulser
Gandalf
Input
TRG IN
Detector
Out
Amplifier
Out
In
Pre – Amplifier (CREMAT CR – 110/CR – 111)
Test Input
Out
Input
Analogue readout Schematic diagram

## Slide 18: Amplitude distribution of beam particles signals
Gain ~ 12.5K
(16 pad:
the trigger covers a larger area)
Gain ~ 3.8 K
(32 pad:
trigger fully included 
100% efficiency for MIPs)
MICROMEGAS:
600 V 650 V 675 V
Evaluation of the landau due to the charged particles with Mesh voltage

## Slide 19: Amplitude distribution of beam particles signals for different Drift field values
EDrift = -100 V/cm
EDrift = +1000 V/cm

## Slide 20: Charged particle signals vs. drift field
100 V/cm

## Slide 21: Photon signal vs. drift field
X – Axis of the plot is
Y – Axis is the drift field applied.
The number of detected photoelectrons depends on the drift field:
photoelctron detection efficiency to be maximized
100 V/cm

## Slide 22: Photon signal and Charged particle signal vs. drift field
50V/cm
Red points are scaled.

## Slide 23: Cerenkov Photon amplitude Distribution
Gain ~ 130K
Č photon
beam
~ 4 times the gain for the same stability condition compared to triple THGEM configuration in 2012

## Slide 24: Interceptor position scan
Interceptor Scan
The remotely controlled movable interceptor allows for changing the number of photons in the corona
Chart: Photon multiplicity per trigger vs interceptor position
| 3.8210000000000001E-2 | 17.690000000000001 | 15.93 | 14.1 | 12.23 | 10.39 | 8.5589999999999993 | 6.1509999999999998 | 4.3179999999999996 | 2.484 | 0.64949999999999997 | 0
th 20 | 0.27728 | 0.062218 | 0.063736 | 0.10066 | 0.12189 | 0.14993 | 0.17399 | 0.18602 | 0.23091 | 0.26717 | 0.25829 | 0.28187 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
fit th20 | 0.063736 | 0.10066 | 0.12189 | 0.14993 | 0.17399 | 0.18602 | 0.23091 | 0.26717

## Slide 25: Digital Readout
Digital Readout Setup
DREISAM CARD
ROOF Board
CMAD Boards
Protection Boards
Readout chain: same as RICH-1 – MAPMT
  C-MAD
  Roof
  DREISAM card
No need for FE protection boards – 2012:
Fighting against noise during the entire Test
  Impossible to run with all channels together
  Very high thresholds ( from 6 to 15 fC) (~3 fC in 2012 Test Beam)

## Slide 26: Cerenkov Ring Image
OFF
Log scale
2012 for comparison
2012 for comparison
Digital Images

## Slide 27: Time response
The time distribution response is improved and affected by a lower noise level if compared to the 2012 data
  For comparison: triple THGEM time spectra from 2012 test beam
  Capacitive/resistive hybrid PD 2014
  2012 lower gain

## Slide 28: Digital results
Time Resolution

## Slide 29: Conclusion
The hybrid with capacitive anode performed at the Test Beam as they did in the Lab.
The hybrid PD with capacitive micromegash allows to operate the MICROMEGAS at voltage bias which are 100 V larger than for the standard one 
  Larger gain with less THGEM voltage and higher stability
  No other large MPGD has ever been operated with a beam at 105 gain
  Excellent time response
  Nice device suitable for single Cherenkov photon detection
Future GOAL:
  Read-out & noise need to fine tuned
  HV powering system can be upgraded.
  600 X 600mm2 prototype is in the preparation to be tested at our INFN Trieste LAB.

## Slide 30
Thank you

## Slide 31: 55Fe Spectra for 11780 gain of the capacitive Micromegas

## Slide 32: Time response from 2011
Small prototype: time response study (2011)
G = 2.0 * 105
G = 1.1 * 105
G = 0.9 * 105
G = 1.4 * 105

## Slide 33: BACK UP
Each CMAD readout board read 8 pads.
Each ROOF board connects 8 CMAD card (means: 64 pads)
Each DREISAM connected to each roof boards (Means each DRIESAM read 64 Pads)
So we need 12 DREISAM boards where 6 of the roofs are half empty.
64 channels per card, compact solution
optical data transfer (40 MByte/s)
high rates per channel 10 MHz @ 100 kHz trigger rate
time resolution < 100 ps
based on dead time free F1-TDC

## Slide 34: Progress of 600 X 600mm2 prototype
Now the goal is to build a 600X600mm2 Prototype to be build and to test it in lab.
The pieces are already produced and ready to be commissioned in our Trieste Lab.

## Slide 35: Progress of 600 X 600mm2 prototype
Production procedures for 300X600mm2 THGEMs
  stripping dry-film
  development
  etching
  image transfer

## Slide 36: Progress of 600 X 600mm2 prototype
  multi-spindle drilling

## Slide 37: Progress of 600 X 600mm2 prototype
  connector and anode HV side
  Micromegas side (protected)

## Slide 38: Progress of 600 X 600mm2 prototype

## Slide 39: Progress of 600 X 600mm2 prototype

## Slide 40: Progress of 600 X 600mm2 prototype

## Slide 41: Progress of 600 X 600mm2 prototype

## Slide 42: Progress of 600 X 600mm2 prototype

## Slide 43: Progress of 600 X 600mm2 prototype

## Slide 44: Progress of 600 X 600mm2 prototype

## Slide 45: Progress of 600 X 600mm2 prototype

## Slide 46: Progress of 600 X 600mm2 prototype
large fused silica windows
field and drift wire frame
PD support frames
lenses and MAPMTs
THGEMs +CsI and Micromegas

## Slide 47: Progress of 600 X 600mm2 prototype
radiator:
C4F10
5 m
6 m
3 m
MWPC’s + CsI
UV mirror
wall
Al vessel
radiator gas: C4F10
PMTs
beam pipe

## Slide 48: Progress of 600 X 600mm2 prototype
radiator:
C4F10
5 m
6 m
3 m
MWPC’s + CsI
UV mirror
wall
Al vessel
radiator gas: C4F10
PMTs
beam pipe
THGEMs + CsI
Foreseen for 2016