## Slide 1: Beam based model
Tobias Persson
Jonne Moeskops
Mattias Fjellstrom
Jaime Coello de Portugal
Ghislain Roy
Piotr Skowroński

## Slide 2: The Model (our understanding)
Provide more detailed machine model that accounts for all dynamical information available in the control system
  For example orbit or implemented corrections
  For a given moment in past as well as “on-line”
Applications
  To check effects of settings changes (what happens if …)
  To help the machine setup
  To provide data for model-based measurements
  Verify the accuracy of the model against measurements

## Slide 3: Global Goals
Machine settings
online and historic
the model
MADX scripts
Twiss table
Strength files
Converter(s)
Measurements
Orbit modelling
machine setup
model dependent measurements
machine studies
Tools for
Improving the model
Tools for
Beam orbit
Misalignments

## Slide 4: Things which will be of extra interest for the OMC
Get the orbit and settings of the machine at a certain time.
  Useful for analysing data from an MD.
  Things which are not yet done but in the plan:
Create a model with the present settings of the MQTs.
  Will be an improved model which can use for the full response.
After a beam process is created the settings can be extracted and the MD can be validated calmly in the office.
Create model between match points.

## Slide 5: Model extractor
lhcmodel/lhcmodelextractor
Extends Jorg’s YASP orbit extractor
  accsoft-steering-logging-extractor-gui
Added command line options preserving the GUI functionality
For optics, it finds nominal b* and links appropriate modifier files
/afs/cern.ch/eng/lhc_online_model/v0.01/extractor/ Examples file gives a list of concrete examples
  Extract beam orbits between two Timestamps every minute and writes them to directory ./beamorbits/
lhc-model-extractor.sh -oe
-time "2012-09-01 11:00:00" "2012-09-01 11:02:00" 00 01 00
-p beamorbits/
  Extract beam orbits between begin of RAMP and end of STABLE every 30 minutes for fill 3000
lhc-model-extractor.sh -oe -fill 3000 ramp stable 00 30 00
  Extract optics and orbit from timber and lsa to create a Madx script for beam 1, write output files to directory ./madxextract/ and reads configurations from the default file configuration.properties
lhc-model-extractor.sh -e "2012-08-24 09:00:00" B1 -p madxextract/
Tobias Persson
Jonne Moeskops

## Slide 6: Summary
For me the project has evolved into an infra structure project for analysis.
  Instead of everyone writing there own scripts to extract orbits, tune, etc it is provided by the bb-model.
  The members of the OMC team could in this context be one of the main users.
    So please come with feedback and suggestions!