## Slide 1
Pawel Krakowski
TE-VSC-ICM
LHC R2E for vacuum control systems
Vacuum, Surfaces & Coatings Group
Technology Department
Automation Forum-electronics session, 6 Nov 2014

## Slide 2
Types of ionizing radiation
Radiation levels in LHC
Radiation effects on electronics
Vacuum controls exposed to radiation
LHC R2E activities
Introduction

## Slide 3
Types of Ionizing radiation
Bq [s-1] the quantity of radioactive material that decays per second
Fluence [cm-2∙y-1] (HEH – High Energy Hadron) the total number of particles that intersect a unit area in a specific time interval of interest.
Gy [J∙kg-1] (Dose) the absorption of one joule of radiation energy by one kilogram of matter
Sv [J∙kg-1] the health effect of low levels of ionizing radiation on the human body. Depends on the type of radiation.
How many apples will fall on this area in a year?
The particle
Hits received by the sleeper
How many apples fall from a tree in time ?
Will the headache be the same regardless of the size or weight of the apple?
The source
Charged particles interact strongly and ionize directly
Neutral particles
interact less, ionize indirectly, penetrate further

## Slide 4
Material Damage
R2E Cumulative damage
R2E Single-Event
Effects
LHC machine electronics
Experiments
Protected UJ
Shielded RE/UA
Tunnel ARCs/LSS
Commercial
Hardened RadTol
Custom Boards +commercial
Damage
Experiment caverns
Earth orbit
deep space
environment
Radiation levels in LHC

## Slide 5
Accelerator tunnel
Underground service areas
Mobile equipment
LSS : only passive components
ARC : some active components
Sector valves and ion pumps
Pressure gauges
Other
only used without beam
Pumps and gauges
Vacuum controls in LHC

## Slide 6
For now all controls in low HEH areas and negligible TID
P7
P8
P1
P2
P3
P4
P5
P6
RE18
UA151
UA27
UA23
RE28
RE22
UJ32
UJ33
RE38
RE42
UA43
UA47
RE48
RE52
RE58
USC55
UA63
UA67
RE62
RE68
TZ76
UJ76 Patchpanels only
RE78
UA83
UA87
RE88
RE82
Vacuum controls in service areas

## Slide 7
with HL-LHC
TID is negligible all the time
HEH fluence will increase by one order of magnitude
HEH flux levels in service areas
Location |  | RUN-2 |  | RUN-3 | HL-LHC | 
 |  | 2015 | [2016; 2018] | [2020; 2022] | [2025; 2035+] | 
 |  | HEH Fluence [cm-2y-1] |  |  |  | 
REs | shielding as is | - | 1E+06 | 2E+06 | 4E+06 | 8E+06
UA23, UA83 | ok, but to be monitored during operation | 1E+06 | 2E+06 | 4E+06 | 8E+06 | 2E+07
TZ76 (1st 15m), UA63/67 (behind ducts) UJ33 |  |  |  |  |  | 
All Other OK |  |  |  |  |  | 

## Slide 8
Radiation effects
Radiation effects on electronics
Cumulative accumulating during the whole LHC lifetime, due to the energy deposited by radiation in the electronics
Stochastic
immediate effects very localized, event induced by a single particle
SEE (Single event effects)
TID (Total ionizing dose) the dose is deposited by particles passing through the materials constituting the electronic devices.
DD (Displacement damage)
Transient
SEU SEFI
Destructive
SEL SET SEGR SEBO
MOS
Bipolars
Optoel.
CMOS

## Slide 9
n
Silicon atoms
Atomic level
Vacancies
Frankel defect
Displacement damage
Defects accumulate and gradually destroy the silicon lattice
no charge

## Slide 10
MOS transistor
Source
Gate
Drain
Gate Oxide
p-type
extra holes
SiO insulator
Charged particle
Charged particle ionize the matter creating electron-hole pairs
Radiation effects on electronics
n-type
extra electrons

## Slide 11
Radiation effects on electronics
electrons collected by junctions create
parasitic current
SEE (Single Event Effect)
holes accumulate and gradually degrade the transistor function
TID (Total Ionizing Dose)
What can happen after…?

## Slide 12
Radiation effects on electronics
CMOS
N
N
N
P
P
P
Parasitic bipolar transistors
Latch-Up:
  causes VDD and GND to short
  Can result in self-destruction, at best a malfunction requiring a power cycle

## Slide 13
Radiation effects on electronics
TID + DD
  In time components degrade slowly
  There are no unwanted “stops”
  The final failure can be predicted Interventions can be planned
SEE
  Electronics can work without any signs of malfunction
Gy ∙ y-1
Time
HEH [cm-1∙y-1]
Expected life time
Failure probability
Failure probability
  Failures can appear and rapidly increase in frequency
Nonzero probability of a failure
Destructive failures possible
Immediate interventions needed
Threshold
Notes: Cumulative effects are gradual effects taking place during the whole
lifetime of the electronics exposed in a radiation environment. A device
sensitive to TID or displacement damage will exhibit failure in a radiation
environment when the accumulated TID (or particle fluence) has reached its
tolerance limits. It is therefore in principle possible to foresee when the
failure will happen for a given, well known and characterized component.
On the contrary, Single Event Effects are due to the energy deposited by one
single particle in the electronic device. Therefore, they can happen in any
moment, and their probability is expressed in terms of cross-section. A
device sensitive to SEE can exhibit failure at any moment since the
beginning of its operation in a radiation environment.

## Slide 14
Requirements for radiation tests
Radiation environment
Where in the machine the electronics is installed?
What levels of radiation are expected?
  TID (Gy)
    >1-5 Gy/y
  HEH (n/cm2)
    >1E7 n/cm2/y
Rad-effects of Concern
Test procedure
Test Facilities
  Component classification:
    component type based technology available expertizes and reports
  Effects and criticality
sample design and irradiation procedure
sample readouts and powering
best statistics as possible
CHARM &Co-60
PSI
Fraunhofer
other
Radiation test in 4 easy steps

## Slide 15
Equipment installed in radiation environment:
Front-end electronics for Pirani and Penning
In total 224 connection boxes:
  328 active Pirani
  328 active Penning
Penning
Pirani
Vacuum controls equipment near ARC dipoles
Pawel Krakowski
Pawel Krakowski

## Slide 16
  in order to survive run-2 and run-3 (10 years), electronics must withstand min 80 Gy
  for another 10 years of HL-LHM, an ~160 Gy must be accounted
  radiation tests will be done up to max 500Gy [~2 x (80 + 160)]
  to evaluate up to which TID they withstand
  Samples will be shipped to Fraunhofer Institute by the end of October
  if they do not withstand next 10 years (run2 + 3),
    replacement must be foreseen, or an alternative design must be considered
Vacuum controls equipment near ARC dipoles
RUN-1 |  |  | 
2011 |  | 2012 | 
HEH Fluence [cm-2y-1] | Dose [Gy y-1] | HEH Fluence [cm-2y-1] | Dose [Gy y-1]
- | - | 1E+08 | 0.2
RUN-2 |  |  | 
2015 |  | [2016; 2018] | 
HEH Fluence [cm-2y-1] | Dose [Gy y-1] | HEH Fluence [cm-2y-1] | Dose [Gy y-1]
2E+08 | 0.4 | 2E+08 | 0.4
RUN-3 | 
[2020; 2022] | 
HEH Fluence [cm-2y-1] | Dose [Gy y-1]
4E+08 | 0.8
HL-LHC |  |  | 
[2025; 2035+] |  |  | 
HEH Fluence [cm-2y-1] | Dose [Gy y-1] | HEH Fluence [cm-2y-1] | Dose [Gy y-1]
8E+08 | 1.6 | 2E+09 | 3.2

## Slide 17
24VDC power supply for fixed vacuum pumping groups near quadruples
  running in the presence of beam
  installed near ARC quadrupoles, and in the LSS near SMs and ITs
No data for IT!
  Specification for the TID/SEE radiation test under preparation
  Alternative design or relocation must be taken into account
Vacuum controls equipment near MQ
Location | RUN-1 |  | RUN-2 |  |  |  | RUN-3 |  | HL-LHC |  |  | 
 | HEH Fluence [cm-2y-1] | Dose [Gy y-1] | HEH Fluence [cm-2y-1] | Dose [Gy y-1] | HEH Fluence [cm-2y-1] | Dose [Gy y-1] | HEH Fluence [cm-2y-1] | Dose [Gy y-1] | HEH Fluence [cm-2y-1] | Dose [Gy y-1] | HEH Fluence [cm-2y-1] | Dose [Gy y-1]
 | 2012 |  | 2015 |  | [2016; 2018] |  | [2020; 2022] |  | [2025; 2035+] |  |  | 
ARC MQ | 3E+08 | 0.5 | 5E+08 | 1.0 | 5E+08 | 1.0 | 1E+09 | 2.0 | 2E+09 | 4.0 | 4E+09 | 8.0
DS MQ | 3E+09 | 5.0 | 5E+09 | 10.0 | 5E+09 | 10.0 | 1E+10 | 20.0 | 2E+10 | 40.0 | 4E+10 | 80.0
DS Worst | 5E+09 | 10.0 | 1E+10 | 20.0 | 1E+10 | 20.0 | 2E+10 | 40.0 | 4E+10 | 80.0 | 8E+10 | 160.0
IT | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ?

## Slide 18
Replacement of 96 Turbo molecular pumps and their controllers. Currently Alcatel ACT250R controller is installed directly under the ARC MQ cryostats, near to the pump installation.
Proposed solution:
      Long cable connection between controller installed in radiation safe areas (alcoves, caverns) and the HiPace 300 pump installed on the cryostat
Other options are taken into consideration
Options for equipment relocations

## Slide 19
Beam dumps due to vacuum controls failures, induced by radiation :
Very small statistics (5 events)
2 Blockings of PLC
3 switching power supplies in valve controllers were burned
Failures in P7 before relocation
Piquet intervention in P7 | 
Equipment | Date
PLC | 03.09.2012
PLC | 29.09.2012
DC Power Supply | 11.05.2012
DC Power Supply | 05.10.2012
DC Power Supply | 07.10.2012

## Slide 20
Vacuum equipment relocation in P7
48 patch panels installed in UJ76
8 of 27 existing racks used
patch panel groups the same equipment
~ 280 cables extended from the UJ76 to the TZ76 by a maximum length of ~180m

## Slide 21
All equipment relocated to TZ76 corridor
~200 new interracks cables installed
The closest Vacuum rack is located more than 100 m from UJ76 access doors, where the flux is
< 1E+6 [cm-2y-1]
Considered as safe for electronics
Safe
Not safe
Relocation
Old installation
~100 m
Pawel Krakowski
UJ access door
15 m
HEH 1%
Vacuum equipment relocation in P7

## Slide 22: Problems not solved by P7 relocation
source of fluctuations in Penning readings in LSS7
HV cable ? gauge ? controller?

## Slide 23
Thank you for the attention