65nm TDC readout interface
Paul Davis
University of Alberta
March 3rd 2015

---
GBT Elink
Very flexible
Each GBT can provide up to 40 Elink interfaces for a total bandwidth of 3.2Gb/s
400mV SLVS
Elink interfaces run at 80Mb/s, 160Mb/s or 320Mb/s
Can use one clock with multiple lanes
Elink can send/receive DDR or SDR data.
No protocol defined for data.
Phase uncertainty with Elink clocks != 40Mhz. Protocol needs to be able to synchronize phase.

---
Aurora Interface
Link protocol
8b/10b or 64b/66b encoded
Framed or Streamed data, flow control
Protocol is open but licenced cores available from Xilinx for ASICs
Not sure how much it gains us except for handling some of the syncronization, channel bonding etc.