## Slide 1: PLL meeting
05/03

## Slide 2: Triple redundant PFD

## Slide 3: Progress
PFD
  Layout done & verified
  Programmable resistor done
Charge pump
  Layout done & verified
Divider
  Layout of individual blocks (%16 TMR , /2 CML) done & verified
VCO
  Layout has to be updated to new size but verified old one
Digital logic (FSM + programming)
  Done P&R
Jitter
  280fs RMS
  1.2ps p2p
  20-30 dB CMRR

## Slide 4: To be done
VCO buffer (level shifter)
IO (Cern)
PLL SEE counters
Total layout
Something else?

## Slide 5: Input receiver
Input as 40MHz sine wave
  Lot of jitter (3ps p2p)
  Due to low slew rate
Square wave
  Generate with 700fs RJ (available @ Cern)
  Crystal oscillator