## Slide 1: HL-LHC : What is it and What challenges it represents for VSC
V. Baglin on behalf of WP12
CERN-TE-VSC

## Slide 2: Outline
Introduction
Inner Triplets
Layout
Crab cavities
Collimation
SC links and cryogenics
Options
LS2
Summary

## Slide 3: 1. Introduction

## Slide 4
LS2 starting in 2018 (July) => 18 months + 3 months BC
LS3 LHC: starting in 2023 => 30 months + 3 months BC
Injectors: in 2024 => 13 months + 3 months BC
Beam commissioning
Technical stop
Shutdown
Physics
(Extended) Year End Technical Stop: (E)YETS
Goal of 3’000 fb-1 by mid 2030ies
LHC roadmap: schedule beyond LS1
F. Bordry
LIU + HL-LHC
~ 100-
120 fb-1

## Slide 5
Plan approved by CERN management upon preparation in HL-LHC Coord Group and RLIUP
0.75 1034 cm-2s-1
50 ns bunch high pile up 40
1.7 1034 cm-2s-1
25 ns bunch pile up 45
1.7-2.2 1034 cm-2s-1
25 ns bunch pile up 60
Lumi saturation &
Technical bottlenecks:
50  25 ns
Run I
Run II
Run III
VSC Seminar, CERN, December 5, 2014
L. Rossi

## Slide 6
HiLumi Design Study: overview
19 Work Packages with 6 WP under the EU funded HiLumi Design Study
Integration started with vigor as well as Preliminary Technical Specifications and Quality Assurance
Several upgrades already in LS2: e.g. Cryo, SC link P7, Cryo-Collimators with 11 T , MoGr Coll’s)
Proof of main hardware by 2016
Final Prototypes to be tested by 2017-2018 (IT, D1, D2, LRBBwire, CC)
Start construction 2017/18 for IT, CC, other main hardware
IT String test (integration) in 2019-20; Main Installation 2023-24
Though schedule, but – based on LHC experience – feasible; 6 months shift of LS2 and 1 year shift of LS3 of the new LHC schedule ease the task.
Cost: 750 MCHF (Material, CERN accounting)
L. Rossi
PDR (preliminary design report) in 2014
Cost and Schedule Review by March 2015
TDR (technical design report) by 2015
HL-LHC installation:
    2018-2019 during LS2
    mainly 2023-2024 during LS3
A real challenge for VSC in the coming years !!!

## Slide 7: HL-LHC Baseline Parameters - WP2 charge – PLC
Parameter | Nominal LHC​ (design report) | HL-LHC 25ns (standard)​ | HL-LHC 25 ns (BCMS) | HL-LHC 50ns
Beam energy in collision [TeV] | 7 | 7 | 7 | 7
Nb | 1.15E+11 | ​2.2E+11 | 2.2E11 | ​3.5E+11
nb | ​2808 | ​27481 | 2604 | ​1404
Number of collisions at IP1 and IP5 | 2808 | 2736 | 2592 | 1404
Ntot | 3.2E+14 | 6.0E+14 | 5.7E+14 | 4.9E+14
beam current [A] | ​0.58 | 1.09 | 1.03 | 0.89
x-ing angle [μrad]​ | 285 | 590 | 590 | 590
β* [m] | 0.55 | ​0.15 | 0.15 | ​0.15
εn [μm]​ | 3.75 | ​2.50 | 2.50 | 3
r.m.s. bunch length [m] | ​7.55E-02 | ​7.55E-02 | ​7.55E-02 | ​7.55E-02
Geometric loss factor R0 without crab-cavity | ​0.836 | 0.305 | 0.305 | 0.331
Geometric loss factor R1 with crab-cavity | (0.981) | 0.829 | 0.829 | 0.838
Peak Luminosity without crab-cavity [cm-2 s-1] | 1.00E+34 | 7.18E+34 | 6.80E+34 | 8.44E+34
Virtual Luminosity with crab-cavity: Lpeak*R1/R0 [cm-2 s-1] | (1.18E+34) | 19.54E+34 | 18.52E+34 | 21.38E+34
Events / crossing without levelling w/o crab-cavity | ​27 | 198 | 198 | 454
Levelled Luminosity [cm-2 s-1] | - | ​5.00E+34 | 5.00E34 | 2.50E+34
Events / crossing (with levelling and crab-cavities for HL-LHC) | 27 | 138 | 146 | 135
Levelling time [h] (assuming no emittance growth) | - | 8.3 | 7.6 | 18.0
New IT Quads & ATS
Collision values
Crab Cavity
required
LIU required
Impedance, efficiency etc.
Levelling
required
VSC Seminar, CERN, December 5, 2014
Efficiency requires long fill times (ca. 10h)!
VSC to review performance compatibility with HL-LHC to identify consolidation
and build new systems compatible with HL-LHC

## Slide 8: Only with 350 fb-1/y (Llev=7.5 1034 and some optimism) the goal is reachable
M. Lamont
Quality management of LHC and its injector is a must to reach the required efficiency (R2E, R2P, spare, performance follow up … )

## Slide 9: Availability and Downtime
Upgrade of interlocking system (integration to avoid spurious dump)
Reduction of (generous) of interlock levels
R2E
Robust and reliable equipments
Identification of “fast” repair scenario
Etc.
M. Brugger
D. Wolmann

## Slide 10: The HL-LHC Project
New IR-quads Nb3Sn (inner triplets)
  New 11 T Nb3Sn (short) dipoles
  Collimation upgrade
  Cryogenics upgrade
  Crab Cavities
  Cold powering
  Machine protection
  …
Major intervention on more than 1.2 km of the LHC
Project leader: Lucio Rossi; Deputy: Oliver Brüning
F. Bordry
Close collaboration across all the VSC sections is a must

## Slide 11: High Luminosity LHC Participants
L. Rossi
Identification of potential partners for future design studies, HL-LHC procurement and installation

## Slide 12: Organisation
https://espace.cern.ch/HiLumi/default.aspx
A single point of entry (VB and RK) for a TEAM work across VSC and partners

## Slide 13: Documentation
Definition and follow up of HL-LHC TE-VSC project structure is needed

## Slide 14: 2. Inner Triplets

## Slide 15: Focussing quadrupole and merging dipole
New : Q1, Q2, Q3, CP (corrector package), D1
All operating at 1.9 K
Magnet aperture increase in IT quads : 70 mm to 150 mm, 140 T/m
Superconducting D1 (aperture 150 mm, 5.6 T)
Present IT+D1 to be completely removed (radiation to personnel !!)
Interconnects to be redesigned
Decrease beta (i.e beam size) at collision point (beta*) from 55 cm to 15 cm
HL-LHC
Present IT
NC D1
IT Quads. w/ Nb3Sn
SC D1
IT Quads.& D1
Corrector
Package
Q1
Q2a
Q2b
Q3
ATLAS
CMS

## Slide 16: Impact of radiation to personnel around IT
1 month cooling time, dose rates at 40 cm from the cryostat
Nominal scenario
Representing any LS after LS3
~ x4 wrt to LS3
~ x16 wrt LS1
C. Adorisio

## Slide 17: Impact of radiation to personnel around IT (2)
Estimation of WDP (work dose plan) can also be done for LS3 and the removal of the present inner triplet magnets to optimize the work-methods
Dose maps available from TAS to D1
CERN Objective : 3 mSv/year maximum during LS (Rule for Cat B personnel : 6 mSv/y)
Case study : When ? any LS after LS3, nominal
C. Adorisio
 |  |  | Collective dose (man mSv) | 
What | Where | How ? | 1 month cooling time | 4 months cooling time
Valve exchange | TAS-Q1 | 3 teams 5 workers | 3 | 1
PIM exchange | Q1-Q2 IC | 6 teams 8 workers | 21 | 8
Optimisation of design, equipment robustness, intervention procedures (WDP) with use of remote tooling and training of people is MANDATORY
/2.5

## Slide 18: Impact of debris onto IT+D1
700 MJ per beam (7 TeV, 2.2 1011 ppb, ~ 2800 b)
14 kW delivered in collisions, on each side:
  TAXS absorber with aperture, 54 mm, takes 750 W
  5 kW impact the machine  shielding is needed to protect the cold masses
F. Cerutti
Target :
  < 4 mW/cm3
  < 40-50 mGy
Mainly Q3 affected
1 kW in the cold mass
800 W in the beam screen

## Slide 19: Impact of debris onto IT+D1: shielded beam screen
Operating temperature : 40 -60 K
16 mm absorbers in Q1, 6 mm absorbers from Q2 to D1
Tungsten blocks
(mechanically connected to the beam screen tube)
Cooling tubes
Perforated Cu colaminated tube
Thermal links
Copper
Elastic supporting system
Ref: 13th HL-LHC Technical Committee – 7/10/204
C. Garion
Design studies underway
Mechanical analysis : impact of quench, heat transfer, supporting system
Tests with tungsten prototypes
Assembly of the Q1 beam screen

## Slide 20: Impact of debris onto IT+D1: shielded beam screen (2)
Q2-Q3 2015: short (1 m long) prototype
Defining, controlling tolerances and alignment is a challenge
Engineering specification and prototyping to start by 2015
16 mm absorber
(Q1)
6 mm absorber (Q2=>D1)
To be validated by C&S review
New cold bores
Octagonal shape, 4 cooling channels
~ 700 kg per Quadrupole

## Slide 21: Impact of electron cloud onto IT+D1: a-C coating
Extrapolation for the HL-LHC of Run 1 observations predicts large heat load due to electron cloud on the beam screen of the inner triplets
This increase of heat load will be accompanied by increase of background to the experiments
To reduce the heat load to ~ 200 W on the beam screen, amorphous carbon (a-C) coating is proposed (SEY~ 1.1)
This base line must be validated at cryogenic temperature with LHC type beams
G. Iadarola, G. Rumolo
3rd Joint HiLumi LHC-LARP Annual Meeting, Daresbury
11-15/01/2013

## Slide 22: COLDEX in SPS with –a-C coating
a-C beam screen held at 50 K, 5 k then 10 K while cold bore ~ 4K
LHC type beams circulating in SPS (3 9/11/2014):
    Heat load < 1 W/m
    Pressure rise < 5 10-9 mbar
    Main gas is H2
~2.2 m, ID 67 beam screen
Internally coated with amorphous carbon
Refurbishment and operation of COLDEX : strong support and commitment of many CERN groups: TE-CRG, BE-OP, BE-ABP, TE-EPC, EN-ICE
Thanks to L. Rossi, HL-LHC project leader, crab cavities, WP 4, and cryogenic, WP9, projects for their support to operate COLDEX during 2016
R. Salemme
a-C coating validation at cryogenic temperature must be continued

## Slide 23: Radiation dose to a-C coating and shielded beam screen
Behaviour of a-C coating under irradiation started
F. Cerutti
dose up to GGy
dominated by electro-magnetic components
Electromagnetic
Hadronic

## Slide 24: 3. Layout

## Slide 25: Optics: HL-LHC V1.1
New optic for HL-LHC : ATS (Achromatic Telescopic Squeezing), blow-up β in the arcs to reduce β*
New Matching section
Triplet
D2 Crab Q4
Cavities
D1
TAS
Right side of IR1/IR5
R. De Maria
Changes in IR1/5
  TAS aperture reduced .
  Triplet, BPM, corrector layout update.
  D1-D2 length reduction.
  TAN new aperture and separation.
  Displacement Q4 by 10m towards the arc
  3 to 4 crab cavities per side per beam.
  New MCBRD – MCBYY length and strength
  for crab cavity beam based alignment.
  Additional masks and collimators
  Q5: MQYL to MQY at 200 T/m.
Changes in IR6
  Q5: MQYL to 2x MQY.
S. Fartoukh
Complete dismounting of LSS1 & 5
New beam screens : procurement !
New layout

## Slide 26: The magnet zoo in the IR
Triplet QXF (LARP and CERN)
Separation dipole D1 (KEK)
Recombination dipole D2
(INFN design)
Q4 (CEA)
Skew corrector (INFN)
Corrector sextupole (INFN)
Corrector dodecapole (INFN)
Corrector octupole (INFN)
Corrector decapole (INFN)
Orbit corrector (CIEMAT)
E. Todesco
Cross-sections in scale
Many beam screens with interconnects and cold warm transitions to be designed, produced & installed
C. Garion

## Slide 27: Layout
LHCLSXH__0010 and LHCLSXHT__0010
Vacuum functionalities introduced
Optimisation of areas : TAS-Q1, interconnects, TAN-D2, crab cavities
P. Fessia
Q1 to be shifted towards arc by ~ 1 m ?
Large enough to accommodate cooling tubes
Shorter TAN and innovative solutions to accommodate TCTs + masks
Dismountable CC modules
Space reservation for option: BBLR compensator
DQR, no Alfa and DFBA removed
Masks in all cells

## Slide 28: Heat load
Heat load working group to be resumed in 2015 (WP9)
  defines necessity on a-C coating with WP2 and WP12
  Total heat load on the beam screen cooling circuit IT+D1
G. Iadarola
Need for heat load reduction for the triplets & D1 of IR1/ and IR2/8
Study in-situ coating and clearing electrodes
Optimise cooling efficiency
Identify beam screens to be treated for electron cloud
  HL-LHC: IR1 and 5
  LHC: IR2 and 8
Acceptable
Limit = 100W ?

## Slide 29: 4. Crab cavities

## Slide 30: Crab cavities: luminosity
Increase instantaneous luminosity by a factor 16 by “crabbing” the bunches
Requires luminosity levelling to minimise number of event per crossing
B. Palmer
F. Zimmermann, R. Calaga
Crab cavities maximise luminosity and can be used for luminosity levelling:
  when luminosity is too high, CC are almost off and are slowly turned on to compensate proton burning  allow to optimise integrated luminosity

## Slide 31: Crab cavities
Installed between D2 and Q4
all CC operating at 2 K
Two designs to evaluate (RF dipole and double quarter wave cavities)
Bulk Nb cavities
Installed on left and right side of IP1 and IP5
D2
Q4
LARP-BNL
LARP-ODU-JLAB

## Slide 32: Crab cavities
Operating pressure ~ 10-10 mbar with beams
Vacuum instrumentation on the modules is under definition
Drawings and leak detection procedures needs to be validated by VSC
Cryomodules for the DQW (left) and RFD (right) cavities respectively
R. Calaga, O. Capatina

## Slide 33: Crab cavities and electron cloud
  Bulk Nb treatment is well defined (EDMS 1389669, 150 micron chemical etching, 600 deg heat treatment, 10-20 micron chemical etching, high pressure water rinsing and finally a 120 deg bake)
Impact of the electron cloud in the CC modules must be evaluated for:
  Nb cavity itslef
  Inter-cavity tube
  Module cold warm transition
Samples needed for qualification
1.1 < Nb film SEY < 1.7
N. Hilleret et al., Appl. Phys. A 79, 1085-1091 (2003)
N. Hilleret et al. EPAC 2000, Vienna, Austria
Electron conditioning

## Slide 34: Layout D2-Q4
  Room temperature (except CC modules): bakeable and NEG coated
4 Sectorised CC modules:
  Standard sectorisation valves (VA__), length 655 mm, at extremity
  Specific sectorisation assembly, length 400, between modules. To be defined & designed. 2 beam line:
    2 roughing valve
    3 sector valve (beam interlocked)
    3 penning gauges + 2 ion pump + 2 pirani gauges
LHCLSXH_0010
side view
A typical VA__

## Slide 35: Layout D2-Q4: 2nd beam pipe
  The 2nd beam pipe is held at 2 K and has cold warm transition (CWT) !
  Current material is Nb, diameter limited by space
  In LHC, maximum length without beam screen is < 1 m (to be revised for HL-LHC)
  Detailed studies are needed to comply with vacuum stability and pressure level
A beam screen between
2 cryogenic pipes ?
A beam pipe with
Antechamber ?
CWT
CWT

## Slide 36: 5. Collimation

## Slide 37: 11 T – DS collimator
  Arc Dispersion Suppressor areas (Q7 to Q11) serve as “energy spectrometer” : a collimator is needed to reduce background to ALICE with ion operation and to reduce beam loss on the cold masses with proton beams
  Using NbSn3 technology, the dipole field can be increased up to 11 T
  A standard LHC dipole can be replaced by two 11 T magnets and one collimator (TCLD)
F. Savary
Interconnect
Collimator
11 T dipole cold mass
By-pass cryostat
15660 mm

## Slide 38: 11 T – DS collimator
  The Target Collimator Long Dispersion suppressor, TCLD, collimator operates at room temperature and is sectorised
F. Savary
S. Redaelli
VSC needs to complete the integration (2nd beam line in particular)
Installation of two assemblies are expected in IP2 (left and right) for LS2 (2018-19)
  IR 7: 2 TCLDs per side to improve collimation cleaning
  IR 1/5: 2 TCLDs per side to allow high luminosity
LS3

## Slide 39: Collimation and protection layout IP1/5
  Tertiary collimators, TCTs, in cell 4 and 5
  Better protection of apertures, asynchronous beam dumps and possible reduction of background to the experiments
  Upgrade of TCL4 mask: design with larger jaws
  TCLX4
  Upgrade of TAXN
  Inserting Inermet180
  Length reduce from 3.5 to ~ 2 m
S. Redaelli
F. Cerutti, L. Esposito
Drawing and performance validation on new components by VSC
Possible anticipated upgrade during LS2

## Slide 40: Impedance upgrade
  IR 3/7 : 2nd generation secondary collimators, Target Colimator Secondary Pick-up Metallic, TCSPM, with Molybdenum Carbide Graphite (MoGr) and in jaw beam position monitors.
  Reduce impedance by 90 %, deployment in 2 batches
S. Redaelli
LS2
  IR 1/5 : 2nd generation tertiary collimators, Target Colimator Terticary Pick-up Metallic, TCTPM, with Molybdenum Carbide Graphite (MoGr) and in jaw beam position monitors.
  To be installed during LS3 (or during (E)YETS if needed)

## Slide 41: Possible future upgrades
  IR 3/7, in the pipe line :
    Primary collimators, Target Collimator Primary Pick-up, TCPP, with in jaw beam position monitors.
    Shower absorbers, TCLA
    Passive absorbers, TCAP
At the end, the complete LSS3 and LSS7 might be upgraded for HL-LHC during :
  - (E)YETS
  LS2
  LS3
Optimisation of tooling, procedures (with WDP definition) and increase of equipment robustness is MANDATORY

## Slide 42: 6. SC links and Cryogenics

## Slide 43: Superconducting links
  SC links are used for cold powering systems.
  Provides protection against R2E
  DFAs will replace DFBs
  DFBAs and DFBMs will be removed from LSS7: installation during LS2
A. Ballarino
  DFBA’s will be removed from LSS1/5
Y. Muttoni
P. Fessia
Requires dismounting of vacuum equipments
Impact on integration and vacuum layout

## Slide 44: Cryogenics
  Creation of a cryoplant in LSS4 for the RF system: installation LS2
S. Claudet
  LS3: upgrade of P1 and P5

## Slide 45: 7. Options: not in base line but under study

## Slide 46: Options
  in IP1,5, 7 as previously but also IP4 and IP8
P. Fessia

## Slide 47: Option: hollow e-lens
  Hollow electron beams running coaxially to the proton beam will provide an active control of beam halo population and beam loss rate. Installation LS2-LS3
S. Redaelli
D. Perini
  5T field
  3 m long
  RT vacuum system, bakeable

## Slide 48: Option: mini-TAN IP8
  Installation in LS2 !
  Protects the D2 from increased luminosity in LHCb
  Under design: length ~ 2.2 m
I. Efthymiopoulos

## Slide 49: Option: cristal collimation
  A possible mean to improve collimation cleaning while reducing impedance
  A test bed already (partially) installed in LSS7 !
  More details by the end of 2015 ….
S. Redaelli

## Slide 50: Option: BBLR
  Vague ideas:
    Short term : Exchange of a TCT with a TCT with embedded wire for LS2
    Long term: A co-linear 20 A electron beam located between TAN and D1 ?
D. Perini
Y. Papaphilippou
H. Schmickler

## Slide 51: Option: BI
  No schedule but ideas !
  Halo-diagnostics for HL-LHC
R. Jones
  Gas jet techniques
  Use of Beam Gas Vertex
  Use of scattered electrons
  Optical techniques using synchrotron radiation

## Slide 52: 8. LS2

## Slide 53: Beam transfer and kickers
  Injection protection elements to be installed in LS2
    TDIS can have about same integrated absorber length as present TDI
      Preliminary design: two modules with low Z absorber + one module with high Z absorber
      TDI interferometry on the way to be installed during run II
      3 x 1.5 modules
        2 x low Z material (graphite) + 1 x high Z material
    TCDD aperture reduction possibly necessary to protect D1
      D1 damage limit required, decision end 2014
    TCLIA and TCLIB likely not replaced for protection reasons
      However TCLIA IP2 larger opening because of ALICE ZDC?
J. Uythoven
These upgrades must be compatible with HL-LHC
IP

## Slide 54: Beam dumping system
  To be potentially upgrade in LS3 only
    Verification of TCDS for HL-LHC beams: will likely need to be upgraded.
    Check the already modified TCDQ : further upgrade not foreseen in the baseline.
    Check TDE heating after multiple dumps – nitrogen venting.
    Check TDE window – if this is an issue, might need to change dilution pattern. This is not part of the HL-LHC baseline.
J. Uythoven

## Slide 55: Kickers and electron cloud
  LS1 MKI bypass tubes NEG coated, as nearby equipment.
  Ceramic tube can still be an issue with SEY values 6 – 10. Required SEY < 1.4
  Cr2O3 coated ceramics SEY  2, conditioned to < 1.4
  Contract placed to develop application method for Cr2O3 coating of MKI ceramic chamber to reduce SEY. If successful apply on prototype magnet
  Looking for position in machine for passive prototype
J. Uythoven, M. Barnes
NEG coated bypass tubes
Cr2O3
Conditioning

## Slide 56: LHC Experiments upgrades
  Work packages for LS2 (EDMS 1065775)
  Reduced ALICE Be beam pipe
  New VErtex LOcator for LHCb
  Replacement of stainless steel to Aluminum chambers for CMS
M. Gallilee
These upgrades must be compatible with HL-LHC
(EDMS 13601088-91)

## Slide 57: 9. Summary

## Slide 58
Summary
  HL-LHC is a vast project
  Installation will be in two phases : LS2 AND LS3
  Design already started in many fields
  Next important milestone is Cost and Schedule Review: 9-10-11 March 2015
      CONS project to be distinguish for HL-LHC project
  Technical design report, TDR, by 2015

## Slide 59: Thank you for your attention

## Slide 61: Focussing quadrupole and merging dipole
ATLAS
CMS
New : Q1, Q2, Q3, CP (corrector package), D1
all operating at 1.9 K
Present IT+D1 to be completely removed (radiation to personnel !!)
Interconnects to be redesigned
Decrease beta (i.e beam size) at collision point (beta*) from 55 cm to 15 cm