## Slide 1: International review of the HL-LHC 11T Dipole for DS Collimation Mechanical design (TE – MSC – Large Magnet Facility)
F. Lackner, a summary of work performed by:
M. Karppinen, B. Auchmann, C. Kokkinos,
J. Murtomaki, T. Lyon, D. Smekens, C. Loeffler

## Slide 2: Outline
CERN 11T design
  Design criteria - key parameters
  Cross-section of the 1in1 and 2in1 magnet
  Shimming and mechanical concept
Overview of magnet assembly process
Structural analysis
  Mechanical model
  Boundary conditions
  FEA - Coil pre-stress and peek-stress
    Assembly – 1.9 K – 12 T
Summary

## Slide 3
  Mechanical design criteria's - key parameters
CERN 1in1
CERN 2in1
Main mechanical parameters | 1-1 | 2-1
Aperture [mm] | 60 | 
Yoke outer diameter [mm] | 510 | 550
Magnetic length [mm] | 1690 | 1690/5300
Shell thickness [mm] | 12 | 15
Horizontal EM-force Fx per side at Inom [kN/m] | 6.22 | 6.23
Vertical EM-force Fy per coil at Inom [kN/m] | 3.18 | 3.15
Longitudinal EM-force Fz per coil at Inom [kN] | 472 | 474
Stored energy at Inom [kJ/m] | 445 | 897
Nominal current Inom [kA] | 11.85 | 11.85
The presentation is focusing on the CERN design, not including comparison to other designs or concepts.

## Slide 4
The mechanical design of the magnet has to provide rigid support (clamping) of the Nb3Sn coil.
It is essential to accommodate the coil with minimum distortion of the conductor positioning.
The intention is to clamp the magnet assembly by using thermal contraction in the welding shells.
The half yoke assembly interface shall mechanically protect the collared coil assembly during operation (Yoke gap shall remain closed). Providing rigid assembly.
  Mechanical design criteria

## Slide 5
  Design: Separate collared coils
  Interchangeability of coils - testing of collared coils in a 1in1 structure

## Slide 6
Pole wedge
Shim
Filler
wedge
Loading plate
  Most of the coil pre-stress obtained by collaring
  Symmetric loading - low bending stress in the coil
  Better control of pre-stress - “sliding cinematic” on pole
  The concept of pole loading
Collared coil assembly
Courtesy of M. Karppinen

## Slide 7
  A Close up of the magnet intersection
J.
Overview: J. Murtomaki

## Slide 8
  Pole shim
  Collar/yoke shim (default: 0.4 mm)
  Pole adjustment shim (default: 0.2 mm)
  Gap closing @ room temperature remaining closed to 12 T.
  Stainless-steel shell
1.
2.
3.
4.
  Design features – 1in1
(3) is an optional knob.
(2) and (4) must be controlled in order to close the yoke gap at RT.
5.

## Slide 9
  Close up on magnet assembly
Original design foresees a welded end ring
Bolt pre-stress applied from end-ring to end-plate
Final design welded end plates (simplifying assembly)
Welding shell
Rod
Yoke
Yoke
End Plate
End Plate
Coil
End Plate
Dummy
Coil Block
Welded end plates

## Slide 10
  Assembly process less influenced by friction (vs. horizontal split)
  Closed gap at RT and up to 12 T providing rigid support for the collared coil
  Better controlled (collared) coil deformation
  Vertically split yoke
Short model welding press (LMF), assembly in 90° rotation
MBHSP101 assembly
Collared coil shimming
Top yoke assembly
Prior insertion to welding press

## Slide 11
  FEA Coil pre-stress and peak stress 1
  Keep coils under compression at all stages, especially at cold/12T, and avoid excessive stresses during collaring (lower than 150 MPa)
  Minimal elliptic deformation
  Minimal stress gradient in the coils
  Easy tuning of pre-loading by shimming
Boundary conditions for the collared coil assembly

## Slide 12
  FEA Coil pre-stress and peak stress 2
Courtesy of H. Kokkinos
RT
1.9 K
11.22 T
12 T

## Slide 13
  Welded stainless steel skin
MIG welding tests, FEA on shell stress:

## Slide 14
Separate collared coils
Most of the coil pre-stress obtained by collaring
Symmetric loading
Better control of pre-stress
Testing of collared coils in 1in1 structure
Vertically split yoke
Assembly process less influenced by friction (vs. horizontal split)
Closed gap at RT and up to 12 T to provide rigid support for the collared coil
Better controlled (collared) coil deformation
Rigid inner yoke
    Symmetric loading of collared coil
Welded stainless steel shell
  Design features – 2in1

## Slide 15
  Pole shim
  Collar/yoke shim (default: 0.4 mm)
  Pole adjustment shim (default: 0.2 mm)
  Gap closing @ room temperature remaining closed to 12 T.
  Stainless-steel shell
  Design features – 2in1
(3) is an optional knob.
(2) and (4) must be controlled in order to close the yoke gap at RT.
1
2
3
4
5

## Slide 16
After CM assembly
at 293 K
At 1.9 K, I = 0 A
B0 = 12 T
Under collaring
press
After collaring
-138 MPa
-140
0
-138 MPa
  FEA Coil pre-stress and peak stress
Courtesy of B. Auchmann

## Slide 17
  Shell stress
Chart: Load steps
| 0. Assembly at RT | 1. Cradle loading 375 t/m | 2. Welding contraction | 3. After welding | 4. Cryo | 5. 11-T | 6. 12-T
12mm frictionless 190MPa | 0 | 0 | 175 | 189.6951 | 370.8909 | 374.5726 | 375.1378
12mm bonded 190MPa | 0 | 0 | 175 | 190.3122 | 369.8956 | 367.878 | 367.7454
12mm frictionless 140MPa | 0 | 0 | 120 | 137.49 | 309.6656 | 313.174 | 313.874
12mm bonded 140MPa | 0 | 0 | 120 | 140.2805 | 308.9338 | 306.9197 | 307.0027
Stress in the shell (average), 12 mm thickness:

## Slide 18
  Shell stress
Chart: Load steps
| 0. Assembly at RT | 1. Cradle loading 375 t/m | 2. Welding contraction | 3. After welding | 4. Cryo | 5. 11-T | 6. 12-T
15mm frictionless 190MPa | 0 | 0 | 175 | 188.3885 | 367.6405 | 371.3199 | 371.8487
15mm bonded 190MPa | 0 | 0 | 175 | 189.2351 | 366.0908 | 364.3861 | 364.1655
15mm frictionless 115MPa | 0 | 0 | 95 | 112.1031 | 278.3449 | 281.9468 | 282.5376
15mm bonded 115MPa | 0 | 0 | 95 | 114.4756 | 277.4025 | 275.6815 | 275.5323
Stress in the shell (average), 15 mm thickness:
Max. achievable based on MIG technology

## Slide 19: Summary
Pole loading concept was successfully tested on the demonstrator and first short model assembly; Important engineering features were confirmed:
  Efficient transfer of the collaring force into the coils;
  Good control and easy adjustment of the assembly parameters;
  Minimal bending of the coils;
  FEA shows that pre-stress is below 150 MPa under all operating conditions.
Further work:
  Improve understanding of required shimming based on metrological inspection of coils after short model tests and disassembly;
  Iterating FEA with updated model from metrological inspection on coil;
  Careful analysis and comparison of measured values required;
  Refinement of previous models used to verify axial stresses on bullets and end plate;
  Friction based FEA would allow another insight on the coil pre&peak-stress.

## Slide 20: References
F. Savary et al., “Status of the 11 T Nb3Sn Dipole Project for the LHC” This conference.
M. Karppinen et al., “Design of 11 T Twin-Aperture Nb3Sn Dipole Demonstrator Magnet for LHC Upgrades”, IEEE Trans. on Appl. Supercond., v. 22, no. 3, June 2012, p. 4901504.,
A.V. Zlobin et al., “Status of the 11 T 2-in-1 Nb3Sn Dipole Development for LHC”, IPAC’2014, Dresden, June 2014.,
A.V. Zlobin et al., “Development of Nb3Sn 11T Single Aperture Demonstrator Dipole for LHC, Upgrades”, Proc. of PAC’2011, NYC, 2011, p. 1460.,
A.V. Zlobin et al., “Design and Fabrication of a Single-Aperture 11T Nb3Sn Dipole Model for LHC Upgrades”, IEEE Trans. on Applied Supercond.,
A.V. Zlobin et al., “Status of a Single-Aperture 11 T Nb3Sn Demonstrator Dipole for LHC Upgrades”, this conference., 2012,
M. Karppinen et al., “Design of 11 T Twin-Aperture Nb3Sn Dipole Demonstrator Magnet for LHC Upgrades”, IEEE Trans. on Applied Supercond., 2012,

## Slide 21: Spare slides

## Slide 22
 | P1 | P2 | M1 | M2
Under press | -110 | -65 | -95 | -82
Spring-back | -87 | -45 | -45 | -73
Yoke assy. | -137 | -48 | -60 | -110
Cool down | -111 | -44 | -55 | -90
12 T | -10 | -37 | -126 | -139
  Coil pre-stress and peak stress
Azimuthal coil stress:
Von Mises
Azimuthal stress
P1
M1
P2
M2
Yoke assembly RT
Yoke assembly RT

## Slide 23
  Comparison CERN - FNAL
Pole loading design
Integrated pole design

## Slide 24
  Comparison CERN - FNAL
St. Steel (Nr.15)
E(293K) = 195 GPa
E(4.2K) = 215 Gpa
α= 2.7/(1000*293)
Kapton (Nr.16)
E(293K) = 2.5 GPa
E(4.2K) = 2.5 Gpa
α= 5.8/(1000*293)
St. Steel (Nr.11)
E(293K) = 195 GPa
E(4.2K) = 215 Gpa
α= 2.9/(1000*293)
Nippon St. Steel (Nr.5)
E(293K) = 195 GPa
E(4.2K) = 215 Gpa
α= 2.7/(1000*293)
Titanium alloy (Nr.19)
E(293K) = 115 GPa
E(4.2K) = 125 Gpa
α= 1.7/(1000*293)
Steel (Nr.7)
E(293K) = 210 GPa
E(4.2K) = 225 Gpa
α= 2.05/(1000*293)
Insulation (Nr.18)
E(293K) = 28 Gpa (x)/34 Gpa (y)
E(4.2K) = 14 Gpa (x)/23 Gpa (y)
αx= 8.31e-6
αy= 2.42e-5
St. Steel (Nr.21)
E(293K) = 190 GPa
E(4.2K) = 210 Gpa
α= 2.64/(1000*293)
St. Steel (Nr.6)
E(293K) = 190 GPa
E(4.2K) = 210 Gpa
α= 2.64/(1000*293)
Cable (Nr.13)
E(293K) = 40 Gpa (r)/40 Gpa (θ)
E(4.2K) = 45 Gpa (r)/40 Gpa (θ)
αr= 2.9/(1000*293)
αθ= 3.3/(1000*293)
Haris Kokkinos
Courtesy of H. Kokkinos