## Slide 1: Cryostat for the 11 T magnets and collimator integration
HL-LHC 11 T Dipole for DS Collimation
8th to10th December, 2014
D. Duarte Ramos, C. Mucher, L. Gentini, T. Sahner, H. Prin, R. Wawrowski, F. Savary, V. Baglin

## Slide 2: Outline
Main integration requirements
Conceptual design: Layout, main features, interfaces
Cryostat main components and assembly sequence
Collimator design
Beam vacuum equipment and collimator length
Current leads for the trim circuit
Work in progress
Conclusion

## Slide 3: Main integration requirements
Compatibility with installation and transport constraints: not larger than existing cryostat (ø1055)
Create a room temperature vacuum sector in the LHC continuous cryostat
  Cold to warm transitions (CWT)
  Sector valve after each CWT for vacuum separation during magnet cooldown or collimator bakeout. RF-shielded gate valves and bellows for impedance reasons
  DN35 ports on the cold sectors to send an RF emitter ball through the full arc after warm up and before cooldown
Compatibility with existing cryogenic and electrical systems, ensuring their continuity
Prevent loss of alignment during evacuation with independent supports for collimator and cryostat
Minimise changes to other magnets: keep interconnects standard if possible
Collimator
Vacuum enclosure
Magnet
Magnet
1.8K Heat exchanger
Beam vacuum
Lines E, C’, K
RF emitter
RF emitter
Bus bars

## Slide 4: Solution: MB replacement unit
Same 15660 mm length between interconnect planes as an LHC MB
Connection cryostat between two 11 T magnets to integrate the collimator
LHC MB replaced by 3 cryostats + collimator, all independently supported and aligned:
Same interfaces at the extremities: no changes to nearby magnets, standard interconnection procedures & tooling

## Slide 5: Connection cryostat for collimator integration
Collimator support jacks
Cryostat support jacks
Cold mass enlarged to Ø750 on the collimator side
Constant LHC arc outer flange diameter: Ø1055
Flexible interconnects for alignment independency and thermal contraction
Interconnects use standard components and tooling despite the new compact layout

## Slide 6: Interfaces driving the design
QRL side
K2
M2
V2
W
Y
M1
M3
E
C’
V1
K1
X
N

## Slide 7: Cross section of the connection cryostat and collimator
Dedicated collimator design.
One collimator design fits both beam lines
M2
W
Y
M1
M3
E
C’
X
N
Collimator supported directly on the concrete slab
Larger cold mass extremity to open up space for the collimator

## Slide 8: Cryostat support layout
Magnet’s fixed points near the centre: for small contractions at the intermediate interconnects and minimum change wrt replaced MB
Distance between jacks shared with DS magnets Q11, Q10, Q8: 3705 mm
Gives nearly ideal cold foot distance for minimum cold mass deformation: 3430 mm (estimated less than 0.1 mm sag even with a 10 mm thick shell)
W-sleeve on the downstream interconnect cannot be fully open but still acceptable for interconnecting work

## Slide 9: Magnet cryostats
1- Pre-assembly of bottom tray, E-line, support posts, C’-line
2- Cold mass and N-line subassembly placed on bottom tray
3- MLI and thermal shield
4- Insertion into vacuum vessel; finishing of instrumentation feedthroughs and current leads
Finished units are not interchangeable but many shared components, including the vacuum vessel.
Follows all LHC cryostat design principles.

## Slide 10: Connection cryostat
1- Pre-assembly of transfer lines comprising piping, busbars, supports thermal shield and MLI (supports to be designed)
2- Insertion of transfer lines into vacuum vessel
3 - Alingment of tranfer lines and welding of cold to warm transitions
4 - Welding of thermal shield front plates and thermalizations
Simple vacuum vessel design. Precision machining of interfaces after welding.

## Slide 11: Collimator
Integrated expansion joint with RF bridge
for alingnment and installation clearance
‘Quick’ CF flange for removal and connection of collimator
Based on TCLD design from 2010
New design of actuation system in order to comply with integration constraints
Pre-aligned support stand
Collimator can be exchanged without re-alignment
BPM buttons

## Slide 12: Beam vacuum and collimator length
Option B: Second beam line at 1.9 K
Beamscreen on second line imposes a minimum interconnect length
Collimator length: 650 mm jaw (1130 flange to flange)
Option A: Second beam line at room temperature (bakeable)
Sector valve on second beam line cannot be facing the collimator bellows as initially thought
Collimator length: 600 mm jaw (1080 flange to flange)
Active jaw length in tungsten
Total collimator length (active+480 mm)
Decision and validation to be done with full scale mockups

## Slide 13: Current leads for the trim circuit
2x 300 A conduction cooled leads
Only one location is possible
Integration and design to be started
Gas cooled leads not possible both for lack of space and cryogenics
Conduction cooled leads: about 3.6 W/kA to 1.9 K (c.f. A. Ballarino)
Local solution: applicable everywhere in the LHC
RT copper cables  towards power converter
Similar to a Dipole Corrector Feedthrough in the SSS (EDMS 328999)

## Slide 14: Work in progress
Mechanical and thermal calculations
Magnetic field induced by main busbars
Material selection
Detailed design of components (pipe routing, welding configurations, bellows, supports, etc.)
Connection to cold test bench
Handling and transport interfaces
Assembly breakdown structure, quality control requirements and procurement strategy

## Slide 15: Conclusion
Integration has been the main challenge since the beginning of the project.
The present concept of cryostat maximises the length available for the collimator and room temperature vacuum equipment.
The integration of the current leads for the trim circuit are the next challenge. We are confident that it can be done, but this may no longer allow a single vacuum vessel design for both magnets.
The magnet cryostats follow the LHC design basics.
One configuration designed to fit all possible locations in the LHC (with local trim).
No changes required to nearby magnets.
Interconnecting work done in the tunnel takes advantage of existing procedures thanks to many LHC standard components and tooling.

## Slide 17: Heat loads
Additional heat loads to 1.9 K with respect to replaced MB cryostat
  One additional magnet support post: 49 mW
  Connection cryostat supports: ~100 mW
  Cold to warm transitions:
    Option warm second beam line (4 CWT): ~8 W
    Option cold second beam line (2 CWT): ~4 W
  Current leads 2x300 A: 2.2 W

## Slide 18: The first 11 T cryo-assembly concept
Independently cryostated and handled cold masses, linked through two short transfer lines
Transfer lines with expansion joints mechanically decouple cryostats A and B
Splice and piping interconnect in the tunnel, all other work prior to installation
Can use the existing TCLD collimator design with modified the supports
Collimator
Lines M, E, N, K, C’
Reinforced jacks to widstand vacuum forces
11 T cold mass A
11 T cold mass B
Line X
Independently supported collimator
Busbar splice and interconnect done in the tunnel
Flexible S-shaped busbar stabiliser
Busbar lyra

## Slide 19: 3D Integration

## Slide 20: Before the 11 T magnet development: QTC (2010)
Main drawback: extensive machine layout changes to create space
4.0 m + 0.5 m interc. = 4.5 m installation length

## Slide 21: Could the QTC cryostat concept be “extended”?
Can only be finished after cryostating
Dealing with welding distortions is a major issue
  Distortions amplified with length
  Adjustment of cold supports posts is required
  Complicated assembly procedure
Longitudinal butt-welds
Cover closure w/ fillet welds
New approach needed