## Slide 1
Andrew Hutton for Bob Rimmer
A compact, modular cryomodule concept suitable for a range of applications and for industrial production
LHeC Workshop, 24-26/6/2015

## Slide 2: MEIC RF Systems
MEIC baseline design updated in Jan 2015
PEP-II warm RF adopted for electron ring
  Proven technology, looking for a new home
  Enough cavities and klystrons available
  476.3 MHz buckets can be filled from CEBAF linac with simple timing system
Ion ring frequency now 952.6 MHz
Crab cavity system now 952.6 MHz
Cooler source and ERL now 952.6 MHz
Ion injector chain not affected

## Slide 3
MEIC Conceptual Design
Stage I MEIC
  CEBAF as full-energy e-/e+ injector
  3-10 GeV e-/e+
  8-100 GeV protons
  <40 GeV/u ions
Stage II EIC
  up to 20 GeV e-/e+
  up to 250 GeV protons
  up to 100 GeV/u ions
updated
IP
Future IP
Ion Source
Booster
MEIC
Collider
Rings
12 GeV CEBAF
Halls A, B, C
Electron Injector
Hall D
SRF Linac
e-RF
i-SRF +
NCRF
Crab
Crab
Cooling
e-RF
?

## Slide 4: High level RF parameters
 | electron ring NCRF |  |  |  | Proton SRF |  | Lead ion | 
Energy | 4 | 5 | 10 | GeV | 30 | 100 | 40 | GeV/u
Frequency | 476.3 | 476.3 | 476.3 | MHz | 952.6 | 952.6 | 952.6 | MHz
Current | 3.00 | 3.00 | 0.71 | A | 0.50 | 0.50 | 0.50 | A
SR power per ring | 1.08 | 2.65 | 10.00 | MW | - | - | - | MW
Energy Loss per Turn | 0.36 | 0.88 | 14.12 | MV | - | - | - | MV
Veff | 0.36 | 0.88 | 14.12 | MV | - | - | - | MV
Vpeak | 1.74 | 3.44 | 20.56 | MV | 4.94 | 18.95 | 17.93 | MV
Syn. Phase | 12.01 | 14.89 | 43.39 | degree | 0.0 | 0.0 | 0.0 | degree
Vgap | 0.43 | 0.34 | 0.79 | MV | 1.23 | 1.18 | 1.20 | MV
Gradient | 1.4 | 1.1 | 2.5 | MV/m | 7.8 | 7.522 | 7.591 | MV/m
Beam Power per Cavity | 271.2 | 264.8 | 384.6 |  | - | - | - | 
Forward Power | 455.5 | 497.8 | 492.0 | kW | 51.0 | 46.94 | 109.88 | kW
Cavity Power Loss | 27.0 | 16.9 | 89.3 | kW | 23.4 | 21.6 | 22.0 | W@4K
Reflected Power | 157.3 | 216.1 | 18.0 | kW | 50.9 | 46.9 | 109.9 | kW
Qext | 8.89E+03 | 8.89E+03 | 8.89E+03 |  | 7.07E+04 | 7.07E+04 | 3.08E+04 | 
Minimum Cavity Number | 4 | 10 | 26* |  | 4 | 16 | 15 | 
*Assumes 2 cavities per klystron.

## Slide 5: Crab cavity
Design by ODU (Alejandro Castilla, Ph.D project)
952.6 MHz “RF dipole” like LHC
Modest RF system (no beam loading)
Must have good HOM damping
Count for 1 IP in baseline
Assume cryostat cost/cavity same as ion storage ring

## Slide 6: MEIC modular cryostat
Goals:
Take the best features of previous JLab designs
Modular approach to hold various different cavities
Design suitable for industrial production
Simple concepts, low parts count to reduce costs

## Slide 7: Basic Decisions
Continuous (lower cryogenic losses) or discrete (cryostat easier to service)
Tuner motors inside cryostat (lower losses) or outside (easy repair)
Helium distribution at 2K (cryostat simpler) or 4K (lower cryogenic losses)
Fixed coupling (simpler) or variable (lower RF losses)

## Slide 8: JLab SNS module experience is the starting point • Ion Storage Ring cryomodules (4 x 4-seater) • e-cooler Booster (1 x 4-seater) • e-cooler Linac CM (1 x 4-seater 5-cell) • Crab Cavity CMs (2 x 2-seater and 4 x 4-seater) Updated modular design under development
A. McEwen
SNS high b module
MEIC SRF design basis

## Slide 9
Example: five-cell with symmetric HOM end group and coaxial FPC.
One helium vessel per cavity (SNS style).
End mount tuner (not shown).
The large helium vessel can accommodate alternative cavity shapes with few or no modifications.
Stainless steel He vessel and bellows.
Cavity and helium vessel

## Slide 10
Cavity “pair”
Cavities assembled as hermetically sealed pairs
He vessels connected (no separate two-phase pipe)
Large He inventory, large free surface area
VTA tested as a unit
If good: straight to module
Minimal degradation from VTA to module
Pairs supported by rods from vacuum vessel (no space frame)

## Slide 11
Modular cryostat containing “cavity pairs”
One piece or with bridging sections
Bridged version can be separated for repair or shipping
SNS type supply and return end cans shown
Modular cryostat

## Slide 12
Bridging section showing cold valves, beamline bellows
Bolted vacuum vessel connection, helium circuit connections
Access to tuners, HOM cables etc.
Could also contain magnet, BPM or HOM load (e.g. XFEL)
Close-up of bridging section

## Slide 13
Close up of coupler section in the middle of each “pair”
Longitudinal fixed point is in the plane of the coupler
Bellows between cavities and helium vessels provide compliance for cool-down and alignment.
Coupler section

## Slide 14
Exploded view showing details of modular construction

## Slide 15
Examples: ion ring cavity
Single cell 952.6 MHz
On-cell HOM dampers
Individual He vessel

## Slide 16
Crab cavity (RF dipole)
Example: Crab cavity

## Slide 17
Example: 650 MHz low b cavity
PIP-II b=0.6 650 MHz cavity

## Slide 18
Example: 400 MHz b=1 spoke cavity
Double spoke b=1 cavity
LCLS-II magnet package

## Slide 19
Example: 1.3 GHz LCLS-II production cavity
LCLS-II production cavity

## Slide 20
This approach provides flexibility and modularity to accommodate a wide range of cavity types, frequencies and a variety of potential applications.
The simple, low-cost modular components allow for common tooling and assembly practices.
Well suited to industrial production.
Allows pre-qualified modular units to be shipped, combined at the point of use, or returned for repair.
This concept combines many of the best and proven features of previous JLab designs but goes beyond any existing module.
Summary

## Slide 21: Collaboration CERN-JLab
Collaboration on Research and Development on
ERL Cavities and Cryomodules
1. Objective of the collaboration
  Following the MOU signed between CERN and JLAB on cooperation in superconducting RF accelerator technologies, this agreement, Appendix X, aims to develop a conceptual design and fabricate a prototype cavity suitable for LHeC. The aim of the prototype cavity is to validate the basic RF design in vertical test.
2. Organization of the Collaboration:
  JLAB: Robert Rimmer
  CERN: Karl-Martin Schirm

## Slide 22: Collaboration CERN-JLab
3. Technical Scope of the Collaboration:
3.1. JLAB responsibilities for:
  Technical advice and recommendations for cavity design and cryomodule integration.
  Design and fabrication of cavity dies and tooling.
  Fabrication of one 5-cell cavity and one single cell cavity.
  Chemical processing and vertical testing of the cavities.
3.2. CERN responsibilities for:
  Interface and requirements document(s) providing necessary technical information for LHeC cavities.
  Technical materials including niobium sheet, flanges, brazed transitions etc. consistent with CERN regulations.
  Engineering support and analysis as needed to comply with CERN regulations.

## Slide 23: Thanks! And to JLab colleagues esp. Jim Henry for the 3D models