## Slide 1: Abstract: The future Electron Ion Collider (EIC) LHeC will be able to collide electrons with protons/ions. Electron acceleration is based on a concept of Energy Recovery Linacs (ERL) with maximum energies of 60 GeV and almost completely recovering the energy during deceleration to the initial energy. We present: eRHIC, an ERL for LHeC (an example with almost double reduction in size of the linac, from 2 x 10 GeV to 2 x 5.345 GeV) from the present solution, using two Non-Scaling Fixed Field Alternating Gradient beam lines. This would reduce the three beam lines to two, and raise the luminosity for 34% from the electron current of 6.6 mA to 8.9 mA, for the synchrotron radiation limit of 15 MW.
ERL designs based on FFAG arcs
(eRHIC, LHeC, Cornell)
Dejan Trbojevic

## Slide 2
OUTLINE
Electron Ion Colliders eRHIC and LHeC
SUMMARY:
Advantages come from multiple passes through the linac bring reduction in the linac size and of three beam circulating lines to two, reducing the synchrotron radiation – raising 42% the luminosity
NS-FFAG: Introduction to the concept
Lattice examples of the eRHIC and ERL LHeC

## Slide 3
Layout of eRHIC with 21.2 GeV ERL
CeC PoP

## Slide 4
Linac-Ring Option - LHeC Recirculator
total circumference ~ 8.9 km
The baseline 60 GeV ERL option proposed can give an e-p luminosity of 1033 cm-2s-1 (extensions to 1034 cm-2s-1 and beyond are being considered)
© F. Zimmermann

## Slide 5: NS-FFAG LHeC Recirculator with 12 GeV ER
12 GeV/pass
LHC
IP
Linac
Injector
10 MeV
dump
60 GeV
48 GeV
60 GeV
High energy
NS-FFAG
Acceleration
60 GeV
12 GeV
24 GeV
36 GeV
LOW energy
NS-FFAG
Acceleration
48 GeV
60 GeV
High energy
NS-FFAG
Deceleration
36 GeV
24 GeV
12 GeV
LOW energy
NS-FFAG
Deceleration

## Slide 6: NS-FFAG LHeC Recirculator with 12 GeV ER
12 GeV/pass
LHC
IP
Linac
Injector
10 MeV
dump
60 GeV
36 GeV
24 GeV
12 GeV
48 GeV
60 GeV
LOW energy
NS-FFAG
Deceleration
High energy
NS-FFAG
Acceleration
12 GeV
24 GeV
36 GeV
LOW energy
NS-FFAG
Acceleration
60 GeV
48 GeV
High energy
NS-FFAG
Deceleration

## Slide 7: NS-FFAG LHeC Recirculator with ER
LHC
54.55GeV
43.644 GeV
NS-FFAG
High energy
NS-FFAG
10.906 GeV
21.829 GeV
32.735 GeV
NS-FFAG
LOW energy
NS-FFAG
60 GeV
5.453 GeV/pass
IP
Linac 2
Injector
17 MeV
Dump
17 MeV
5.453 GeV/pass
Linac 1

## Slide 8: NS-FFAG LHeC Recirculator with ER
LHC
43.644 GeV
54.550 GeV
NS-FFAG
High energy
NS-FFAG
32.735 GeV
21.829 GeV
10.906 GeV
NS-FFAG
LOW energy
NS-FFAG
60 GeV
5.453 GeV/pass
IP
Linac 2
Injector
17 MeV
Dump
17 MeV
5.453 GeV/pass
Linac 1

## Slide 9
OUTLINE: NS-FFAG for eRHIC and LHeC
WHAT IS Non-Scaling FFAG?
Orbits in NS-FFAG cells
Tune dependence on momentum
Path length dependence on energy
Straight section design
By pass design

## Slide 10: The AGS NS-FFAG, May 1983 D2-Muon Channel Experiment 745
dp/p=-55,-45%
dp/p=-15,-25%
dp/p=-5,-5%
dp/p= -55, 25 %
NIM 179(1981) 95-103
TRIUMF Vancouver p-m channel
D. Trbojevic, E.D. Courant, and A. A. Garren
Fall 1999,”FFAG Lattice Without Opposite Bends”,
HEMC’99 Workshop, dp/p= -30, 50 %

## Slide 11: SCALING VS. NON-SCALING FFAG
0.03 meters
Dx = Dx * dp/p
0.9 meters
Linear magnetic field:
B = Bo+ r Go
3 cm
To reduce the orbit offsets to ±4 cm range,
for momentum range of dp/p ~ ± 50 %
the dispersion function Dx has to be of the order of:
Dx ~ 4 cm / 0.5 = 8 cm
D magnet = reverse bend
Magnetically inefficient
VERY BAD for synchrotron radiation (10MW)
Linear magnetic field:
B = Bo+ r Go

## Slide 12: EMMA the first Non-Scaling FFAG (Electron Model for Many Applications) Daresbury Laboratory
LEARNING FROM PREVIOUS EXPERIENCE FROM WORKING NON-SCALING FFAG “EMMA”
(Being aware that EMMA is a much more difficult application of FFAG than eRHIC in many ways)
ELECTRON ENERGY RANGE IN EMMA WAS BUILT TO SIMULATE MUON ACCELERATION 10 – 20 GeV

## Slide 13
NS-FFAG Layout of the eRHIC
Option #1 Energy
50 mA
Linac 1.322 GeV
#1 7.944 GeV
#2 9.266 GeV
#3 11.910 GeV
#4 13.232 GeV
#5 14.554 GeV
#6 15.876 GeV
1.322+0.012 GeV
Option #2 Energy
10 mA
Linac 1.322 GeV
#1 6.622 GeV
#2 7.944 GeV
#3 9.266 GeV
#4 10.588 GeV
#5 11.910 GeV
#6 13.232 GeV
#7 14.554 GeV
#8 15.876 GeV
#9 17.198 GeV
#10 18.520 GeV
#11 19.842 GeV
#12 21.164 GeV
Injector 0.012 GeV
Energy
#1 1.334 GeV
#2 2.565 GeV
#3 3.978 GeV
#4 5.300 GeV
Linac 1.322 GeV
6.622 – 15.876 GeV

## Slide 14: eRHIC FFAG Rings in Perspective
Orbits exaggerated transversely 5000x, shape of hexagonal RHIC is evident
© Stephen Brooks

## Slide 15: Non-scaling FFAG for Muon Acceleration
47.8 mm
-29.5 mm
N=66
DRIFT FOR A
CAVITY
QF
QD
QF
CELL LENGTH 5 m
Extremely strong focusing with a small dispersion function
- Tunes vary
Orbit offsets are small
- Magnets are small
- Large energy acceptance

## Slide 16: Studies in the eRHIC NS-FFAG lattice
Magnet misalignment, gradient errors, magnetic field variation due to temperature, reproducibility of the magnetic fields.
Chuyu Liu
Chuyu Liu
Yue Hao
Correcting misalignment errors
François Méot
dp/p=0
dp/p=±10-4
66
48
48
66
eo-rms=50 p mm
5000 electrons
François Méot
SPIN DIFFUSION
30 G
0.01 G
0.01 G
30 G
François Méot

## Slide 17: The prototype of eRHIC will be built at Cornell
Dejan Trbojevic, Workshop on the LHeC, June 24-26, 2015

## Slide 18
76 – 286 MeV NS-FFAG Cornell Lattice 100 cells : Orbits and magnets in the 10.5 m diameter
5/21/15
18
BD
QF/2
13.598
x (mm)
-13.364
32.99 cm
10.99 cm
3 cm
-8.98 mm
GD = -27.493 T/m
ByD = 0.5044 T
GF = 42.54 T/m
ByF =-0.104 T
BDmin= 0.504+(-27.49*11.9 mm)=0.177 T
BFmax= -0.104 + 42.54 * (13.598 mm) = 0.4745 T
BFmin = -0.104 + 42.54* (-13.364 mm) = -0.673 T
BDmax= 0.504+(-27.49*-8.98mm) =0.751 T
11.9 mm
4.0 cm
11 cm
BF= -0.104 + 42.54 * x =0
x = 0.104/42.54 = 2.44 mm
BD=0.504 + (-27.493) x = 0
x = + 18.331 mm
286 MeV
216MeV
76 MeV
146 MeV
LINAC ENERGY 70 MeV
Injector 6 MeV
4.0 cm
QF/2
ECEN=225 MeV
qD=73.93 mrad
11.2
15.8
qF/2=-11.088/2 mrad
qF/2=-11.088/2 mrad
2.44

## Slide 19
OPERA cell is QF-QD-drift. Axis is straight. E = 76, 146, 216, 225 (reference) 286 MeV
FIELD
TRAJECTORIES
From Francois Meot and Nick Tsoupas

## Slide 20
OPERA cell is QF-QD-drift. Axis is straight.
From Francois Meot and Nick Tsoupas

## Slide 21
OPERA cell is QF-QD-drift. Axis is straight. MAXIMAL STABLE AMPLITUDES, H, V :
From Francois Meot and Nick Tsoupas

## Slide 22
OPERA cell is QF-QD-drift. Axis is straight. DYNAMICAL ACCEPTANCE
From Francois Meot and Nick Tsoupas

## Slide 23: Layout of the LHeC-LHC-SPS
From Oliver Brüning

## Slide 24
54.547 GeV
43.641 GeV
5.453 GeV
El. GUN
17 MeV
# 1 NS-FFAG beam line:
3 passes for acceleration
3 passes for recovery
# 2 NS-FFAG beam line:
2 passes for acceleration
2 passes for recovery
#2
Beam
Dump
λ/2
LHC
60 GeV
5.453 GeV
60 GeV
32.735 GeV
21.829 GeV
10.923 GeV
#1
54.547 GeV
43.641 GeV
32.735 GeV
21.829 GeV
10.923 GeV
#1
#2
Thomas Roser’s idea

## Slide 25
4.2/2=2.1
θD=2.4063 mrad
θF=4.594/2 mrad
ρD=914.286 m
x(mm)
θF=4.594 /2 mrad
0.0
ρF=914.286 m
ρF=914.286 m
GF= 30.299 T/m
GD=-40.127 T/m
7.00 m (897.5 cells = 2p*1000 m)
0.30 m
BF= 0.182 T
BD= 0.182 T
43.600 GeV
-2.26
1.33
LHeC ARC– 2 x 5.453 GeV linacs:
Orbits in the basic cell of the High energy NS-FFAG 54.55 - 43.644 GeV
4.2/2=2.1 m
54.550 GeV
0.30 m
GF= 30.299 T/m
BF=0.182 T
50.0 GeV
2.2 m

## Slide 26: Betatron Functions for Ec=50 GeV, 2 x 5.453 GeV linacs
by
bx
Dx

## Slide 27: Merging FFAG arcs to the straight section in eRHIC
7.75 mm

## Slide 28
4.2/2=2.1
θD=2.4063 mrad
θF=4.594 mrad
ρD=914.286 m
x(mm)
θF=4.594 /2 mrad
0.0
ρF=914.286 m
ρF=914.286 m
GF= 8.576 T/m
GD=-13.935 T/m
7.00 m (897.5 cells = 2p*1000 m)
0.30 m
BF= 0.1058T
BD= 0.1058 T
24.006 GeV
-9.8
16.3
LHeC-ERL with 2 x 5.453 GeV linacs
Orbits in the basic cell of the Low energy NS-FFAG 10.923 - 32.735 GeV
4.2/2=2.1 m
36.004 GeV
0.30 m
GF= 8.576 T/m
BF=0.1058 T
ECEN=29 GeV
2.2 m
10.923 GeV
-24.3
-14.9
13.7

## Slide 29: Betatron Functions for Ec=29 GeV, 2 x 5.453 GeV linacs
by
bx
Dx

## Slide 30
Synchrotron Radiation in LHeC with 2 x 5.453 GeV linacs Two NS-FFAG 43.6-54.6 GeV and 10.9-32.7 GeV
Maximum Collision Energy 60 GeV
E(GeV) | Total Power (MW) 8.87035 mA | Total Power (MW) 6.6 mA
54.550 | 7.5779 | 5.6383
43.644 | 4.2080 | 3.1310
32.735 | 1.3902 | 1.0344
21.829 | 1.2881 | 0.9584
10.923 | 0.5359 | 0.3987
TOTAL | 15.000 | 11.1608

## Slide 31: NS-FFAG for the LHeC ERL-ONE 12 GeV LINAC
0.010 GeV
Linac 11.998 GeV
48.002GeV
60 GeV
60 GeV after collisions
60.000 GeV
60 GeV
36.004 GeV
12.008 GeV
0.010 GeV
DUMP
El. GUN
60.000 GeV
48.002 GeV
12.008 GeV
#2
CIRCUMFERENCE 8.9 km
10 passes through
the linac
#1
24.006 GeV
36.004 GeV
12.008 GeV
24.006 GeV
24.006 GeV
24.006 GeV
12.008 GeV
48.002 GeV
60.000 GeV
36.004 GeV
36.004 GeV
#2
#1
12.008 GeV
48.002 GeV
60.000 GeV
36.004 GeV
24.006 GeV
0.010 GeV

## Slide 32
Synchrotron Radiation in LHeC with one 12 GeV linac Two NS-FFAG 48-60 GeV and 12-36 GeV
Maximum Collision Energy 60 GeV
E(GeV) | Total Power (MW) 6.7834 mA | Total Power (MW) 6.6 mA
54.550 | 6.4562 | 6.2816
43.644 | 4.6537 | 4.5279
32.735 | 2.5812 | 2.5115
21.829 | 0.8544 | 0.8313
10.923 | 0.4546 | 0.4423
TOTAL | 15.000 | 14.5945

## Slide 33: FFAG-ERL at CERN 240 m circumference
Dejan Trbojevic, Workshop on the LHeC, June 24-26, 2015
72.9 m
30.0 m
47.1 m

## Slide 34
A cost effective eRHIC design with 1.332 GeV linac and maximum energy of 21.2 GeV is shown.
A proposal for replacement of the 2 x 10 GeV linacs and three arcs, with 2 x 5.453 GeV linacs and two NS-FFAG arcs, respectively.
A cost-effective solution with lower synchrotron radiation, hence 34 % larger luminosity for the same limit on the value of 15 MW for the total loss from synchrotron radiation.
CONCLUSION

## Slide 35: Scaling down LHeC energies
Circumference of the LHC: CLHC = 26,658.88320 m
1/3 CLHC = 8,886.29440 m [60 GeV - Linacs 2x10x3] 10 GeV Linac ~2x 1 km+6.283+4x0.151
1/4 CLHC = 6,664.72080 m [45 GeV - Linacs 2x7.5x3]7.5 GeV linac 0.75 km
1/5 CLHC = 5,331.77664 m [36 GeV –Linacs 2x6x3]
FFAG solutions:
1/3 CLHC = 8,886.29440 m [60 GeV - Linacs 2x5.453x2]
    Or [ 60 GeV – one linac 12 GeVx2 FFAG lines]
1/4 CLHC = 6,664.72080 m [45 GeV –Linacs 2x4.125 GeV]
    Or [ 45 GeV one linac 11.245 GeV[
1/5 CLHC = 5,331.77664 m [36 GeV –one linac 8.99 GeV]