## Slide 1
Proposal for a common interface
for our PIC Poisson Solvers
--- PyPIC? ;-) ---
G. Iadarola, G. Rumolo
PyHEADTAIL meeting – 16/12/2014

## Slide 2
Introduction
  In many of our codes, Particle in Cell (PIC) algorithms are used to compute the Electric Field generated by a set of charged particles in a set of discrete points (can be the locations of the particles themselves, or of another set of particles)
  Typically 4 stages:
  Charge scatter from macroparticles (MPs) to grid
  Calculation of the electrostatic potential at the nodes
  Calculation of the electric field at the nodes (gradient evaluation)
  Field gather from grid to MPs
Notes:   changing with energy

## Slide 3
Basic stages of a PIC algorithm
  Standard Particle In Cell (PIC)  4 stages:
  Charge scatter from macroparticles (MPs) to grid
  Calculation of the electrostatic potential at the nodes
  Calculation of the electric field at the nodes (gradient evaluation)
  Field gather from grid to MPs
Internal nodes
External nodes (optional)
Uniform square grid

## Slide 4
  Standard Particle In Cell (PIC)  4 stages:
  Charge scatter from macroparticles (MPs) to grid
  Calculation of the electrostatic potential at the nodes
  Calculation of the electric field at the nodes (gradient evaluation)
  Field gather from grid to MPs
Basic stages of a PIC algorithm

## Slide 5
  Standard Particle In Cell (PIC)  4 stages:
  Charge scatter from macroparticles (MPs) to grid
  Calculation of the electrostatic potential at the nodes
  Calculation of the electric field at the nodes (gradient evaluation)
  Field gather from grid to MPs
  Boundary conditions (e.g., perfectly conducting, open, periodic)
Basic stages of a PIC algorithm
  Different numerical approaches to the solution with different advantages and drawbacks.
  Already implemented in our codes:
  FASTION, HEADTAIL and PyHEADTAIL: Open space FFT solver (explicit, very fast but open boundaries)
  HEADTAIL: Rectangular boundary FFT solver (explicit, very fast but only rectangular boundaries)
  FASTION: dual grid (see Lotta’s presentation)
  PyECLOUD (and PyEC4PyHT): Finite Difference implicit Poisson solver (arbitrary chamber shape, sparse matrix, possibility to use Shortley Weller boundary refinement, KLU fast routines, computationally more demanding)

## Slide 6
  Standard Particle In Cell (PIC)  4 stages:
  Charge scatter from macroparticles (MPs) to grid
  Calculation of the electrostatic potential at the nodes
  Calculation of the electric field at the nodes (gradient evaluation)
  Field gather from grid to MPs
Basic stages of a PIC algorithm

## Slide 7
  Standard Particle In Cell (PIC)  4 stages:
  Charge scatter from macroparticles (MPs) to grid
  Calculation of the electrostatic potential at the nodes
  Calculation of the electric field at the nodes (gradient evaluation)
  Field gather from grid to MPs
Basic stages of a PIC algorithm

## Slide 8
  We could collect all the code we already have in a common tool (PyPIC? ;-)), with a common interface. This would mean:
  A single implementation for common features (scatter, gather, etc…)
  All implementations become naturally available for all users (fast rectangular or dual grid in PyECLOUD and PyHEADTAIL, Finite Difference in FASTION)
  With a bit of tweaking we could get a first space charge module for PyHEADTAIL (?) (practically already debugged…)
  New implementations easier to test and debug and immediately available for all usages
Advantages of a common interface
Something like this…

## Slide 9
  class ACertainPIC:
  def __init__ (self, geometry, grid, numerical_param):
  ……..
  def scatter(self, x_mp, y_mp, q_mp):
  ……..
  def solve(self)
  ……..
  def gather (self, x_mp, y_mp):
  ……..
  return Ex_mp, Ey_mp
  ……..
First idea on a possible interface

## Slide 10
  Example of usage:
  import PyPIC.PIC_FFT as PyPICFFT
  mypic = PyPICFFT(xmin, xmax, dx, ymin, ymax,dy)
  <some code which gives x_mp, y_mp, q_mp>
  mypic.scatter(x_mp, y_mp, q_mp)
  mypic.solve()
  Ex_mp, Ey_mp = mypic.gather(x_mp, y_mp)
First idea on a possible interface

## Slide 11
  Now I want to change the solver:
  import PyPIC.PIC_FFT as PyPICFFT
  mypic = PyPICFFT(xmin, xmax, dx, ymin, ymax,dy)
  <some code which gives x_mp, y_mp, q_mp>
  mypic.scatter(x_mp, y_mp, q_mp)
  mypic.solve()
  Ex_mp, Ey_mp = mypic.gather(x_mp, y_mp)
First idea on a possible interface

## Slide 12
  Now I want to change the solver:
  #import PyPIC.PIC_FFT as PyPICFFT
  import PyPIC.PIC_FD as PyPICFD
  #mypic = PyPICFFT(xmin, xmax, dx, ymin, ymax,dy)
  mypic = PyPICFD(chamber_object, dx, dy)
  <some code which gives x_mp, y_mp, q_mp>
  mypic.scatter(x_mp, y_mp, q_mp)
  mypic.solve()
  Ex_mp, Ey_mp = mypic.gather(x_mp, y_mp)
First idea on a possible interface

## Slide 13
  If I want compare the two:
  import PyPIC.PIC_FFT as PyPICFFT
  import PyPIC.PIC_FD as PyPICFD
  mypic1 = PyPICFFT(xmin, xmax, dx, ymin, ymax,dy)
  mypic2 = PyPICFD(chamber_object, dx, dy)
  <some code which gives x_mp, y_mp, q_mp>
  mypic1.scatter(x_mp, y_mp, q_mp)
  mypic1.solve()
  Ex1_mp, Ey1_mp = mypic1.gather(x_mp, y_mp)
  mypic2.scatter(x_mp, y_mp, q_mp)
  mypic2.solve()
  Ex2_mp, Ey2_mp = mypic2.gather(x_mp, y_mp)
  print norm(Ex1-Ex2)/norm(Ex1)
  print norm(Ey1-Ey2)/norm(Ey1)
First idea on a possible interface

## Slide 14
Thanks for your attention!

## Slide 15
  Standard Particle In Cell (PIC)  4 stages:
  Charge scatter from macroparticles (MPs) to grid
  Calculation of the electrostatic potential at the nodes
  Calculation of the electric field at the nodes (gradient evaluation)
  Field gather from grid to MPs
Internal nodes:
External nodes:
Can be written in matrix form:
A is sparse and depends only on chamber geometry and grid size
 It can be computed and LU factorized in the initialization stage to speed up calculation
Basic stages of a PIC algorithm