## Slide 1: Field Mapping: Magnetic axis of FC2, SSU & SSD
V. Blackmore
CM41
9th February, 2015
1/44
Field Mapping, CM41

## Slide 2: The problem
Alignment
Geometric, magnetic and mapper axes
2/44
Field Mapping, CM41

## Slide 3: Magnet Alignment
Survey point
Coil
Bellows
Reference particle
3/44
Field Mapping, CM41

## Slide 4: Co-ordinate systems
Survey point
Coil
Mapper
Hall probe
Geometric axis
The co-ordinate system defined with respect to the survey points on the magnet exterior.
NB: Not the co-ordinate system of the MICE Hall…
4/44
Field Mapping, CM41

## Slide 5: Co-ordinate systems
Survey point
Coil
Mapper
Hall probe
Magnetic axis
The co-ordinate system defined with respect to the coils on the magnet bobbin.
Also the line along which
5/44
Field Mapping, CM41

## Slide 6: Co-ordinate systems
Survey point
Coil
Mapper
Hall probe
Mapper axis
The co-ordinate system defined with respect to the centre of the measurement disc on the CERN field mapper.
6/44
Field Mapping, CM41

## Slide 7: Co-ordinate systems
Survey point
Coil
Mapper
Hall probe
Measure the magnetic axis with the mapper
Transform from mapper to geometric co-ordinates
Sounds easy!
… right?
7/44
Field Mapping, CM41

## Slide 8: Co-ordinate systems
Coil
Mapper
Hall probe
Catch: We measure the field components in the mapper system.
=
is the rotation of the magnetic axis around the -axis. There may be a corresponding rotation around the -axis
8/44
Field Mapping, CM41

## Slide 9: Co-ordinate systems
Coil
Mapper
Hall probe
Catch: We measure the field components in the mapper system.
=
9/44
Field Mapping, CM41
Notes: SOH CAH TOA

## Slide 10: Test field maps*
Define a measurement grid in the mapper system: .
Transform measurement grid to coil system:
Calculate field in coil system:
Transform fields back to mapper system:
Now have ‘measurements’ of a tilted coil (or coils) in mapper system.
* Here just look at rotations, offset in would be a constant shift.
10/44
Field Mapping, CM41
Notes: SOH CAH TOA

## Slide 11: Test field maps
To first approximation, at a particular , should be linear with and similarly for ,
On the axis in the magnet system, . So in the mapper system, on the axis we would see,
If we were offset from the axis, would represent that offset. In the perfectly aligned magnet system, .
11/44
Field Mapping, CM41

## Slide 12: Test Magnet: “FC-like”
Assume that there is no rotation and that the mapper and magnetic axes are aligned.
  At each , fit
  Then is the position of the axis at that . (Similar for )
Know the real position of the magnetic axis for this test case.
Pulled away from true axis by and contributions
Anyone who remembers this talk at CM40 might recognise this “feature”!
12/44
Field Mapping, CM41

## Slide 13: Test Magnet: “FC-like”
Assume that there is no rotation and that the mapper and magnetic axes are aligned.
  At each , fit
  Then is the position of the axis at that . (Similar for )
Best fit line real axis
13/44
Field Mapping, CM41

## Slide 14: Test Magnet: “FC-like”
is large, so axis tilts gain a non-negligible contribution
  Fit again, but with true and :
Can’t ignore this
Assuming that , so not perfect (c.f. slide 11)
NB: This slide blatantly cheats at the fit to prove a point. We need to find and still!
14/44
Field Mapping, CM41

## Slide 15: Test Magnet: “FC-like”
Using fitted values of , estimate (and similarly for ) and plot the residual
  Getting and perfectly, still limited by knowledge of at the level of 1G ( error on Hall probe)
NB: This slide blatantly cheats at the fit to prove a point. We need to find and still!
15/44
Field Mapping, CM41

## Slide 16: Test Magnet: “FC-like”
Using fitted values of , estimate (and similarly for ) and plot the residual
  Even if and are found perfectly, still limited by knowledge of at the level of 1G ( error on Hall probe)
NB: This slide blatantly cheats at the fit to prove a point. We need to find and still!
16/44
Field Mapping, CM41

## Slide 17: Test Magnet: “FC-like”
Finding and :
  calculated from , (slide 13)
  Excludes contributions from and
  At the magnetic axis, we would measure,
  Improve future iterations by calculating and using current ‘best fit’ line to
  Then feed forward to next iteration (i.e. beginning at slide 14…)
17/44
Field Mapping, CM41

## Slide 18: Test Magnet: “FC-like”
No cheating this time – attempt to retrieve and
18/44
Field Mapping, CM41

## Slide 19
Test Magnet: “FC-like”
No cheating this time – attempt to retrieve and
-
19/44
Field Mapping, CM41

## Slide 20: FC1
Finding the axis of FC1
Run 3
100 A
Flip mode
20/44
Field Mapping, CM41

## Slide 21: Try on FC1
(Run 3, 100A, flip mode)
More ‘wiggly’ than model data
21/44
Field Mapping, CM41

## Slide 22: Try on FC1
(Run 3, 100A, flip mode)
 Residuals are much larger than expected – so what’s going on…
22/44
Field Mapping, CM41

## Slide 23: Transverse vector field
Field vector,
Points along vector
Points behind vector
A Maxwellian field’s vectors should all point to the axis
 some systematic effect (possibly additionally tilted probes)
This plot indicates a position for reference.
23/44
Field Mapping, CM41

## Slide 24: Correction?
At each , look at . Should be 0 for all rotations of the mapper disc, but is not so.
Subtract the average from each measurement…
24/44
Field Mapping, CM41

## Slide 25: Transverse vector field
Field vector,
Points along vector
Points behind vector
Now vectors point towards “the axis”.
But: Is a correction for needed?
This plot indicates a position for reference.
25/44
Field Mapping, CM41

## Slide 26: Try on FC1 (again)
(Run 3, 100A, flip mode)
More ‘wiggly’ than model data
26/44
Field Mapping, CM41

## Slide 27: Try on FC1 (again)
(Run 3, 100A, flip mode)
 Better! Can compare axes with and without correction to get an idea of overall effect…
27/44
Field Mapping, CM41

## Slide 28: FC1
Correction had largest effect on -axis result, but still small.
28/44
Field Mapping, CM41

## Slide 29: FC2
“Run 3”
100 A
Flip mode
With correction
29/44
Field Mapping, CM41

## Slide 30: FC2
(Run 3, 100A, flip mode)
Has more ‘character’ than FC1
Reminder: All lines are in the mapper co-ordinate system.
30/44
Field Mapping, CM41

## Slide 31: FC2
(Run 3, 100A, flip mode)
31/44
Field Mapping, CM41

## Slide 32: Spectrometer Solenoids
Ode to awkward magnets
32/44
Field Mapping, CM41

## Slide 33: The ‘SS’ Saga
Q1: In the 4T ‘flat field’ region...
  Where is the axis of a uniform solenoid?
  Will exclude this region from fits
The mapper carriage is different for the SS mapping
  Longer (~5m, rather than 3)
  More flex and wobble
  More difficult to align to the bore before measurements begin (?)
Measurements taken slightly differently (a complete loop of the Hall probes is two “runs”
Survey of the mapper movement during measurements for FC1 & FC2 show ~0.1mm movement.
Much worse for SS’s… for example!
33/44
Field Mapping, CM41

## Slide 34: Beautiful survey plots from LBNL
The mapper’s movement is fairly complex – still digesting!
34/44
Field Mapping, CM41

## Slide 35: USS
“Runs 21 & 22”
“100% solenoid mode”
Excluding m region
With correction
(First magnet mapped)
35/44
Field Mapping, CM41

## Slide 36: USS, fitting over full -range
Non-uniform, E2 needs turning down
(see DSS for ‘tweaked’ flat field) – Also see this in MAUS with ‘default’ currents.
Field
Axis fit
36/44
Field Mapping, CM41

## Slide 37: USS, excluding m region
Excluded field points here, this is a plotting artifact.
Field
Axis fit
37/44
Field Mapping, CM41
Scale change

## Slide 38: USS, excluding m region
Excluded region
Excluded region
Larger residuals than for FC1 & FC2.
Still some oddities in transverse vector plots (see supporting material)
38/44
Field Mapping, CM41

## Slide 39: DSS
“Runs 25+26”
“100% flip mode”
Excluding m region
With correction
39/44
Field Mapping, CM41

## Slide 40: DSS, fitting over full -range
Much flatter with tweaked currents.
40/44
Field Mapping, CM41
DSS has smaller ‘wiggle’ here than USS

## Slide 41: DSS, excluding m region
41/44
Field Mapping, CM41
Scale change

## Slide 42: DSS, excluding m region
Excluded region
Excluded region
Residuals on par with FC2 (still worse than FC1)
Still more to learn (and still need error bars)
42/44
Field Mapping, CM41

## Slide 43: “Results”
FC1 | 
FC2 | 
DSS (Excluding m region) | 
USS (Excluding m region) | 
FC1 | 
FC2 | 
Equations describing current (Feb 2015) best fit to magnetic axis in mapper co-ordinate system (units are m!)
43/44
Field Mapping, CM41

## Slide 44: To do:
Investigate vector plots from SS’s more thoroughly
Correction to necessary?
  One Hall probe cube ‘contains’ 3 independent Hall sensors
Apply survey
  ‘Swingy’ travel through SS’s needs help!
Think really, really hard about the errors
… Then the remaining field map exercise!
44/44
Field Mapping, CM41