## Slide 1: Power, electronics, cabling. Infrastructure of LHCb upgrade workshop.
J. Buytaert.
19 February 2015

## Slide 3: ASIC/sensor/hybrid/module
sensor tile = 3 ASICs + sensor (a.k.a. triple / assembly)
hybrid = kapton pcb for 2 tiles (= 6 ASICs)
  hosts the GBTx for slow and fast control signals (ECS/TFC)
  maybe hosts the GBT-SCA (providing ADC + reset) t.b.d.
module = cooling substrate with hybrid and tiles on both sides
  all module connection are electrical (not optical), basically power and high speed links
ASIC
~42 mm
Sensor tile
ASIC
ASIC
~14 mm
‘Hybrid circuit’
‘module’

## Slide 4: Detailed overview of a ‘slice’ & locations
vacuum feed-through
HV PS
LV PS
3 data links
7 data links
GBTx
6 x ECS
6 x CLK
6 x TFC
LV
T1,2
HV
1 module =
2 x front-end hybrids
PCIe40
12 x DC/DC
10 x VTTx
3 x VTRx
GBTx
2 x GBLD
4 x DC/DC
2 x SCA
1 x opto & power board “OPB”
SOL40
off-detector electronics
(remote)
GBLD
SCA?
VMON
< 1 m
Interlock
4 x HV
TOPB
2 x (10) data links
52 slices in the whole VELO.
reset
Flex cables
Optical fibers
Inside vacuum vessel
Periphery of vacuum vessel
Surface P8
‘Cabling’
Barrack
D2 UX85A
Note: no more use of ‘balcony’

## Slide 5: Low voltage power
Reuse of existing CAEN Easy system (in D2).
  It is able to deliver the power for the upgrade.
  It has high number of channels. Need 52*3=156.
  It is stable.
  Lifetime of power supplies can be >15 years.
  As long as maintenance contract is in place. (cfr ATLAS & CMS).
Reuse of existing LV long distance cables.
  60 meter, ~0.5 Ohm. Acceptable voltage drop 2V-3V.
  Possible need to adapt patch panel on detector side.

## Slide 6: Low voltage power.
Power requirements (maximal):
  1 full station: 64W
    Module : ~33W
    OPB board: ~31W
  52 stations: 3.3 kW
    Module : ~1.7 kW
    OPB board: ~1.6 kW
All voltages(1.2V, 1.5V, 2.5V) for OPB and module are derived by DC-DC converters from 3 incoming 5V ‘bulk’ supplies.
OPB cooling: forced air cooling probably necessary.

## Slide 7: High Voltage power.
Upgrade needs twice more channels than current VELO.
  1 individual HV per sensor tile. (208 tiles).
  Need to reach 1000V. (current ISEG <700V)
  Requires new HV supplies.
  Additional long distance HV cabling. Existing cables can be reused.
  New patch panels on both ends.

## Slide 8: Optical long distance cabling.
Data.
  Unidirectional (GWT serial format @ 5.12Gbps)
  20 (22?) links per station.
  full VELO:
    Needed : 1040 (1144?) links.
    Installed : 9 ‘trunk cables’, i.e. 1296.
      2 x MPO (=24 fibres) per station. (4 fibres unused).
    Spare: 24% (13%?).
    Reduce to 8 trunk cables ?
      Requires ‘shuffling’ of fibres at detector & Tell40 side. (cassettes). Equal cost ?
      Less “elegant”: MPO fibres shared between modules.

## Slide 9
Module 1
MPO-MPO Adaptors Path Panel
Option 2 for DATA
UX85 caverne
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
??
??
Total 26 Modules / side
12f
MPO
LC
PM85 pit
Surface
12f
MPO
12f
MPO
12f
MPO
MPO 1
MPO 2
MPO 3
MPO 4
144f
…
MPO 1
AMC40
PCIe
2 MPO Input
for Module 1
MPO
MPO-MPO Adaptors Path Panel
12f
MPO
12f
MPO
MPO 4
MPO 2
Trunk 1
for Module 3
…
…
…
MPO 12
Spare
Spare
MPO 3
AMC40
PCIe
2 MPO Input
for Module 2
MPO
MPO-MPO Adaptors Path Panel
12f
MPO
12f
MPO
Module 2
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
??
??
LC
Spare
Spare
11 used
11 used
11 used
11 used
Ex:48f?
5-10m
MPO-MPO Adaptors Path Panel
5-10m
330-350m
1-3m

## Slide 10: Optical long distance cabling.
ECS & TFC.
  Standard GBT serial format @ 4.8Gbps. Bidirectional.
  3 links per station:
    1 for each of 2 hybrids
    1 local OPB control & monitoring
  Full VELO:
    Needed: 156 x 2=312 links
    Installed: 3 trunk cables. (432 links)
    Spares: 38%. Could be shared with other sub-detector (RICH or UT?)

## Slide 11
MPO
MPO
Ex:48f?
5-10m
Module 1
MPO-MPO Adaptors Path Panel
for TFC
UX85 caverne
1
2
3
Total 26 Modules / side
12f
MPO
LC Duplex
PM85 pit
Surface
MPO
MPO
MPO 1
MPO 2
MPO 3
MPO 4
144f
…
MPO 1
SOL40
MPO
MPO-MPO Adaptors Path Panel
12f
MPO
12f
MPO
MPO 4
MPO 2
Trunk TFC/ECS 1
…
…
…
MPO 12
MPO 3
MPO
1f
Module 2
1
2
3
1f
Module 3
1
2
3
Module 4
1
2
3
1f
MPO
5-10m
330-350m
1-3m