## Slide 1: (SOME) EFFECTS NEAR TRANSITION
E. Métral (CERN)

## Slide 2: (SOME) EFFECTS NEAR TRANSITION
E. Métral (CERN)
Transition energy

## Slide 3: (SOME) EFFECTS NEAR TRANSITION
E. Métral (CERN)
Transition energy
Longitudinal beam dynamics “far” below or above transition

## Slide 4: (SOME) EFFECTS NEAR TRANSITION
E. Métral (CERN)
Transition energy
Longitudinal beam dynamics “far” below or above transition
Transition crossing (with the example of the CERN PS machine)

## Slide 5: (SOME) EFFECTS NEAR TRANSITION
E. Métral (CERN)
Transition energy
Longitudinal beam dynamics “far” below or above transition
Transition crossing (with the example of the CERN PS machine)
Transverse (slow) head-tail instability

## Slide 6: (SOME) EFFECTS NEAR TRANSITION
E. Métral (CERN)
Transition energy
Longitudinal beam dynamics “far” below or above transition
Transition crossing (with the example of the CERN PS machine)
Transverse (slow) head-tail instability
Fast (vertical) single-bunch instability

## Slide 7: (SOME) EFFECTS NEAR TRANSITION
E. Métral (CERN)
Transition energy
Longitudinal beam dynamics “far” below or above transition
Transition crossing (with the example of the CERN PS machine)
Transverse (slow) head-tail instability
Fast (vertical) single-bunch instability
  Crossing transition in the CERN PS

## Slide 8: (SOME) EFFECTS NEAR TRANSITION
E. Métral (CERN)
Transition energy
Longitudinal beam dynamics “far” below or above transition
Transition crossing (with the example of the CERN PS machine)
Transverse (slow) head-tail instability
Fast (vertical) single-bunch instability
  Crossing transition in the CERN PS
  Injecting just above transition in the CERN SPS

## Slide 9: (SOME) EFFECTS NEAR TRANSITION
E. Métral (CERN)
Transition energy
Longitudinal beam dynamics “far” below or above transition
Transition crossing (with the example of the CERN PS machine)
Transverse (slow) head-tail instability
Fast (vertical) single-bunch instability
  Crossing transition in the CERN PS
  Injecting just above transition in the CERN SPS
Conclusion

## Slide 10: TRANSITION ENERGY (1/3)
Momentum compaction factor

## Slide 11: TRANSITION ENERGY (1/3)
Momentum compaction factor

## Slide 12: TRANSITION ENERGY (1/3)
Momentum compaction factor
Machine circumference
Beam momentum
Horizontal dispersion
Bending radius

## Slide 13: TRANSITION ENERGY (1/3)
Momentum compaction factor
Machine circumference
Beam momentum
Horizontal dispersion
Bending radius
=> Parameter coming from the accelerator lattice

## Slide 14: TRANSITION ENERGY (1/3)
Momentum compaction factor
Machine circumference
Beam momentum
  In most circular machines, αp > 0
Horizontal dispersion
Bending radius
=> Parameter coming from the accelerator lattice

## Slide 15: TRANSITION ENERGY (1/3)
Momentum compaction factor
Machine circumference
Beam momentum
  In most circular machines, αp > 0
Horizontal dispersion
Bending radius
=> Parameter coming from the accelerator lattice
Gamma transition

## Slide 16: TRANSITION ENERGY (1/3)
Momentum compaction factor
Machine circumference
Beam momentum
  In most circular machines, αp > 0
  However, αp < 0 is also possible (e.g. CERN LEAR machine) => Called “Negative Momentum Compaction” (NMC) or “Imaginary γt” lattice
Horizontal dispersion
Bending radius
=> Parameter coming from the accelerator lattice
Gamma transition

## Slide 17: TRANSITION ENERGY (2/3)
  Assume αp > 0

## Slide 18: TRANSITION ENERGY (2/3)
  Assume αp > 0
    dp > 0 => dC > 0

## Slide 19: TRANSITION ENERGY (2/3)
  Assume αp > 0
    dp > 0 => dC > 0
    dp > 0 => dv > 0

## Slide 20: TRANSITION ENERGY (2/3)
  Assume αp > 0
    dp > 0 => dC > 0
    dp > 0 => dv > 0
  => What happens to the revolution frequency frev = v / C?

## Slide 21: TRANSITION ENERGY (2/3)
  Assume αp > 0
    dp > 0 => dC > 0
    dp > 0 => dv > 0
    At (very) high energy, v ≈ clight and remains constant => frev 
  => What happens to the revolution frequency frev = v / C?

## Slide 22: TRANSITION ENERGY (2/3)
  Assume αp > 0
    dp > 0 => dC > 0
    dp > 0 => dv > 0
    At (very) high energy, v ≈ clight and remains constant => frev 
    At low energy, v increases faster than C => frev 
  => What happens to the revolution frequency frev = v / C?

## Slide 23: TRANSITION ENERGY (2/3)
  Assume αp > 0
    dp > 0 => dC > 0
    dp > 0 => dv > 0
    At (very) high energy, v ≈ clight and remains constant => frev 
    At low energy, v increases faster than C => frev 
  => What happens to the revolution frequency frev = v / C?
There is an energy for which the velocity variation is compensated by the trajectory variation (i.e. dfrev = 0):
=> TRANSITION ENERGY

## Slide 24: TRANSITION ENERGY (3/3)
Slip factor

## Slide 25: TRANSITION ENERGY (3/3)
Slip factor

## Slide 26: TRANSITION ENERGY (3/3)
Slip factor
Relativistic mass factor of the beam

## Slide 27: TRANSITION ENERGY (3/3)
Slip factor
    η < 0 below transition
Relativistic mass factor of the beam

## Slide 28: TRANSITION ENERGY (3/3)
Slip factor
    η < 0 below transition
    η = 0 at transition => Isochronous condition
Relativistic mass factor of the beam

## Slide 29: TRANSITION ENERGY (3/3)
Slip factor
    η < 0 below transition
    η = 0 at transition => Isochronous condition
    η > 0 above transition
Relativistic mass factor of the beam

## Slide 30: LONGITUDINAL BEAM DYNAMICS “FAR” BELOW OR ABOVE TRANSITION (1/2)
(Bucket) separatrices:

## Slide 31: LONGITUDINAL BEAM DYNAMICS “FAR” BELOW OR ABOVE TRANSITION (1/2)
(Bucket) separatrices: Below transition

## Slide 32: LONGITUDINAL BEAM DYNAMICS “FAR” BELOW OR ABOVE TRANSITION (1/2)
(Bucket) separatrices: Below transition

## Slide 33: LONGITUDINAL BEAM DYNAMICS “FAR” BELOW OR ABOVE TRANSITION (1/2)
(Bucket) separatrices: Below transition

## Slide 34: LONGITUDINAL BEAM DYNAMICS “FAR” BELOW OR ABOVE TRANSITION (1/2)
(Bucket) separatrices: Below transition
Above transition

## Slide 35: LONGITUDINAL BEAM DYNAMICS “FAR” BELOW OR ABOVE TRANSITION (1/2)
(Bucket) separatrices: Below transition
Above transition

## Slide 36: LONGITUDINAL BEAM DYNAMICS “FAR” BELOW OR ABOVE TRANSITION (1/2)
(Bucket) separatrices: Below transition
Above transition

## Slide 37: LONGITUDINAL BEAM DYNAMICS “FAR” BELOW OR ABOVE TRANSITION (2/2)
Particle trajectories:

## Slide 38: LONGITUDINAL BEAM DYNAMICS “FAR” BELOW OR ABOVE TRANSITION (2/2)
Particle trajectories: Below transition

## Slide 39: LONGITUDINAL BEAM DYNAMICS “FAR” BELOW OR ABOVE TRANSITION (2/2)
Particle trajectories: Below transition

## Slide 40: LONGITUDINAL BEAM DYNAMICS “FAR” BELOW OR ABOVE TRANSITION (2/2)
Particle trajectories: Below transition

## Slide 41: TRANSITION CROSSING (1/9)
“Far” below or above transition  Adiabaticity condition

## Slide 42: TRANSITION CROSSING (1/9)
“Far” below or above transition  Adiabaticity condition
“Close” to transition, the adiabaticity condition is not satisfied => Non-adiabatic synchrotron motion

## Slide 43: TRANSITION CROSSING (1/9)
“Far” below or above transition  Adiabaticity condition
“Close” to transition, the adiabaticity condition is not satisfied => Non-adiabatic synchrotron motion
  When the time is close enough to transition, the particle will not be able to catch up with the rapid modification of the bucket shape

## Slide 44: TRANSITION CROSSING (1/9)
“Far” below or above transition  Adiabaticity condition
“Close” to transition, the adiabaticity condition is not satisfied => Non-adiabatic synchrotron motion
  When the time is close enough to transition, the particle will not be able to catch up with the rapid modification of the bucket shape
  Nonadiabatic time

## Slide 45: TRANSITION CROSSING (1/9)
“Far” below or above transition  Adiabaticity condition
“Close” to transition, the adiabaticity condition is not satisfied => Non-adiabatic synchrotron motion
  When the time is close enough to transition, the particle will not be able to catch up with the rapid modification of the bucket shape
  Nonadiabatic time

## Slide 46: TRANSITION CROSSING (1/9)
“Far” below or above transition  Adiabaticity condition
“Close” to transition, the adiabaticity condition is not satisfied => Non-adiabatic synchrotron motion
  When the time is close enough to transition, the particle will not be able to catch up with the rapid modification of the bucket shape
  Nonadiabatic time
~ 2 ms for the nTOF bunch in the CERN PS

## Slide 47: TRANSITION CROSSING (2/9)
nTOF bunch in the CERN PS

## Slide 48: TRANSITION CROSSING (2/9)
nTOF bunch in the CERN PS

## Slide 49: TRANSITION CROSSING (2/9)
nTOF bunch in the CERN PS
=> γt ≈ 6.1

## Slide 50: TRANSITION CROSSING (3/9)

## Slide 51: TRANSITION CROSSING (3/9)

## Slide 52: TRANSITION CROSSING (4/9)
Longitudinal mismatch (due to the longitudinal Space Charge): IN STATIC

## Slide 53: TRANSITION CROSSING (5/9)
Longitudinal mismatch (due to the longitudinal Space Charge): IN DYNAMIC (i.e. crossing transition)

## Slide 54: TRANSITION CROSSING (6/9)
Longitudinal mismatch (due to the inductive part of the longitudinal Broad-Band impedance): IN DYNAMIC (i.e. crossing transition)

## Slide 55: TRANSITION CROSSING (7/9)
Remedies

## Slide 56: TRANSITION CROSSING (7/9)
Remedies
  Avoid crossing transition in the design phase => αp < 0

## Slide 57: TRANSITION CROSSING (7/9)
Remedies
  Avoid crossing transition in the design phase => αp < 0
  If transition crossing cannot be avoided, the “γt jump” is the only (known) method to overcome all the intensity limitations => Artificial increase of the transition crossing speed by means of fast pulsed quadrupoles (at non zero dispersion locations)

## Slide 58: TRANSITION CROSSING (7/9)
Remedies
  Avoid crossing transition in the design phase => αp < 0
  If transition crossing cannot be avoided, the “γt jump” is the only (known) method to overcome all the intensity limitations => Artificial increase of the transition crossing speed by means of fast pulsed quadrupoles (at non zero dispersion locations)

## Slide 59: TRANSITION CROSSING (7/9)
Remedies
  Avoid crossing transition in the design phase => αp < 0
  If transition crossing cannot be avoided, the “γt jump” is the only (known) method to overcome all the intensity limitations => Artificial increase of the transition crossing speed by means of fast pulsed quadrupoles (at non zero dispersion locations)
Effective crossing speed ~ 50 times faster with the γt jump

## Slide 60: TRANSITION CROSSING (8/9)
  Asymmetric or symmetric γt jump?

## Slide 61: TRANSITION CROSSING (8/9)
  Asymmetric or symmetric γt jump?

## Slide 62: TRANSITION CROSSING (8/9)
  Asymmetric or symmetric γt jump?

## Slide 63: TRANSITION CROSSING (9/9)

## Slide 64: TRANSITION CROSSING (9/9)

## Slide 65: TRANSVERSE (SLOW) HEAD-TAIL INSTABILITY (1/2)
If the sign of the chromaticity (which is equal to ~ -1 for an uncorrected machine like the PS) is not changed (in both transverse planes) above transition, a (single-bunch) head-tail instability may develop

## Slide 66: TRANSVERSE (SLOW) HEAD-TAIL INSTABILITY (1/2)
If the sign of the chromaticity (which is equal to ~ -1 for an uncorrected machine like the PS) is not changed (in both transverse planes) above transition, a (single-bunch) head-tail instability may develop
  This instability can be damped through Landau damping using octupoles, which introduce some amplitude detunings. This method was first used in the past to stabilize the PS beams

## Slide 67: TRANSVERSE (SLOW) HEAD-TAIL INSTABILITY (1/2)
If the sign of the chromaticity (which is equal to ~ -1 for an uncorrected machine like the PS) is not changed (in both transverse planes) above transition, a (single-bunch) head-tail instability may develop
  This instability can be damped through Landau damping using octupoles, which introduce some amplitude detunings. This method was first used in the past to stabilize the PS beams
  However, the better method of changing the sign of the chromaticities (and keeping them to small positive values) by acting on the optics with sextupoles was then adopted, and it has become a routine operation at the CERN PS for many years

## Slide 68: TRANSVERSE (SLOW) HEAD-TAIL INSTABILITY (1/2)
If the sign of the chromaticity (which is equal to ~ -1 for an uncorrected machine like the PS) is not changed (in both transverse planes) above transition, a (single-bunch) head-tail instability may develop
  This instability can be damped through Landau damping using octupoles, which introduce some amplitude detunings. This method was first used in the past to stabilize the PS beams
  However, the better method of changing the sign of the chromaticities (and keeping them to small positive values) by acting on the optics with sextupoles was then adopted, and it has become a routine operation at the CERN PS for many years
      => The chromatic frequency should be (slightly) positive to avoid the head-tail mode 0 (most critical) from developing

## Slide 69: TRANSVERSE (SLOW) HEAD-TAIL INSTABILITY (1/2)
If the sign of the chromaticity (which is equal to ~ -1 for an uncorrected machine like the PS) is not changed (in both transverse planes) above transition, a (single-bunch) head-tail instability may develop
  This instability can be damped through Landau damping using octupoles, which introduce some amplitude detunings. This method was first used in the past to stabilize the PS beams
  However, the better method of changing the sign of the chromaticities (and keeping them to small positive values) by acting on the optics with sextupoles was then adopted, and it has become a routine operation at the CERN PS for many years
      => The chromatic frequency should be (slightly) positive to avoid the head-tail mode 0 (most critical) from developing

## Slide 70: TRANSVERSE (SLOW) HEAD-TAIL INSTABILITY (2/2)
Example of transverse (slow) head-tail instability observed in the CERN PS at injection (below transition)

## Slide 71: TRANSVERSE (SLOW) HEAD-TAIL INSTABILITY (2/2)
Example of transverse (slow) head-tail instability observed in the CERN PS at injection (below transition)
  Consecutive traces at a pick-up superimposed

## Slide 72: TRANSVERSE (SLOW) HEAD-TAIL INSTABILITY (2/2)
Example of transverse (slow) head-tail instability observed in the CERN PS at injection (below transition)
  Consecutive traces at a pick-up superimposed
  Standing-wave patterns with 4 nodes (called “mode 4”)

## Slide 73: TRANSVERSE (SLOW) HEAD-TAIL INSTABILITY (2/2)
Example of transverse (slow) head-tail instability observed in the CERN PS at injection (below transition)
  Consecutive traces at a pick-up superimposed
  Standing-wave patterns with 4 nodes (called “mode 4”)
Measurements

## Slide 74: TRANSVERSE (SLOW) HEAD-TAIL INSTABILITY (2/2)
Example of transverse (slow) head-tail instability observed in the CERN PS at injection (below transition)
  Consecutive traces at a pick-up superimposed
  Standing-wave patterns with 4 nodes (called “mode 4”)
Measurements
Analytical prediction (for a bunch going through the centre of the pick-up)

## Slide 75: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (1/14)
A simple formula is obtained from 5 seemingly diverse formalisms (in the absence of space charge and transverse feedback), assuming i) a Broad-Band impedance and ii) the long-bunch regime:

## Slide 76: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (1/14)
A simple formula is obtained from 5 seemingly diverse formalisms (in the absence of space charge and transverse feedback), assuming i) a Broad-Band impedance and ii) the long-bunch regime:
  Coasting-Beam approach with peak values

## Slide 77: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (1/14)
A simple formula is obtained from 5 seemingly diverse formalisms (in the absence of space charge and transverse feedback), assuming i) a Broad-Band impedance and ii) the long-bunch regime:
  Coasting-Beam approach with peak values
  Fast Blow-Up

## Slide 78: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (1/14)
A simple formula is obtained from 5 seemingly diverse formalisms (in the absence of space charge and transverse feedback), assuming i) a Broad-Band impedance and ii) the long-bunch regime:
  Coasting-Beam approach with peak values
  Fast Blow-Up
  Beam Break-Up

## Slide 79: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (1/14)
A simple formula is obtained from 5 seemingly diverse formalisms (in the absence of space charge and transverse feedback), assuming i) a Broad-Band impedance and ii) the long-bunch regime:
  Coasting-Beam approach with peak values
  Fast Blow-Up
  Beam Break-Up
  Post Head-Tail

## Slide 80: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (1/14)
A simple formula is obtained from 5 seemingly diverse formalisms (in the absence of space charge and transverse feedback), assuming i) a Broad-Band impedance and ii) the long-bunch regime:
  Coasting-Beam approach with peak values
  Fast Blow-Up
  Beam Break-Up
  Post Head-Tail
  Transverse Mode-Coupling Instability (TMCI)

## Slide 81: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (2/14)
Example of TMCI

## Slide 82: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (2/14)
Example of TMCI
Courtesy of Benoit Salvant
Qs
(Synchrotron tune)

## Slide 83: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (2/14)
Example of TMCI
Courtesy of Benoit Salvant
Qs
(Synchrotron tune)

## Slide 84: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (2/14)
Example of TMCI
Courtesy of Benoit Salvant
Qs
(Synchrotron tune)

## Slide 85: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (2/14)
Example of TMCI
Courtesy of Benoit Salvant
Synchrotron period
Instability rise-time
Qs
(Synchrotron tune)

## Slide 86: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (2/14)
Example of TMCI
Courtesy of Benoit Salvant
Synchrotron period
Instability rise-time
Qs
(Synchrotron tune)

## Slide 87: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (2/14)
Example of TMCI
Courtesy of Benoit Salvant
Synchrotron period
Instability rise-time
Qs
(Synchrotron tune)
Qs0 approaching transition

## Slide 88: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (3/14)
i) 1st assumption: Broad-Band impedance

## Slide 89: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (3/14)
i) 1st assumption: Broad-Band impedance
Imaginary part
Real part

## Slide 90: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (3/14)
i) 1st assumption: Broad-Band impedance
Imaginary part
Real part

## Slide 91: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (4/14)
ii) 2nd assumption: long-bunch regime

## Slide 92: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (4/14)
ii) 2nd assumption: long-bunch regime

## Slide 93: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (5/14)
Simple formula (with the 2 assumptions):

## Slide 94: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (5/14)
Simple formula (with the 2 assumptions):

## Slide 95: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (5/14)
Try to decrease the impedance and/or increase the resonance frequency => Impedance reduction campaign
Simple formula (with the 2 assumptions):

## Slide 96: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (5/14)
Try to decrease the impedance and/or increase the resonance frequency => Impedance reduction campaign
Simple formula (with the 2 assumptions):
Change the optics to increase the betatron tune (decrease the beta function at critical impedances) and/or go further away from transition => New optics needed

## Slide 97: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (5/14)
Try to decrease the impedance and/or increase the resonance frequency => Impedance reduction campaign
Increase the beam longitudinal emittance (when possible)
Simple formula (with the 2 assumptions):
Change the optics to increase the betatron tune (decrease the beta function at critical impedances) and/or go further away from transition => New optics needed

## Slide 98: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (5/14)
Try to decrease the impedance and/or increase the resonance frequency => Impedance reduction campaign
Increase the beam longitudinal emittance (when possible)
- Increase the chromatic frequency
- Chromaticity jump in case transition has to be crossed
Simple formula (with the 2 assumptions):
Change the optics to increase the betatron tune (decrease the beta function at critical impedances) and/or go further away from transition => New optics needed

## Slide 99: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (5/14)
Try to decrease the impedance and/or increase the resonance frequency => Impedance reduction campaign
Increase the beam longitudinal emittance (when possible)
- Increase the chromatic frequency
- Chromaticity jump in case transition has to be crossed
Simple formula (with the 2 assumptions):
Change the optics to increase the betatron tune (decrease the beta function at critical impedances) and/or go further away from transition => New optics needed
* No dependence on Qs!

## Slide 100: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (6/14)
In the PS

## Slide 101: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (6/14)
In the PS: even in the presence of the γt jump, together with the change of the sign of both chromaticities when transition is crossed, a fast vertical single-bunch instability is observed (with the nTOF bunch) when no longitudinal emittance blow-up is applied before transition

## Slide 102: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (6/14)
In the PS: even in the presence of the γt jump, together with the change of the sign of both chromaticities when transition is crossed, a fast vertical single-bunch instability is observed (with the nTOF bunch) when no longitudinal emittance blow-up is applied before transition
, R, V signals
Time (10 ns/div)
~ 700 MHz
Head stable
Tail unstable

## Slide 103: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (6/14)
In the PS: even in the presence of the γt jump, together with the change of the sign of both chromaticities when transition is crossed, a fast vertical single-bunch instability is observed (with the nTOF bunch) when no longitudinal emittance blow-up is applied before transition
, R, V signals
Time (10 ns/div)
=> Instability suppressed by increasing the longitudinal emittance
~ 700 MHz
Head stable
Tail unstable

## Slide 104: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (7/14)
=> Similar observation on other beams (e.g. below with the beam for the Antiproton Decelerator) when the longitudinal emittance is too small

## Slide 105: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (7/14)
=> Similar observation on other beams (e.g. below with the beam for the Antiproton Decelerator) when the longitudinal emittance is too small
Courtesy of Rende Steerenberg

## Slide 106: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (8/14)
In the SPS

## Slide 107: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (8/14)
In the SPS

## Slide 108: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (8/14)
In the SPS
Instability (initially) suppressed by increasing the chromaticity

## Slide 109: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (9/14)
1st trace (in red) = turn 2
Last trace = turn 150
Every turn shown
Head
Tail
 Travelling-wave pattern along the bunch

## Slide 110: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (10/14)
1st trace (in red) = turn 2
Last trace = turn 150
Every turn shown

## Slide 111: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (11/14)
γt was recently modified in the SPS to increase the TMCI intensity threshold above the foreseen intensities for the future upgrade

## Slide 112: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (11/14)
γt was recently modified in the SPS to increase the TMCI intensity threshold above the foreseen intensities for the future upgrade
Simple rough estimate of γt for machines made of simple FODO cells:

## Slide 113: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (11/14)
γt was recently modified in the SPS to increase the TMCI intensity threshold above the foreseen intensities for the future upgrade
Simple rough estimate of γt for machines made of simple FODO cells:
  Approximating the machine radius by the bending radius, yields

## Slide 114: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (11/14)
γt was recently modified in the SPS to increase the TMCI intensity threshold above the foreseen intensities for the future upgrade
Simple rough estimate of γt for machines made of simple FODO cells:
  Approximating the machine radius by the bending radius, yields

## Slide 115: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (11/14)
γt was recently modified in the SPS to increase the TMCI intensity threshold above the foreseen intensities for the future upgrade
Simple rough estimate of γt for machines made of simple FODO cells:
  Approximating the machine radius by the bending radius, yields
  Inserting this in the definition of αp (and then expressing γt) yields

## Slide 116: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (11/14)
γt was recently modified in the SPS to increase the TMCI intensity threshold above the foreseen intensities for the future upgrade
Simple rough estimate of γt for machines made of simple FODO cells:
  Approximating the machine radius by the bending radius, yields
  Inserting this in the definition of αp (and then expressing γt) yields

## Slide 117: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (11/14)
γt was recently modified in the SPS to increase the TMCI intensity threshold above the foreseen intensities for the future upgrade
Simple rough estimate of γt for machines made of simple FODO cells:
  Approximating the machine radius by the bending radius, yields
  Inserting this in the definition of αp (and then expressing γt) yields
    => If one wants to modify γt, (increase or decrease its value) one should modify the horizontal tune

## Slide 118: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (12/14)
TMCI intensity threshold with the old (Q26) optics at injection: ~ 1.7 1011 p/b

## Slide 119: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (12/14)
TMCI intensity threshold with the old (Q26) optics at injection: ~ 1.7 1011 p/b
Predictions going from Q26 to the new (Q20) optics:

## Slide 120: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (12/14)
TMCI intensity threshold with the old (Q26) optics at injection: ~ 1.7 1011 p/b
Predictions going from Q26 to the new (Q20) optics:
  Q26:

## Slide 121: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (12/14)
TMCI intensity threshold with the old (Q26) optics at injection: ~ 1.7 1011 p/b
Predictions going from Q26 to the new (Q20) optics:
  Q26:
  Q20:

## Slide 122: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (12/14)
TMCI intensity threshold with the old (Q26) optics at injection: ~ 1.7 1011 p/b
Predictions going from Q26 to the new (Q20) optics:
  Q26:
  Q20:
  => A gain of a factor 0.0362 / 0.0162 ≈ 2.2 in the intensity threshold was expected

## Slide 123: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (13/14)
Measurements
=> Good agreement with simple formula

## Slide 124: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (13/14)
Measurements
=> Good agreement with simple formula
Courtesy of Benoit Salvant et al.

## Slide 125: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (13/14)
Measurements
=> Good agreement with simple formula
Courtesy of Benoit Salvant et al.
Courtesy of Hannes Bartosik et al.

## Slide 126: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (13/14)
Measurements
=> Good agreement with simple formula
Gain of a factor 4.5 / 1.7 ≈ 2.6
Courtesy of Benoit Salvant et al.
Courtesy of Hannes Bartosik et al.

## Slide 127: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (14/14)
Very good agreement between measurements and simulations

## Slide 128: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (14/14)
Very good agreement between measurements and simulations
Courtesy of Hannes Bartosik et al.

## Slide 129: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (14/14)
Very good agreement between measurements and simulations
Courtesy of Hannes Bartosik et al.

## Slide 130: FAST (VERTICAL) SINGLE-BUNCH INSTABILITY (14/14)
Very good agreement between measurements and simulations
=> Intensity threshold with the new (Q20) optics: ~ 4.5 1011 p/b
Courtesy of Hannes Bartosik et al.

## Slide 131: CONCLUSION (1/2)
Stability of synchrotron motion (when crossing transition):

## Slide 132: CONCLUSION (1/2)
Stability of synchrotron motion (when crossing transition):

## Slide 133: CONCLUSION (1/2)
Stability of synchrotron motion (when crossing transition):
Head-Tail instability (when crossing transition): change the sign of the chromaticity (both planes) => Positive chromatic frequency

## Slide 134: CONCLUSION (1/2)
Stability of synchrotron motion (when crossing transition):
Head-Tail instability (when crossing transition): change the sign of the chromaticity (both planes) => Positive chromatic frequency

## Slide 135: CONCLUSION (1/2)
Stability of synchrotron motion (when crossing transition):
Head-Tail instability (when crossing transition): change the sign of the chromaticity (both planes) => Positive chromatic frequency
  Transverse Mode-Coupling Instability => With the 2 assumptions: i) Broad-Band impedance and ii) long-bunch regime (effects of space charge and transverse feedback still under discussion…)

## Slide 136: CONCLUSION (1/2)
Stability of synchrotron motion (when crossing transition):
Head-Tail instability (when crossing transition): change the sign of the chromaticity (both planes) => Positive chromatic frequency
  Transverse Mode-Coupling Instability => With the 2 assumptions: i) Broad-Band impedance and ii) long-bunch regime (effects of space charge and transverse feedback still under discussion…)
  Impedance reduction

## Slide 137: CONCLUSION (1/2)
Stability of synchrotron motion (when crossing transition):
Head-Tail instability (when crossing transition): change the sign of the chromaticity (both planes) => Positive chromatic frequency
  Transverse Mode-Coupling Instability => With the 2 assumptions: i) Broad-Band impedance and ii) long-bunch regime (effects of space charge and transverse feedback still under discussion…)
  Impedance reduction
  Increase longitudinal emittance (as in the PS)

## Slide 138: CONCLUSION (1/2)
Stability of synchrotron motion (when crossing transition):
Head-Tail instability (when crossing transition): change the sign of the chromaticity (both planes) => Positive chromatic frequency
  Transverse Mode-Coupling Instability => With the 2 assumptions: i) Broad-Band impedance and ii) long-bunch regime (effects of space charge and transverse feedback still under discussion…)
  Impedance reduction
  Increase longitudinal emittance (as in the PS)
  Increase the |slip factor| (as in the SPS) and/or the tune

## Slide 139: CONCLUSION (1/2)
Stability of synchrotron motion (when crossing transition):
Head-Tail instability (when crossing transition): change the sign of the chromaticity (both planes) => Positive chromatic frequency
  Transverse Mode-Coupling Instability => With the 2 assumptions: i) Broad-Band impedance and ii) long-bunch regime (effects of space charge and transverse feedback still under discussion…)
  Impedance reduction
  Increase longitudinal emittance (as in the PS)
  Increase the |slip factor| (as in the SPS) and/or the tune
  Increase the chromatic frequency (below or above transition)

## Slide 140: CONCLUSION (1/2)
Stability of synchrotron motion (when crossing transition):
Head-Tail instability (when crossing transition): change the sign of the chromaticity (both planes) => Positive chromatic frequency
  Transverse Mode-Coupling Instability => With the 2 assumptions: i) Broad-Band impedance and ii) long-bunch regime (effects of space charge and transverse feedback still under discussion…)
  Impedance reduction
  Increase longitudinal emittance (as in the PS)
  Increase the |slip factor| (as in the SPS) and/or the tune
  Increase the chromatic frequency (below or above transition)
  “Chromaticity jump” when transition needs to be crossed => Not only the sign needs to be changed (for Head-Tail reason) but the shape could be optimised (for TMCI reason)

## Slide 141: CONCLUSION (2/2)
Increasing the |slip factor| also helps for i) the Longitudinal Mode-Coupling Instability and ii) the fast single-bunch electron cloud instability

## Slide 142: CONCLUSION (2/2)
Increasing the |slip factor| also helps for i) the Longitudinal Mode-Coupling Instability and ii) the fast single-bunch electron cloud instability
Attractive operation of synchrotrons under an isochronous or quasi-isochronous condition to (naturally) achieve very short bunches

## Slide 143: CONCLUSION (2/2)
Increasing the |slip factor| also helps for i) the Longitudinal Mode-Coupling Instability and ii) the fast single-bunch electron cloud instability
Attractive operation of synchrotrons under an isochronous or quasi-isochronous condition to (naturally) achieve very short bunches
=> Requires

## Slide 144: CONCLUSION (2/2)
Increasing the |slip factor| also helps for i) the Longitudinal Mode-Coupling Instability and ii) the fast single-bunch electron cloud instability
Attractive operation of synchrotrons under an isochronous or quasi-isochronous condition to (naturally) achieve very short bunches
=> Requires
    An accurate control of the first high-order component of the momentum compaction factor to provide the necessary momentum acceptance

## Slide 145: CONCLUSION (2/2)
Increasing the |slip factor| also helps for i) the Longitudinal Mode-Coupling Instability and ii) the fast single-bunch electron cloud instability
Attractive operation of synchrotrons under an isochronous or quasi-isochronous condition to (naturally) achieve very short bunches
=> Requires
    An accurate control of the first high-order component of the momentum compaction factor to provide the necessary momentum acceptance

## Slide 146: CONCLUSION (2/2)
Increasing the |slip factor| also helps for i) the Longitudinal Mode-Coupling Instability and ii) the fast single-bunch electron cloud instability
Attractive operation of synchrotrons under an isochronous or quasi-isochronous condition to (naturally) achieve very short bunches
=> Requires
    An accurate control of the first high-order component of the momentum compaction factor to provide the necessary momentum acceptance
    Effective ways to damp all the collective instabilities

## Slide 147: REFERENCES
E. Métral and D. Möhl, Transition Crossing, Volume I of "Fifty years of the CERN Proton Synchrotron”, CERN–2011–004, June 2011, p. 59 (http://project-ps50.web.cern.ch/project-PS50/Document_proof/for-printer/cern2011-004.pdf)
and all the references therein
Detailed studies for the CERN PS => Sandra Aumon, High Intensity Beam Issues in the CERN PS, CERN-THESIS-2012-261 (http://cds.cern.ch/record/1517412/files/CERN-THESIS-2012-261_2.pdf). Supervisor: Simone Gilardoni
Detailed studies for the CERN SPS => Hannes Bartosik, Beam Dynamics and Optics Studies for the LHC Injectors Upgrade, CERN-THESIS-2013-25 (http://cds.cern.ch/record/1644761/files/CERN-THESIS-2013-257.pdf). Supervisor: Yannis Papaphilippou