## Slide 1
BEAM LOSS CONSEQUENCES
Francesco Cerutti
on Intensity Limitations in Particle Beams
CERN November 2015

## Slide 2
BEAM LOSSES
on beam intercepting devices (targets, collimators, dumps, stoppers, stripping foils, … )
  regular
  accidental: smearing failures, injection mis-steering, asynchronous beam dump, top-off
diffused
  synchrotron radiation, beam-gas interaction, gas bremsstrahlung
debris from regular collisions at the interaction points
on unexpected obstacles (UFO, ULO, … )

## Slide 3
interplay of many physical processes described by different theories/models
multiple scattering
hadron-nucleus
reaction
particle decay
low energy neutron
reaction
ionization
electromagnetic
shower
6 GeV proton in liquid argon
the microscopic view
INTERACTION WITH (ACCELERATOR) MATERIAL:

## Slide 4
proton beam on a 1 m long and 10 cm radius copper rod
160 MeV
7 TeV
LINAC4
and LHC
the macroscopic view
INTERACTION WITH ACCELERATOR MATERIAL:
ionization
electromagnetic shower

## Slide 5
Heating energy deposition (integral power)
Thermal shock energy deposition (power density)
Quenching energy deposition (power density)
Deterioration energy deposition (dose), particle fluence, DPA
Oxidation, radiolysis, ozone production energy deposition
Gas production residual nuclei production
Single event effects in electronic devices high energy hadron fluence [+ neutron fluence, energy deposition (dose)]
Shielding requirements particle fluence (prompt dose equivalent)
Access limitations, radioactive waste, air activation residual dose rate and activity
Beam Loss Monitors (BLM) energy deposition
Radiation Monitors (RadMon) thermal neutron and high energy hadron fluence
Tumor cell destruction energy deposition (dose, biological dose)
CONSEQUENCES
relevant macroscopic quantity

## Slide 6
ENERGY LOSS BASICS [I]
mean energy loss rate
C. Amsler et al.,
Phys. Lett. B667 (2008) 1
bremsstrahlung
ionization
20 MeV for e - on Cu
shell, Barkas, Mott corrections
effective charge for low energy high Z ions

## Slide 7
ENERGY LOSS BASICS [II]
ionization energy loss fluctuations
J.Bak et al.,
Nucl. Phys. B
288 (1987) 681
2 GeV/c beams
on 0.1mm Si
protons
positrons
energy deposition
200 MeV protons in water

## Slide 8
3 MeV PROTON DUMP
Intensity: 65mA over 100μs
Beam size: 4.5mm σx = σy
orthogonal impact
tilting
beam
z
y
85% gain!
C. Maglioni, V. Vlachoudis, EDMS 1182648
graphite

## Slide 9
HIGH Z ION BEAMS
350 MeV/n 238U
two pulses
one pulse
per beam particle
dE/dz [10 MeV/mm]
1 mm
GSI S-334 experiment (courtesy of J. Lettry)
Intensity: 2.4 109 ions per pulse
Beam size: 0.85 mm FWHM
tantalum target

## Slide 10
HIGH ENERGY PROTON BEAMS
Fe 7.9 26 1.76 15.1
Beam particles cannot come to rest
and are lost by nuclear non-elastic interaction …
… generating neutral pions whose decay
initiates electromagnetic showers

## Slide 11
HADRONIC AND ELECTROMAGNETIC SHOWERS
particle fluence and energy deposition development
100 GeV protons on lead
100 GeV protons on iron
space-averaged particle spectra

## Slide 12
ENERGY DEPOSITION
transversally integrated
[different from peak density profile, which depends on beam size]

## Slide 13
5 TeV PROTON BUNCH ON TERTIARY COLLIMATOR [I]
Intensity: 1.3 1011 p
Beam size: 1.75 μm rad norm. emittance (0.3 mm sx and 0.19 mm sy)

## Slide 14
5 TeV PROTON BUNCH ON TERTIARY COLLIMATOR [I]
Pmax 30 GPa
t = 1 ns
t = 85 ns
t = 2.8 ms
Compression Wave (red)
+ Rarefaction Wave (blue)
Compression Wave
reaches W-Cu interface
t = 3.2 ms
t = 4.2 ms
t = 5.6 ms
t = 6.6 ms
t = 3.7 ms
Compression Wave
reaches Cu-Ni Pipes
Pmax 160 MPa
Pmax 500 MPa
Pmax 2.2 GPa
Compression Wave bouncing back in W jaw
courtesy of A. Bertarelli and his team
shock wave propagation
Intensity: 1.3 1011 p
Beam size: 1.75 μm rad norm. emittance (0.3 mm sx and 0.19 mm sy)

## Slide 15
courtesy of A. Bertarelli and his team
Plastic Strain
Max 1.4%
(on Water Pipes)
Particle spray on the opposite jaw Sticking droplets?
~8 mm
Intensity: 1.3 1011 p
Beam size: 1.75 μm rad norm. emittance
(0.3 mm sx and 0.19 mm sy)
5 TeV PROTON BUNCH ON TERTIARY COLLIMATOR [III]

## Slide 16
6.5 TeV PROTON BEAM REGULAR CLEANING
Cumulated losses: 1.15 1016 p per year on the betatron cleaning insertion collimators
passive absorbers
~3MGy
~2MGy
shower from the collimators
additional factor 3
peak dose reduction provided by tungsten masks
warm magnets

## Slide 17
IP7
TCP B1
Q5
Q4
TCP
LOSS PATTERN MEASUREMENT AND PREDICTION
Loss rate: 1 MW on the betatron cleaning insertion collimators

## Slide 18
THE LHC 14 TeV CoM COLLISION DEBRIS
150 W absorbed in the TAS
650 W going through the TAS
of which
150 W absorbed in the triplet
proton-proton collisions
950 W towards each (L&R) side
Instantaneous luminosity: 1034 cm-2 s-1
right of ATLAS
cold magnets

## Slide 19
DEBRIS CAPTURE IN THE “TRIPLET”
lost in Q1
end of the
TAS shadow
right of ATLAS

## Slide 20
MARGIN TO QUENCH
round optics
142.5 μrad half crossing angle
V crossing in ATLAS (IR1)
H crossing in CMS (IR5)
x
x
different behavior reflecting the crossing plane variation for the same
magnetic configuration of the triplet (FDF in the horizontal plane for
positively charged particles coming from the IP)
- IR1 triplet (Q2a) reaches the design limit at nominal luminosity
peak dose [MGy] after 300 fb-1, relevant for triplet (i.e. coil insulator) lifetime

## Slide 21
DISPLACEMENTS PER ATOM
It is a “measure” of the amount of radiation damage in inorganic materials 0.3 dpa means that on average 3 atoms out of 10 have been displaced once from their site within the structural lattice
Displacement damage can be induced by all particles
produced in the hadronic cascade, including high energy photons
(through photonuclear reactions).
It is directly related to energy transfers to atomic nuclei
i.e. (restricted) NIEL
Sn/S is going down with energy and up with charge
 NIEL/DPA are dominated by low energy heavy recoils!
partition function Sn/(Sn+Se)
16O in Silicon
107Ag
in Gold
total kinetic
nuclear stopping power

## Slide 22
SUPERCONDUCTOR DEGRADATION
tracklength fraction [%] | 
photons | 88
electrons/positrons | 7
neutrons | 4
pions | 0.45
protons | 0.15
[N. Mokhov
and his team]
HL-LHC
Integrated luminosity: 3000 fb-1
Nb3Sn coils
dominant contribution to DPA
from recoils by low energy (<20 MeV) neutrons

## Slide 23
HYDROGEN AND HELIUM GAS PRODUCTION
Spallation reactions induced by protons, neutrons, pions, … produce a variety of particles including protons (1H), deuterons (2H) , tritons (3H), 3He, and alphas (4He). The least energetic of these products (which are also the most abundant) can stop in the target assembly giving rise to a hydrogen and helium buildup.
These gases can lead to grain boundary embrittlement and accelerated swelling.
In the case of the CNGS target, for 1.4 1020 protons on target one expects about 4 1021 H atoms.
Assuming that all H atoms are desorbed from the target solid structures, this corresponds to 150 ml of atomic H at atmospheric pressure (75 ml if we assume they combined into molecules).

## Slide 24
REDOX
Ball bearings exposed
to hadronic showers in air
Ionising radiation creates radicals chemically active
PVC dehydrochlorination by X and g-rays
Cl- ions react with water droplets and create a very corrosive environment
energy deposition

## Slide 25
OZONE PRODUCTION
under the assumption of no O3 decomposition
(yielding in the  expression a neglected term kPeV/V with k decomposition constant
equal to 1.4 10-16 cm3/eV)
[NCRP Report 51, LEP Note 379]
deposited power
conversion factor

## Slide 26
ELECTRONICS FAILURES [I]
Electronics
Ventilation Units
CV,crane,
fire controls
Gy per 4.5 1019 p.o.t.
CNGS 2007 physics run, 8 1017 protons on target delivered ( 2% of a nominal CNGS year )
Single event upsets in ventilation electronics caused ventilation control failure and interruption of communication
Predicted dose levels
[in agreement with measurements]

## Slide 27
ELECTRONICS FAILURES [II]
collimator controls

## Slide 28
MAIN RADIATION EFFECTS ON ELECTRONICS
 |  |  | relevant physical quantity the effect is scaling with
Single Event effects (Random in time) | Single Event Upset (SEU) | Memory bit flip (soft error) Temporary functional failure | High energy hadron fluence [cm-2] (but also thermal neutrons!)
 | Single Event Latchup (SEL) | Abnormal high current state Permanent/destructive if not protected | High energy hadron fluence [cm-2]
Cumulative effects (Long term) | Total Ionizing Dose (TID) | Charge build-up in oxide Threshold shift & increased leakage current Ultimately destructive | Ionizing dose [Gy]
 | Displacement damage | Atomic displacements Degradation over time Ultimately destructive | Silicon 1 MeV-equivalent neutron fluence [cm-2] {NIEL -> DPA}

## Slide 29
HOW HIGH ENERGY HADRONS?
28Si(n,xa) cross section
5 MeV
>20 MeV
plus

## Slide 30
MONITORING AND BENCHMARKING
FH>20MeV [cm-2] (L2012) | 5RM08S | 5RM09S
FLUKA | 6.1 108 | 3.0 107
DATA | 4.56 108 (256 upsets) | 4.32 107 (25 upsets)
Agreement within 30%
RadMons
th
ev
qe

## Slide 31
FCCee
FCCee
FCCee
RADIATION LEVELS
LHC + Experiments
Avionic
Sea Level
ISS
COTS Systems
Hardened Electronics
Electronics
Damage
Custom Boards with COTS
Space & Deep Space

## Slide 32
17 GeV ELECTRON BEAM ENVIRONMENT
role of photoneutrons!
courtesy of M. Santana-Leitner
dump of the Linear Coherent Light Source @ SLAC
[rad=0.01Gy]
= 10 Gy
dose limit

## Slide 33
MITIGATION/PREVENTION STRATEGY
design shielding
relocate
identify forbidden regions
install radiation resistant equipment
CNGS radiation issues solved
during shutdown 2007-2008
2007
2008
< 106 heh/cm2
107  109 heh/cm2
high energy hadron fluence
per nominal CNGS year

## Slide 34
FACILITY SHIELDING DESIGN
For radiation protection purposes, depending on the aspects to be considered,
particle fluence in a given location is transformed into effective dose or ambient dose equivalent (Sv)
through the use of respective sets of conversion coefficients, which are a function of particle type and energy.
Prompt dose equivalent outside a radiation facility, reflecting the relevant radiation level in a public space during normal or accidental operation of the facility, is the quantity to minimize below acceptable limits.
top view of the ISR tunnel on the side of the n_TOF EAR-2 vertical beam line
(for neutrons from 1.6 1012 Hz 20 GeV/c protons on lead)
with default* shielding
* 80 cm thick 2m high concrete block
† triple concrete volume + two iron plates
with improved† shielding
0.5 μSv/h classification limit
I. Bergström, V. Vlachoudis, J. Vollaire

## Slide 35
ACTIVATION
A high energy nuclear reaction on a high Z nucleus fills roughly the whole charge and mass intervals of the nuclide chart

## Slide 36
…
…
1h
8h
1d
7d
etc.
I, Dt
0, Dt
In, (Dt)n
DELAYED RADIATION FROM RADIOACTIVE DECAY
Bateman equations
production
rate
growth by parent decay
decay
which are solved for a given irradiation profile at different cooling times
1h
yielding (specific) activities [Bq(/g)] – to be compared to legal exemption limits –
and residual dose rates [uSv/h] by the decay radiation (mainly electromagnetic)

## Slide 37
DURING SHUTDOWN
SM
@ 40 cm
SM
HL-LHC final focus triplet around ATLAS and CMS 900fb-1 between Long Shutdowns
[C. Adorisio and S. Roesler,
HL-LHC TC, Sep 30, 2014]

## Slide 38
AIR ACTIVATION
The activity of an air radioisotope (7Be, 11C, 13N, 15O, 38Cl, 39Cl, etc.) in the irradiation area
at the end of the irradiation period T is
where is the relative air exchange rate during irradiation,
i.e. the fraction of the air volume renewed per unit time
and is the saturation activity
irradiated air volume
differential fluence rate of (hadron) particles (P=p,n,p±)
production cross section
air atom density (T=12C,14N,16O,40Ar)
Amount of activity released into atmosphere all along the irradiation period
( is the time taken by the air flux to reach the release point from the irradiated area)
Amount of activity released into atmosphere after the end of the irradiation
( and as and but referring to the shutdown period)

## Slide 39
Meas. PET
MC Dose
not just damage
HUMAN MATTERS
K. Parodi et al., PMB52, 3369 (2007)
MC PET
TP Dose
1 Field
2 Field
proton therapy (tumor cell destruction)

## Slide 40
CREDITS
In addition to explicit references, work of and material from
I. Besana, V. Boccone, M. Brugger, L.S. Esposito, A. Ferrari,
A. Lechner, R. Losito, A. Mereghetti, N. Mokhov, S. Roesler,
P.R. Sala, L. Sarchiapone, E. Skordis, A. Tsinganis, V. Vlachoudis
CERN FLUKA TEAM and FLUKA COLLABORATION
CERN COLLIMATION TEAM, CERN MAGNET GROUP,
and CERN RADIATION PROTECTION TEAM