## Slide 1: TORCH: a possible application in LHCb
TORCH (Timing Of internally Reflected CHerenkov light) is a detector concept for high-precision TOF over large areas Under development as a possible addition to the LHCb upgrade
R&D project funded by the ERC (2013–16) between CERN, Bristol and Oxford Universities, with industrial partner Photek (UK) Mainly focused on developing a suitable photon detector
Assuming the R&D is successful, a proposal will be made to LHCb for the full detector, which would be a client for the new TDC
New CERN ps TDC meeting, 12 February 2015
Roger Forty (CERN)
Rui Gao (Oxford)

## Slide 2: TORCH detector
TORCH module
Layout for LHCb
MCP pixellisation
MCP prototype
Aiming for 10–15 ps resolution per track, to separate π/K < 10 GeV
Use Cherenkov light trapped in quartz plate, a la DIRC
Focused onto photon detectors around edge, ~ 50 ps / photon
Photon detector MCP-PMT: require 1. long lifetime (done, ALD coating) 2. fine pixellisation (in progress) 3. large active area (next year)
Assuming 1024 channels/MCP Application in LHCb ~ 200 MCPs → ~ 3000 x 64 ch. readout chips

## Slide 3: Prototyping
Prototype prepared for beam test this year
Read-out electronics: NINO + HPTDC Aim to use TOT from NINO for charge measurement → charge division
Test-beam setup
Electronics to read out MCP
NINO32
HPTDC
Readout Adaptor
Readout Board
LHCb upgrade environment: 40 MHz collisions
High track multiplicity → high rate ~ 500 kHz/ch.
35 x 12 x 1cm quartz plate
Focusing + MCP mount
Electronics

## Slide 4: TORCH TDC Requirements -1
Background and constrains: TDC to be integrated with NINO32 (IRPICS-2) front-end and LHCb trigger-less readout.
Time reference: 40Mhz
Hit interface: LVDS is preferred so NINO32 can be connected directly
Hit rates: 1Mhz per channel average, local hit rate may be 5 time higher.
Hit pulse width: should be able to register NINO pulse (2.5-6ns)
Acceptable deadtime:5ns
Time resolution: 12ps binning is fine
Power supply: no particular requirements
Readout: GBT preferred, configurable via GBT-SCA

## Slide 5: TORCH TDC Requirements-2
Trigger requirements:
  Non triggered 40Mhz LHCb trigger-less readout
            Data are aligned using BXID
            Readout only fine counter in TDC to save bandwidth
  Triggered mode are useful for test beams
    Latency: Programmable ranged hundreds nanoseconds,
    Rate: Less than 1Mhz, for test beams only
    Trigger window: Programmable up to 4095 x 25ns
How many TDCs do you need, when:
  Assuming 64-ch TDC, 3K in 5 years time if TORCH detector is approved,
  Individual samples for development
Radiation dosage: Less then 100krad/ year, (100krad/year is the estimated dosage for RICH 2 in upgrade)

## Slide 6: The End

## Slide 7: Back up slides

## Slide 8: NINO32 interfacing to SLVS
0.2v
40R
40R
5mA transistor drivers
Current circuit, IRPICS-1 to drive HPTDC - LVDS
IRPICS-1, Possible SLVS driver
200mV swing, 0.2V common voltage
On PCB
IRPICS-2 has built-in LVDS drivers
AC couple to SLVS – overdrive the SLVS