## Slide 1
DETECTOR TECHNOLOGIES
Lecture 1: Principles of detection
- Generalities about detectors
- Interaction of particles with matter

## Slide 2
Goal :
Observation and identification of final states
(whatever the processus)
A particle : Mass
Electrical Charge
Moment
Energy
Lifetime
(spin, flavour, color….)
A Detector : does not give any measurement.
Gives an information coming after an interaction with the particle

## Slide 3
Energy deposition
- Limited (the particle goes almost undisturbed)
Momentum
Electrical charge (if magnet)
 Trajectography
- Total (the particle stops)
Energy
Various processes
But first : some important notions
(supposed to be known ?)

## Slide 4
Types of detectors :
Trackers (position and momentum measurement)
Calorimeters (energy measurement)
Identifiers (identification of various types of particles)
Trigger counters

## Slide 5
CROSS SECTION :
Probability of a phenomenon (interaction with the detector) to occur.
σ (E) =
F = incident flux of particles
Ns = emitted number of particles
Ω = Solid angle
MEAN FREE PATH :
Average distance travelled by a particle between 2 consecutive interactions
in matter (detector) :
σ = total interaction cross section
n = number of interactive centers per unit volume

## Slide 6
TIME OF FLIGHT :
For particles with a timelife of o :
Of course, in the laboratory, for a particle with a speed v,
 =  o
and then,
DISTANCE OF FLIGHT :
Mean distance in the detector for a particle with a lifetime ₒ
measured in the laboratory

## Slide 7
Particle | c  (cm)
 | ∞ (stable)
e+ / e- | ∞ (stable)
µ | 6.6 10 4
neutrino | ∞ (stable)
πO | 2.5 10-6
π+ / π- | 780
K+ / K- | 371
K0s | 2.7
K0l | 1554
p | ∞ (stable)
n | 2.7 10 13
High energetic particle (particles at speed ≈ c
quasi-transparent detector

## Slide 8
INTERACTION OF PARTICLE WITH MATTER :
Depends on the type of interactions
ELECTROMAGNETIC : λ ≈ µm
ionization
pairs creation (e+ e-, electrons – holes…)
photon emission (Bremstrahlung, Cerenkov effect)
STRONG : λ ≈ cm
hadronic showers of neutrons
(but the observed signal will be due to EM interaction)
WEAK : λ ≈ 1015 m (neutrinos)
GRAVITY : ??
Depends on the type of particle
CHARGED
NEUTRAL
And of course, ENERGY, MEAN FREE PATH, LIFETIME

## Slide 9
In order to detect a particle, it must
- interact with the material of the detector
- transfer some energy in a recognizable way (signal to be processed)
4 CLASSES OF PARTICLES
Heavy (m > me ) charged particles
Light (m ≈ me ) charged particles
Photons
Hadrons
3 POSSIBILITIES
Ionization (EM)
Radiation (EM)
Nuclear interaction (Strong)

## Slide 10
HEAVY (m > me ) CHARGED PARTICLES : IONIZATION
Energy loss (energy transferred to the medium ) by ionization in MeV g-1 cm2
Where : K = 4 π NA re2 me = 0.3071
A, Z : atomic mass and number relative to the medium
NA : Avogadro’s number
Tmax : maximum possible energy transferred to an electron in the medium
(see J. Collot’s lecture)
z : charge of the incoming particle
,  : relatives to the particle
→ dE/dX in MeV.g-1.cm2
→ valid only for M>m
→ dE/dX depends on ,
→ dE/dX does not depend on M
Bethe-Bloch, 1932

## Slide 11
Non-relativistic
 = p/m < 1  -dE/dx α -5/3
 ≈ 4  Minimum Ionizing Particle (MIP)
Relativistic increase
 > 4  -dE/dx α 2 ln()
HEAVY (m > me ) CHARGED PARTICLES : IONIZATION

## Slide 12
Relativistic rise :
- more distant collisions,
increasing the transverse
electric field with 
Typical for
gas : 1.5
liquid : 1.1
HEAVY (m > me ) CHARGED PARTICLES : IONIZATION

## Slide 13
Direct identification by energy loss
in Ar-CH4 80-20 %
(DELPHI
Direct identification by energy loss
in Ne-CO2 90-10 %
(ALICE TPC)
HEAVY (m > me ) CHARGED PARTICLES : IONIZATION

## Slide 14
Corrections to the Bethe-Bloch formula :
Density effect : the density of the medium will have a screening effect on the relativistic rise (important for solids and liquids)
Gaz
Solids
Liquids
HEAVY (m > me ) CHARGED PARTICLES : IONIZATION

## Slide 15
Corresponds to an energy loss by charged particle : Bethe-Bloch
But : small mass : electrons may be deflected
interaction electron – electron : collisions between identical particles
Bethe-Bloch :
Bethe-Bloch
For electrons
LIGTH (m≈me) CHARGED PARTICLES : IONIZATION

## Slide 16
For any charged particle :
When accelerated (or deccelerated), in the nucleus electric al field,
any charged particle emits photons
From :Bethe, H.A., Heitler, W., 1934. On the stopping of fast particles and on the creation of positive electrons
Z : médium
z, m, E : particle
CHARGED PARTICLES : RADIATION (Bremsstrahlung)
= 1 for e+, e-
= 1.3 10-5 for µ
= 2.3 10-5 for π
= 2.7 10-7 for p
Up to 100 GeV, on can neglect the
Bremssttrahlung if particle ≠ e+ or e-

## Slide 17
Xo : radiation length (characteristic of the medium)
Medium | Xo (g cm-2)
Hydrogen | 63.1
Helium | 94.3
Carbon | 42.7
Aluminium | 24.0
Iron | 13.8
CHARGED PARTICLES : RADIATION (Bremsstrahlung)
For electrons,
Can be rewritten as

## Slide 18
CONSEQUENCE : CRITICAL ENERGY
The energy loss has 2 components :
- ionization (for heavy and energetic particles, it is ≈ constant
- radiation ( for heavy particles, it is almost negligible) proportional to E
The critical energy (Ec) is defined as the energy at which the two mechanisms are equal
For gas
For liquids and solids

## Slide 19
Note : table for electrons only (the most sensitive)
for other particles, it would scale to the square of the particle mass

## Slide 20
INTERACTION OF CHARGED PARTICLES

## Slide 21
CHARGED PARTICLES (Hadrons) : Coulomb scattering and interactions
Hadrons are interacting mainly with the nucleus by (strong interaction)
- collisions (coulomb))
- interaction (strong force)
X
Phenomenon governed by the interaction lengths λT (collisions) and λi (interactions)

## Slide 22
Range : measured of the stopping power
for various material
for different energies (momentum)

## Slide 23
Hadronic shower : λ instead of Xo

## Slide 24
CONSEQUENCE : RANGE IN MATTER
In a medium a particle will loose its energy by any means
(ionization radiation, scattering) until it stops in the medium
Of course, it depens on the MASS and ENERGY of the incoming particle
Of course, it depens on the DENSITY and the THICKNESS of the medium
Almost negligible for High Energy Physics

## Slide 25
ENERGY LOSS DISTRIBUTION
The Bethe-Bloch formula describes the average energy loss of charged particles.
But there can be large fluctuations which have an effect on larger energy losses
The fluctuation around the mean is decribed by an asymetric distribution
Landau distribution :
In fact, for thin absorbers, the reality is more a convolution
of a Landau and a Gaussian distribution…
Energy deposited by 736 MeV/c proton in Silicon
(Xo = 9.4 cm , Ec = 39 MeV for electrons)

## Slide 26
INTERACTION OF PHOTONS
Photons are interacting with matter through 3 types of processes:
- Photoelectric emission Absorption
σ 1 / E3
- Compton scattering Deflection
σ 1 / E
- Pair production Absorption
σ constant (above threshold)
Note : Main effect : electron production.
Attenuation
µ : realtive to the medium and the absorption cross section
σABS = σphot + σCompton + σpairs

## Slide 27
INTERACTION OF PHOTONS : PHOTOELECTRIC EMISSION
A. Einstein, 1905
 + A A+ + e-
Again : Energy transfert to an electron :
Ee = E  - Ebinding
For E  > Ebinding σphot Z5 / E  7/2
For E  >> Ebinding σphot Z5 / E 
Dominant process for E  < 100 keV

## Slide 28
h
h’
e-

T
INTERACTION OF PHOTONS : COMPTON SCATTERING
e
Cross section : calculated using QED :
Klein – Nishima formula
Θe can not be > /2
Intergating over Ω :
σCompton =
σCompton α Z / E 

## Slide 29
INTERACTION OF PHOTONS : PAIRS PRODUCTION
  e- + e+
Needs a nucleus
or another electron…
Threshold :
And because m nucleus >> m e
Cross section :
For higher energies ( > 10 MeV) :
Note : If enough energy, the positron will annihilate with another electron,
producing another photon, which will annihilate in a pair …
Electromagnetic shower

## Slide 31
INTERACTION OF PHOTONS : PAIRS PRODUCTION
Note : If enough energy, the positron will annihilate with another electron, producing another photon, which will annihilate in a pair …
Electromagnetic shower
The ATLAS electromagnetioc calorimeter

## Slide 32
CERENKOV EMISSION
When a particle is moving faster than the velocity of ligth in a given medium
production of photons
Treshold : (n is the refractive index of the medium)
Photon production is rather small :
Energy loss is very small (can be neglected):
10-3 MeV.cm2.g-1 for solids
0.01 – 0.2 MeV.cm2.g-1 for He, H2
Typical : 0.35 µm < λ cerenkov < 0.55 µm

## Slide 33
Identification of particles by measurement of Θ (Experience Babar)

## Slide 34
TRANSITION RADIATION
Transition radiation is a photon emission (X) occuring when a charged particle passes through inhomogeneous media, such as a boundary between two different media with different dielectric properties
Emission at an angle
Very low rate
In the momentum range 1 – 10 GeV, only electrons produce transition radiation with a relatively low probablity (1%) per boundary crossing.
Thus, a TRD is mostly used for electron identification.